## Slide 1
KMAKorea Meteorological Administration
NMSC National Meteorological satellite center
DCC BRDF
produced by SBDART model
for COMS visible calibration
GSICS WebMeeting, 14 August 2013
Minjin CHOI
National Meteorological Satellite Center / Korea Meteorological Administration
Korea

## Slide 2
GSICS Activity of KMA for visible channel
KMA Installed vicarious calibration system for visible channel using 5 targets. ocean, desert, water cloud, deep convective cloud (DCC), moon
We have tested with these target data since 2011.
Target | Ocean | Desert | Water cloud | Deep convective cloud | Moon
Period | Sep. 2011 ~ Present |  |  |  | 
Source | Regular observation |  |  |  | Special obs. (twice a month)
Obs. | - Pacific Ocean - Indian Ocean | - Simpson Desert in Australia | - Over ocean regions - Overcast clouds | - High reaching overcast clouds | - moon

## Slide 3
Result from DCC target is consistent with other target data, making linear regression line with high correlation.
The degradation are about 4.36% (2.75%/year) from the moon and 3.28% (2.07%/year) from the other 4 targets from Sep. 2011 to Apr. 2013.
Result of GSICS will be displayed on KMA’s homepage by the end of 2013.
GSICS Activity of KMA for visible channel

## Slide 4
Satellite data
Well-calibrated
IR band (10.8 μm)
TB11
Selected DCC pixels
Assumption of input parameters
COT=200, re = 20 μm,
Cloud height = 1~15km
Tropical profiles
Simulated visible radiances
Yes
No
Observed visible radiances
Vicarious calibration
Cloud Radiative transfer modeling
Visible band (0.67 μm)
Same FOV
vicarious calibration algorithm using DCC
Sohn et al. 2009, Ham and Sohn2010
Threshold conditions
1
2
3

## Slide 5
target pixel
9 x 9
environmental pixels
STD,
STD/Mean
part 1: Selection of DCC targets
Threshold conditions to select the overshooting DCCs
Solar geometry |  | SZA ≤ 40º
Viewing geometry |  | VZA ≤ 40º
 | - geometry criteria: to minimize navigation errors and 3-D radiative effects | 
Surface type |  | No restriction
 | - no restriction of surface type: less influence on reflectance of DCC targets | 
Cloud conditions (1) |  | target pixel: TB11 ≤ 190 K
 | - only temperature criterion: overshooting DCCs represent cloud top temperature lower than the TTL temperature (~190 K) | 
Cloud conditions (2) |  | environmental pixel: STD(TB11) ≤ 1K
 |  | environmental pixel: STD(R0.6)/Mean(R0.6) ≤0.03
 | - two types of homogeneity checks: to avoid selection of cloud edge or small-scale plumes | 
TB11: brightness temperature at 10.8 μm, R0.6: reflectance at 0.67 μm, STD: standard deviation in environmental (9x9) pixels
convective clouds whose tops extended from 14 to 19 km with extremely high reflectivity

## Slide 6
part 2: cloud RTM description (1/2)
DISORT model
SBDART (Santa Barbara Disort Radiative Transfer) model (Ricchiazzi et al. 1998) - based on DISORT (Discrete Ordinates Radiative Transfer) model - capable up to 32 streams - relatively accurate and efficient RTM for cloudy atmosphere
KMA used some options as follows:
  phase function: delta-fit method (Hu et al. 2000) - bulk phase function: strong forward peak and thousands of Legendre polynomials - needed to truncate method for the phase function in the forward direction - to reduce the computational burden without degrading accuracy
  gases absorption: correlated-k-distribution (CKD) method (Kratz 1995; Kratz and Rose 1999) - gaseous absorption associated with Rayleigh scattering
  sfc. info.: oceanic surface properties for any surface type

## Slide 7
part 2: cloud RTM description (2/2)
DISORT model
Scattering properties: Baum model Baum et al. (2005a and 2005b) for non-spherical ice particles
  - based on in-situ measurements to obtain habit fractions (Heymsfield et al., 2002) - use single scattering properties of droxtals, hexagonal plates, hollow columns, solid columns, bullet rosettes, and aggregates
  (Yang and Liou, 1996a and 1996b; Yang et al., 2003a and 2003b) - band averaged scattering properties with respect to re by integration of single scattering properties
    Qext (extinction efficiency), ω0 (Single scattering albedo),
    g (asymmetry factor), P(Θ) (phase function), fd (delta transmitted energy)

## Slide 8
part 2: RTM inputs
# of streams | 20 | Cloud conditions | Ice phase (use Baum scattering model)
Simulation wavelength | 0.57488 μm – 0.77992 μm |  | COT = 200
 | (interval: 0.04101μm) |  | Effective radius = 20 μm
Filter function | rectangular filter |  | Cloud top-height = 15 km
Geometry | SZA, VZA, SAA, VAA (Observed pixels information) |  | Cloud depth = 14 km
surface type (BRDF) | Ocean |  | 
atmosphere | Tropical standard profile |  | 
Input |  | Sfc. | Atmos. | AOT | Cloud |  |  | 
Parameters |  | albedo | profiles | At 0.55 μm | COT | re | Zc | Zc
Reference value |  | Oceanic | TRO | 0 | 200 | 20 μm | 15 km | 14 km
Input range |  | 0 – 0.4 | MLS | 0 – 3 | 100 – 400 | 10 – 30 | 12 – 18 | 10 – 14
Maximum uncertainty | SZA = 0º | 0.09% | 1.29% | 0.14% | 4.79% | 1.64% | 0.15% | 0.24%
 | SZA = 10º | 0.09% | 1.29% | 0.14% | 4.79% | 1.96% | 0.16% | 0.24%
 | SZA = 20º | 0.09% | 1.29% | 0.14% | 4.74% | 2.35% | 0.18% | 0.24%
 | SZA = 30º | 0.09% | 1.30% | 0.14% | 4.60% | 3.02% | 0.21% | 0.24%
 | SZA = 40º | 0.08% | 1.30% | 0.13% | 4.41% | 3.02% | 0.21% | 0.24%
uncertainty ranges
in Appendix of Sohn et al. (2009)
RTM input parameters for COMS calibration using DCC target

## Slide 9
part 3: Methodology for DCC BRDF test
BRDF structure
0º
180º
90º
270º
20º
40º
60º
radial axis
VZA
tangential axis
RAA
incident radiation
SZA
- geometry (degree)
  - SZA = [10, 20, 30, 40]
  - VZA = [0, 5, 10, … 55, 60]
  - RAA = [5, 15, 20, … 170, 175]
RAA: relative azimuth angle between SAA and VAA
(0 ≤ RAA <180)
- cloud parameter
  - COT = [50, 75, 100, 200, 400]
  - Re = [10, 20, 30, 40] (μm) - cloud top height = 15 km - cloud base height =1 km
- other inputs
  - COMS ch.1 (0.675 μm), MODIS ch.1, 2, 3, 4
  - tropical standard profile
Test plan

## Slide 10
75
100
200
400
10 μm
20 μm
30 μm
40 μm
part 3: Results 1
(SZA = 20º)
0º
180º
90º
270º
20º
40º
60º

## Slide 11
75
100
200
400
10 μm
20 μm
30 μm
40 μm
0º
180º
90º
270º
20º
40º
60º
part 3: Results 2
(SZA = 30º)

## Slide 12
part3: Result 3
SZA = 20º, COT = 200, Re = 20 μm
COMS ch.1
(0.675 μm)
MODIS ch.1
(0.645 μm)
MODIS ch.2
(0.847 μm)
MODIS ch.3
(0.466 μm)
MODIS ch.4
(0.554 μm)
Qext | 2.0022 | 2.0019 | 1.9963 | 2.0038 | 1.9942
ω0 | 1.0000 | 1.0000 | 0.9999 | 1.0000 | 1.0000
g | 0.8118 | 0.8118 | 0.8124 | 0.8100 | 0.8105
0º
180º
90º
270º
20º
40º
60º
0º
180º
90º
270º
20º
40º
60º
0º
180º
90º
270º
20º
40º
60º
0º
180º
90º
270º
20º
40º
60º
0º
180º
90º
270º
20º
40º
60º
0.94 – 1.00

## Slide 13
Summary
SBDART model could be constructed bi-directional reflectance distribution structure above cloud layer with respect to various input parameters and wavelength of channels, not implying Lambertian surface.
simulated reflectance using SBDART for COMS vicarious calibration is ranging from 0.93 to 1.02.
DCC BRDF is highly dependent on scattering parameterization of RT model.
Vicarious calibration for COMS using DCC target has been conducted well in spite of dependency on the result of RT model simulation.
Result from DCC target is consistent with other target data and the degradation are about 3.28% (2.07%/year) from Sep. 2011 to Apr. 2013.

## Slide 14
Back-up slides

## Slide 15: COMS
Communication, Ocean, and Meteorological Satellite(COMS)
Location : 128.2°E
Operational : April 1st, 2011~
Design life time : 7 years(2011~2018)
Payload : MI(Meteorological Imager)
GOCI(Geostationary Ocean Color Imager)
Transponder for communication
The first visible image of COMS
(2010. 7. 12 11:15 KST)

## Slide 16: Visible channel radiometric model
Radiance: R = m∙X + b ( )
where m = linear calibration coefficient, i.e. the slope (pre-launch determined)
X = digital counts
b = intercept (measured by the count values of spacelook data)
No on-board calibration for slope m
⇒ Ground calibration must be needed!!

## Slide 17: Results (Scatter Plot)
Date | Slope | Intercept | Date | Slope | Intercept
2011.09 | 0.866794 | 0.030549 | 2012.07 | 0.847942 | 0.039423
2011.10 | 0.883913 | 0.015551 | 2012.08 | 0.871089 | 0.024997
2011.11 | 0.865026 | 0.033198 | 2012.09 | 0.870726 | 0.023313
2011.12 | 0.869005 | 0.020513 | 2012.10 | 0.859446 | 0.025622
2012.01 | 0.873601 | 0.018751 | 2012.11 | 0.873348 | 0.016775
2012.02 | 0.871341 | 0.025278 | 2012.12 | 0.859193 | 0.022906
2012.03 | 0.860161 | 0.026934 | 2013.01 | 0.856222 | 0.021422
2012.04 | 0.878237 | 0.024862 | 2013.02 | 0.864552 | 0.014774
2012.05 | 0.881722 | 0.025316 | 2013.03 | 0.854285 | 0.018082
2012.06 | 0.870585 | 0.027393 | 2013.04 | 0.856494 | 0.02709
Scatter plot by using ocean/desert/WC/DCC
- slope= 0.864972
- intercept= 0.024749

## Slide 18: Results (Time Series)
The mean values of ratio for each target are between -2.5~ -1.2%/year from September 2011 to April 2013.
All methods for respective targets are different from each other. But, all targets have the similar trend with negative slope.
 | Slope | Intercept | Change of means(%/year)
Desert | -0.2093 | 103.2595 | -2.5116
Moon | -0.1588 | 96.8657 | -1.9056
WC | -0.1384 | 93.3438 | -1.6608
DCC | -0.1050 | 89.8470 | -1.26
Slopes and intercepts of regression lines for each target

## Slide 19: The number of sampled points
The mean of sampled days of desert and DCC are over 15 days. On the other sides, These values related about ocean and WC are under 15.

## Slide 20: Results (Degradation)
The degradation are about 4.36%(2.75%/year) from the moon and 3.28%(2.07%/year) from the other 4 targets from September 2011 to April 2013.

## Slide 21
Criteria: TB11 ≤ 190K, STD9×9 of TB11 ≤ 1K
MODIS-derived cloud properties for cold clouds (TB ≤ 190K)
More than 85% pixels show COT=100 which means that real COT could be greater than 100.
14.3%
20.4%
65.3%
About 65% of pixels show COT > 150.
Sohn et al. 2009
Observation of MODIS
simulation result

## Slide 22
Sohn et al. 2009
Simulation of MODIS reflectance
(by assuming re=20 μm, COT=200 )
1) Pixel-based value
2) error histogram
3) on daily basis

## Slide 23
comparison of scattering properties
applied Mie phase function
applied Baum scattering model
Cloud BRDF
(SZA=30º, COT=40, 6 kinds of re)
Ham et al. 2009

## Slide 24
10 μm
20 μm
30 μm
40 μm
75
100
200
400
SZA=10º

## Slide 25
10 μm
20 μm
30 μm
40 μm
75
100
200
400
SZA=20º

## Slide 26
10 μm
20 μm
30 μm
40 μm
75
100
200
400
SZA=30º

## Slide 27
10 μm
20 μm
30 μm
40 μm
75
100
200
400
SZA=40º