## Slide 1: Ocean Colour Instrument Calibration
RSP
Ewa J. Kwiatkowska

## Slide 2: What is ocean colour?
Ocean colour
monitoring of oceanic, coastal and inland waters in the visible range of the spectrum
Primary products
water-leaving radiance or reflectance
concentrations of water constituents: marine phytoplankton (chlorophyll pigment), sediments, coloured dissolved matter, water transparency
Climate and seasonal forecasting
coupled ocean-atmosphere physical-biogeochemical models
air-sea CO2 exchange – carbon flux, phytoplankton produce half of the oxygen we breath
air-sea heat exchange – phytoplankton absorption of light and water optical turbidity
Coastal and marine environment
good environmental status of marine environment (EC Marine Strategy Framework Directive)
water quality
harmful algal blooms, natural disasters, human activities
Marine resources management and forecasting
good ecological and chemical status (EC Water Framework Directive)
fisheries, aquaculture
water resources

## Slide 3: Sentinel-3 OLCI
OLCI optical layout
~68.5° FoV
across-
track-tilt
5 cameras
 | OLCI bands |  center |  width
1 | aerosol, in-water properties | 400 | 15
2 | yellow substance, detritus | 412.5 | 10
3 | chlorophyll absorption max | 442.5 | 10
4 | chlorophyll and other pigments | 490 | 10
5 | suspended sediments, red tide | 510 | 10
6 | chlorophyll absorption min | 560 | 10
7 | suspended sediments | 620 | 10
8 | chlorophyll absorption and fluorescence | 665 | 10
9 | fluorescence | 673.75 | 7.5
10 | chlorophyll fluorescence peak | 681.25 | 7.5
11 | chlorophyll fluorescence ref, atmospheric correction | 708.75 | 10
12 | vegetation, clouds | 753.75 | 7.5
13 | O2 R-branch absorption | 761.25 | 2.5
14 | atmospheric parameters, O2A cloud top pressure | 764.375 | 3.75
15 | cloud top pressure | 767.5 | 2.5
16 | O2 P-branch absorption | 778.75 | 15
17 | atmospheric correction | 865 | 20
18 | vegetation, water vapour reference | 885 | 10
19 | water vapour, land | 900 | 10
20 | atmospheric correction, H2O absorption | 940 | 20
21 | atmospheric correction, aerosols | 1020 | 40
OLCI configuration
5 Camera Optical Sub Assemblies (COSA)
5 Focal Plane Assemblies (FPA)
5 Video Acquisition Modules (VAM)
1 Scrambling Window Assembly
1 Calibration Assembly allowing radiometric and spectral calibrations
1 OLCI Electronic Unit (OEU) managing all the instrument functions
OLCI - programmable imaging spectrometer

## Slide 4
Ocean colour observation conditions
satellite observes both oceans and the atmosphere
atmosphere must be accurately modeled and removed
  absorption from gases, O3, H2O, O2, NO2, CO2
  scattering from air molecules
  scattering and absorption from aerosols
(
) ∙ tg
Lt – total top-of-the-atmosphere (TOA) radiance
Lr – radiance from molecular (Rayleigh) scattering, tabulated for sensor wavelengths, geometries, dependent on pressure, wind speed
La – radiance originated from aerosol scattering
Lra – interaction of molecular and aerosol scattering
Lwc – white cap radiance at the surface, approximated using wind speed
Lg – sunglint radiance, estimated using wind-ruffled sea surface model
Lw – water-leaving radiance
transmittances:
t – atmospheric diffuse transmittance, tabulated for aerosol models
T – direct transmittance of the atmosphere
    tg – gaseous t., estimated using gas concentrations and absorption spectra
unknown: La and Lw
OC Sensor

## Slide 5
Ocean colour signal magnitude
Percentage of Lw() in Lt()
1% error in instrument calibration
10% error in water-leaving radiances, Lw
atmosphere contributes approximately 90% of the measured signal
10%
20%
0%
30%
40%
50%
Case 1 – open ocean waters dominated by phytoplankton and their byproducts,
great majority of the global ocean

## Slide 6
Ocean colour accuracy requirements
Measurement requirements
water-leaving radiances, Lw
5% absolute uncertainty in blue/green (all docs)
0.5% stability per decade (GCOS)
chlorophyll concentration, Ca
30% absolute uncertainty (in case 1)
3% stability over a decade (GCOS)
uncertainties are present in processing algorithms, including atmospheric correction
to meet the measurement requirements, Lt need to have uncertainties better than 0.5%
characterization of components (straylight, polarization, diffuser BRDF, detectors...) about 0.2%

## Slide 7
OLCI calibration requirements
absolute radiometric uncertainty 2% (≤ 900nm)
inter-band radiometric uncertainty 1%
no long-term stability requirement
Pre-launch – sensor is characterized in a laboratory
On-orbit – regular radiometric and spectral calibrations track temporal changes in sensor response
      OLCI / MERIS
radiometric calibration
solar diffuser-1 every 15 days
solar diffuser-2 every 3 months
spectral calibration
erbium diffuser every 3 or 6 months
Fraunhofer lines (for validation)
O2 A-band (for validation)
Direct instrument calibration
camera 1
camera 2
camera 3
camera 4
camera 5
MERIS
MERIS
spectral evolution 5cameras
Erbium peak 408nm
Erbium peak 520nm
radiometric evolution

## Slide 8
System Vicarious Calibration
Earth-view – comparison against an independent source; single gain per band
Calibration of the combined instrument-algorithm system
MERIS / OLCI
NIR calibration
oceanic gyres, e.g. South Pacific Gyre
VIS calibration
in situ SI-calibrated source, << 5% Lw uncertainty
2% uncertainty
<< 0.5% uncertainty
Direct calibration
Pre-launch – laboratory
On-orbit – on-board calibrators
Vicarious instrument calibration
Measurement requirements
water-leaving radiances, Lw
5% absolute uncertainty in blue/green

## Slide 9
GSICS vicarious calibration methods
Calibration verification methods
  Absolute calibration over Rayleigh – uncertainty ~ 3.5%
  Inter-band calibration over sunglint – uncertainty ~ 2%
  Inter-band calibration over DCC – uncertainty ~2%
  Cross-calibration over desert – uncertainty ~ 3-4%
  Cross-calibration over Antarctica – uncertainty ~ 2%
Calibration methods
  Moon radiometric degradation trending (long-term stability) – uncertainty ~ 0.1% per mission in SeaWiFS, lunar measurements used in MODISes and VIIRS
  Modified System Vicarious Calibration for polarization and RVS degradation modelling in MODIS-Terra and Aqua – uncertainty < 1%
  Detector radiometric equalization at TOA radiances for MERIS cameras over Dome Concordia site in Antarctica and for MODIS detectors per mirror side over oligotrophic waters
OLCI calibration requirements
absolute radiometric uncertainty 2%
inter-band radiometric uncertainty 1%

## Slide 10: Ocean colour validation
      bio-optical and atmospheric products
      instrument calibration and characterization
      spatial and temporal stability of algorithms
      instrument processing chain
      science algorithm development
product validation,
quick response to
degradation,
systematic
development
calibration labs
for in situ
instrumentation,
inter-calibration
round robins
bio-optical
field measurement
protocols
validation sites,
field campaigns,
new instruments
and validation
concepts
databases of
in situ validation
measurements
satellite L1/L2
data extractions,
matchups with
in situ, trending
satellite L3
trending, anomalies,
mission
inter-comparisons
satellite data
frequent internal
reprocessings to
test cal/char/alg
revisions
validation

## Slide 11
∙Rrs (490 nm)
∙Rrs (412 nm)
∙Rrs (443 nm)
G. Zibordi (AAOT, Abu Al Bukhoosh, Gustav Dalen Tower, Helsinki Lighthouse)
J. Icely (Algarve) V. Brando (LJCO)
D. Antoine (BOUSSOLE) K. Ruddick (MUMMTriOS)
D. McKee (BristolIrishSea) H. Feng & H. Sosik (MVCO)
M. Kahru (California Current) J. Werdell & NOMAD’s PIs
S. Belanger (CASES) S. Kratzer (NWBalticSea, Palgrunden)
G . Schuster & B. Holben (CoveSEAPRISM) P-Y. Deschamps (SIMBADA)
H. Loisel (EastEngChannel, FrenchGuyana) D. Siegel (PlumesAndBlooms)
S. Ahmed & A. Gilerson (LISCO) K. Voss (MOBY)
A. Hommerson (WaddenSea) B. Gibson & A. Weidemann (WaveCIS)
∙Rrs (510 nm)
∙Rrs (560 nm)
in situ
MERIS
Ca
mission-long matchups with in situ
a few hundred points
uncertainties
15 to 20%
and higher
high variance precludes stable accuracy assessment

## Slide 12
Deep-Water (depth > 1000m)
Oligotrophic (Chlorophyll < 0.1)
Mesotrophic (0.1<Chlorophyll<1)
Eutrophic (1<Chlorophyll<10)
Level-3 analyses
Region ID | Minimum Latitude | Maximum Latitude | Minimum Longitude | Maximum Longitude
AtlN55 | 50.0 | 60.0 | -50.0 | -20.0
PacN45 | 40.0 | 50.0 | -179.0 | -140.0
PacN35 | 30.0 | 40.0 | -179.0 | -140.0
PacN25 | 20.0 | 30.0 | -179.0 | -140.0
PacN15 | 10.0 | 20.0 | -179.0 | -140.0
PacEqu | -10.0 | 10.0 | -179.0 | -140.0
PacS15 | -20.0 | -10.0 | -179.0 | -140.0
PacS25 | -30.0 | -20.0 | -179.0 | -140.0
PacS35 | -40.0 | -30.0 | -179.0 | -140.0
PacS45 | -50.0 | -40.0 | -179.0 | -140.0
AtlS55 | -60.0 | -50.0 | -20.0 | 10.0
Hawaii | 15.0 | 25.0 | -163.0 | -153.0
SIO | -35.0 | -25.0 | 75.0 | 85.0
SPG | -32.0 | -22.0 | -139.0 | -129.0
AtlNE | 36.0 | 40.0 | -74.0 | -70.0
MERIS reprocessing 2
reprocessing
2011
MERIS reprocessing 3
MERIS reprocessing 3
nLw 412 nm anomalies
2-3%
MERIS r.3, nLw 443 nm
camera-to-camera trends
instrument and algorithm L3 evaluations over spatial and temporal domains
tens of thousands of points
uncertainties
1 to 4%
low variance supports stable accuracy assessment

## Slide 13: Ocean colour calibration highlights
ocean colour is extra sensitive | low signal impacted by instrument degradation and algorithms
get the L1B right | below 0.5% absolute uncertainty
vicariously calibrate | hyperspectral, Si-calibrated source, << 5% Lw uncertainty
get water-leaving radiance (or reflectance) right | primary Level-2 product
revise and test calibration (and algorithms) | frequent internal reprocessings to evaluate spatial and temporal accuracy and stability of evolving instrument calibration models
in situ validation measurements are inadequate on their own | overall statistical accuracy of the mission but sparse data with high variance
use Level-3 global and regional time-series | low variance, stable accuracy assessment
full mission reprocessings | routine reprocessings to incorporate new instrument knowledge and assure consistent time series