## Slide 1: JMA GPRC Report
Masaya Takahashi
Meteorological Satellite Center / Japan Meteorological Agency
(visiting scientist at EUMETSAT from Mar. 2014 to Feb. 2015)

## Slide 2: Contents
Update of JMA GSICS members
Progress of the MTSAT calibration system on GSICS
  Infrared channel
  Visible channel inter-calibration/vicarious calibration
Contribution to SCOPE-CM phase2 projects
Towards Himawari-8/AHI inter-calibration
VIS/NIR vicarious calibration using Metosat-9/SEVIRI as proxy data
Observation quality monitoring
Summary and future plans

## Slide 3
2014 JMA GSICS members
Executive Panel (EP)
(new) Kotaro BESSHO (Mr)
GSICS Research Working Group (GRWG)
(new) Keita HOSAKA (Dr)
Masaya TAKAHASHI (Mr)
Kenji DATE (Mr)
GSICS Data management Working Group (GDWG)
(new) Masaya TAKAHASHI (Mr), vice chair
GPRC points of contacts for operational matters
Masaya TAKAHASHI (Mr)
Great appreciation for Dr. Manik Bali’s acceptation of the interim GDWG chair!

## Slide 4: Contents
Update of JMA GSICS members
Progress of the MTSAT calibration system on GSICS
  Infrared channel
  Visible channel inter-calibration/vicarious calibration
Contribution to SCOPE-CM phase2 projects
Towards Himawari-8/AHI inter-calibration
VIS/NIR vicarious calibration using Metosat-9/SEVIRI as proxy data
Observation quality monitoring
Summary and future plans

## Slide 5: Progress of the MTSAT IR calibration system on GSICS
Current status of MTSAT-1R/-2 IR GSICS Correction
Demonstration phase, started in July 2010
Reference sensor: Metop-A/IASI and Aqua/AIRS
Toward the Pre-Operational phase
Additions and modifications to the netCDF conventions, merge of RAC (Re-Analysis Correction) files
To meet the requirement of EUMETSAT bias plotting tool, completed in July 2013
Uncertainty evaluation
ongoing, will be completed during my stay in EUMETSAT

## Slide 6
Comparison of TB bias on the EUMETSAT bias plotting tool
Requirements for the visualization on the bias plotting tool
RAC data are only supported (all information should be contained in one file)
Function enhancement will be discussed in the GDWG breakout session
We modified MTSAT-2 vs. AIRS/IASI IR RAC format in July 2013
Easy comparison of GSICS Corrections are realized!
MTSAT-2 10.8 um
Meteosat-10 10.8 um
Many thanks for supports and comments of EUMETSAT and NOAA
Time series of 11μm channel TB difference against Metop-A/IASI
on http://vgsics.eumetsat.int/plotter/

## Slide 7
Uncertainty evaluation of MTSAT vs. IASI IR correction
Method: Hewison (2013), already evaluated for MSG/SEVIRI and GOES/Imager
Progress of MTSAT-2/Imager:
Systematic errors have been calculated (but not for full error sources)
Random error evaluation is underway (will be finished in 2014)
3.8 [μm] 6.8 [μm] 10.8 [μm] ch 12.0 [μm]
Contribution on each source of systematic error to the standard uncertainty of TB
Total systematic uncertainty Temporal mismatch Longitudinal mismatch Latitudinal mismatch
in collaboration with Dr. Tim Hewison
WG_13.10 : JMA to complete Uncertainty analysis for MTSAT-IASI products by analyzing random errors contribution from spatial and temporal variability at least …
[K]
Uncertainty of TB [K]
Open

## Slide 8: Progress of the MTSAT VIS calibration system on GSICS
Result of MTSAT-2 in Feb. 2011
Simulated reflectivity
Observed reflectivity
A) Vicarious calibration using radiative transfer calculation
Method: Comparison of observed and simulated radiance for particular targets
Target: Wide range of radiances
Cloud-free ocean/land, Liquid water cloud, Deep Convective Cloud (DCC)
Radiative transfer calculation:
RSTAR (Nakajima and Tanaka [1986,1988])
Input data: Independent of GEO data
JMA Re-Analysis atmos. profiles, MODIS L1B, BRDF, Aura/OMI total column ozone, …
Aerosol/Cloud optical parameters (e.g., optical thickness) are retrieved from MODIS L1B data
in collaboration with the University of Tokyo

## Slide 9
B) Inter-calibration of NASA’s method using DCC
Progress of the MTSAT VIS calibration system on GSICS
In collaboration with Dr. Sebastien Wagner
Time series of monthly DCC pixel statistics and MTSAT-2 visible channel gain
mode
mean
mode
mean
MTSAT-2/Imager DN
Aqua/MODIS Radiance [W/m^2/sr/um]
Good agreements with the ATBD and other GPRC results
Monthly MODIS statistics (central) are used to derive gain (right)
Comparison of DCC method with RT simulation method
Similar trends, whereas large seasonal variation in the vicarious method
NASA DCC method
Vicarious method using RTM
MTSAT-2 VIS Gain [(W/m^2/sr/um)/DN]
DCC session
tomorrow: 3b

## Slide 10
Towards demonstration-phase …
GSICS Correction (NetCDF) filename/contents
Will be proposed in the Wednesday’s GRWG VIS session by Sebastien and will be checked in the GDWG breakout session
Product type:
E.g., Re-Analysis Correction (RAC) and Near Real Time Correction (NRTC) for GEO-LEO IR product
Should we produce the same kinds of products as the IR correction?
Time series of MTSAT-2 DCC digital counts statistics (mode/mean)
Monthly average
30-day rolling average on a daily basis

## Slide 11: Progress of the MTSAT VIS calibration system on GSICS
C) Lunar calibration using the ROLO model
In collaboration with Dr. Bartolomeo Viticchie
Applicable to JMA GEO satellites except for MTSAT-1R (due to its scanning pattern)
Experience of GMS-5 lunar calibration with the support of Dr. Tom Stone
We got started with MTSAT-2 lunar calibration in this March w/ Dr. Viticchie
In the near future, this method will be applied to Himawari-8/AHI VIS/NIR bands
Preliminary result of MTSAT-2 lunar calibration using the ROLO model (time series of calibration slope against the ROLO model)

## Slide 12: Contents
Update of JMA GSICS members
Progress of the MTSAT calibration system on GSICS
  Infrared channel
  Visible channel inter-calibration/vicarious calibration
Contribution to SCOPE-CM phase2 projects
Towards Himawari-8/AHI inter-calibration
VIS/NIR vicarious calibration using Metosat-9/SEVIRI as proxy data
Observation quality monitoring
Summary and future plans

## Slide 13: Contribution to SCOPE-CM phase2 projects
Name | Leader | SCOPE-CM partners
Land surface albedo from geostationary satellites (LAGS) | Alessio Lattanzio (EUMETSAT) | JMA, NOAA
Inter-calibration of passive imager observations from time-series of geo stationary satellites (IOGEO) | Rob Roebeling (EUMETSAT) | CMA, DWD, JMA, NOAA
Sustained production of International Satellite Cloud Climatology Project (ISCCP) cloud products | Kenneth Knapp (NOAA) | CMA, EUMETSAT, INPE, JMA, City College New York
Atmospheric Motion Vectors and Clear/All Sky Radiances from historical meteorological satellites in geostationary and polar orbit | Kotaro Bessho (JMA) | EUMETSAT, NOAA
JMA has contributed to SCOPE-CM since the initiative’s establishment
IOGEO project w/ Rob Roebeling
Joined kick off web meeting in February 2014
LAGS project w/ Mr. Alessio Lattanzio
In 2014, we will re-calibrate 2001 GMS-5 visible channel data using DCC method
SCOPE-CM Phase 2 projects with JMA involvement, starting in January 2014
Vicarious calibration using RT simulation will be helpful for the re-calibration

## Slide 14
Re-calibration of historical satellites:
GMS-5 visible channel re-calibration before 2000
GMS-5: operated from June 1995 to May 2003
Developed vicarious calibration technique cannot be directly applied before 2000 due to a lack of MODIS data
Solution: Use of constant/climatological value for optical parameters
Preliminary results
Similar tendency, but difference of slope magnitude and some spikes
Can be useful for comparison with other re-calibration methods
Observed reflectivity
w/ MODIS
Sep. 2000
Detector-2
y = 1.241 x – 0.0082
DCC
Cloud
Land
Sea
w/o MODIS,
w/ climatological aerosol
Sep. 2000
Detector-2
y = 1.0885 x – 0.0039
Simulated reflectivity
DCC
Sea
Observed reflectivity
1999 2000
Time series of regression coefficient: slope
(monthly mean for detector-2)

## Slide 15: Contents
Update of JMA GSICS members
Progress of the MTSAT calibration system on GSICS
  Infrared channel
  Visible channel inter-calibration/vicarious calibration
Contribution to SCOPE-CM phase2 projects
Towards Himawari-8/AHI inter-calibration
VIS/NIR vicarious calibration using Metosat-9/SEVIRI as proxy data
Observation quality monitoring
Summary and future plans

## Slide 16: Himawari-8/9: Next generation JMA’s GEO satellites
“Himawari”: a nickname of JMA’s GEO satellites, meaning sunflower in Japanese
JMA will launch Himawari-8 in summer 2014 and begin its operation in 2015. The launch of Himawari-9 is also planned in 2016.
AHI (Advanced Himawari Imager) has 16 bands
10 minutes for full disk observation, 2.5 minutes around Japan
Band | Central Wavelength [μm] | Spatial Resolution
1 | 0.43 - 0.48 | 1Km
2 | 0.50 - 0.52 | 1Km
3 | 0.63 - 0.66 | 0.5Km
4 | 0.85 - 0.87 | 1Km
5 | 1.60 - 1.62 | 2Km
6 | 2.25 - 2.27 | 2Km
7 | 3.74 - 3.96 | 2Km
8 | 6.06 - 6.43 | 2Km
9 | 6.89 - 7.01 | 2Km
10 | 7.26 - 7.43 | 2Km
11 | 8.44 - 8.76 | 2Km
12 | 9.54 - 9.72 | 2Km
13 | 10.3 - 10.6 | 2Km
14 | 11.1- 11.3 | 2Km
15 | 12.2 - 12.5 | 2Km
16 | 13.2 - 13.4 | 2Km
●
●: MSG
●
●
●
●
●
●
●
●
●
●
Advanced Himawari Imager (AHI)
Band | Central Wavelength [μm] | Spatial Resolution
1 | 0.55 – 0.90 | 1Km
2 | 3.50 – 4.00 | 4Km
3 | 6.50- 7.00 | 4Km
4 | 10.3 – 11.3 | 4Km
5 | 11.5 – 12.5 | 4Km
as of MTSAT-1R/2
Information can be found on: http://mscweb.kishou.go.jp/

## Slide 17: A Sequence of Himawari-8/9 AHI Observation in 10 minutes Time Frame
Over Japan (1)
every 2.5 min.
Over Japan (2)
every 2.5 min.
Typhoon monitoring
every 2.5 min.
Land-mark
extraction (1)
every 30 sec.
Land-mark
extraction (2)
every 30 sec.
A combination of one "Full Disk" and "small sectored” scans in 10 minutes
This super-rapidscan (every 30 seconds) mode will also be used for the lunar observations
___
Full Disk Observation
in every 10 min.

## Slide 18
VIS/NIR vicarious calibration using Metosat-9/SEVIRI as proxy data
Research for the preparation of Himawari-8/AHI vicarious calibration
Same method for MTSAT, in good agreement with GMS/MTSAT results
Issue: the way to carry out this method for other AHI VIS/NIR bands ( 0.46, 0.51, 2.26 μm) before the launch of Himawari-8
Comparison of reflectivity between Metosat-9/SEVIRI and our vicarious calibration using RT simulation
SEVIRI L1.5 data are provided in the collaboration framework between EUMETSAT and JMA.

## Slide 19
Observation quality monitoring
Prototype of calibration change alert derived from MTSAT-2 vs. IASI NRTC Correction
Diurnal variation of TB biases derived from GEO-LEO IR collocation data
ΔTB [K] ΔTB [K]
ΔTB [K] ΔTB [K]
10.8 [μm]
12.0 [μm]
10.8 [μm]
12.0 [μm]
Calibration change alert discussed in the June 2013 web meeting
Diurnal variation of TB biases discussed in the paste F2F/web meetings
Bias monitoring using global/regional NWP is under development
GEO-GEO inter-comparison will also be carried out, if data are available in JMA
MTSAT-2 against Metop-A/IASI Aqua/AIRS
MTSAT-2 against Metop-A/IASI Aqua/AIRS
in collaboration with Mr. Peter Miu
Soft limit

## Slide 20
MTSAT calibration system on GSICS
IR: uncertainty evaluation will be finished in 2014
VIS:
GSICS correction using DCC: will enter the demonstration phase
Lunar calibration: will implement to the JMA calibration system
Vicarious calibration: continue collaboration research w/ the Univ. of Tokyo
SCOPE-CM phase2 projects
Join discussions and re-calibrate GEO data for IOGEO, LAGS and ISCCP projects
Himawari-8/9
Preparation for operational inter/vicarious calibration system
Information of GSICS correction will be included in NRT distribution
Summary and future plans
We would like to proceed cooperatively with the GSICS colleagues!

## Slide 21
Backup Slides

## Slide 22
Predicted SRFs (Spectral Response Function) of AHI
Himawari-8
MTSAT-2
Available on http://mscweb.kishou.go.jp/himawari89/space_segment/srf_201206/AHI_SpectralResponsivity.zip
VIS
NIR
LWIR
SWIR
MWIR

## Slide 23: NRT (Near Real Time) distribution with GSICS Information
Action EP-12.05: “Each GPRC to consider implementing the near real time
distribution of both the operational calibration information and the
corrected calibration information, as part of the L1 data formats”
For MTSAT:
Difficult to include it due to big impacts on users
For Himawari-8/-9:
Now under consideration (will be announced in a few month)
Correction coefficients against one reference sensor
Window period to be used in a regression
Ancillary information (text block)
Calibration method, reference sensor name, …
Tentative plan of calibration information included in Himawari-8/-9 NRT data
(The information will be valid when GSICS Correction enters Operational-phase)