## Slide 1: Defining Primary GSICS References - an Evolving Concept for Inter-Calibration Products
Tim Hewison
(EUMETSAT) (GRWG Chair)
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:

## Slide 2: Current Situation
GSICS Inter-Calibration Products
  Defined by (Monitoring – Reference) Instruments
GEO-LEO IR Products based on MetopA/IASI
  Based on SNO method
  Now in Pre-Operational mode
  + Aqua/AIRS as transfer to characterise diurnal variations
  Developing Delta Corrections for MetopB/IASI
GEO-LEO VIS Products based on Aqua/MODIS
  Based on DCC method
  Soon to be in Demonstration mode

## Slide 3: Motivation to Change
New reference instruments becoming available
  MetopB/IASI, SNPP/CrIS, ...
  VIIRS, ...
Need to define Archive Recalibration Corrections
  To support generation of FCDRs
Aim to merge multiple references
  Define a Primary GSICS Reference by consensus
  After bias adjustment
More methods becoming available
  DCC, Lunar, Rayleigh, ...
  Ultimately aim to combine multiple methods

## Slide 4: Requirements
Long-term continuity of GSICS Products
  Without calibration jumps between references
  Although their uncertainty will change...
Ensuring Traceability
  back to single Primary Reference
  For each Spectral Band
Radiometric Consistency
  Cover a broad range of applicability

## Slide 5: Proposed Solution
Define one Primary GSICS Reference instrument
  for each Spectral Band (VIS/NIR/TIR/UV/...)
  and application area (NRTC/RAC/ARC/...)
  by consensus agreement
  based on a set of criteria (TBD)
  supported by a Traceability Statement

## Slide 6: Proposed Solution – Transfer Ref
Inter-calibrations using other Transfer References to incorporate Delta Corrections already applied
  to correct back to Primary GSICS Reference
Delta Corrections
  Normally based on double differences
  In channel-space of monitored instruments
  Over extended overlap period between references

## Slide 7: Proposed Solution - Versions
If we change the Primary GSICS Reference
  e.g. If a better reference becomes available in future
  or for different applications (e.g. Archive Recalibration)
  by consensus agreement
  Would potentially introduce a calibration jump
Need to create new Version of each GSICS Product
  Submit through a streamlined review process (GPPA)
  Revise uncertainty evaluation
  Revise traceability statement

## Slide 8: Proposed Solution to Combine Methods
Define one Primary Method?
Or do weighted average of Methods

## Slide 9: What does this mean for the User?
Users only have to select:
  Monitored Instrument
  Spectral Band
  Time Period
  Product Version (usually most recent)
  (Optionally) Override default Primary GSICS Reference
    To select a Transfer Reference
Benefits:
  Less to implement
  Less choice => Less scope for error

## Slide 10: How?
Generate RAC/NRTC/Daily Products
  Using both Primary and Transfer References
  During whole overlap period
Define Delta Correction
  Define Delta Correction Period
    Check for Jumps, Trends - Define break points if necessary
    Define Weights to merge references after Delta Correction?
  Evaluate Delta Correction Uncertainty
Apply Delta Correction into GSICS products
  May include results from transfer refs for optional use

## Slide 11: What do we need to do?
Seek users’ feedback on this proposal
Define netCDF format & content of GSICS Products
Revise
  User Guides,
  Traceability Statement,
  Uncertainty Analysis
Define new structure on GSICS Data Servers
Start generating products
  in parallel with current products
Modify GSICS plotting tool
  to work with new products
Extend above Concept to combine methods

## Slide 12: Outline Delta Correction ATBD
Specific Example: GEO-LEO IR
Three options to generate Delta Corrections:
  Derive from RAC-like files
  Derive from Daily Correction files
  Derive from Collocations
First need to define Primary GSICS Reference
  In practice, this will depend on the above results

## Slide 13: Specific Example 1: GEO-LEO IR - RAC
Generate intermediate RAC-like products for (Mon-Ref1) and (Mon-Ref2)
Check periods over which each reference is available
Define/Refine date range over which to evaluate Delta Correction
  Default: Whole overlap period
Read coefficients from RAC (Mon-Ref1) and (Mon-Ref2)
Calculate Double Difference coefficients from time series of RAC(Mon-Ref2)-RAC(Mon-Ref1)
Identify any step changes in the DD time series – if significant:
  split overlap period and treat as separate reference & Go to 3
Identify any periodicity in the DD time series – if significant:
  limit date range to n periods, define uncertainty growth & Go to 3
Identify any drifts in the DD time series – if significant:
  limit date range to create period with insignificant changes, define uncertainty growth & Go to 3
Define Delta Correction as mean of Double Difference coefficients and covariance
  Correcting covariance for oversampling in RAC time series
Apply Delta Correction to (Mon-Ref2) to generate RAC for dates when Ref1 not available

## Slide 14: Specific Example 2: GEO-LEO IR - Daily
Generate intermediate Daily Correction products for (Mon-Ref1) and (Mon-Ref2)
Check periods over which each reference is available
Define/Refine date range over which to evaluate Delta Correction
  Default: Whole overlap period
Read coefficients from Daily(Mon-Ref1) and (Mon-Ref2)
Calculate Double Difference coefficients from time series of Daily(Mon-Ref2)-Daily(Mon-Ref1)
Filter time series of DD time series to reject outliers
Identify any step changes in the DD time series – if significant:
  split overlap period and treat as separate reference & Go to 3
Identify any periodicity in the DD time series – if significant:
  limit date range to n periods, define uncertainty growth & Go to 3
Identify any drifts in the DD time series – if significant:
  limit date range to create period with insignificant changes, define uncertainty growth & Go to 3
Define Delta Correction as mean of Double Difference coefficients and covariance
Apply Delta Correction to (Mon-Ref2) to generate RAC for dates when Ref1 not available

## Slide 15: Specific Example 3: GEO-LEO IR –Collocations
Generate intermediate Collocation products for (Mon-Ref1) and (Mon-Ref2)
Check periods over which each reference is available
Define/Refine date range over which to evaluate Delta Correction
  Default: Whole overlap period
Recalculate RAC-like products from collocations of (Mon-Ref1) and (Mon-Ref2)
Calculate Double Difference coefficients from time series of RAC(Mon-Ref2)-RAC(Mon-Ref1)
Identify any step changes in the DD time series – if significant:
  split overlap period and treat as separate reference & Go to 3
Identify any periodicity in the DD time series – if significant:
  limit date range to n periods, define uncertainty growth & Go to 3
Identify any drifts in the DD time series – if significant:
  limit date range to create period with insignificant changes, define uncertainty growth & Go to 3
If no significant changes:
Define Delta Correction as weighted regression from all remaining collocations
  coefficients and covariances
Apply Delta Correction to (Mon-Ref2) to generate RAC for dates when Ref1 not available

## Slide 16
Junk beyond here...

## Slide 17: Diurnal Cycles w/ multiple References
Metop-A/IASI
Metop-B/IASI
Aqua/AIRS
S-NPP/CrIS
Meteosat-9/SEVIRI
ΔIASIB-IASIA - Tie 9:30am/pm Time series together }
ΔAIRS-CrIS - Tie 1:00am/pm Time series together }-Combine -> Blended Ref*
ΔAIRS-IASIA - Characterise diurnal cycle }
* Blending could be just ‘averaging’ – susceptible to calibration differences
Or after bias adjustment = traceable to Metop-A/IASI

## Slide 18: Blending References
Metop-A/IASI
Metop-B/IASI
Meteosat-9/SEVIRI
ΔIASIB-IASIA - 50-50 Blend* of References during whole overlap
* Blending could be just ‘averaging’ – susceptible to calibration differences
Or after bias adjustment = traceable to Metop-A/IASI
Weight
0% 100%
Time

## Slide 19: Blending References
Metop-A/IASI
Metop-B/IASI
Meteosat-9/SEVIRI
ΔIASIB-IASIA - 50-50 Blend* of References after initial delay
  E.g. 1yr to evaluate Double Differences and develop Delta Correction
* Blending could be just ‘averaging’ – susceptible to calibration differences
Or after bias adjustment = traceable to Metop-A/IASI
Weight
0% 100%
Delay
Time

## Slide 20: Blending References
Metop-A/IASI
Metop-B/IASI
Meteosat-9/SEVIRI
ΔIASIB-IASIA - Tapering Blend* of References after initial delay
  Updating Delta Corrections during overlap period
* Tapering Blend is only applicable to Archive Recalibration Corrections, where we know the start and end dates of the references’ availability in advance
Weight
0% 100%
Time

## Slide 21: Conclusions
Need to generate double differences for all overlap period
Analyse these to characterise reference differences
Should probably not extrapolate trends
  But could reconstruct them from multiple references
May not need Delta Corrections until current reference instrument dies
But then Delta Corrections will be needed instantly
  For continuity of RACs, NRTCs
  To trace them back to previous references
So need to start generating double differences asap
  And define Delta Corrections to be ready when needed

## Slide 22: Questions
Should we extrapolate periodic cycles?
  If we can model/understand them & they are significant
  Or use last n whole years
Is it OK to extrapolate uncertainty like this for NRTC/RAC?
  For Delta Correction, keeping constant DD bias after Ref1 is dead
Is there any point in generating Delta corrections for current RAC/NRTC using the same smoothing period?
  Or should we calc DD over whole overlap period? (or n years?)
Is this concept applicable to other GSICS Products?
  DCC, Lunar, ...
Can we make blended reference for Archive Re-Cal/RACs?
  With or without bias adjustment?

## Slide 23: Urgent Questions
How to characterise diurnal calibration variability?
  Do we need to include this in RAC/NRTC netCDF or document it?
How to define Delta Corrections for IASI-B->A?
  Just from double difference of RAC & NRTC – same periods (As agreed in 2014 GRWG Meeting) - No added value
  Average of all RACs/NRTCs over overlap period? (Correlated)
  Average of selected RACs/NRTCs every 29/14d? (Uncorrelated)
  Calculate Variograms from RACs/NRTCs over 30d-Nyquist
  Recalculate regression from all collocations in overlap period?
    Need more data – Any advantages?
  As 2, 3 or 4, but for only the most recent n years (avoids aliasing seasonality e.g. from n.5 years)