## Slide 1: Microwave Product Filenaming and Metadata standards
Manik Bali
MW Subgroup Meeting
January 13, 2015

## Slide 2: Outline
Introduction
        Microwave Product -Types
Proposed MW Product File naming Convention
Typical NetCDF datafile contents
MW Data file content requirements
        DWD SSMI Product
        NOAA MSU AMSU Cross Calibration Products
Proposed MW Metadata Standards
MW products as Primary Reference Product
Conclusions

## Slide 3: Introduction
Two main classes of products in GSICS
Correction Products. [RAC and NRT]
Contain bias, offset and un-certainty estimates
Primary Reference Products.[Under Development]
Delta Corrections, ability to map to a preferred reference
NOAA MW-Correction [FCDR] product has the ability to back compute
radiance of a chosen reference. ***
As per EP-14 FCDR would not be GSICS products, however correction products would be
This presentation proposes GSICS MW Product Filenaming and Metadata standards by considering the existing GSICS IR metadata standards and the MW metadata standards followed by contemporary cross calibration products to fulfill requirements of their own agencies.

## Slide 4: Proposed MW Product File Naming convention
Masaya’s presentation in VIS Cal group
GSICS file naming convention:
https://gsics.nesdis.noaa.gov/wiki/Development/FilenameConvention
Follows the rules given in the General File
W.M.O. Manual on The Global Telecommunication System
GSICS file naming convention:
https://gsics.nesdis.noaa.gov/wiki/Development/NetcdfConvention
 Relies on the following NetCDF conventions:
NetCDF Climate and Forecast Metadata Convention
http://cf-pcmdi.llnl.gov/documents/cf-conventions/latest-cf-conventions-document-1/
NetCDF Attribute Convention for Dataset Directory
http://www.unidata.ucar.edu/software/netcdf-java/formats/DataDiscoveryAttConvention.html
pflag_productidentifier_oflag_originator_yyyyMMddhhmmss[_freeformat].type[.compression]
References
  W_XX-EUMETSAT-Darmstadt,SATCAL+RAC+GEOLEOVISNIR,MSG3+SEVIRI Aqua+MODIS_C_EUMG_20130601000000_demo_01.nc
  W_US-NESDIS-STAR,SATCAL+NRTC+GEOLEOIR,GOES13+Imager-MetopA+IASI_C_KNES_20140312120000_preop_01.nc

## Slide 5
GSICS file naming convention:
https://gsics.nesdis.noaa.gov/wiki/Development/FilenameConvention
Follows the rules given in the General File
W.M.O. Manual on The Global Telecommunication System
References
  W_XX-EUMETSAT-Darmstadt,SATCAL+RAC+GEOLEOVISNIR,MSG3+SEVIRI Aqua+MODIS_C_EUMG_20130601000000_demo_01.nc
  W_US-NESDIS-STAR,SATCAL+NRTC+GEOLEOIR,GOES13+Imager-MetopA+IASI_C_KNES_20140312120000_preop_01.nc
  W_US-NESDIS-STAR,SATCAL+RAC+LEOLEOMW,NOAA14+MSU-NOAA15+AMSU_C_KNES_20140312120000_preop_01.nc
pflag_productidentifier_oflag_originator_yyyyMMddhhmmss[_freeformat].type[.compression]
Proposed MW Product File Naming convention

## Slide 6
Cross Calibration Data files are created in NetCDF Format.
Datafiles have three main sections
      Global Attributes[ Should gives a brief overview of the product]
        Info about file creation [source, filename etc], Funding Project, One line description and Usage
        Time stamps [Creation, data validity]
        Geospatial Information- Data Coverage [min/max lat lon]
        References – ATBD’s/doi numbers/Usage/etc
      Dimensions[x,y extent]
      Variables [Used by users]
        Calibration Coeff. For eg. Mon – Ref bias and offset, uncertainty and related SNO variables
Need to Standardize meta data in each section
Typical NetCDF datafile contents

## Slide 7
MW Data File Contents requirements
User Friendly format, easy to read and use Content
Aligned with Meta data Standards of producer Satellite agency
Product contents shall support GSICS bias Monitoring tool or the bias monitoring at GPRC in NRT/RAC .

## Slide 8
Harmonized with existing GSICS Standards
User Friendly format, easy to read and use Content
Harmonized with Contemporary Cross Calibration Products
Requirements should be general not very stringent so that it allows easy submission and acceptance of products.
Should be backed with strong technical support by the authors.
Should take into account budgetary constraints of satellite operators and long term maintenance and dissemination of the product.
Standards of producer Satellite agency standards shall be acceptable in GSICS/GPPA
Product should be monitored in bias Monitoring tool or the member satellite agency
MW Data File Contents requirements

## Slide 9
GSICS IR Metadata Conventions
https://gsics.nesdis.noaa.gov/wiki/Development/NetcdfConvention
NCDC Guidelines for CDR
http://cf-pcmdi.llnl.gov/documents/cf-conventions/latest-cf-conventions-document-1/
NetCDF Attribute Convention for Dataset Directory
http://www.unidata.ucar.edu/software/netcdf-java/formats/DataDiscoveryAttConvention.html
Reference Documents
Existing GSICS Products ( IR )
Contents of contemporary MW Cross Calibration Products
    2 NOAA Products ( MSU/AMSU, NCDC Maturity Level-6, Author: Cheng-Zhi Zou),
    DWD FCDR ( SSMI, Author: Fennig Karsten)
Reference Datasets
MW Data File Contents requirements

## Slide 10
Global Attributes

## Slide 11
GSICS IR METADATA STANDARD: Global Attributes:
:Conventions = "CF-1.6" ;
:Metadata_Conventions = "Unidata Dataset Discovery v1.0" ;
:standard_name_vocabulary = "CF Standard Name Table (Version 19, 22 March 2012)" ;
:project = "Global Space-based Inter-Calibration System <http://gsics.wmo.int>" ;
:title = "MSG2+SEVIRI vs MetOpA+IASI GSICS Near Real-Time Correction" ;
:summary = "Coefficients of the GSICS Correction for the infrared channels of a GEOstationary imager using a LEO hyperspectral reference instrument"
:institution = "EUMETSAT" ;
:date_created = "2015-01-09T13:16:55Z" ;
:date_modified = "2015-01-09T13:16:55Z" ;
:license = "Calibration information delivered as a GSICS operational product is generated in accordance with GSICS principles and practices.;\n",
"GSICS operational and demonstration products may be used and redistributed freely. Scientific publications using GSICS operational or demonstration products should however acknowledge both GSICS and the relevant producer organization.;\n",
"There is no warranty on the data express or implied, including warranties of merchantability and fitness for a particular purpose, or any assumed legal liability for the accuracy, completeness, or usefulness, of this information. The user of the data do so at their own risk." ;
:naming_authority = "int.eumetsat.gsics" ;
:creator_name = "EUMETSAT - European Organization for the Exploitation of Meteorological Satellites" ;
:creator_email = "ops@eumetsat.int" ;
:creator_url = "http://www.eumetsat.int" ;
:references = "ATBD, Unidata NetCDF, Climate Format Conventions, EUMETSAT IASI 1C Native Format Guide" ;
:

## Slide 12
history = "2015-01-08T22:20:00Z hypirsno_match_file_nc collocation_criteria=v0.31;\n",
"2015-01-08T22:20:00Z hypirsno_collocate v0.3 collocation_criteria=v0.31;\n",
:processing_level = "demonstration/v03.06.00" ;
:time_coverage_start = "2015-01-08T00:00:00Z" ;
:time_coverage_end = "2015-01-08T24:00:00Z" ;
:geospatial_lat_min = -35.f ;
:geospatial_lat_max = 35.f ;
:geospatial_lon_min = -35.f ;
:geospatial_lon_max = 35.f ;
:geospatial_lat_units = "degrees_north" ;
:geospatial_lon_units = "degrees_east" ;
:id = "W_XX-EUMETSAT-Darmstadt,SATCAL+NRTC+GEOLEOIR,MSG2+SEVIRI-MetOpA+IASI_C_EUMG_20150108000000_demo_03.nc" ;
:wmo_data_category = 30s ;
:wmo_international_data_subcategory = 4s ;
:local_data_subcategory = 1s ;
:keywords = "GSICS, satellites, inter-calibration, etc." ;
:reference_instrument = "MetOpA IASI" ;
:monitored_instrument = "MSG2 SEVIRI" ;
:window_period = "P14D" ;
:comment = "Use the NRTC with the time closest to the time of interest. Take great caution when applying it at a date where this difference is greater than the window_period." ;
:readMeDocURL = "http://www.eumetsat.int/Home/Main/DataProducts/Calibration/Inter-calibration/" ;
:number_of_times = 1 ;
:number_of_validities = 2 ;

## Slide 13
dimensions:
xDim = X;
yDim = Y ;
tDim = T ;
bDim = 2 ;
Global Attributes of DWD MW FCDR Product
Example -1

## Slide 14: Example -2
// glob al attributes:
:Conventions = "CF-1.6" ;
:title = "NOAA/NESDIS/STAR MSU Level-1C Product" ;
:source = "MSU Level-1b" ;
:methodology = "Integrated Microwave Inter-Calibration Approach (IMICA), formerly known asSimultaneous Nadir Overpass (SNO) Method" ;
:references = "doi:10.1029/2005JD006798;doi:10.1175/2008JCLI2233.1;doi:10.1175/2009JTECHA1333.1" ;
:history = "None" ;
:comment = "None" ;
:Metadata_Conventions = "CF-1.6,Unidata Dataset Discovery v1.0,NOAA CDR v1.0,GDS v2.0" ;
:standard_name_vocabulary = "CF Standard Name Table (v16, 11 October 2010)" ;
:id = "W_US-NESDIS-STAR,SATCAL+OPR+IMICA,C_KNES_NOAA-10+D87003.S0102.E0256_L1C_V1.3.nc" ;
:naming_authority = "gov.noaa.ncdc" ;
:date_created = "20130515T113945Z" ;
:license = "No constraints on data access or use" ;
:summary = "Swath data of Level-1C products derived from MSU onboarding NOAA polar-orbit satellites" ;
:keywords = "EARTH SCIENCE > ATMOSPHERE > ATMOSPHEREIC TEMPERATURE >
Global Attributes for MW -MSU Cross Calibration Product

## Slide 15
TEMPERATURE PROFILES" ;
:keywords_vocabulary = "NASA Global Change Master Directory (GCMD) Earth Science Keywords, Version 6.0" ;
:cdm_data_type = "Swath" ;
:processing_level = "NOAA Level 1C" ;
:creator_name = "Cheng-Zhi Zou" ;
:creator_url = "http://www.star.nesdis.noaa.gov/smcd/emb/mscat/index.php" ;
:creator_email = "cheng-zhi.zou@noaa.gov" ;
:institution = "NOAA/NESDIS/STAR" ;
:geospatial_lat_min = -89.22f ;
:geospatial_lat_max = 89.73f ;
:geospatial_lon_min = -179.52f ;
:geospatial_lon_max = 178.95f ;
:time_coverage_start = "19870103T010223Z" ;
:time_coverage_end = "19870103T025652Z" ;
:contributor_name = "Cheng-Zhi Zou, Cheng-Zhi Zou, Jian Li, Cheng-Zhi Zou, Cheng-Zhi Zou, Cheng-Zhi Zou, Jian Li" ;
:contributor_role = "principalInvestigator, pointOfContact, pointOfContact, author, originator, processor, processor" ;
:acknowledgment = "This project was supported in part by a grant from the NOAA ClimateData record (CDR) Program for satellites" ;

## Slide 16
:cdr_program = "NOAA ClimateData record (CDR) Program for satellites" ;
:cdr_variable = "fcdr_BrightnessTemperature_IMICA, fcdr_BrightnessTemperature_IMICA_LimbCorrected,fcdr_BrightnessTemperature_OPR,fcdr_BrightnessTemperature_OPR_LimbCorrected" ;
:metadata_link = "gov.noaa.ncdc:ToBeAssigned" ;
:product_version = "v1r3" ;
:platform = "TIROS-N,NOAA-06,NOAA-07,NOAA-08,NOAA-09,NOAA-10,NOAA-11,NOAA-12,NOAA-14" ;
:sensor = "MSU > Microwave Sounding Unit" ;
:spatial_resolution = "109.3km at nadir" ;
:uncertainty = "CH2:0.8K; CH3:0.8K; CH4:0.8K" ;
:IMICACoefficients = "CH2: deltaR=-0.0000 mu= 6.2500/r/nCH3: deltaR=-0.0000 mu= 5.6300/r/nCH4: deltaR=-0.0000 mu= 4.9500 " ;
}

## Slide 17
// global attributes:
:Conventions = "CF-1.6" ;
:title = "NOAA/STAR MSU Atmospheric Layer Temperature TCDR" ;
:source = "NOAA/NESDIS_MSU_Radiance_FCDR" ;
:references = "Zou, C.-Z. and W. Wang (2010), Stability of the MSU-derived atmospheric temperature trend, J. Atmos. Oceanic Technol., Vol. 27, 1960-1971.Zou, C.-Z., M. Gao, M.Goldberg (2009), Error structure and atmospheric temperature trends in observations from the Microwave Sounding Unit, J. Climate, 22, 1661-1681, DOI: 10.1175/2008JCLI2233.1.Zou, C.-Z., M. Goldberg, Z. Cheng, N. Grody, J. Sullivan, C. Cao, and D. Tarpley (2006), Recalibration of microwave sounding unit for climate studies using simultaneous nadir overpasses, J. Geophys. Res., 111, D19114, doi:10.1029/2005JD006798. " ;
:Metadata_Conventions = "CF-1.6,Unidata Dataset Discovery v1.0, NOAA CDR v1.0, GDS v2.0" ;
:standard_name_vocabulary = "CF Standard Name Table (v26, 08 Novemeber 2013)" ; :id = "NOAA_STAR_TCDR_MSU_channel_TMT_V01R00_197811_200609.nc" ;
:naming_authority = "gov.noaa.ncdc“; :date_created = "2014-02-24 20-17-07Z" ;
:license = "No constraints on data access or use." ;
dimensions:
xDim = 144 ;
yDim = 72 ;
tDim = 334 ;
bDim = 2 ;
Global Attributes for AMSU Cross Calibration Product
Example -3

## Slide 18
:summary = "NOAA/NESDIS/STAR Version 1.0 Advanced Microwave Sounding Unit A (AMSU-A) level 1c radiance Fundamental Climate Data Record (FCDR); inter-calibrated channels 4-14 brightness temperatures using the Integrated Microwave Inter-Calibration Approach (IMICA, formerly known as simultaneous nadir overpass method, Zou and Wang 2011) and with quality flags, from 1998 - present; NOAA operational calibrated brightness temperatures (channels 4-14), as well as limb effect corrected IMICA and operational calibrated brightness temperatures using Goldberg (2001) method, are also provided." ;
:keywords = "SPECTRAL/ENGINEERING>MICROWAVE>BRIGHTNESS TEMPERATURE" ;
:keywords_vocabulary = "NASA Global Change Master Directory (GCMD) Earth Science Keywords, Version 8.0" ;
:cdm_data_type = "Swath" ;
:creator_name = "Cheng-Zhi Zou" ;
:creator_email = "Cheng-Zhi.Zou@noaa.gov" ;
:institution = "NOAA/NESDIS/STAR>Center for Satellite Application and Research, NESDIS, NOAA, U.S. Department of Commerce" ;
:geospatial_lat_min = -89.3761f ;
:geospatial_lat_max = 89.5457f ;
:geospatial_lon_min = -179.9412f ;
:geospatial_lon_max = 179.9771f ;
:time_coverage_start = "2013-11-30 21-11-19Z" ;
:time_coverage_end = "2013-11-30 22-31-19Z" ;
:contributor_name = "Cheng-Zhi.Zou, Wenhui Wang" ;
:contributor_role = "Principle Investigator and the architect of the IMICA approach, the author of the Java-based AMSU-A Radiance FCDR processing code and the support scientist who derived new calibration coefficients for AMSU-A channels 4-14 and helped improve the IMICA approach." ;
:cdr_program = "NOAA Climate Data Record Program for satellites, FY 2011." ;
:cdr_variable =

## Slide 19
fcdr_brightness_temperature_IMICA_ch4,fcdr_brightness_temperature_IMICA_ch5,fcdr_brightness_temperature_IMICA_ch6,fcdr_brightness_temperature_IMICA_ch7,fcdr_brightness_temperature_IMICA_ch8,fcdr_brightness_temperature_IMICA_ch9,fcdr_brightness_temperature_IMICA_ch10,fcdr_brightness_temperature_IMICA_ch11,fcdr_brightness_temperature_IMICA_ch12
metadata_link = "gov.noaa.ncdc:C00787" ;
:product_version = "v01r00" ;
:platform = "NOAA-15" ;
:sensor = "AMSU-A>Advanced Microwave Sounding Unit A" ;
:spatial_resolution = "50km at nadir" ;
:STAR_SatelliteName = "n15" ;
:STAR_SatelliteID = 4 ;
:STAR_SatelliteIDInternal = 9 ;
:uncertainty_estimate_IMICA = "ch4: 0.750K ch5: 0.750K ch6: 0.750K ch7: 0.750K ch8: 0.750K ch9: 0.850K ch10: 0.900K ch11: 0.900K ch12: 1.100K ch13: 1.300K ch14: 1.700K" ;
:STAR_nScanLines = 601 ;
:STAR_LimbCorrectionScheme = "Goldberg 2001" ;
:STAR_IMICA_coefficients = "\n", Calibration Coefficients
"ch4: Delta0=-0.0000e-5 Kappa=-0.0000e-5 Mu0=-0.2690 Lamda=0.0000\n",
"ch5: Delta0=-0.0000e-5 Kappa=-0.0000e-5 Mu0=0.3000 Lamda=0.0000\n",
"ch6: Delta0=1.4060e-5 Kappa=-0.6140e-5 Mu0=0.0000 Lamda=0.4420\n",
"ch7: Delta0=-0.0000e-5 Kappa=-0.0000e-5 Mu0=0.3000 Lamda=0.0000\n",
"ch8: Delta0=-0.0000e-5 Kappa=-0.0000e-5 Mu0=0.6670 Lamda=0.0000\n",
"ch9: Delta0=-0.0000e-5 Kappa=-0.0000e-5 Mu0=0.0770 Lamda=0.0000\n",
"ch10: Delta0=-0.0000e-5 Kappa=-0.0000e-5 Mu0=0.3460 Lamda=0.0000\n",
"ch11: Delta0=0.5318e-5 Kappa=-0.0000e-5 Mu0=0.2510 Lamda=0.0000\n",
"ch12: Delta0=-0.0000e-5 Kappa=-0.0000e-5 Mu0=1.1150 Lamda=0.0000\n",
"ch13: Delta0=-0.0000e-5 Kappa=-0.0000e-5 Mu0=1.5000 Lamda=0.0000\n",
“

## Slide 20
Variables

## Slide 21
The GSICS (IR) standard Variables are calibration coefficients and Uncertainty Estimates calculated from global means.
Contemporary MW Cross Calibration products provide corrected radiances 2D fields ( Lat Lon Time) calculated from MW observations spanning 2 Decades.
Variables are also pixel level Quality Flags ( way beyond what is required for acceptance in GSICS).Variables are well characterized quantities in 2-3 Dimensions.

## Slide 22
Example-1 MW Product Meta Data
float time(tDim) ;
time:long_name = "time" ;
time:standard_name = "time" ;
time:units = "days since 1978-1-1 00:00:00" ;
time:coordinates = "time" ;
time:_FillValue = -9999.f ;
time:valid_range = 0.f, 20000.f ;
float latitude(yDim) ;
latitude:long_name = "latitude" ;
latitude:standard_name = "latitude" ;
latitude:units = "degrees_north" ;
latitude:coordinates = "latitude" ;
latitude:_FillValue = -9999.f ;
latitude:valid_range = -90.f, 90.f ;
float longitude(xDim) ;
longitude:long_name = "longitude" ;
longitude:standard_name = "longitude" ;
longitude:units = "degrees_east" ;
longitude:coordinates = "longitude" ;
longitude:_FillValue = -9999.f ;
longitude:valid_range = -180.f, 180.f ;
float longitude_bounds(xDim, bDim) ;
longitude_bounds:long_name = "longitude_bounds" ;
longitude_bounds:standard_name = "longitude" ;
longitude_bounds:units = "degrees_east" ;
longitude_bounds:_FillValue = -9999.f ;
longitude_bounds:valid_range = -180.f, 180.f ;

## Slide 23
Program for satellite" ;
:cdr_program = "NOAA Climate Data Record Program for satellites, FY 2009." ;
:cdr_variable = "tcdr_MSU_channel_TMT" ;
:metadata_link = "To be obtained from NCDC" ;
:product_version = "v01r00" ;
:platform = "TIROS-N,NOAA-06,NOAA-07,NOAA-08,NOAA-09,NOAA-10,NOAA-11,NOAA-12,NOAA-14" ;
:sensor = "MSU>Microwave Sounding Unit" ;
:spatial_resolution = "2.50 latitude by 2.50 longitude" ;
Example-1 MW Product Meta Data

## Slide 24
variables:
short Year(ScanLine) ;
Year:long_name = "Year" ;
Year:units = " " ;
Year:missing_value = -9999s ;
Year:valid_max = 2006s ;
Year:valid_min = 1978s ;
short DayOfYear(ScanLine) ;
DayOfYear:long_name = "Day of the year" ;
DayOfYear:units = " " ;
DayOfYear:missing_value = -9999s ;
DayOfYear:valid_max = 366s ;
DayOfYear:valid_min = 1s ;
int MillisecondOfDay(ScanLine) ;
MillisecondOfDay:long_name = "Millisecond of the day" ;
MillisecondOfDay:units = " " ;
MillisecondOfDay:missing_value = -9999 ;
MillisecondOfDay:valid_max = 86400000 ;
MillisecondOfDay:valid_min = 1 ;
dimensions:
ScanLine = 267 ;
ScanStep = 11 ;
Channel = 4 ;
ect = 1
float ScanTime(ScanLine) ;
ScanTime:long_name = "Scan start time (UTC) in a referenced or elapsed time format" ;
ScanTime:standard_name = "time" ;
ScanTime:units = "seconds since 1987-01-01T00:00:00.00Z " ;
ScanTime:missing_value = -9999.f ;
ScanTime:valid_max = 3.5e+07f ;
ScanTime:valid_min = 0.f ;
Example-2 MW Product Meta Data

## Slide 25
byte QualityFlag(ScanLine) ;
QualityFlag:long_name = "Scan line quality flags based on 32-bit MSU level-1b scan flags" ;
QualityFlag:units = " " ;
QualityFlag:missing_value = -99b ;
QualityFlag:valid_max = 2b ;
QualityFlag:valid_min = 0b ;
QualityFlag:flag_values = "0 1 2 " ;
QualityFlag:flag_meanings = "0=good scan; 1=good in at least one channel/pixel; 2=bad scan" ;
byte ASDFlag(ScanLine) ;
ASDFlag:long_name = "Ascending/Descending Flag" ;
ASDFlag:units = " " ;
ASDFlag:missing_value = -99b ;
ASDFlag:valid_max = 1b ;
ASDFlag:valid_min = 0b ;
ASDFlag:flag_values = "0 1" ;
ASDFlag:flag_meanings = "0=Descending; 1=Ascending"
Example-2 MW Product Meta Data

## Slide 26
float Longitude(ScanLine, ScanStep) ;
Longitude:long_name = "Longitude" ;
Longitude:standard_name = "longitude" ;
Longitude:units = "degrees_east" ;
Longitude:missing_value = -9999.f ;
Longitude:valid_max = 180.f ;
Longitude:valid_min = -180.f ;
float Latitude(ScanLine, ScanStep) ;
Latitude:long_name = "Latitude" ;
Latitude:standard_name = "latitude" ;
Latitude:units = "degrees_north" ;
Latitude:missing_value = -9999.f ;
Latitude:valid_max = 90.f ;
Latitude:valid_min = -90.f ;
Example-2 MW Product Meta Data

## Slide 27: Proposed MW Cross Calibration Standards
Product Shall follow the GSICS Filenaming convention ( strong justification needs to be given if not).
The Global Attributes shall follow the CF-1.5 or higher standards. These attributes shall give an overview of the product, related publications references , versioning, .
Variables should be able to give the user complete handle on the usage of the MW product. User feedback be key evidence of this.
Product shall have at least the following variables
    Calibration Coefficients
    Uncertainties
    Monitored and/or Reference Radiance
MW Products that follow within the preview of GSICS Inter-Calibration shall follow the following standards to get the GPPA stamp of acceptance.
Standard GSICS Convention

## Slide 28: MW Products as Primary Reference product
W_XX-EUMETSAT-Darmstadt,SATCAL+RAC+GEOLEOIR,MSG2+SEVIRI_C_EUMG_20110101000000_preop_01.nc
NOAA_STAR_TCDR_MSU_channel_TMT_V01R00_197811_200609.nc
The NOAA MW CDR Product or the DWD SSMI Product Can be included as a Correction Product
They can also be included as a Primary Reference Product.

## Slide 29: Conclusions
A very flexible Metadata standard for GSICS MW cross calibration product has been presented. This allows products to be aligned with their respective satellite operators and yet be accepted by GSICS thereby allowing participation in GSICS with minimal allocation or resources.
It is proposed that Global Attributes shall follow CF-1.5 or higher standards and shall provide to the user a complete overview of the product.
It is proposed that Variables should be able to give complete control to users of the product and give the ability to monitor the product in NRT in the GPRC and/or bias monitoring tool.
Examples of existing high quality MW Cross Calibration products have been presented that have users worldwide.