## Slide 1
2015 GSICS Annual Meeting (23-27 Mar 2015) @New Delhi, India
Tae-Hyeong OH, Dohyeong KIM, Hyesook Lee and Minju GU
National Meteorological Satellite Center
Korea Meteorological Administration
COMS
visible channel calibration
- issue for moon target -

## Slide 2: Lunar Calibration(IMPS)
Moon irradiance as measured by the COMS/MI
where
NP: the total number of pixels in the lunar disk image
RP : an individual radiance measurement(i.e. pixel) on the Moon
Ω: the solid angle of a pixel (sr), corresponding to one visible detector, i.e. 28 µrad
16/28: the over-sampling rate of MI along E-W axis
Moon irradiance computed from the ROLO
where
Dm-v: the moon-viewer distance in km i.e. Moon-satellite
Dm-s: the moon-sun distance in AU
COMS Moon observation L1A data
ROLO model of USGS(ver.311g)
COMS ephemerides data
- absolute phase angle
- Selenographic longitude of the sun
- Selenographic longitude of COMS
- Selenographic latitude of COMS
Moon observation time
L1A Moon data (1200*2080)
(b) IMPS moon area
Calculate a imager response the observed irradiance and ROLO irradiance

## Slide 3: Lunar Calibration(GIRO)
(a) L1A Moon data (699*699)
Observed Moon data (2016-06-17 07:43:13)
(b) GIRO moon pixel (699*699)
threshold : 900 counts
Re-make a Moon data
(count and radiance, 699*699) from level 1 data
Figure (a)
Select moon pixels above a threshold (900 count)
Figure (b)
Calculate (sanity check)
the observed irradiance
the integrated DC signal
the DC offset
the number of pixels
Calculate a imager response with the observed irradiance and ROLO irradiance from the GIRO_secondrelease
L1A Moon data (1200*2080)

## Slide 4: Dataset
Prepare the dataset to compare the result of IMPS and GIRO_fourthrelease
Satellite | Time Coverage | Observations | channel | Phase-angle range [deg] | Useful Observation for ROLO calibration
COMS | April 2011 ~ September 2014 | 81 | 1 | -92 ~ 92 | 79
79 COMS MI - VIS observations available
Instrument | Channel | SRF in GIRO NetCDF format
COMS MI | VIS06 | Yes

## Slide 5: Results: IMPS vs GIRO
Compare the ratio using the result of IMPS and GIRO_fourthrelease
  /(IMPS): degradation = -5.97 % (-1.41 %/year)
  /(GIRO): degradation = -4.26 % (-0.98 %/year)
IMPS_slope = -0.0048
IMPS_degradation = -5.97 (1.41%/yr)
GIRO_slope = -0.0034
GIRO_degradation = -4.26 (0.98%/yr)
Moon area size :(699*699)

## Slide 6: Sensitivity Test : threshold
Calculate observed irradiance through the threshold(850, 900, 950) to define the moon pixel
850_degradation = -4.11 %(0.95%/yr)
900_degradation = -4.26 %(0.98%/yr)
950_degradation = -4.48 %(1.03%/yr)
850_slope = -0.0033
900_slope = -0.0034
950_slope = -0.0036
Moon area size :(699*699)

## Slide 7: Sensitivity Test : threshold
Calculate observed irradiance through the threshold(850, 900, 950) to define the moon pixel
  Threshold : 850 count
    slope : -0.0033 / degradation : -4.11% (-0.95%/year)
    Correlation coefficient : -0.864
  Threshold : 900 count
    slope : -0.0034 / degradation : -4.26% (-0.98%/year)
    Correlation coefficient : -0.731
  Threshold : 950 count
    slope : -0.0036 / degradation : -4.48% (-1.03%/year)
    Correlation coefficient : -0.554

## Slide 8: Moon area size test
Ocean
Compare the ratio(Obs_irr/GIRO_ROLO_irr) with moon area ratio
  Size of Moon area
    699*699 / 599*699 / 499*699 / 349*599 / 319*549 / 319*554
  To define moon area similar with IMPS moon area
    319*554 : 176726 pixels
    Mean Moon pixels of IMPS : 176675
  Calculate the ratio (Obs_irr / ROLO_irr) of total pixel for each moon area
    699*699 : -3.76897 % / slope : -0.00304
    499*699 : -3.91396 % / slope : -0.00316
    349*599 : -4.02183 % / slope : -0.00324
    319*554 : -4.04176 % / slope : -0.00326

## Slide 9: Moon area size test

## Slide 10: Perturbation Test (using GIRO_PERT)
Variation of GIRO ROLO Irradiance through change of satellite position
13
  GIRO ROLO irradiance is very stable within ±0.01% when satellite position are change random with 0.5km~2km
  Phase angle of moon change with in ±0.02% through satellite position’s variation

## Slide 11: Summary & Issues
by Moon target
  In 79 cases of COMS lunar observation
  Compare the result of IMPS and GIRO_fourthrealese
    Degradation(IMPS) is about -5.97%(-1.41%/year) and GIRO is about -4.26%(-0.98%/year)
Issues
  Vary the ratio of observed irradiance and ROLO irradiance with threshold
  And also change the ratio through Moon area size
  Need more test to define the Moon pixel and Moon area size

## Slide 12: Action Items (GSICS Lunar Workshop)
Lunar Calibration Workshop(1~4 Dec. 2014) Summary
GLCWS_14.8 Data Sharing
  All participants to report any restrictions on the use of their datasets in relation to the proposed data sharing policy
  KMA will share the lunar compulsory data
Lunar Irradiance Model Developments
  to investigate possibility of their agency participating in funding the establishment of a new lunar observation facility
  interest in contributing but no existing mechanism for such an international funding. Further investigations needed

## Slide 13
Thank you 