## Slide 1
Reference Measurements for the TEMPO Mission
Kelly Chance, Xiong Liu,
Raid M. Suleiman,
Smithsonian Astrophysical
Observatory
David Flittner, Jay Al-Saadi,
NASA LaRC
Scott Janz, NASA GSFC
Joint GSICS GRWG-UVSG &
CEOS WGCV-ACSG @ NCWCP
October 8, 2015

## Slide 2: Introduction
Question 5. What external resources, if any, are regarded as reference measurements. Does your community have any common standards to which all retrieval algorithms are tied or compared? Are there solar spectra that your community regard as the reference?
Answer for TEMPO:
  Reference measurements for the spectral variation of parameters related to modeling solar UV-Vis backscatter (more to follow)
  There does not seem to unanimous use of standards.

## Slide 3: TEMPO Reference Measurements
In general the approach is to use the best available ancillary data
  Spectral resolution finer than the instrument resolution
  Captures the important physics, e.g. variation with temperature
List includes:
  Solar Spectrum
  Molecular Scattering Coefficients
  Trace Gas Absorption Coefficients
  Surface Spectral Albedo
Notes: In general the approach is to use the best available sources for solar input flux, scattering & absorption coefficients and

## Slide 4: TEMPO Reference Solar Spectrum
Solar spectrum is SAO2010 (aka Chance & Kurucz 2010, doi:10.1016/j.jqsrt.2010.01.036)
  <300nm: Balloon based observations (Hall/Anderson)
  >305nm: Ground based FTS (Kurucz et al., 1984)
  Merged over 300nm to 305nm range
  Corrected for telluric lines
  FTS normalized to irradiance data of Thuillier et al. 2003
  Good for wavelength calibration (cross-correlation), determining instrument line shape (slit) function, Ring effect correction, and correction for spectral undersampling of atmospheric spectra

## Slide 5: TEMPO Reference Absorption Cross-sections
Most relevant cross-sections for TEMPO Baseline Products (O3, NO2, H2CO) are:
  Molecular scattering: Bodhaine et al., 1999
  O3: Brion, Daumont, Malicet, et al. (aka BDM)
  NO2: Vandaele, et al., 1998
  H2CO: Cantrell et al., 1990
  O4: Vandaele, et al., 2003

## Slide 6: General Question
“Does your sensor use vicarious calibration methods? If so, what adjustments are derived?”
Anticipate performing radiance comparisons with LEO instruments such as TropOMI and VIIRS/JPSS to verify radiance calibration and possible transfer standard within the global Air Quality Constellation
Experience has shown that measurement/model residuals for cases with low model uncertainty can also provide fractional radiance adjustment.

## Slide 7: Example: OMI Radiance Residuals
Liu et al., 2010
CROSS TRACK POSITION

## Slide 8: Nominal Daily Operations
22 co-adds per mirror position meet SNR and 60 minute scan duration requirements
8-12 scans acquired per day, seasonally varying, and twilight imaging periods
2 Dark calibrations/day
1 Solar calibration performed per day over the entire year
Note: Scan mirror parked at off-null position overnight for pointing stability
Courtesy of Ball Aerospace Technologies, 28-31 July 2014 TEMPO Instrument PDR

## Slide 9: Radiometric Calibration Concept of Operations
Solar Diffuser Calibrations CONOPS:
Performed at a constant obliquity of 30° (diffuser normal to solar angle)
Yields greatest calibration consistency
Yearly variation of calibration time illustrated at right
Currently baselining prior to local midnight but design does not preclude post-midnight calibrations
Linearity observation includes 20 (TBR) integration times and dark collects
Activity | Frequency | Activity | Frequency
Dark Imaging | Twice/day | Working Diffuser Linearity Observation | Every 3 months
Working Solar Diffuser Observation | Once/day | Reference Solar Diffuser Observation | Every 6 months

## Slide 11: Hourly atmospheric pollution from geostationary Earth orbit
PI: Kelly Chance, Smithsonian Astrophysical Observatory
Instrument Development: Ball Aerospace
Project Management: NASA LaRC
Other Institutions: NASA GSFC, NOAA, EPA, NCAR, Harvard, UC Berkeley, St. Louis U, U Alabama Huntsville, U Nebraska, RT Solutions, Carr Astronautics
International collaboration: Korea, U.K., ESA, Canada, Mexico
Selected Nov. 2012 as NASA’s first Earth Venture Instrument
  Instrument being implemented, delivery May 2017
  NASA will arrange hosting on commercial geostationary communications satellite with launch expected NET 11/2018
Provides hourly daylight observations to capture rapidly varying emissions & chemistry important for air quality
  UV/visible grating spectrometer to measure key elements in tropospheric ozone and aerosol pollution
  Exploits extensive measurement heritage from LEO missions
  Distinguishes boundary layer from free tropospheric & stratospheric ozone
Aligned with Earth Science Decadal Survey recommendations
  Makes many of the GEO-CAPE atmosphere measurements
  Responds to the phased implementation recommendation of GEO-CAPE mission design team
  North American component of an international constellation for air quality observations

## Slide 12: TEMPO science overview
US air quality standards continue to become more stringent to better protect human health
New and transient pollution sources (e.g., vehicular traffic, oil & gas development, trans-boundary pollution) are growing in importance yet are very difficult to monitor from ground networks
Many areas that are not currently monitored are expected to violate proposed ozone standards
TEMPO measurements will provide data to help solve this national challenge
US EPA ozone 8-hour design projections to 2020
TEMPO science questions
What are the temporal and spatial variations of emissions of gases and aerosols important for air quality and climate?
How do physical, chemical, and dynamical processes determine tropospheric composition and air quality over scales ranging from urban to continental, diurnally to seasonally?
How does air pollution drive climate forcing and how does climate change affect air quality on a continental scale?
How can observations from space improve air quality forecasts and assessments?
How does intercontinental transport affect air quality?
How do episodic events, such as wild fires, dust outbreaks, and volcanic eruptions, affect atmospheric composition and air quality?

## Slide 13: Typical TEMPO-range spectra (from ESA GOME-1)

## Slide 14: Baseline and threshold data products
Species/Products | Required Precision | Temporal Revisit
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric SO2 | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric C2H2O2 | 4.0 × 1014 molecules cm-2 | 3 hour
Aerosol Optical Depth | 0.10 | 1 hour
Minimal set of products sufficient for constraining air quality
Across Greater North America (GNA): 18°N to 58°N near 100°W, 67°W to 125°W near 42°N
Data products at urban-regional spatial scales
  Baseline ≤ 60 km2 at center of Field Of Regard (FOR)
  Threshold ≤ 300 km2 at center of FOR
Temporal scales to resolve diurnal changes in pollutant distributions
Collected in cloud-free scenes
Geolocation uncertainty of less than 4 km
Mission duration, subject to instrument availability
  Baseline 20 months
  Threshold 12 months

## Slide 15: TEMPO instrument concept
Measurement technique
  Imaging grating spectrometer measuring solar backscattered Earth radiance
  Spectral band & resolution: 290-490 + 540-740 nm @ 0.6 nm FWHM, 0.2 nm sampling
  2 2-D, 2k×1k, detectors image the full spectral range for each geospatial scene
Field of Regard (FOR) and duty cycle
  Mexico City/Yucatan Peninsula to the Canadian tar/oil sands, Atlantic to Pacific
  Instrument slit aligned N/S and swept across the FOR in the E/W direction, producing a radiance map of Greater North America in one hour
Spatial resolution
  2.1 km N/S × 4.7 km E/W native pixel resolution (9.8 km2)
  Co-add/cloud clear as needed for specific data products
Standard data products and sampling rates
  Most sampled hourly, including eXceL O3 (troposphere, PBL) for selected areas
  H2CO, C2H2O2, SO2 sampled hourly (average results for ≥ 3/day if needed)
  Nominal spatial resolution 8.4 km N/S × 4.7 km E/W at center of domain (can often measure 2.1 km N/S × 4.7 km E/W)
  Measurement requirements met up to 50o for SO2, 70o SZA for other products

## Slide 16: Instrument layout
Calibration Mechanism Assembly
Telescope Assembly
Spectrometer Assembly
Scan Mechanism Assembly
Focal Plane
Assembly
Focal Plane Electronics
Instrument Support
Assembly
Radiator Assembly
Instrument
Control Electronics
Notes: Most of final drawings done; detectors in-house; grating ordered; optical bench ordered

## Slide 18
Stratospheric Aerosol and Gas Experiment
SAGE III on ISS
An Earth Science Mission on the International Space Station
Example of SAGE Internal Data Consistency
Joe Zawodny, Larry Thomason,
Sharron Burton, Rob Damadeo
NASA Langley Research Center
October 8, 2015

## Slide 19: SAGE III Approach
Make accurate, high-vertical-resolution profiles of ozone, aerosol extinction, and other trace species using the heritage Occultation Technique
Utilize both the Sun and the Moon

## Slide 20: The Data to Work With
Reference exo-atmospheric scans across the sun characterize the Source and Instrument for each event
Scans across the sun looking through the atmosphere provide measure of atmospheric slant path transmission
Transmission = I /Io
Io
I

## Slide 21: Effect of Source Variations
Spatial variations in source intensity can map into temporal variations due to:
  Apparent rotation into and out of scan plane
  Misplacement of Field of View (FOV) on the face of the sun
  Occurs for Io and I scans
Variations produce increased uncertainty in transmission & species concentration

## Slide 22: Example of Effect on Io

## Slide 23: Correlations Allow for Corrections
Variations are correlated spectrally and spatially
Use correlations to:
  Modify the placement of FOV on face of source
  Account for rotation of source
Uncorrected
Corrected
Wavelength 1
Wavelength 2

## Slide 24: Improved SAGE Data Products
Corrections greatly reduces the variance in transmission, ~40%
[Burton, et al. 2010]
Corrected
Uncorrected

## Slide 25: Backup