## Slide 1: Calibration Status for the GOME Instrument
D. Loyola, B. Aberle, M. Coldewey-Egbers, N. Hao, S. Slijkhuis
Joint GSICS GRWG-UVSG and CEOS WGCV-ACSG Meeting
NCWCP College Park, October 8th 2015

## Slide 2: Evolution of the Ozon Hole over Antarctic

## Slide 4: ESA Project GOME-Evolution
First reprocess the GOME L1b products for the complete mission
  Analyze and optimize the in-flight calibration
  Update the level 0-to-1 algorithms
  Validate the L1b product
  Products in netCDF CF compliant with the Sentinels
Water Vapour as operational GOME product
Outreach
  WebGalery for atmospheric composition missions
  School-lab experiment for secondary school

## Slide 5: Global Ozone Monitoring Experiment
GOME/ERS-2 launched in April 1995 and decommissioned in July 2011
Nadir-viewing spectrometer that measures solar radiation reflected and/or scattered in the Earth‘s atmosphere or from its surface
4 Diode Arrays Detectors (1024 pixels)
  Channel 1: 237-316nm
  Channel 2: 311-405nm
  Channel 3: 405-611nm
  Channel 4: 595-793nm
3 Polarization Measurement Devices
  PMD 1 : 295-397nm
  PMD 2 : 397-580nm
  PMD 3 : 580-745nm
GOME optical layout (courtesy of ESA)

## Slide 6: GOME In-Flight Calibration
Spectral calibration
  Instrument houses a platinum-chromium-neon (PtCrNe) emission lamp
  Wavelength calibration using well-known spectral positions of these emission lines
Pixel-to-Pixel Gain (PPG) correction using LED measurements
Dark Current correction
  Monitor thermal leakage and associated noise of 4 channels (4096 detector pixels) by periodically taken dark-side measurements
  Correct PMDs for their zero offset and noise
Sun and Moon measurements

## Slide 7: Processing flow for calibration parameters

## Slide 8: Number of In-Flight Calibration Measurements
Loss of global coverage in May 2003 due to failure of on-board tape recorder

## Slide 9: GOME Degradation Monitoring
Channel 4
Channel 3
Channel 2
Channel 1
Ch1 Ch2 Ch3 Ch4
Dichroic filter
Anomalies in 2001 due to gyroscope failure

## Slide 10: PMD Measurements and Q-Factors
PMD Signal
Q-Factors
Change vs. 1995

## Slide 11: GOME Pre-disperser Temperature
Quartz pre-disperser prism is one of the key elements in the optical system
Refractive index depends on wavelength and temperature
Temperature increases along an orbit due to warming of the satellite by the sun and partly because light passes through the instrument
Temperature changes affect the wavelength calibration
Long-term increase is due to degradation of the thermal system
Outliers are connected to instrument and cooler switch-offs

## Slide 12: Spectral Lamp Measurements
Ch 1: 283nm
Ch 2: 391nm
Ch 3: 582nm
Ch 4: 668nm

## Slide 13: LED Measurements + Pixel-to-Pixel Gain Correction
Typical PPG correction factor
Ch 4
Ch 3
Ch 2
Ch 1

## Slide 14: Dark Current Measurements vs. Integration Time (IT)
→ Increase: 4-6 BU/s / 10 years
IT pattern: Scan
(Band 1a: 12s and Bands 2-4: 1.5s)
IT pattern: LED
(Bands 1-4: 30s)
IT pattern: Moon
(Band 1a: 60s and Bands 2-4: 6s)

## Slide 15: Dark Current Noise
SAA
Old
IT pattern: Scan IT pattern: LED IT pattern: Moon

## Slide 16: PMD Noise + Zero Offset
IT pattern: Scan IT pattern: LED IT pattern: Moon

## Slide 17: Assessing L1b via L2 Retrievals – DOAS
Oct. 01, 1997, orbit: 12804
GOME O3 SCD difference
between new L1 and old L1 is very small (about -0.03%). DOAS fitting residual using new L1 improve at most situations (about 0.9%) compared to using old L1 data.
GOME NO2 SCD difference between new L1 and old L1 is very small (about 0.07%). DOAS fitting residual using new L1 improve a little (about 1.0%) compared to using old L1 data.

## Slide 18: Assessing L1b via L2 Retrievals – GODFIT
Relative degradation 325-335nm
Reference sector: Mediterranean sea, clear sky
Courtesy C. Lerot (BIRA)

## Slide 19: Product Harmonization – from GOME to Sentinels
Fillvalues
1s
1s
1s
0.5s
0.5s
0.5s
0.5s
0.5s
1s
1s
1s
4s
Nadir/Band-xy (Integration-time 1s or 0.5s)
Same netCDF CF format for all UVNS sensors