## Slide 1: Fast and Accurate Collocation of CrIS and VIIRS
Likun Wang1*, Bin Zhang1, Denis Tremblay2, Yong Han3
1.* Univ. of Maryland, College Park, MD; Likun.Wang@noaa.gov
2. Science Data Processing Inc., Laurel, MD
3. NOAA/NESDIS/STAR, College Park, MD
2016 GSICS Annual Meeting, Japan

## Slide 2: VIIRS Instrument
Copied from Raytheon Website
16 M-bands (750m); 5 I-Bands (375m); 1 DNB Band (750m)
Notes: 1) VIIRS provide imagery of the Earth Surface, it has very high resolution
1) 22 bands 3) all kinds of EDR, vegetation, land, cloud, ice, Aerosol

## Slide 3: CrIS Operational Concept
2,200 km Swath
Downlink
NWP, EDR Applications
Decode Spacecraft Data
±50° Cross track Scans
3x3 Array of CrIS FOVs (Each at
14-km Diameter)
Ground Station
RDR = Raw Data Record
SDR = Sensor Data Record
EDR = Environmental Data Record
30 Earth Scenes
RDRs
EDRs
Co-Located ATMS SDRs
Global Temperature, Moisture, Pressure Profiles
CrIS on NPP
RDRs
Interferograms
Calibrated / Geolocated Spectra
SDRs
CrIS SDR Algorithm

## Slide 4: Motivation
Combination of CrIS Spectra and VIIRS Products
NWP Data assimilations
Physical parameter retrievals
Inter-calibration
land surface
cloud properties
Providing sub-pixel information for CrIS observations using collocated high-spatial resolution VIIRS products

## Slide 5: Outline
Using CrIS and VIIRS as an example to explore general issues on collocation of two satellite sensors
CrIS and VIIRS are two independent instruments, though on the same platform
  Not like IASI and AVHRR on MetOp
  No alignment requirements when design
  Separate geolocation fields
Fast and accurate collocation algorithm suitable for operational use
Are CrIS and VIIRS perfect align together?
  If not, collocated products can introduce errors and uncertainties, making data assimilation even worse.

## Slide 6: VIIRS vs. CrIS: Spectrally
CrIS spectra are overlapped with VIIRS SRFs for M13, M15, and M16, and I5
10.8 µm
12.0 µm
4.05 µm

## Slide 7: VIIRS vs. CrIS: Spatially
VIIRS I5 bands
CrIS at 900 cm-1
Resolution: 375m (I) or 750m (M) 14.0km nadir
Scan Angle: 58.3° 48.3 °
Sampling: Continuous Sub-sample

## Slide 8: Collocation of CrIS with VIIRS
CrIS Footprints
CrIS Footprints
overlapped with
VIIRS image
Collocation of the measurements from two satellite sensors (either on the same satellite platform or not) involves pairing measurements from two sensors that observe the same location on the Earth but with different spatial resolutions.
It is challenging to do it on the Earth Surface using latitude and longitude.
1) Footprint rotation and distortion off nadir; 2) Searching! Searching! Searching!

## Slide 9: Collocation of CrIS with VIIRS Using line-of-sight vector
It is better to collocate CrIS and VIIRS in space instead of on the Earth Surface
If we can retrieve line-of-sight vector of CrIS and VIIRS
The collocation of VIIRS and CrIS can be simplified as examining the angles between two vectors.
  No worry about FOV distortion

## Slide 10: Retrieve LOS Vectors
Azimuth, Zenith, Range in Local Spherical Coordinate
(East, North, Up) in meter in Local East, North, Up (ENU) Coordinate
Geodetic Latitude, Longitude, and Altitude (LLA) Coordinate
Earth-centered, earth-fixed (ECEF) Coordinate

## Slide 11: K-D Tree Search
In computer science, a k-d tree (short for k-dimensional tree) is a space-partitioning data structure for organizing points in a k-dimensional space.
 | Average | Worst case
Search | O(log n) | O(n)

## Slide 12: CrIS Spatial Response Function
Ideally, VIIRS images should be convolved with CrIS spatial response function.
CrIS detector response function: a cutoff value of ±0.963°/2 (14.0 km at nadir) is about 41.19% to its peak value but already collects 98% of total radiation falling on the detector.
The box-car spatial response is good enough to represent the real CrIS spatial response.
0.963° 14.0km
VIIRS (Box Car Average) - (Spatial Response Convolution): ~0.0023K

## Slide 13: CrIS-VIIRS BT Diff. Map
Large diff. can be seen at the end of scan
Ascending
Descending

## Slide 14: Misalignment between CrIS and VIIRS at the end of scan

## Slide 15: VIIRS Geolocation Very Accurate ! (I5 band: 375m resolution)
Table 2. VIIRS Geolocation Accuracy |  | 
Residuals | First Update | Second Update
 | 23 February 2012 | 18 April 2013
Track mean | −24 m, −7% | 2 m, 1%
Scan mean | −8 m, −2% | 2 m, 1%
Track RMSE | 75 m, 20% | 70 m, 19%
Scan RMSE | 62 m, 17% | 60 m, 16%
Wolf et al. 2013
from Wolf et al. 2013

## Slide 16: CrIS Geolocation Assessment Using VIIRS as a reference
The misalignment between CrIS and VIIRS can be caused by the CrIS geolocation error.
Can we use VIIRS as a reference to check CrIS geolocation accuracy?
The purpose is to identify the error characteristics of CrIS LOS pointing vector by comparing them with the truth.
Furthermore, if the systematic errors are found, a new set of co-alignment parameters should be retrieved based on assessment results to improve the geolocation accuracy.
CrIS
VIIRS (Truth)
Earth Ellipsoid
Satellite

## Slide 17
Interferometer
Overview of NPP/JPSS
Geolocation Algorithms
Attitude Determination & Control System (ADCS)
SGP4
CrIS (or other instrument)
GEOLOCATION Assessment
feedback
Coordinate transformation
ADCS
Sensor Isolation
system
Spacecraft
Function call to common geo:
ellipIntersect(outPt,inst2SC,exitVec, dlat,lon,satazm,satzen,range)
Spacecraft
Orbital
ECI
ECEF(ECR)
Geodetic
Common GEO
Geolocate each FOV
GCP/Maps/Ground truth
the other instrument measurements with enough geolocation accuracy
Comparing the truth and CrIS Geo fields
JPSS or any satellite
Pos/Vel/Quaternion (RPY)
Modified from C. Cao
SSM

## Slide 18: Retrieved the CrIS LOS vector relative to Spacecraft
LOS vector in S/C
(satellite Pitch, Roll, and Yaw angle)
Geolocation Fields
(satellite range, azimuth, and zenith angle)
LOS vector in ECEF or ECR
(lat , Lon)
LOS vector in orbit frame
(satellite velocity, geodetic nadir)
+
Triad Method
the Earth
Satellite

## Slide 19: Defining α and β angles of CrIS LOS vector in Spacecraft Coordinate
X: InTrack
Z: from satellite Pointing Earth Surface
Y: CrossTrack
P: unit vector of LOS in SBF (x, y, z)
β = atan(y/z)
α = atan(x/z)
Notes: 1) Spacecraft coordinates forms two planes: satellite in-track planes and cross-track planes. 2) LOS vectors projected onto these two planes; 3) two angels can be defined: alpha and beta, which exactly corresponds to LOS; 4) When alpha and beta changes, LOS vector is also changed. 5) The whole idea is to change alpha and beta and find the true LOS relative to VIIRS.

## Slide 20: α and β Angles varying with Scan Position (FOV5)
α
β
Noted that the yaw patterns of α angles are caused by the Earth Rotation
when retrieving them in ECEF.

## Slide 21: α and β angles are step-by-step perturbed by 21 steps with a angle of 375/833/1000.0
α

## Slide 22: Using VIIRS to find best collocation position
FOR 30

## Slide 23: Flowchart for VIIRS-CrIS Alignment Check
Produce new CrIS LOS vector in SBF
Convert CrIS LOS vector into ECEF
Collocate VIIRS and CrIS
Output Collocated Results
Perturb α and β angles with small angles
CrIS LOS Vector in ECEF
CrIS Geo. Field
VIIRS Vector in ECEF
VIIRS Geo. Field
CrIS Sat_P and V in ECEF
Compute LOS Vector in
Orbit Frame
Compute LOS Vector in S/C Frame
Loop by 21x21
steps

## Slide 24: IDPS Data Geolocation Performance
This is root cause of misalignment between CrIS and VIIRS.
CrIS FOV size in-track and cross-track direction
in-track direction
cross-track direction
Notes: Slow, point out the figures at left.

## Slide 25: New Geometric Parameters
SDR Algorithm Process
LOS in IOAR coordinate = ILS parameters (3x3)
Convert from IOAR to SSMF coordinate (2 angles)
3) Compute normal to SSM mirror in SSMF (30 Scan Pos) (60 angles)
4) Apply SSM mirror rotation to get LOS in SSMF coordinate
5) Convert from SSMF to SSMR coordinate (3 angles)
6) Convert from SSMR to IAR coordinate (3 angles)
7) Convert from IAR to SAR (3 angles)
8) From SAR=> SBF coordinate (0 angels)
9) From SBF=> Spacecraft (3 angles)
Given the assessment results with 60 angles,
the best strategy is to retrieve 60 scan mirror
rotation angles.
Notes: This part needs not to be detailed.

## Slide 26: New SSMF In-track Angles
Values in EngPKT
New Values

## Slide 27: Retrieved SSMF Cross-track Angles
Values in EngPKT
New Values
New -EngPKT

## Slide 28: Geolocation Performance (New Parameters)
Zoom in
in-track direction
cross-track direction

## Slide 29: Only correct cross-track direction

## Slide 30: correct cross-track and in-track Direction

## Slide 31
IDPS
New Codes + New EngPkt
Another Validation Case
CrIS-VIIRS I5 image
Polar Region

## Slide 32: Conclusion
Line-of-sight based collocation to avoid FOV distortion
K-D tree based-search to speed up program
CrIS geolocation has been adjusted to perfectly align with VIIRS.
The method can work for other two sensors on different platform also.