## Slide 1
NMSC/KMA
KMA Agency Report
2016 GSICS Annual Meeting (29 Feb ~ 4 Mar 2016 )@ Tsukuba, Japan

## Slide 2: Current Status of KMA
Visible channel
  Operate vicarious calibration system using targets on the Earth
  Keep studying the moon targets for vicarious calibration
Infrared channel
  Operate GSICS GEO-LEO Inter-calibration system
   using IASI-A, IASI-B, AIRS and CrIS
  Investigate the cold bias correction in WV with SRF correction
Preparation for the Demonstration Phase
  Prepare to enter the Demonstration Phase of the GSICS Procedure for Product Acceptance

## Slide 3: Visible Channel
Time series of slopes and intercepts
a scatter plot for 30 days data
get a slope/intercept
trend of slope for long period
Results of Moon and DCC (RTM)
Ocean
Desert
Water Cloud
DCC
Scatter plot
using ocean/desert/WC/DCC
for all data until now
  slope= 0.861
  intercept= 0.019
Ocean
Desert
Water Cloud
DCC
Slope(moon)=-5.802%
Slope(4 targets)=-5.717%

## Slide 4: Visible Channel (DCC and Moon)
Visible Calibration by Lunar, DCC(RTM and NASA method)
  In 102 cases of COMS lunar observation
  Result from DCC target is consistent with other target data, making linear regression line with high correlation
  Comparison with Lunar, DCC(RTM) and DCC(NASA method)
Results of Lunar, DCC(RTM) and DCC(NASA method)
  Moon : 1.2318/year, DCC(RTM) : 1.1689/year from April 2011 ~ December 2015
  DCC(NASA): 0.9757/year from April 2011 ~ December 2013
  Need more investigation for the DCC result with NASA method

## Slide 5: LEO(CrIS) TB vs. GEO TB
check the TB bias for each IR channels
period: CrIS(Jan. 2014 - Dec. 2015)
LEO TB (K)
COMS TB (K)
COMS TB (K)
LEO TB (K)
IR2(12.0 μm)
IR1(10.8μm)
SWIR(3.8μm)
WV(6.8μm)
In SWIR of CrIS, large bias due to much shorter spectral coverage of MI broadband

## Slide 6: Monthly variation of TB Bias & RMSE
monthly variation of TB bias and RMSE
period: AIRS IASI-A (April 2011 - Dec. 2015) IASI-B (Aug. 2013 - Dec. 2015) CrIS(Jan. 2014 - Dec. 2015)
TB Bias (COMS-LEO)
TB RMSE
AIRS IASI-A IASI-B CrIS
IR1
IR2
WV
SWIR
IR1
IR2
WV
SWIR
Mean bias -0.0208
Mean bias -0.0283
Mean bias 0.0142
Mean bias 0.0088
IR1
IR2
WV
SWIR
Double Diff.(IASI/A TB bias- IASI/B TB bias)

## Slide 7: Infrared Channel(WV anomaly-1)
Currently, check the trend of TB bias for WV
Large negative bias for warm temperature
Period: Jan. 2014 - Dec. 2014
TB Bias(COMS-LEO) (K)
COMS TB (K)
*Refrence: Myoung-Hwan Ahn, Su Jeong Lee, Dohyeong Kim “Estimation of uncertainties in the spectral response function of the water vapor channel of a meteorological imager”, Proc. SPIE, 2015
For estimated shift of the SRF center position, match the band averaged radiance from IASI and COMS/MI radiance
SRF shift : 2.79±1.73 cm-1
Period: April. 2011 - Jan.2012 (16 different days including four seasons)
< Two Methods>
1) Original MI + IASI(SRF shifted by +2.8cm-1 shift)
2) (SRF) Corrected MI + IASI(SRF shifted by +3.4cm-1 shift)
IASI WV SRF +2.8 cm-1 shift
WV(6.7μm)
Bias=-0.8373
RMSE=0.4211
COMS Radiance [Wm-2sr-1mm-1]
Shifted SRF [cm-1]

## Slide 8: Infrared Channel(WV anomaly-2)
Result of IASI SRF shift and the trend of TB bias for WV
Period: Jan. 01.2014 - Dec.12.2014
LEO TB (K)
COMS TB (K)
+ IASI o IASI_3.4
Bias -0.8307 -0.1051
RMSE 0.4112 0.3882
Slop 0.9817 0.9846
Inter. 3.6385 3.6457
+ IASI o IASI_2.8
Bias -0.8307 -0.0277
RMSE 0.4112 0.3905
Slop 0.9817 0.9837
Inter. 3.6385 3.9394
COMS TB (K)
TB Bias(COMS-LEO) (K)
IASI IASI_2.8 IASI_3.4
Bias -0.8307 -0.0277 -0.1051
RMSE 0.4112 0.3905 0.3882
COMS TB (K)
Original : Original MI + Original IASI
Method1 : Original MI + IASI SRF shifted by +2.8cm-1
Method2 : Corrected MI + IASI SRF shifted by +3.4cm-1
WV(6.7μm)

## Slide 9: Infrared Channel (summary)
GSICS GEO-LEO Inter-calibration for COMS IR channels
  Period : AIRS, IASI-A(April 2011 - Dec. 2015), IASI-B(Aug. 2013 - Dec. 2015), CrIS(Jan. 2014 - Dec. 2015)
  TB bias : IR1< 0.13K, IR2<0.02K and IR3<-1.0K(<0.1 after correction)
    TB bias of CrIS show the smallest(0.03K, -0.01K) among four instruments for IR1 and IR2
    SWIR of CrIS shows systematic uncertainties due to its much shorter spectral coverage of MI broadband
    Investigate SRF shift (+2.8cm-1) to correct the large negative bias of WV channel
  Seasonal variation : the same pattern between AIRS and CrIS
    TB bias has two peaks around March and Sep.-Oct.
  Diurnal variation : At the local midnight, the biases of all four IR channels shows gradual increasing patterns which may be caused by midnight effect
    Investigate MBCC effect on the IR channels
  Results of GSICS are displayed on KMA’s homepage http://nmsc.kma.go.kr/html/homepage/en/gsics/gsicsMain.do

## Slide 10: Application of GSICS correction
1. Sea Surface Temperature (SST)
2. Insolation (INS, Shortwave Radiation)
Area: 0-45°N, 105-160°E
Data: COMS/MI IR data, GTS buoy SST data
Nighttime SST
Daytime SST
Bias=0.5377
Before Correction
Bias=0.0627
After Correction
Pyranometer
(Variation Monthly RMSE)
(Variation Monthly Bias)
Study Area : 30-40°N, 120-130°E
Data : COMS/MI Vis data, Pyranometer(Ground station)
Bias=0.0928
Before Correction
Bias=0.0208
After Correction
Bias=11.88
Before Correction
Bias=2.22
After Correction

## Slide 11: COMS IR for Demo phase
Preparation for COMS IR to enter the Demonstration Phase of the GSICS Procedure for Product Acceptance(GPPA)
  Preliminary version of ATBD and sample data (Nov. 2014)
  Checking sample data format

## Slide 12
Thank you…