## Slide 1: USGS Agency Report to GSICS March 20, 2017
Tom Stone, USGS-Flagstaff (GRWG)
Ron Morfitt, USGS-EROS Data Center (GRWG)
Greg Stensaas, USGS-EROS Data Center (GSICS EP)

## Slide 2: Overview
Landsat Mission Status
  Spacecraft status
  Instrument performance and anomalies
  Landsat 7 end-of-mission considerations
GSICS-related Actions and Activities
  CGMS Working Paper on requirements for absolute lunar calibration
  Radiometric comparison of Landsat-8 OLI and Sentinel-2A MSI
  Cal/Val Center of Excellence
  JACIE
Other Activities

## Slide 3: Landsat 7 Observatory Status
Attitude Control System
X-band System
S-band System
Performance nominal
Enhanced Thematic Mapper +
Electrical System
Solid State Recorder
Reaction Control System
1/07/04 Fuel line #4 thermostat #1a failure
2/24/05 Fuel line #4 thermostat failure;
Primary heater circuit disabled
4/25/13 Fuel line #2 thermostat failure;
Redundant heater circuit disabled
Solar Array
5/14/2002 Circuit #14 Failure
5/16/2005 Circuit # 6 Failure
8/13/2008 Circuit #14 recovery
14 circuits remain operating
no impact to ops
11/15/1999 SSR PWA #23 Loss
02/11/2001 SSR PWA #12 Loss
12/07/2005 SSR PWA #02 Loss
08/02/2006 SSR PWA #13 Loss
03/28/2008 SSR PWA #22 Loss
09/03/2008 SSR PWA #23 Recovered
10/12/2013 SSR PWA #11 Loss
Each PWA is 4% loss of launch capacity
Boards are likely recoverable
Performance nominal
•05/05/2004 Gyro 3 Shut Off
•1-gyro control system in development
•5/31/2003 SLC Failure
•4/01/2007 Bumper mode
Remote Tlm Cmd (RTC) Box
•09/27/2014 RTC A Failover
•10/18/2014 Clock Generator Circuit failure
•Battery performance nominal
On orbit since April 1999

## Slide 4: Landsat 7 — Mission-Limiting Factors
Final delta–inclination maneuver executed on 07 February 2017
  crossing time expected to drift to 09:45 (nom. 10:00) by early 2020
Component Anomalies: Mission status that prompts consideration of decommissioning
  End of science mission: A critical failure of either the ETM+ or supporting bus subsystem
  Imminent failure of critical sub-system component capability that is considered necessary to execute the decommission plan
    Loss of critical subsystem redundancy may not be an exit trigger and would be evaluated on a case-by-case basis
    Examples include ACS gyro or C&DH S-band transponder
Fuel Reserves
  Sufficient fuel must be maintained to meet mission decommissioning requirements

## Slide 5: Landsat 7 — Mission Extension Options
Place Landsat 7 in a disposable orbit appx 8 km below 705 km
  EOM estimate late 2020 — coincides with L9 launch
  May be extended to mid 2021 if L9 is delayed
Participating with NASA’s Satellite Servicing Projects Division
  https://sspd.gsfc.nasa.gov/restore-L.html
  L7 identified as client to be captured and refueled
    Would commence after the end of the science mission
  Several options for fuel use (dependent upon health of the spacecraft)
    Must meet 25 year re-entry
    Could be used to raise the inclination (MLT) if desired
    Potential for underflights of L8 and L9 for calibration purposes
    Could return to 705 km if L9 fails to reach orbit
    Could potentially perform science off of WRS

## Slide 6: Landsat 8 Observatory Status
Operational Land Imager
Thermal Infrared Sensor
Propulsion Subsystem
Thermal Control System
-Reaction Wheel 4 Heater erratic cycling
Electrical Power System
Attitude Control System
- CSS-9 current spikes
RF Communications
Command & Data Handling System
On orbit since Feb. 2013
- TIRS Alt Con Ops developed and has been used since Nov. 2015

## Slide 7: Landsat 8 Satellite Status
All spacecraft subsystems are nominal
Instrument special ops:
  One TIRS DS/BB calibration, in addition to those bracketing other TIRS cals per TIRS Modified Con Ops Calendar, was performed on Dec. 30 to maintain the two week interval for TIRS cals. This was the first instance of just a TIRS DS/BB being scheduled.
  TIRS Alternative Con Ops. developed and has been in use since Nov 2015.

## Slide 8: Landsat 7 ETM+ Radiometric Trending
ETM+ stability primarily monitored using PICS
On-board calibrators (2- lamps and a diffuser) were deemed unreliable after few years since launch

## Slide 9: Landsat 8 OLI Radiometric Trending
On-board calibrators and lunar observations are much more precise than PICS
PICS tend to indicate larger drift than on-board calibrators and moon across all the bands
OLI and ETM+ show similar behavior across PICS, indicating more changes in site behavior than the sensors

## Slide 10: GSICS-related Activities
CGMS Working Paper on requirements for absolute lunar calibration
In response to CGMS action on GSICS: CGMS-43 A43.01
  “GSICS to establish the requirements for absolute lunar calibration and prepare a white paper describing the tentative way to meet those requirements in case they go beyond current capabilities.”
Working Paper prepared by T. Stone
  sent to GRWG members for review; revised based on comments received
  delivered to CGMS secretariat, presented at CGMS-44, WG-II (Thanks Dohyeong !)
Recommendations to CGMS:
Satellite instrument operators should adopt requirements to view the Moon with solar band sensors.
Satellite operating agencies should support proposals and programs to acquire the necessary measurements of the Moon to develop a new, high-accuracy, SI-traceable lunar reference standard for reflected solar wavelengths.
Long-term continuity of absolute solar spectral irradiance measurement with SI-traceable accuracy should be ensured.

## Slide 11: GSICS-related Activities
  Radiometric comparison of Landsat-8 OLI and Sentinel-2A MSI
Analysis conducted by Md. Obaidul Haque, SGT/USGS-EROS
Methodology:
  Use near-simultaneous collection of Sentinel-2A MSI and Landsat-8 OLI over Pseudo Invariant Calibration Site (PICS)
    Libya 4 WRS2 Path 181 Row 40, S2A Tile 34RGT (~98x48km)
  Three sets of data were used for radiometric cross calibration
    Same day collection of S2A and L8 data on 12Aug15
    S2A and L8 data collected 4 days apart, 30Dec15 and 03Jan16
    S2A and L8 data collected 6 days apart, 29Jan16 and 04Feb16
    Hyperion data for spectral adjustment collected 28Jul15, 7Sep15, 30Dec15 and 03Feb16
  Apply spectral band adjustment factor (SBAF)
  Compute TOA reflectance from selected ROIs
  Compare TOA reflectance only for similar S2A/L8 bands

## Slide 12: Radiometric comparison of Landsat-8 OLI and Sentinel-2A MSI
OLI
MSI
ROI
HYP
Footprints over Libya 4

## Slide 13: Radiometric comparison of Landsat-8 OLI and Sentinel-2A MSI
Difference in TOA Reflectance
Cross calibration using near simultaneous acquisitions
%Difference in TOA Reflectance (S2-L8)/L8% |  |  |  |  |  |  | 
Band | CA | Blue | Green | Red | NIR | SWIR1 | SWIR2
Set0 | 4.692 | -1.386 | 0.654 | 1.101 | 1.443 | 1.709 | 0.910
Set1 | 4.182 | -1.478 | 0.740 | 0.804 | 0.935 | 1.721 | 1.979
Set2 | 4.430 | -0.078 | 0.633 | 1.104 | 2.024 | 2.183 | 1.020

## Slide 14: GSICS-related Activities
Calibration/Validation Center of Excellence
Currently under development, a part of USGS Earth Resources Observation and Science (EROS) Center
  To consolidate broad expertise within USGS on on-orbit cal/val
  Strategic plan formulated
  Initial implementation set for June 2017
Calibration workshop being planned for Fall 2017

## Slide 15: GSICS-related Activities
Joint Agency Commercial Imagery Evaluation (JACIE) program
Consists of representatives from USGS, NASA, NOAA and the U.S. Dept. of Agriculture
Performs product analysis of commercial and other remote sensing data and information products
  Provides independent characterizations of image and image-derived end products
  Provides independent verification of commercial imagery data quality
Provides Earth scientists with awareness of commercial imagery
Annual Workshop
  2017 JACIE workshop to be held at USGS Headquarters in Reston, Virginia, September 19–21, 2017
https://calval.cr.usgs.gov/jacie

## Slide 16: Other Activities
Preparing for Landsat 9 launch (est. December 2020)
Planning for Landsat 10
Continue on-orbit calibration and validation efforts
  RadCalNet
  PICS
  Lunar
Joint agency efforts
  MOU between USGS and NOAA
Requirements Capabilities and Analysis for Earth Observations
  http://remotesensing.usgs.gov/rca-eo
Land Product Characterization System
  http://landsat.usgs.gov/lpcs.php

## Slide 17
Thank You!