## Slide 1
1
2016 HIMAWARI-9
2014 HIMAWARI-8
Masaya Takahashi and Arata Okuyama
Meteorological Satellite Center, Japan Meteorological Agency
Himawari-8/AHI Lunar Calibration Updates
2017 GRWG/GDWG Annual Meeting, 20-24 March 2017, Madison, USA

## Slide 2: Contents
Himawari-8/AHI Lunar Observation
Lunar Calibration Results using GIRO
  Phase Angle Dependence on Lunar Irradiance Ratio between AHI and GIRO
  Correction of AHI Radiance and its Impacts on Lunar Irradiance Ratio
  Lunar Inter-calibration w.r.t. Aqua/MODIS
  Summary and Future Plans
Acknowledgement:
AHI lunar calibration has been done in collaboration with EUMETSAT (Sebastien Wagner), USGS (Tom Stone) and NOAA (ABI calibration team)

## Slide 3: Advanced Himawari Imager (AHI) on Himawari-8
Band | Central Wavelength [μm] | Spatial Resolution [km] | # of detectors (*) | Levels of digital count [bit]
1 | 0.47 | 1 | 676 (3) | 11
2 | 0.51 | 1 | 676 (3) | 11
3 | 0.64 | 0.5 | 1460 (3) | 11
4 | 0.86 | 1 | 676 (6) | 11
5 | 1.6 | 2 | 372 (6) | 11
6 | 2.3 | 2 | 372 (6) | 11
7 | 3.9 | 2 | 332 (6) | 14
8 | 6.2 | 2 | 332 (6) | 11
9 | 6.9 | 2 | 332 (6) | 11
10 | 7.3 | 2 | 332 (6) | 12
11 | 8.6 | 2 | 332 (6) | 12
12 | 9.6 | 2 | 332 (6) | 12
13 | 10.4 | 2 | 408 (6) | 12
14 | 11.2 | 2 | 408 (6) | 12
15 | 12.4 | 2 | 408 (6) | 12
16 | 13.3 | 2 | 408 (6) | 11
AHI Field of View Center (VNIR)
ITT EXELIS(2013): AHI-8 EQUIPMENT MANUAL 2
CALIBRATION AND ALIGNMENT HANDBOOK Rev. J
*Number of redundant detector columns per side

## Slide 4
Region 4, 5: mainly used for landmark observation, but region 5 is also used for lunar observation
Full Disk Observation
every 10 min. (23 swaths)
Region 1
2000 x 1000km
(NE Japan)
Every 2.5 min.
Region 2
2000 x 1000km
(SW Japan)
Every 2.5 min.
Region 3
1000 x 1000 km
(Target Area)
Every 2.5 min.
Region 4
1000 x 500 km
(Landmark Area)
Every 30 sec.
Region 5
1000 x 500 km
(Landmark Area)
Every 30 sec.
Pre-defined area
Flexible observation area
AHI FoR
Earth edge
Lunar observations
Band5 (1.6μm)
Full Disk / Regional Observation in 10 minutes Repeat Cycle

## Slide 5
2015-09-28
A day of total lunar eclipse
and super moon
Band05 (1.6 μm)
Band07 (3.9 μm)

## Slide 6: AHI Lunar Observation
Performed using Region 5 (1000x500km for the earth scene) flexible observation
Just one scan to observe the Moon
1 observation / 30 seconds
-> huge number of observations
Earth disk
MTSAT-2/Imager
(Jul.2010 – Dec.2013)
98 Obs. / 3.5 years
Lunar phase angle [deg]
Full moon
-180 -120 -60 0 60 120 180
Earth disk
AHI FoR
Himawari-8/AHI
(4 Mar. 2015 – 30 Oct. 2016)
26167 Obs. / 20 months

## Slide 7: AHI Lunar Observation for GIRO
More than 7000 (150 days) useful lunar obs. for GIRO within the applicable phase angle:
2 deg <= |phase angle| <= 92 deg
B01 (0.47μm)
B02 (0.51μm)
B03 (0.64μm)
B04 (0.86μm)
B05 (1.6μm)
B06 (2.3μm)
2015-08-01T03:03:26Z (phase angle: 10.5deg)
Time series of AHI lunar phase angle [deg]
[deg]

## Slide 8: Time Series of ΔIrr in AHI VNIR Bands Pre-launch determined Cal. Coeffs. are used for whole period of time
Band1 (0.47μm) Band2 (0.51μm) Band3 (0.64μm)
Band4 (0.86μm) Band5 (1.6μm) Band6 (2.3μm)
2 12 22 32 42 52 62 72 82 92
Phase angle [deg]
Difference of lunar irradiance between the observation and GIRO [%]
Phase angle dependence in Band1-3
Suggests possible issues in AHI VNIR calibration, but
Trends are good agreements with other Cal/Val methods (next slide) when specific phase angle is focused
Phase angle dependence in Band4-6
Seems to be reasonable because similar results are derived in SEVIRI (shown later)

## Slide 9: Validation of On-board Calibration Slope
Band1 (0.47μm) Band2 (0.51μm) Band3 (0.64μm)
Band4 (0.86μm) Band5 (1.6μm) Band6 (2.3μm)
Updates of Cal. slope
Error bar: stdv. of slopes
Improvement of accuracy after updating calibration slopes based on SD observation
~0.5%/year of degradation trend in band 1-4
+6.1% bias for band 5, -4.3 % bias for band 6 based on ray-matching validation
Time series of ratios between AHI observations and reference values

## Slide 10: AHI Lunar Calibration – Lunar Phase Angle Dependence
MSG1/SEVIRI NIR1.6
Himawari-8/AHI Band5 (1.6 μm)
2015-03-04 to 2016-10-17 (7405 Obs. )
ΔIrr (%)
Phase angle (deg)
Good agreement with SEVIRI NIR1.6, but not with SEVIRI VIS 0.6
Possible issues in AHI calibration
10
Difference of lunar irradiance between the observation and GIRO [%]
ΔIrr (%)
Himawari-8/AHI Band3 (0.64 μm)
SEVIRI results from B. Viticchie at the Lunar Calibration Workshop in Dec. 2014
MSG2/SEVIRI VIS 0.6

## Slide 11: Impact study of correcting observed lunar irradiance using VIIRS ray-matching inter-cal approach
Motivation:
Phase angle dependence on ΔIrr in 0.47, 0.51 and 0.64 μm bands
might be caused by AHI calibration
nonlinearity which is seen in ray-matching VIIRS (next slide)?

## Slide 12: Correction of AHI radiance using VIIRS ray-matching results
Nonlinearity in AHI calibration?
1. Extract dark scene
(i.e. TB@10.4 μm > 295 K）
2. Derive radiance correction slope by linear regression (force fitting) of GEO/LEO radiances
3. Correct observed lunar irradiance and re-compute ΔIrr: (irrObs/irrRolo-1)*100
AHI Band3 (0.64 μm) –VIIRS I01 (0.64 μm) ray-matching

## Slide 13
w/o irradiance correction w/ irradiance correction
0.47 μm
0.64 μm
0.47 μm
0.64 μm
Main Impacts: ΔIrr shift to negative value
Reduction of ΔIrr variation: at some periods of time, but not enough
Nonlinearity may not be the root cause
Need for other investigations (e.g. stability of deep space counts)
Impacts of observed lunar irradiance correction on ΔIrr
+10
+4
0
-7
+3
-3
+2
-6

## Slide 14: Inter-calibration (proposed by S. Wagner in 2016)
Compute lunar irradiances using:
SRF of monitored instrument (i.e. AHI)
Observation time and satellite position of reference instrument (i.e. Aqua/MODIS)
and compare with observed lunar irradiance by MODIS (SBAF is also taken into account)
2. Take an average of the results of 1
Assumption : well calibrated (no degradation), no phase angle dependence
3. Take difference between monitored/reference instruments and derive inter-calibration result

## Slide 15: ΔIrr of Himawari-8/AHI Band4 (0.86 μm)
6 7 8 9 [%]
Relative difference of AHI lunar irradiance vs. GIRO: ~7.5% +/- ~2%
Pre-launch calibration coefficients are used

## Slide 16
-2 -1 0 1 2 [%]
ΔIrr: shifted from 7.5 (+/- 2) [%] to ~0 [%] (SBAF is currently not considered)
Inter-calibration w/ other instruments (e.g. SEVIRI) is underway in collaboration with S. Wagner
Inter-calibrated ΔIrr of Himawari-8/AHI Band4 (0.86 μm)
with reference to Aqua/MODIS Ch2 (0.858 μm)

## Slide 17: Summary and Future Plans
More than 7000 Himawari-8/AHI lunar observations from March 2015 to November 2016 were used
Lunar irradiance ratio between AHI and GIRO
  Phase angle dependence in Band 1, 2, 3 (0.47, 0.51, 0.64 μm)
  Possible issue in AHI calibration was found, but need further investigations to figure out the root cause
  Keep a collaboration with USGS
  Phase angle dependence in Band 4, 5, 6 (0.86, 1.6, 2.3 μm)
  Good agreements with SEVIRI lunar calibration results
  Lunar inter-calibration w.r.t. Aqua/MODIS
  Just started in collaboration with EUMETSAT
  Similar approach for S-NPP/VIIRS is also planned

## Slide 18
Thanks for your attention

## Slide 19: JMA geostationary satellites
GMS (Geostationary Meteorological Satellite)
MTSAT (Multi-functional Transport SATellite )
Back-up operation of GMS-5 w/ GOES-9 by NOAA/NESDIS:
2003/05/22-2005/06/28
(GOES-9)
Aug 1981
GMS-2
(Himawari-2)
Aug 1984
GMS-3
(Himawari-3)
Sep 1989
GMS-4
(Himawari-4)
Mar 1995
GMS-5
(Himawari-5)
Feb 2005
MTSAT-1R
(Himawari-6)
Feb 2006
MTSAT-2
(Himawari-7)
Jul 1977
GMS
(Himawari)
Himawari
2014
Himawari-8
2016
Himawari-9
ⒸNASDA
ⒸNASDA
ⒸNASDA
ⒸNASDA
ⒸNASDA
ⒸSS/L
ⒸMELCO
Satellite | Operation period
GMS | 1978 – 1981
GMS-2 | 1981 – 1984
GMS-3 | 1984 – 1989
GMS-4 | 1989 – 1995
GMS-5 | 1995 – 2003
GOES-9 | 2003 – 2005
MTSAT-1R | 2005 – 2010
MTSAT-2 | 2010 – 2015
Himawari-8 | 2015 – 2022
Himawari-9 | 2022 – 2029
launched on 7 Oct. 2014
Operation started on 7 July 2015
launched on 2 November 2016
Became back up of Himawari-8 on 10 March 2017

## Slide 20: Typical Observation Schedule in 10 minutes Repeat Cycle
[sec]
Full Disk | Region 1 (NE Japan)
BB Obs. | Region 2 (SW Japan)
Space Look | Region 3 (Target Area)
 | Region 4 (Landmark Area)
 | Region 5 (Landmark Area)
Blackbody Obs.
[sec]

## Slide 21: Calibration Slope from SD observation
Band1 (0.47μm) Band2 (0.51μm) Band3 (0.64μm)
Band 4 (0.86μm) Band5 (1.6μm) Band 6 (2.3μm)
8 June 2015: averaged calibration slope from 7 March to 22 May (7 obs.) was applied
Late February 2015: big change in L1 equiv. data processing
~0.5% degradation trend in band 1-4 (no degradation of SD is assumed)
7 Mar
Time series of detector-averaged inverse of calibration slope from SD observation
Inverse of calibration slope [W/m2/sr/μm/count]-1
22 May
Band4 (0.86μm)) Band 5 (1.6μm) Band6 (2.3μm)

## Slide 22: Validation of On-board Calibration Method 1) Vicarious Calibration using RT Simulation
Method: Comparison of observed and simulated radiance for multiple targets (collaboration research with the University of Tokyo and JAXA/EORC [Prof. Nakajima])
Targets:
Cloud-free ocean (rayleigh scattering) , liquid water cloud, *cloud-free land and *deep convective cloud
Radiative transfer calculation:
RSTAR (Nakajima and Tanaka [1986,1988])
Input data: Independent from GEO data
JMA Re-Analysis atmos. profiles (JRA-55/JCDAS)
Aerosol/Cloud optical thickness retrieved from MODIS L1B (M[O,Y]D02SSH)
MODIS BRDF (MCD43C2) for land target
Aura/OMI total column ozone, …
August 2015
Simulated reflectivity
Observed reflectivity
*Under investigation for Himawari-8/AHI as of Oct. 2016

## Slide 23
Inter-calibration based on AHI-VIIRS collocation
Calibration target: cloud pixels
Introduction of dark target (e.g. cloud-free ocean) : under investigation
Spectral Band Adjustment Factor (SBAF) accounting for the spectral mismatch
Band1-5: from NASA Langley SBAF based on SCHIAMACHY (http://cloudsgate2.larc.nasa.gov/SBAF)
Band6: computed using RSTAR simulation
Band1 Band3 Band5
(0.47 μm) (0.64 μm) (1.6μm)
Stats from 17 to 31 Oct. 2016
Validation of On-board Calibration Method 2) Ray-matching with S-NPP/VIIRS

## Slide 24: Lunar Calibration using GIRO
Comparison of observed/predicted disk-integrated lunar irradiance
Robotic Lunar Observatory (ROLO) model: calibration reference developed by USGS
  Empirical model to derive disk-integrated lunar irradiance (Kieffer & Stone 2005, AJ, 129, 2887)
  Based on more than 8 years of lunar observations at Flagstaff, AZ
  Applicable spectral range: 0.35-2.5 µm
  Has been used for many satellite instruments: SeaWiFS, MODIS, MSG/SEVIRI, GOES/Imager, ...
  Accuracy of the reference irradiance
  5 – 10 % uncertainty in absolute irradiance scale
   1 % relative accuracy
GSICS Implementation of the ROLO model (GIRO)
Implemented in 2014, lead by core agencies (USGS, EUMETSAT, NASA, CNES)
Standard reference model for the lunar calibration community

## Slide 25: Web monitoring system of AHI lunar observations (JMA intranet page)
Lunar images of VIS/NIR + SWIR (3.9 μm) bands
Observation time, relative lunar positions and lunar phase angle

## Slide 26
AHI Lunar Calibration - Case Study
AHI FoR
Earth edge
Lunar observations
29 August 2015
Phase angle: from -11.5 to -9.0 [deg]
100 observation / ~90 minutes
Difference of lunar irradiance between the observation and GIRO [%]
Averaged deep space counts
Lunar Phase Angle [deg]
ΔIrr (%)
~0.3 count variation
26
~0.4% variation
~2% increase
Digital counts: after detector equalization (e.g. equivalent to counts in L1B)
Does the trend related with deep space counts?
Band2 (0.51μm)
Band2 (0.51μm)

## Slide 27: Deep Space Counts (Csp) for Calibration Equation
[sec]
Full Disk | Region 1 (NE Japan)
BB Obs. | Region 2 (SW Japan)
Space Look | Region 3 (Target Area)
 | Region 4 (Landmark Area)
 | Region 5 (Landmark Area)
[sec]
Robs: Observed radiance
CA: Raw digital count
Csp: Deep space raw digital count
qn, mn: Coefficients
n: Detector ID
r : Scan mirror reflection coef.
q, f : Incidence angle to SM
Same (constant) values observed at the East (or West) of each Full-disk swath are applied to regional observations including lunar obs.
Moon
Moon
Moon
Moon
Moon
Moon
Moon

## Slide 28: Use of Deep Space Counts at each Lunar Observation in the Calibration Process
Compute Csp_moon for each lunar observation and each detector
Replace nominal Csp with the Csp_moon and re-compute radiance
Convert re-computed radiance to digital counts (equivalent to L1B)
Take average of deep space counts
~0.15 count variation
Mean deep space counts
~0.3 count variation
Calibration process in which Csp is used
Calibration process in which Csp_moon is used

## Slide 29: Reduction of ΔIrr trend
~0.3% variation
ΔIrr (%)
~0.4% variation
Calibration process in which Csp is used
Calibration process in which Csp_moon is used
Calibration equation w/ Csp_moon reduces the up/down trend in ΔIrr
Need for further investigation of remaining ΔIrr trend depending on lunar phase angle

## Slide 30: Phase Angle Dependence Correction of Lunar Irradiance
w/o phase angle correction w/ phase angle correction
Himawari-8/AHI Band5 (1.6 μm)

## Slide 31: A possible scheme for inter-calibration
By definition:
MODIS is the truth  we re-projected in the irradiance space of the monitored instrument:
Reference instrument = Aqua MODIS
Phase angle range = [-56,54]
λ, ϕ = Reference wavelength, Phase
ϕ = “50” = MODIS range
λ’, ϕ’ = Monitored wavelength, Phase
From GLOD/NASA data, we derive the mean
If MODIS is perfectly calibrated and there is no phase dependence:
Consequently:
Wagner (2016)