## Slide 1
Lunar Observation with
an FTIR Imaging Spectrometer: Recent Progress and Beyond
Geng Zhang
Key Laboratory of Spectral Imaging Technology CAS
Xi’an Institute of Optics and Precision Mechanics of CAS

## Slide 2: Equipment Introduction
Main Equipment
SWIR Interference Spectral Imager
(Modified From an Existing Prototype)
Guiding Telescope
ASD Spectral Radiometer
Integrating Sphere

## Slide 3: Equipment Introduction
Lijiang,
Yunnan Province

## Slide 4: Equipment Introduction
FTIR Imaging Spectrometer
Spectral Range：900nm~2500nm
Bands：60
FOV：1.2°x 0.61°
Detector：500(spatial) x 256(spectral)
Focal Length：720mm
Dark Current：0.9DN
SNR：≥1000（50x DTDI）
Parameters

## Slide 5: Data Achieved
14th Jan 2016（2016-01-14-19-59-19）

## Slide 6: Data Achieved
30th Jan 2016（2016-01-30-06-30-02）

## Slide 7: Data Achieved
24th Feb 2016（2016-02-24-00-02-42）

## Slide 8: Data Achieved
Frame
4 |  |  |  |  |  | 
4 |  |  |  |  |  | 
4 |  |  |  |  |  | 
3 |  |  |  |  |  | 
2 |  |  |  |  |  | 
1 |  |  |  |  |  | 
3 |  |  |  |  |  | 
3 |  |  |  |  |  | 
Interferogram
5 |  |  |  |  |  | 
4 |  |  |  |  |  | 
3 |  |  |  |  |  | 
2 |  |  |  |  |  | 
Each line corresponds to an fixed OPD
Original Fames
Interferogram
Scanning Direction
Consists of lines from 256 original frames
Target Points: 1,2,3,4,5……

## Slide 9: Problems and Solutions
Moon’s orbiting speed Desired observation speed
Moon’s orbiting direction Interference direction
Image “shaking” caused by atmosphere turbulence
Bad pixels
Sensor
Moon’s Image
Correct the moon’s image to the desired position
Problems

## Slide 10: Problems and Solutions
Matching current frame to the reference frame to estimation the horizontal and vertical translations w.r.t. desired position.
Most of the image is black
Moon is low textured
Traditional patch based image registration does not work!
Alg.1 Use moon boundary to match the frames to the reference one.
Alg.2 Estimate center positions full moon.
Displacement to the desired position
Solutions
Background is black,
Textures are weak,
Boundary is reliable!

## Slide 11: Translation Estimation
Boundary Matching
Generate fringe-free reference frame
Non-full Moon
(Near) Full Moon
Automatically choose the clean part (lines of high OPD) to match

## Slide 12: Translation Estimation
Boundary Matching
Compute cross correlation between matching frame and reference frame under different translations.
Correlation Map
Peak indicates best matching
Sub-pixel accuracy achieved through interpolation.
5x5 50x50
Peak location

## Slide 13: Translation Estimation
Center Matching
Locate boundary points of the moon
Valid boundary points
End points of the scan lines
Estimate circle center using boundary points
Using chords to estimate the center.
Pyramid searching for subpixel accuracy
Radius Restriction
Chord Voting
Scan Line Searching

## Slide 14: Translation Estimation
Center Matching
Chord voting method: Approximated radius is used.
Pyramid searching method: Not only accurate center position,
But also a better radius estimation.
Why pyramid searching?
Blue line: chord voting method
Red line: after pyramid searching
Circle fitting using estimated center and radius
Contains Error

## Slide 15: Interferogram Extraction
Along-track translation w.r.t. the first frame Integers
Across-track translation w.r.t the first frame Zero
Processing Overview

## Slide 16: Data Rectification
Along-track translation correction
The frame rate of our equipment is about 200 times higher than the desired frame rate.
Choose the frames whose along-track translation w.r.t. the first frame are closest to the nearest integral numbers.
Temporally over-sampled
Inter-frame interpolation is not needed!
Residual error: 0.005 pixel
Frame 1
Frame 198
Frame 395
Frame 794
0 pixel
0.998 pixel
2.003 pixel
2.9999 pixel
Along-track translation w.r.t Frame 1
…
…
…

## Slide 17: Data Rectification
Along-track translation correction (low frame-rate case)
Achieved by inter-frame interpolation (temporal interpolation)
t1
t2
3.52
4.21
4
Along track translation

## Slide 18: Data Rectification
Original
Rectified

## Slide 19: Data Rectification (Compared to other methods)
Extracted Interferograms. (Distortions are rectified)
C1
C2
C3
ours

## Slide 20: Spectrum Reconstruction
Following standard FTIR spectrum reconstruction pipeline
Sample Point 4
Sample Point 1
Sample Point 2
Sample Point 3
(a) Spectral curves generated from the new moon data

## Slide 21: Spectrum Reconstruction
Following standard FTIR spectrum reconstruction pipeline
Sample Point 4
Sample Point 1
Sample Point 2
Sample Point 3
(b) Spectral curves generated from the gibbous moon data

## Slide 22: Spectrum Reconstruction
Following standard FTIR spectrum reconstruction pipeline
Sample Point 4
Sample Point 1
Sample Point 2
Sample Point 3
(c) Spectral curves generated from the full moon case

## Slide 23: Spectrum Reconstruction
1008.5 nm
1252.5 nm
1605.1 nm
1740.7 nm
2039.0 nm
2147.5 nm
(a) Spectral bands reconstructed from the new moon data

## Slide 24: Spectrum Reconstruction
1008.5 nm
1252.5 nm
1605.1 nm
1740.7 nm
2039.0 nm
2147.5 nm
(b) Spectral bands reconstructed from the gibbous moon data

## Slide 25: Spectrum Reconstruction
1008.5 nm
1252.5 nm
1605.1 nm
1740.7 nm
2039.0 nm
2147.5 nm
(c) Spectral bands reconstructed from the full moon

## Slide 26: Lunar Radiance Estimation
Proposed approach rectifies the data accurately.
Smoothest boundary
C1
C2
C3
ours

## Slide 27: Lunar Radiance Estimation
Radiance achieved by absolute calibration using simulated atmosphere transmittance from MODTRAN，Error: 10.7%
Data: 24th Feb 2016（2016-02-24-00-02-42）

## Slide 28: Future Work
Aiming
Develop an automatic moon observing equipment which is able to achieve spectral and spatial data simultaneously.
Requirements
1）Acquiring both spatial and spectral data
2）Automatically following the moon, storing and processing the data
3）Self calibration
FUTURE WORK

## Slide 29: Future Work
Parameters
  Spatial Resolution：≥200×200 (Full Moon)
  Spectral Rage：900~2500nm
  Band MTF：≥0.2
  Band SNR：≥500:1（Full Moon）
  Spectral Resolution：≤10nm

## Slide 30: Future Work
Using two kinds of imaging spectrometers to compensate each other.
FTIR spectral imager base on Sagnac interferometer
high optical sensitivity
stable spectral positions
no spectral mixing
low radiance consistency
non-uniform wavelength
(uniform wave number)
Pros:
Cons:
Dispersive spectral imager using Offner principle
high radiance consistency
Low requirement to the platform
uniform wavelength
spectral mixing
unstable spectral position
Pros:
Cons:

## Slide 31: Future Work
SPECIFICATION
Spectral Range：1um~2.5um
Spectral bands：150
MAX SNR：>1000
Smile distortion：≤10% of a pixel
Keystone distortion: ≤10% of a pixel
Spatial resolution: 0.002°
Field of view: 0.64°
Accuracy of spectral calibration：≤1nm
Accuracy of radiometric calibration：≤5%

## Slide 32: Future Work
The telescope is Ritchey-Chretien Telescope with fore-Lens Corrector, has a focal length of 860mm and an F-number of 4.0. The exit pupil is located near infinity giving a telecentric image, which is required for a proper pupil matching with the spectrometer.
The spectrometer consists of three spherical mirrors and two Féry prisms made from fused silica.

## Slide 33: Future Work
Spot diagram matrix
The spot diagrams are given for five wavelengths from1000 to 2500 nm and at three field points covering the whole field of view. All boxes are 30 µm matching the pixel pitch of the SWIR detector.
Bandwidth of a single pixel
The width of the spectral response function varies between 7.5 and 12.4 nm. The mean bandwidth is 10 nm

## Slide 34: Future Work
Smile distortion
Smile distortion is less than 0.5um, about 0.02 pixel pitch.
Keystone Distortion
Keystone distortion is less than 0.5um, about 0.02 pixel pitch.

## Slide 35: Future Work
The thermal response has been checked for temperatures between 16 and 24°C. The optical performance degradation is negligible. The thermally induced shift of the spectrum on the detector is 1.15 nm/K on the average.
An inner-calibration system based on an integrating sphere will be used to create repeatable and smooth spectral radiance for assessing the spectral and radiometric properties of the spectrometers. This facility allows the monitoring of the instrument at small time intervals.

## Slide 36
Thank You For Listening !
KEY LABORATORY OF SPECTRAL IMAGING TECHOLOGY CAS
XI’AN INSTITUTE OF OPTICS AND PRECISION MECHANICS OF CAS
Geng Zhang gzhang@opt.ac.cn
Shuang Wang wangshuang@opt.ac.cn
Libo Li lilibo@opt.ac.cn