## Slide 1: Current Status of ROLO and Future Development
Thomas C. Stone
U.S. Geological Survey, Flagstaff, AZ USA
GSICS/IVOS 2nd Lunar Calibration Workshop
Xi’an, China
13-16 November 2017

## Slide 2: Introduction to ROLO
A dedicated ground-based telescope facility — the Robotic Lunar Observatory (ROLO):
Lunar disk reflectance model
• empirically derived formulation
• a function of only the geometric variables of phase and the lunar librations:
ROLO telescopes zenith-pointed at dusk
• located at Flagstaff, AZ 2143 m altitude
• operated more than 8 years, acquired >110 000 images in 32 multispectral bands
‒ 23 VNIR bands, 350−950 nm
‒ 9 SWIR bands, 950−2450 nm
• phase angle range from eclipse to 90°

## Slide 3: ROLO Current Status
Telescope facility is dormant; no additional images being acquired
ROLO model is actively used by spacecraft instrument teams, typically for relative calibrations:
  to monitor changes in sensor response with time
    e.g. SeaWiFS achieved 0.13% stability for water-leaving radiances
  for sensor inter-calibration, using the Moon as a common reference
Currently the Moon is not typically used for absolute calibration
  the absolute scale uncertainty for the ROLO model is ~5-10%
    estimate based on comparisons of Moon measurements made by many different instruments
    this level of accuracy is insufficient for a primary on-orbit cal reference
  this is a limitation of the current lunar model, not the Moon
  the Moon potentially can provide an absolute calibration reference with uncertainty ≤1% (k=2)

## Slide 4: Refinement of the ROLO Model
First steps: revise the ROLO data reduction system and reprocess the ROLO dataset
The basis data for lunar modeling are ground-based Moon images
  requires image processing to irradiance, similar to space-based imagers
  requires correcting for atmospheric transmission of the observations
    using extinction measurements from star observations
Refinements to the ROLO system currently completed:
algorithm for stellar irradiance measurements (from ROLO images)
stellar extinction analysis: multi-variate Langley fits
Refinements still needed:
algorithm for Moon irradiance measurements from images
  includes sensor characterization analysis, especially the SWIR camera
applying updated stellar irradiance measurements for absolute scale
  including Vega, potentially other absolute reference stars

## Slide 5: ROLO Dataset Phase and Libration Coverage
These plots show a subset of the ROLO archive, ~2300 Moon observations in the 555 nm band.
The phase and libration parameter space is substantially covered.

## Slide 6: Refinement of the ROLO Model
Next steps: develop a new empirical formulation for the lunar model and fit the reprocessed ROLO dataset
Utilize knowledge gained from current and past lunar calibration accomplishments, e.g.:
  SNPP VIIRS time series shows a libration dependency effect
  instruments with large phase angle coverage (GEOs, PLEIADES) show phase dependency effects
    but lunar irradiance measurements from spacecraft must first be validated !
Develop constraints for fitting the ROLO dataset based on reliable new lunar measurements
  Monday session, GLOD, …
Update the ROLO absolute calibration based on improved knowledge of lunar and stellar irradiances

## Slide 7: Summary and Way Forward
Reprocessing the ROLO dataset and reformulating the ROLO model are necessary, but improving absolute accuracy is essential
  a lunar reference with ≤1% (k=2) accuracy is technically achievable
  ROLO absolute accuracy may be limited by airmass coverage of the star observations
New high-accuracy measurements to characterize the Moon are needed to advance an absolute lunar calibration reference
  tentative requirements for collecting a new lunar measurement database outlined in CGMS Working Paper: CGMS-44 GSICS-WP-02 (2016)
    includes above-atmosphere measurement component
    to achieve the full potential for accuracy, must consider polarization aspects