## Slide 1
Microwave Integrated Retrieval System (MiRS): Overview, Recent Activities, and Applications
Chris Grassotti (NOAA/STAR and U. Md. ESSIC/CICESS)
Quanhua (Mark) Liu (NOAA/STAR), Shuyan Liu (NOAA/STAR and CSU/CIRA),
Yong-Keun Lee (NOAA/STAR and U. Md. ESSIC/CICESS), Ryan Honeyager (NOAA/STAR and JCSDA)
Hurricane Florence N20 and SNPP ATMS RR and TPW, 9-17 Sept 2018

## Slide 2: Outline
Algorithm Overview
Assessments of NOAA-20 and SNPP
  Radiometric and geophysical comparisons: operational product examples, cal/val activities
New Activities/Science Improvements/Applications
  TC Applications: intensity estimation, warm core anomaly retrieval
  Dynamic radiometric bias correction using machine learning
  Blended/Advected Layer PW
Summary and Path Forward

## Slide 3: Algorithm Overview
~ 20 channels (multispectral)
Temp. Profile (100 layers)
Water Vapor Profile (100)
Emissivity Spectrum
(~ 20 channels)
Skin Temperature (1)
Cloud Water Profile (100)
Graupel Water Profile (100)
Rain Water Profile (100)
Satellite Microwave (TB) Measurements (INPUTS)
Geophysical State Vector
(OUTPUTS)
TB (Channel 1)
TB (Channel 2)
TB (Channel 3)
TB (Channel Ntot)
MiRS Components
Forward RT Model (CRTM):
TB= F(Geophysical State Vector)
(2) Jacobians (dTB/dX)
A Priori Background:
Mean and Covariance of
Geophysical State (Dyn Climatol)
Basis Functions for State Vector:
Reduce degrees of freedom
in geophysical profile (~20 EOFs)
Uncertainty of satellite radiances:
Instrument NEDT + Fwd Model
uncertainty
Sensor Noise
MiRS
1D
Variational
Retrieval
MiRS
Postprocessing
RR
CLW
RWP
GWP
TPW
SWE/GS
SIC/SIA
SFR
Derived Products
(OUTPUTS)
MW Only, Variational Approach: Find the “most likely” atm/sfc state that: (1) best matches the satellite measurements, and (2) is still close to an a priori estimate of the atm/sfc conditions.
“Enterprise” Algorithm: Same core software runs on all satellites/sensors; facilitates science improvements and extension to new sensors.
Initial capability delivered in 2007. Currently running on SNPP/ATMS, N18, N19, MetopA, MetopB, F17, F18, GPM/GMI, Megha-Tropiques/SAPHIR. (eventually MetopC…)
Delivery of v11.3 (extended to NOAA-20/ATMS) to operations on June 2018. V11.4 delivered in July 2019, and is currently running in operations.
External Users/Applications: TC Analysis/Forecasting at NHC, Blended Total/Layer PW Animations at NHC and WPC (CSU/CIRA, U. Wisconsin/CIMSS), CSPP Direct Broadcast (U. Wisconsin), NFLUX model (NRL, Stennis), Global blended precipitation analysis at NOAA/CPC (CMORPH),…

## Slide 4: MiRS Users
Many users use MiRS products for operational applications and research.
Operational users, who have subscriptions on PDA, are:
  NWS NHC, NESDIS_VIZLAB, CLASS, STAR, NASA GPM, NAVO, FNMOC, 557TH, NASA JPL, GNC-A, NWC, CHINA CMA, NWS AWIPS, NWS NCO, CIRA, NASA SPORT, SSEC/CIMSS, NESDIS operational applications: eTRaP, blended TPW, blended RR, and IMS
  NHC TC intensity (POC: Galina Chirokova (CIRA))
  International Arctic Research Center, Alaska (POC: Carl Dierking, NOAA Liaison)
  NOAA Climate Prediction Center (POC: Pingping Xie)
  National Ice Center
  NWS Weather Forecast Offices
CSPP generates MiRS products for direct broadcasting
Users also download MiRS from CSPP and generate MiRS products locally

## Slide 5: N20 Radiometric Biases: Time Series TDR Obs-Sim (29 Nov 2017 – 30 Nov 2018)
Chan 7 (54.4 GHz)
Chan 9 (55.5 GHz)
Chan 11 (57.29 ± 0.22 GHz)
Chan 13 (57.29 ± 0.32 GHz)
Chan 20 (183.31 ± 3 GHz)
Chan 6 (53.6 ± 0.12 GHz)
Simulated TBs: ECMWF + CRTM (v2.1.1), clear ocean
ECMWF + CRTM
GDAS + CRTM
Scan Position
Scan Position
Scan Position
Scan Position
Scan Position

## Slide 6: Temperature Profile Validation
N20 500hPa Temperature
N20-ECMWF 500hPa Temp. Diff.
NPP 500hPa Temperature
NPP-ECMWF 500hPa Temp. Diff.
Same instrument: ATMS
50 minute apart

## Slide 7: Temperature Profile Validation based on ECMWF data: Time Series (Nov 2017 – May 2019)
Bias Sea N20
Bias Land N20
Std Dev Sea N20
Std Dev Land N20
100, 300, 500, and 900 hPa

## Slide 8: Temperature Profile Validation based on ECMWF data: Time Series (Nov 2017 – May 2019)
Bias Sea NPP
Bias Land NPP
Std Dev Sea NPP
Std Dev Land NPP
100, 300, 500, and 900 hPa

## Slide 9: Temperature Profile Validation Using Radiosondes
9-20 Jan 2018
9-20 Apr 2018
9-20 Jul 2018
9-20 Oct 2018
Green thick: N20 bias
Brown thick: NPP bias
Green dotted: N20 std
Brown dotted: NPP std

## Slide 10: Precipitation Validation Using Stage IV
MiRS
Stage IV

## Slide 11: Time Series: N20 and NPP vs. Stage IV Dec 2017 – Jun 2019
Req
Req

## Slide 12: Time Series: N20 and NPP vs. Stage IV Dec 2017 – Jun 2019
False Alarm Rate
Req
Req
Req

## Slide 13: Developing a TC-Specific Version of MiRS
  Motivation:
  MiRS data currently used in the operational TC Intensity Algorithm (HISA, developed at CIRA). Utilizes T and WV sounding to estimate warm core structure combined with statistical/dynamic model to predict future intensification.
  Challenge: (1) retrieval of warm core structure complicated due to presence of hydrometeors; scattering signal in TBs can interfere with retrievals (2) hurricane warm core structure is anomalous relative to “global climatology” currently used as a priori constraint in MIRS.
Development of MiRS-TC, a version of MiRS optimized for tropical cyclones, adapting several components:
  Modify use of higher frequency channels in scenes likely to have large amounts of scattering
  Test varying sources of First Guess/Background constraints (developing updated background mean/covariance based on observed TCs)
  Vary number of EOF basis functions for T and WV profiles
Testing ongoing with multiple TC cases
  Dorian (2019), Florence (2018), Joaquin (2016), Matthew (2015), Edouard (2014)
  Planned collaboration with CIRA to determine impact on TC intensity estimates

## Slide 14: Hurricane Florence Precipitation and Temperature Anomaly
ECMWF
Oper
Test
Florence: 2018-09-12
NPP Des
Rain rate and Temperature Anomaly Cross-sections
Hurricane Bonnie, 1998
Kidder at al. (2000)

## Slide 15: TC Florence and Dorian NPP and N20 Temperature Bias: MiRS-ECMWF (Rainy, dist <= 100km)
NPP Des
NPP Asc
N20 Des
N20 Asc
TC Florence
TC Dorian

## Slide 16: Application Using MiRS Data: Hurricane Intensity and Structure Algorithm (HISA)
HISA provides MW-based TC Intensity estimates:
Global
Objective
Independent of Dvorak
Input:
    Temperature profile, CLW from AMSU/ATMS-MiRS or statistical retrievals
    GFS boundary conditions
    ATCF TC track data
Output:
1) Intensity estimates, provided via f-deck
    Maximum sustained wind (Vmax, kt)
    Minimum Sea Level Pressure (MSLP, hPa)
    2) Surface Wind Radii Estimates (nmi), provided via f-deck
    R34, R50, R64 for NE, NW, SE, and SW TC quadrants
3) Azimuthally-averaged gradient winds as a function of geopotential height and distance from TC center.
4) Horizontal 2-D balanced winds (kt) for the local TC environment
Operational on ATMS and AMSU on 7 satellites, is upgraded to work with NOAA20 ATMS
Users: NHC, CPHC, JTWC
 | ATMS-MIRS MAE | AMSU-MIRS MAE
Vmax (kts) | 11.1 (1565) | 13.2 (4346)
Pmin (hPa) | 7.0 (1565) | 8.4 (4347)
R34 (nmi) | 20.0 (344) | 24.9 (1044)
R50 (nmi) | 12.0 (215) | 10.6 (601)
R64 (nmi) | 12.0 (134) | 8.9 (336)
Galina Chirokova (CIRA), John Knaff (NOAA/NESDIS), Scott Longmore (CIRA), Mark DeMaria (NOAA/NWS/NHC), Jack Dostalek (CIRA)
TC Marcus 2018 (SH15)
2-D Winds ATMS-MiRS S-NPP
Vmax
TC Marcus 2018 (SH15)

## Slide 17: Development of a Neural Network for MiRS Radiometric Bias Correction
Why bias correction?
  To remove potential systematic bias between the measurements and the CRTM simulations.
Current bias correction (static):
  statistics of bias over oceanic and clear scenes. The bias is channel and scan position dependent. Local variations are not accounted for.
A machine learning-based bias correction: Neural Network (NN)
  NN was trained to learn the bias structure. Inputs are:
    Brightness temperature (TB) of the measurements,
    Satellite viewing angle,
    latitude,
    other geophysical parameters including cloud liquid water (CLW), total precipitable water (TPW), and Tskin.
Neural Network Schematic
True TB_bias [K] ATMS CH1
NN TB_bias [K] ATMS CH1
NN TB_bias [K] ATMS CH1
True TB_bias [K] ATMS CH1

## Slide 18: NN TB Bias Applied in MiRS
T (CLW<=0.275)
T (CLW>0.275)
WV (CLW<=0.275)
WV (CLW>0.275)

## Slide 19
Application: Blended Layer Precipitable Water
Combines MiRS WV from up to 7 Polar Satellites
for Rapid Refresh and Advection (NWP-based winds)
Gitro et al., 2018: Using the multisensor advected layered precipitable water product in the operational forecast environment. J. Operational Meteor., 6 (6), 59-73, doi: https://doi.org/10.15191/nwajom.2018.0606
To be implemented at NHC and WPC
Layer PW provides detail not present in TPW retrievals.
Courtesy of John Forsythe
Sept 2014 case of extreme precipitation over Central US

## Slide 20: Path Forward
Improvements implemented
  Snowfall rate integration for N20
  Hydrometeors (CLW over land for light rain detection)
  Snow cover/amount (vegetation correction)
  Updated sea ice climatology mask (finer temporal/spatial resolution)  Great Lakes ice detection
Planned further improvements
  Air mass-dependent bias corrections (machine learning)
  Rainy condition sounding (update a priori constraints)
  Experimenting with MiRS version adapted for tropical cyclones (MiRS-TC)
  Hydrometeors: precharacterization of precip type, improvements to CRTM i.e. scattering, particle size/shape distribution in CRTM)
  Applications/user feedback
Planned/ongoing activities
  N20/ATMS validation: Continued daily assessments (as posted to MiRS website) including comparisons with radiosondes, and other in situ data (e.g. for rain rate and land surface temperature)
  Reprocessing of NPP and N20 mission data (Spring/Summer 2020)
  Metop-C to operations (Spring 2020)
  Plan for JPSS-2 (Q1 2022), and EPS-SG A1 (Q4 2022), [SmallSats?]
  MiRS data available at CLASS, and STAR ftp (S-NPP/ATMS, NOAA-20/ATMS, GPM/GMI), CSPP_MIRS
  Software package available for download https://www.star.nesdis.noaa.gov/mirs