## Slide 1
Tim Hewison
Presentation for GSICS Working Groups’ Meeting WebEx, 2020-03-17
Procedure to tune direct inter-calibration algorithm

## Slide 2: Generic inter-calibration algorithm
Follow-up to 2019 GRWG discussion
Can we define a generic process?
  to optimise an SNO/Ray-matching inter-comparison algorithm
  define potential inter-calibration corrections?
Review
  Proposed process
  And iterations
  Proposed metrics

## Slide 3: Steps of generic SNO inter-comparison/inter-calibration
Generate the collocations
Read the collocations
Perform Spectral matching:
Estimate uncertainty on each collocation
Define metric to optimise
Filter the collocations
Compare filtered collocations
Evaluate metric (with uncertainties)
Optimise Period for Rolling window of collocations
Check for other sensitivities – e.g. scan angle & include in function
Tune threshold & filtering parameters to optimise metric
Repeat Steps 6-10 for Different Comparison methods
Define inter-calibration function?
Correct?
Notes: Generate the collocations
  Define collocation size (e.g. REF FOV)
  Degrade resolution of MON dataset
  Define crude time difference
  ...?
  Build Catalogue of MON and REF observations
  Cross-query catalogue to Filter MON and REF
Read the collocations
Perform Spectral matching:
  spectral convolution of hyperspectral
  SBAF for multispectral
  Gap-filling (e.g. for SLSTR 3.7µm)
Estimate uncertainty on each collocation
  Calculate variance of higher resolution (MON) within each REF
  Add radiometric noise (to stop it going to zero)
Define metric to optimise
  e.g. mean uncertainty on bias(es) for reference scene radiance(s)
  Based on requirements and/or capabilities
Filter the collocations by:
  Pixel location difference (x and y)
  time difference
  VZA difference
  SZA threshold (e.g. day/night)
  SAA difference (RSB only)
  RAA difference (RSB only)
  Land/Sea mask (as needed)
  Cloud/Clear mask (as needed)
  Time of Day (if needed)
Compare filter collocations
Evaluate metric (with uncertainties)
Optimise Period for Rolling window of collocations:
  How stable is the bias?
  How long is the bias stable for (within given limits)?
Tune threshold & filtering parameters to optimise metric (n.b. These steps will be iterative with all above - the order may be important!)
Repeat Steps 6-10 for Different Comparison methods - e.g.: (Need to convert results to compare uncertainties!)
  dTb v Tb
  dL v L
  By weighted linear regression
  By normal least squares regression
  By some other method - e.g. polymial fit, multiple regression with various predictors
Define inter-calibration function?
  Based on optimal method from those considered in Step 11.
Correct?
  Is a correction necessary?
  Static/Dynamic?
  Define form of correction
  Generate corrections
  Test

## Slide 4: Discussion: How to Define Metric for Optimisation?
Evaluate for validation dataset
  Covering full range of collocations (radiance, VZA, lat, time, …)
  Not just those used in the algorithm
Uncertainty on bias
  Not bias itself or rms/bias/sd
Units?
  Tb for IR/MW?
  %Reflectance for Reflected Solar Band?
  Radiance may be closer to measurements, but further from requirements – and more uniform from channel to channel
  Need to convert algorithm output into metric to compare!
Dynamic Range?
  Define metric at 1/2/3/n reference scenes? Which?
  Across full dynamic range?
  How to penalise algorithms with restricted dynamic range?

## Slide 5: SLSTR-IASI Example
Defining metric to optimise
  Define metric at 1/2/3/n reference scenes? Which?
  220K + Tb_std?
  200K + Tb_std + 300K?
  Channel-dependent!
  How to penalise algorithms with restricted dynamic range?
    Default max uncertainty if not covered?