## Slide 1: Annual GSICS Calibration Report on the State of the Observing System

## Slide 2: Background/Progress
Action from CGMS-47
Action notified in the GSICS annual meeting in March 2020
Reports reviewed and collected in the GSICS webmeeting on April 16, 2020
Reports include operational GEO imagers and reference LEO instruments
Actionee | AGN item | Action# | Description | Deadline | Status
GSICS | WGII/4 | A47.01 | GSICS to expand GSICS Report on the State of the Observing System to successively cover the calibration status of all instruments relevant GSICS. | CGMS-48 | OPEN

## Slide 3: Outline
Reports on Reference Instruments
  IASI, CrIS, AIRS
  MODIS, VIIRS
Reports on GEO versus IR
Reports on GEO versus VisNIR
Backup – Full reports as submitted

## Slide 4: IR References
IASI-A/B Double Differences using MSG-1, 3, 4 / SEVERI
IASI-A/B, CrIS and AIRS Double Differences using Himawari-8 / AHI

## Slide 5: IASI-A/B Double Differences
After IASI-A change (2019-09-30)
Warm Scenes
No significant trends
  But only 6 months
No significant differences (some statistically significant, but very small)
DD Trend= -0.044+/- 0.020 K/yr IR3.9 Delta(MetopB-A)=-0.023 +/- 0.004 K
DD Trend= -0.021+/- 0.044 K/yr IR6.2 Delta(MetopB-A)=-0.009 +/- 0.008 K
DD Trend= -0.103+/- 0.172 K/yr IR7.3 Delta(MetopB-A)=-0.017 +/- 0.020 K
DD Trend= -0.040+/- 0.027 K/yr IR8.7 Delta(MetopB-A)= 0.014 +/- 0.005 K
DD Trend= -0.038+/- 0.058 K/yr IR9.7 Delta(MetopB-A)= 0.003 +/- 0.010 K
DD Trend= 0.021+/- 0.024 K/yr IR10.8 Delta(MetopB-A)= 0.021 +/- 0.004 K
DD Trend= -0.003+/- 0.023 K/yr IR12.0 Delta(MetopB-A)= 0.021 +/- 0.004 K
DD Trend= -0.026+/- 0.034 K/yr IR13.4 Delta(MetopB-A)= 0.017 +/- 0.007 K

## Slide 6: IASI-A/B Double Differences
Before IASI-A change (2017-09-01/ 2019-09-01)
wrt Meteosat-11
Warm Scenes
No significant trends
Small, but significant differences:
~+0.03K at >9µm
<0.02K at <9µm
DD Trend= 0.004+/- 0.002 K/yr IR3.9 Delta(MetopB-A)=-0.010 +/- 0.001 K
DD Trend= 0.014+/- 0.015 K/yr IR6.2 Delta(MetopB-A)=-0.015 +/- 0.006 K
DD Trend= 0.002+/- 0.006 K/yr IR7.3 Delta(MetopB-A)=-0.003 +/- 0.004 K
DD Trend= -0.005+/- 0.006 K/yr IR8.7 Delta(MetopB-A)= 0.018 +/- 0.003 K
DD Trend= 0.004+/- 0.006 K/yr IR9.7 Delta(MetopB-A)= 0.040 +/- 0.003 K
DD Trend= -0.007+/- 0.006 K/yr IR10.8 Delta(MetopB-A)= 0.019 +/- 0.002 K
DD Trend= -0.005+/- 0.006 K/yr IR12.0 Delta(MetopB-A)= 0.023 +/- 0.002 K
DD Trend= -0.007+/- 0.007 K/yr IR13.4 Delta(MetopB-A)= 0.045 +/- 0.003 K

## Slide 7
Before IASI-B Change (2015/17):
  Warm ~-0.04K at >9µm
  Cold ~-0.1K at >9µm
After IASI-B Change (2017/19):
  Warm ~+0.03K at >9µm
  Cold ~+0.2K at >9µm
After IASI-A Change (2019/20):
  Warm: <+0.02K in all bands
  Cold: <±0.1K at >6µm
🡺 Best match now!
Chart: IASI-B-A at Standard Scene Tb (warm)
| IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Bv1-Av1 | -0.014 | -0.009 | -0.006 | -0.019 | -0.047 | -0.033 | -0.037 | -0.048
u(Bv1-Av1)
Bv2-Av1 | -0.01 | -0.015 | -0.003 | 0.018 | 0.04 | 0.019 | 0.023 | 0.045
u(Bv2-Av1)
Bv2-Av2 | -0.023 | -0.009 | -0.017 | 0.014 | 0.003 | 0.021 | 0.021 | 0.017
Chart: IASI-B-A at Tb=220K (cold)
| IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Bv1-Av1 | 0.014 | -0.006 | -0.011 | -0.179 | -0.147 | -0.111 | -0.109 | -0.103
u(Bv1-Av1)
Bv2-Av1 | 0 | -0.039 | -0.004 | 0.068 | 0.13 | 0.197 | 0.2 | 0.199
u(Bv2-Av1)
Bv2-Av2 | -0.419 | 0.031 | 0.037 | -0.078 | -0.037 | 0.058 | 0.073 | 0.075
Summary of IASI-A/B Double Differences
EUMETSAT report

## Slide 8: Double differences (with Himawari-8/AHI) of the Tb biases @std. radiance
From Reanalysis Correction for Jan. 2020
DD = Tb biases@std.radiance(Ref.sensors) - Tb biases@std.radiance(Metop-A/IASI)
 | Channel Name | BAND07 | BAND08 | BAND09 | BAND10 | BAND11 | BAND12 | BAND13 | BAND14 | BAND15 | BAND16
 | (Central Wavelength in um) | (3.9) | (6.2) | (6.9) | (7.3) | (8.6) | (9.6) | (10.4) | (11.2) | (12.4) | (13.3)
 | Std. Radiance as Tb (K) | 286.0 | 234.6 | 243.9 | 254.6 | 283.8 | 259.5 | 286.2 | 286.1 | 283.8 | 269.7
Metop-A IASI | - | - | - | - | - | - | - | - | - | - | -
Metop-B IASI | DD of the mean bias with Metop-A/IASI [K] | 0.000 | 0.007 | 0.006 | 0.009 | -0.009 | -0.011 | -0.009 | -0.012 | -0.020 | -0.020
Aqua AIRS | DD of the mean bias with Metop-A/IASI [K] | 0.110 | - | -0.082 | -0.048 | - | -0.009 | 0.017 | 0.025 | 0.034 | 0.058
S-NPP CrIS | DD of the mean bias with Metop-A/IASI [K] | - | 0.015 | -0.021 | 0.000 | - | 0.023 | -0.055 | -0.056 | -0.063 | -0.040
JMA report

## Slide 9: Visible References
NOAA-20 VIIRS versus Lunar
S-NPP and NOAA-20 VIIRS Double Differences via PICS
VIIRS DCC Time Series

## Slide 10
NASA report
N20 VIIRS versus Lunar

## Slide 11: NOAA-20 VIIRS RSB Status
Post processing check.
  VIIRS bias trends are derived relative to AQUA MODIS, since no direct SNOs exists between VIIRS.
  Double differencing the two VIIRS bias trends indicates the VIIRS radiometric consistency.
  DCC time series showed upward trends in some bands (~0.3%/year in M1 and M2), but their magnitudes are similar to uncertainty levels
  NOAA-20 VIIRS operational F-factors has been remained in the same level.
    Since 4/27/2018.
NOAA VIIRS team is closely monitoring.
NOAA report

## Slide 12: S-NPP VIIRS RSB Status
Post processing check.
  DCC trending results show very stable response from 2018 to 2020 in VISNIR bands.
  Comparing VIIRS reflectance trending over pseudo-invariant calibration sites (PICS) S-NPP VIIRS indicated stable responses.
    Bias relative to NOAA-20, S-NPP showed on the order of 2-4%
NOAA-20 / S-NPP
NOAA report

## Slide 13: IR Geostationary
CMA FY-2G/H and FY-4A/AGRI
EUMETSAT Meteosat-8, 9, 10, 11/SEVIRI
JMA Himawari-8/AHI
KMA COMS and GK2A
NOAA GOES-16, 17 ABI IR

## Slide 14
FY-2G/H IR Bands
 | IR1_11.0 (286K) | IR2_12.2 (285K) | IR3_6.9 (247K) | IR4_3.8 (285K)
Metop-A/IASI | -0.2593 | -0.7841 | -1.4897 | 1.1197
Metop-B/IASI | -0.2194 | -0.7426 | -1.4335 | 0.9641
 | IR1_11.0 (286K) | IR2_12.2 (285K) | IR3_6.9 (247K) | IR4_3.8 (285K)
Metop-A/IASI | -0.4519 | -1.0307 | -1.1022 | 2.9536
Metop-B/IASI | -0.4653 | -1.0320 | -0.9186 | 1.8630
FY-2G
FY-2H
IR1
IR2
IR3
IR4
IR1
IR2
IR3
IR4
Ref: IASI-A
Ref: IASI-A
Bias at window channels are less than 1k (FY-2G) and 1.5k (FY-2H)
FY-2G/H’s Tb bias at standard Tb show seasonal variation;
CMA report

## Slide 15
FY-4A/AGRI IR Bands
 | CH8_3.8 (286K) | CH9_6.25 (237K) | CH10_7.1 (248.5K) | CH11_8.5 (283K) | CH12_10.8 (286) | CH13_12.0 (285) | CH14_13.5 (258)
Metop-A/IASI | -3.5927 | -0.2230 | 0.6527 | 0.3048 | -0.1227 | -0.1447 | -0.2635
Metop-B/IASI | -3.5148 | -0.2223 | 0.6303 | 0.2745 | -0.1419 | -0.1776 | -0.2756
*Average bias in 2019;
CH 9
CH 10
CH 11
CH 12
CH 13
CH 14
Tb bias are less than 0.7 k (operation phase);
Scene dependent is much more better than FY-2G/H;
No strong seasonal variation;
CMA report

## Slide 16
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.59 | -0.18 | +0.35 | -0.02 | -0.12 | +0.01 | -0.02 | +0.22
Standard Deviation of Bias (K) | 0.03 | 0.09 | 0.09 | 0.05 | 0.08 | 0.04 | 0.04 | 0.07
Mean Drift Rate of Bias (K/yr) | -0.07 | -0.19 | -0.14 | -0.03 | -0.14 | -0.06 | -0.06 | -0.20
Summary Statistics of Meteosat-8/SEVIRI IR Calibration Performance in 2019
The statistics are derived from Meteosat-8/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-B/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Meteosat-8/SEVIRI IR Bands
Time series of Meteosat-8/ SEVIRI Tb biases w.r.t. Metop-B/IASI at standard radiance
Instrument Calibration Landing Page: https://www.eumetsat.int/website/home/Data/Products/Calibration/Instrumentstatusandcalibration/index.html#met8seviri
EUMETSAT report

## Slide 17
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.08 | -0.13 | +0.12 | -0.05 | -0.07 | +0.00 | -0.02 | -1.73
Standard Deviation of Bias (K) | 0.05 | 0.15 | 0.17 | 0.04 | 0.09 | 0.05 | 0.04 | 0.10
Mean Drift Rate of Bias (K/yr) | -0.07 | -0.21 | -0.10 | +0.04 | -0.10 | -0.04 | -0.02 | -0.18
Summary Statistics of Meteosat-9/SEVIRI IR Calibration Performance in 2019
The statistics are derived from Meteosat-9/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-B/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Meteosat-9 operated in Rapid Scan Service during most of this period, which increases the bias uncertainties
Erroneous data introduced in April 2019 – not dedected by quality control – should be reprocessed!
Meteosat-9/SEVIRI IR Bands
Time series of Meteosat-9/ SEVIRI Tb biases w.r.t. Metop-B/IASI at standard radiance
Instrument Calibration Landing Page: https://www.eumetsat.int/website/home/Data/Products/Calibration/Instrumentstatusandcalibration/index.html#met9seviri
EUMETSAT report

## Slide 18
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.58 | -0.23 | +0.09 | +0.03 | -0.03 | +0.03 | -0.02 | -0.86
Standard Deviation of Bias (K) | 0.03 | 0.04 | 0.06 | 0.07 | 0.09 | 0.05 | 0.04 | 0.09
Mean Drift Rate of Bias (K/yr) | +0.08 | -0.00 | -0.01 | -0.04 | -0.10 | -0.07 | -0.02 | -0.23
Summary Statistics of Meteosat-10/SEVIRI IR Calibration Performance in 2019
The statistics are derived from Meteosat-10/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-B/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Meteosat-10/SEVIRI IR Bands
Time series of Meteosat-10/ SEVIRI Tb biases w.r.t. Metop-B/IASI at standard radiance
Instrument Calibration Landing Page: https://www.eumetsat.int/website/home/Data/Products/Calibration/Instrumentstatusandcalibration/index.html#met10seviri
EUMETSAT report

## Slide 19
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.03 | -0.06 | +0.22 | +0.00 | +0.17 | +0.09 | -0.03 | -0.22
Standard Deviation of Bias (K) | 0.01 | 0.05 | 0.04 | 0.07 | 0.04 | 0.04 | 0.03 | 0.17
Mean Drift Rate of Bias (K/yr) | -0.01 | +0.11 | -0.05 | +0.01 | +0.04 | -0.01 | -0.01 | -0.58
Summary Statistics of Meteosat-11/SEVIRI IR Calibration Performance in 2019
The statistics are derived from Meteosat-11/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-B/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Decontaminations introduce calibration jumps – most obvious in the IR13.4 channel due to ice contamination
Meteosat-11/SEVIRI IR Bands
Time series of Meteosat-11/ SEVIRI Tb biases w.r.t. Metop-B/IASI at standard radiance
Instrument Calibration Landing Page: https://www.eumetsat.int/website/home/Data/Products/Calibration/Instrumentstatusandcalibration/index.html#met11seviri
EUMETSAT report

## Slide 20
Summary Statistics of COMS/MI IR Calibration Performance in 2019 (all uncertainties are k=1)
COMS IR Bands
The mean Tb bias at standard Tb is within 0.21K except for WV(6.8µm) channel as reference AIRS.
 | Channel Name (Central Wavelength in μm) | SWIR (3.8) | WV (6.8) | IR1 (10.8) | IR2 (12.0)
 | Std. Scene Tb (K) | 285.9 | 237.6 | 286.3 | 285.1
Metop-A/ IASI | Bias at Std. Scene radiance (K) | 0.17 (±0.05) | -0.02 (±0.03) | 0.20 (±0.08) | 0.08 (±0.06)
Metop-B/ IASI | Bias at Std. Scene radiance (K) | 0.21 (±0.05) | -0.04 (±0.03) | 0.13 (±0.07) | 0.02 (±0.05)
AQUA/ AIRS | Bias at Std. Scene radiance (K) | -0.07 (±0.08) | -0.31 (±0.10) | 0.11 (±0.16) | 0.14 (±0.1)
S-NPP/ CrIS | Bias at Std. Scene radiance (K) | - | -0.17 (±0.08) | 0.08 (±0.14) | 0.09 (±0.09)
KMA report

## Slide 21
Summary Statistics of GK2A/AMI IR Calibration Performance in August-December 2019 (All uncertainties are k=1)
GK2A AMI IR
 | Channel Name (Central Wavelength in μm) | BAND07 (3.8) | BAND08 (6.3) | BAND09 (6.9) | BAND10 (7.3) | BAND11 (8.7) | BAND12 (9.6) | BAND13 (10.5) | BAND14 (11.2) | BAND15 (12.3) | BAND16 (13.3)
 | Std. Scene Tb (K) | 285.9 | 234.9 | 244.1 | 254.5 | 283.7 | 259.1 | 286.1 | 286.0 | 283.8 | 269.4
Metop-A/ IASI | Bias at Std. Scene radiance (K) | 0.04 (±0.07) | -0.06 (±0.01) | -0.12 (±0.01) | 0.01 (±0.01) | 0.03 (±0.01) | -0.05 (±0.02) | 007 (±0.02) | 008 (±0.02) | 0.06 (±0.02) | 0.01 (±0.01)
Metop-B/ IASI | Bias at Std. Scene radiance (K) | 0.08 (±0.08) | 0.06 (±0.01) | -0.10 (±0.01) | 0.01 (±0.01) | 0.02 (±0.03) | -0.08 (±0.02) | 0.04 (±0.02) | 0.05 (±0.02) | 0.03 (±0.02) | -0.01 (±0.02)
AQUA/ AIRS | Bias at Std. Scene radiance (K) | - | -0.03 (±0.01) | -0.21 (±0.01) | -0.05 (±0.01) | - | -0.07 (±0.01) | 006 (±0.02) | 007 (±0.02) | 006 (±0.02) | 0.06 (±0.02)
S-NPP/ CrIS | Bias at Std. Scene radiance (K) | -0.04 (±0.04) | 0.02 (±0.02) | -0.19 (±0.02) | -0.06 (±0.02) | 0.01 (±0.01) | -0.02 (±0.02) | 0.02 (±0.01) | 0.02 (±0.01) | 0.01 (±0.01) | -0.01 (±0.01)
NOAA-20/ CrIS | Bias at Std. Scene radiance (K) | 0.01 (±0.05) | 0.04 (±0.02) | -0.13 (±0.01) | -0.01 (±0.01) | 0.09 (±0.01) | -0.01 (±0.02) | 009 (±0.03) | 0.09 (±0.03) | 0.06 (±0.03) | -0.03 (±0.01)
GK2A AMI IR channels are in general well calibrated
GK2A AMI has relatively large bias around -0.1K~-0.2K for 6.9µm (WV level)
SRF(13.3µm) updated (shifted by -0.8cm-1) on 27 Sep. 2019
KMA report

## Slide 22
Summary Statistics of Himawari-8/AHI IR Calibration Performance in Jan. 2020 (All uncertainties are k=1)
The statistics are derived from Himawari-8/AHI GSICS Re-Analysis Correction (ATBD)
Standard Radiance: typical scene defined by GSICS for easy inter-comparison of sensors’ inter-calibration biases
Himawari-8/AHI Infrared Bands
Time series of Himawari-8/AHI Tb biases w.r.t. Metop-A/IASI at std. radiance
-0.3
-0.2
-0.1
0.0
+0.1
Brightness temperature bias [K]
 | Channel Name | BAND07 | BAND08 | BAND09 | BAND10 | BAND11 | BAND12 | BAND13 | BAND14 | BAND15 | BAND16
 | (Central Wavelength in um) | (3.9) | (6.2) | (6.9) | (7.3) | (8.6) | (9.6) | (10.4) | (11.2) | (12.4) | (13.3)
 | Std. Radiance as Tb (K) | 286.0 | 234.6 | 243.9 | 254.6 | 283.8 | 259.5 | 286.2 | 286.1 | 283.8 | 269.7
Metop-A IASI | Mean Bias (K) | -0.136 | -0.182 | -0.214 | -0.116 | -0.067 | -0.281 | 0.018 | 0.028 | -0.049 | 0.073
 | Stdv. of Bias (K) | 0.003 | 0.004 | 0.004 | 0.004 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003
Metop-B IASI | Mean Bias (K) | -0.136 | -0.174 | -0.208 | -0.107 | -0.076 | -0.291 | 0.008 | 0.016 | -0.069 | 0.053
 | Stdv. of Bias (K) | 0.004 | 0.004 | 0.004 | 0.004 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003
Aqua AIRS | Mean Bias (K) | -0.026 | - | -0.296 | -0.164 | - | -0.290 | 0.034 | 0.053 | -0.015 | 0.131
 | Stdv. of Bias (K) | 0.003 | - | 0.003 | 0.003 | - | 0.002 | 0.002 | 0.002 | 0.002 | 0.002
S-NPP CrIS | Mean Bias (K) | - | -0.166 | -0.235 | -0.116 | - | -0.257 | -0.037 | -0.029 | -0.112 | 0.033
 | Stdv. of Bias (K) | - | 0.004 | 0.004 | 0.004 | - | 0.003 | 0.003 | 0.003 | 0.003 | 0.003
Available at JMA/MSC Web page: https://www.data.jma.go.jp/mscweb/data/monitoring/gsics/ir/monit_geoleoir.html
vs. Metop-A/IASI
JMA report

## Slide 23
 | Channel Name (Central Wavelength in μm) | BAND07 (3.9) | BAND08 (6.2) | BAND09 (6.9) | BAND10 (7.3) | BAND11 (8.6) | BAND12 (9.6) | BAND13 (10.4) | BAND14 (11.2) | BAND15 (12.4) | BAND16 (13.3)
 | Std. Scene Tb* | 286.0 | 234.5 | 244.0 | 254.5 | 284.0 | 259.5 | 286.0 | 286.0 | 283.5 | 269.5
Metop-A/ IASI | Bias at Std. Scene radiance (K) | -0.00 (±0.06) | -0.10 (±0.01) | -0.11 (±0.01) | -0.04 (0.01) | -0.03 (±0.02) | -0.07 (±0.01) | 0.00 (±0.03) | 0.05 (±0.03) | 0.05 (±0.03) | -0.11 (±0.03)
Metop-B/ IASI | Bias at Std. Scene radiance (K) | 0.01 (±0.05) | -0.09 (±0.01) | -0.10 (±0.01) | -0.04 (±0.01) | -0.03 (±0.02) | -0.08 (±0.01) | -0.03 (±0.02) | 0.03 (±0.03) | 0.02 (±0.03) | -0.14 (±0.03)
Metop-C/ IASI | Bias at Std. Scene radiance (K) | 0.01 (±0.06) | -0.09 (±0.01) | -0.10 (±0.01) | -0.05 (±0.01) | -0.03 (±0.02) | -0.05 (±0.02) | -0.02 (±0.03) | 0.03 (±0.03) | 0.03 (±0.03) | -0.13 (±0.03)
S-NPP/ CrIS | Bias at Std. Scene radiance (K) | - | - | -0.11 (±0.01) | -0.05 (±0.01) | - | -0.02 (±0.01) | -0.04 (±0.02) | 0.00 (±0.02) | -0.01 (±0.02) | -0.13 (±0.02)
NOAA-20/ CrIS | Bias at Std. Scene radiance (K) | - | - | -0.09 (±0.00) | -0.04 (±0.01) | - | -0.02 (±0.01) | -0.01 (±0.01) | 0.06 (±0.02) | 0.04 (±0.02) | -0.10 (±0.02)
Summary Statistics of GOES-16/ABI IR Calibration Performance in December 2019 (all uncertainties are k=1)
GOES-16 ABI IR Bands
Either table/figure can be used.
G16 ABI IR bands are well-calibrated. The mean Tb bias at standard radiance/Tb is within 0.15K for all bands.
NOAA report
ABI GS update

## Slide 24
Summary Statistics of GOES-17/ABI IR Calibration Performance in Dec. 2019 at Gainset I Period (All uncertainties are k=1)
GOES-17 ABI IR Bands
 | Channel Name (Central Wavelength in μm) | BAND07 (3.9) | BAND08 (6.2) | BAND09 (6.9) | BAND10 (7.3) | BAND11 (8.6) | BAND12 (9.6) | BAND13 (10.4) | BAND14 (11.2) | BAND15 (12.4) | BAND16 (13.3)
 | Std. Scene Tb (K) | 286.0 | 234.5 | 244.0 | 254.5 | 284.0 | 259.5 | 286.0 | 286.0 | 283.5 | 269.5
Metop-A/ IASI | Bias at Std. Scene radiance (K) | 0.01 (±0.09) | -0.02 (±0.01) | 0.13 (±0.01) | 0.09 (±0.01) | 0.07 (±0.03) | -0.05 (±0.02) | 0.02 (±0.03) | 0.02 (±0.03) | 0.13 (±0.03) | 0.43 (±0.03)
Metop-B/ IASI | Bias at Std. Scene radiance (K) | 0.01 (±0.08) | -0.01 (±0.01) | 0.13 (±0.01) | 0.09 (±0.01) | 0.05 (±0.02) | -0.06 (±0.02) | -0.01 (±0.03) | -0.01 (±0.03) | 0.11 (±0.03) | 0.41 (±0.03)
Metop-C/ IASI | Bias at Std. Scene radiance (K) | 0.01 (±0.08) | -0.01 (±0.01) | 0.13 (±0.01) | 0.09 (±0.01) | 0.05 (±0.02) | -0.06 (±0.02) | -0.01 (±0.03) | -0.01 (±0.03) | 0.11 (±0.03) | 0.41 (±0.03)
S-NPP/ CrIS | Bias at Std. Scene radiance (K) | - | - | 0.14 (±0.03) | 0.08 (±0.04) | - | -0.03 (±0.04) | -0.04 (±0.08) | -0.08 (±0.09) | 0.05 (±0.10) | 0.46 (±0.11)
NOAA-20/ CrIS | Bias at Std. Scene radiance (K) | - | - | 0.16 (±0.03) | 0.09 (±0.03) | - | -0.02 (±0.05) | -0.02 (±0.08) | -0.04 (±0.09) | 0.08 (±0.10) | 0.48 (±0.10)
G17 ABI is in general well calibrated at the gain-set I period when the focal plane module (FPM) temperature is stable.
G17 B16 has relatively large bias at 0.4-0.5K
LWIR FPM Temperature
Gainset I
NOAA report

## Slide 25: VNIR Geostationary
CMA FY-2 & FY-4A
EUMETSAT MSG SEVIRI
KMA GK2A AMI
JMA Himawari-8/AHI
NOAA GOES-16/17 ABI

## Slide 26
FY-4A AGRI RSB
Monitoring and calibration updates using stable target
band | Wavelength (um) | Total attenuation rate(%) | Annual attenuation rate(%)
1 | 0.47 | 40.3 | 14.36
2 | 0.65 | 6.62 | 2.36
3 | 0.82 | -8.56 | -3.05
5 | 1.61 | 6.53 | 2.33
6 | 2.85 | 9.62 | 3.43
Operational Ref bias variation in 2 years;
Normalized response trend using Multi method;
Reflection of Ch1 at DCC and Multi station are consistent;
CMA report

## Slide 27: DCC monitored reflectance of operational VS recalibrated
DCC reflectance (operational)
DCC reflectance (recalibrated)
15% fluctuation in Operational calibration results
Fluctuation was greatly decreased in recalibrated results
CMA report

## Slide 28
Channel Name |  | VIS0.6 | VIS0.8 | NIR1.6 | HRV | Units
Meteosat-8 | Mean Bias (DCC-SSCC) | +14.0 ± 2.3 |  |  |  | %
 | Annual Drift (DCC) | -0.61 ± 0.04 |  |  |  | %/yr
 | Annual Drift (SSCC) | -0.55 ± 0.03 | -0.56 ± 0.03 | -0.05 ± 0.03 | -0.53 ± 0.03 | %/yr
 | Annual Drift (LCS) | -0.58 ± 0.01 | -0.55 ± 0.01 | -0.04 ± 0.02 | -0.55 ± 0.02 | %/yr
Meteosat-9 | Annual Drift (SSCC) | -0.54 ± 0.08 | -0.58 ± 0.07 | -0.05 ± 0.06 | -0.56 ± 0.07 | %/yr
 | Annual Drift (LCS) | -0.57 ± 0.01 | -0.51 ± 0.01 | -0.01 ± 0.02 | -0.53 ± 0.02 | %/yr
Meteosat-10 | Annual Drift (SSCC) | -0.61 ± 0.11 | -0.63 ± 0.10 | -0.04 ± 0.09 | -0.67 ± 0.10 | %/yr
 | Annual Drift (LCS) | -0.80 ± 0.02 | -0.72 ± 0.02 | -0.05 ± 0.07 | -0.89 ± 0.08 | %/yr
Meteosat-11 | Mean Bias (DCC-SSCC) | +10.47 ± 1.6 |  |  |  | %
 | Annual Drift (DCC) | -0.43 ± 0.03 |  |  |  | %/yr
 | Annual Drift (SSCC) | -0.23 ± 0.28 | -0.32 ± 0.27 | -0.11 ± 0.26 | -0.39 ± 0.26 | %/yr
 | Annual Drift (LCS) | -0.57 ± 0.14 | -0.40 ± 0.13 | -0.21 ± 0.45 | -0.46 ± 0.36 | %/yr
Summary Statistics of Meteosat/SEVIRI VIS/NIR Calibration Performance (All Uncertainties are k=1)
Meteosat/SEVIRI Visible Bands 2019
EUMETSAT report

## Slide 29
Mean Bias: Mean and SD of difference of DCC from operational (SSCC) calibration for all 2019 pentad results
Annual Drift: Mean gain drift and uncertainty calculated from DCC and operational (SSCC) over each satellite life
DCC: Demonstration GSICS Deep Convective Cloud inter-calibration, with respect to Aqua/MODIS
SSCC: SEVIRI Solar Channel Calibration System = vicarious calibration used operationally for SEVIRI
Meteosat/SEVIRI Visible Bands - 2019
Time Series of gains derived for Meteosat-8 (MSG1) and -11 (MSG4) VIS0.6 channel SSCC (red), DCC (green).
EUMETSAT report

## Slide 30
Summary Statistics of Himawari-8/AHI VNIR Calibration Performance (All Uncertainties are k=1)
Mean Bias: monthly average and standard deviation of the daily results in January 2020
Annual Drift: calculated using Mean Bias from July 2015 to February 2020
Ray-matching: Spectral Band Adjustment Factors on NASA Langley website compensates Spectral diff. (ATBD)
Vicarious calibration uses optical parameters retrieved from Aqua/MODIS C6 L1B (Reference)
Himawari-8/AHI VIS/NIR Bands
BAND03 (0.64 μm)
BAND05 (1.6 μm)
Trend of the ratio of observation to reference computed using Ray-matching / Vicarious calibration approaches
BAND01 (0.47 μm)
Band name (central wavelength in mm) |  | Band 01 (0.47) |  |  | Band 02 (0.51) |  |  | Band 03 (0.64) |  |  | Band 04 (0.86) |  |  | Band 05 (1.6) |  |  | Band 06 (2.3) |  |  | Units
Ray-matching w/ SNPP/VIIRS | Mean bias | -2.6 | ± | 0.8 | +0.5 | ± | 1.0 | +0.4 | ± | 0.8 | -0.6 | ± | 0.7 | +5.6 | ± | 1.5 | -5.5 | ± | 1.0 | %
 | Annual drift | -0.34 | ± | 0.04 | -0.48 | ± | 0.04 | -0.76 | ± | 0.04 | -0.59 | ± | 0.04 | -0.25 | ± | 0.06 | -0.23 | ± | 0.05 | %/yr
Vicarious cal. using Aqua/MODIS + RTM | Mean bias | -2.7 | ± | 1.6 | -3.6 | ± | 1.5 | -0.9 | ± | 1.5 | +0.5 | ± | 1.3 | +3.7 | ± | 0.9 | -5.0 | ± | 0.8 | %
 | Annual drift | -0.52 | ± | 0.05 | -0.64 | ± | 0.05 | -0.88 | ± | 0.06 | -0.74 | ± | 0.05 | -0.21 | ± | 0.06 | -0.18 | ± | 0.07 | %/yr
Available at JMA/MSC Web page: https://www.data.jma.go.jp/mscweb/data/monitoring/gsics/vis/monit_visvical.html
JMA report

## Slide 31: GK2A AMI VNIR Bands
GEO | Reference Instr. | B01 (0.47 μm) | B02 (0.51 μm) | B03 (0.64 μm) | B04 (0.86 μm) | B05 (1.37 μm) | B06 (1.61 μm)
GK2A AMI | Terra/MODIS | -1.08(±1.27) | -1.55(±2.27) | 3.06(±1.08) | 8.87(±2.18) | 6.45(±0.95) | 4.87(±0.97)
 | SNPP/VIIRS | -3.87(±1.71) | 3.14(±1.49) | 2.41(±1.41) | 1.53(±1.62) | -0.78(±0.69) | 6.88(±1.49)
The mean calibration difference between GK2A AMI and Terra/MODIS, SNPP/VIIRS from Oct. 1, 2019 – Dec. 31, 2019 (unit: %, all uncertainties k=1)
We are testing ray matching method using SNPP/VIIRS.
All the AMI Visible and Near-Infrared (VNIR) channels has very high bias and uncertainty.
That caused by seasonal variation.
We have to keep watching since over 1 year operations.
VIIRS
MODIS
AMI vs MODIS
AMI vs VIIRS
KMA report

## Slide 32: G16/17 ABI VNIR Bands
GEO | Reference Instr. | B01 (0.47um) | B02 (0.64um) | B03 (0.86um) | B04 (1.37um) | B05 (1.6um) | B06 (2.2um)
G16 | SNPP/VIIRS | 5.62(±2.44) | -0.46(±3.12) | 0.16(±3.10) | -2.16(±2.41) | 2.28(±3.06) | -1.70(±1.71)
G17 | SNPP/VIIRS | 1.52(±3.24) | 0.99(±4.45) | 0.00(±3.60) | -1.17(±7.97) | -0.97(±3.36) | -2.61(±2.86)
The mean calibration difference between G16/17 ABI and SNPP/VIIRS from Oct. 1, 2019 – Nov. 30, 2019 (unit: %, all uncertainties k=1)
All the ABI Visible and Infrared (VNIR) channels, except for G16 B01, are within 5% difference to SNPP/VIIRS from 10/01/2019-11/30/2019
  G16 B01 is brighter than SNPP/VIIRS by 5.6%
Slight scene radiance/reflectance dependent bias can be observed at some VNIR bands
  Uncertainty in SRF correction may contribute
G16/17 VNIR calibration is in general very stable since their operations, apart from the B02 LUT updates in April 2019. Long-term monitoring is available:
https://www.star.nesdis.noaa.gov/GOESCal/G16_ABI_VNIR_InterCal_static.php
https://www.star.nesdis.noaa.gov/GOESCal/G17_ABI_VNIR_InterCal_static.php
NOAA report

## Slide 33: Backup: Full Reports
Complete Record of Instrument Reports
  CMA Calibration Report – GEO
  EUMETSAT Annual GSICS Calibration Report
  IMD Agency Report
  JMA Calibration Report
  KMA Calibration Report – GEO
  NASA NOAA-20 VIIRS Calibration Report (as PDF)
  NOAA Calibration Reports GEO, CrIS, VIIRS

## Slide 34: 2020 Annual GSICS Calibration Report - GEO
Chengli Qi
Na Xu, Xiuqing Hu, Hanlie Xu,
Qiang Guo, Boyang Chen, Lin Sun
National Satellite Meteorological Center(NSMC), CMA
2020 GSICS Webmeeting,
16, Apr, 2020

## Slide 35: 2019 Geo Calibration work in CMA
Major satellite/Instrument events of FY-2 & FY-4 relevant to calibration and the impact on the radiance quality
FY-4/GIIRS status updates in 2019 and performance of V3 L1 data.
Radiometric calibration performance for FY-2 & FY-4 Imagers using GSICS inter-calibration/inter-comparison
  Table/Figure summarizing bias/unc: average of last one year or typical time period
  Time series chart of bias/unc: since operation start or last one year
  Scene Dependent Bias: Scatterplot of scene dependent bias

## Slide 36: FY-2 Calibration Events in 2019
http://planet.rssi.ru
FengYun satellite operation information and announcements:
http://www.nsmc.org.cn/en/NSMC/Channels/100029.html
Satellite (status) |  | Current Location | Launch Date | Operation Date
FY-2E | (11, Jan 2019 disengaged) |  | 23, Dec 2008 | Feb 2009
FY-2F | （Op） | 112°E | 13, Jan 2012 | 
FY-2G | （Op） | 105°E | 31, Dec 2014 | 1, Jul 2015
FY-2H | （Op） | 79°E | 5, Jun 2018 | 11, Jan 2019
Major Calibration Related Events | FY-2F | FY-2G | FY-2H
New calibration algorithm (source free) implementation | January, 2020 | January, 2019 | 

## Slide 37: FY-4 Calibration Events in 2019
http://planet.rssi.ru
Satellite (status) |  | Current Location | Launch Date | Operation Date
FY-4A | (Op) | E104.7 | 2016-12-11 | 
Major Calibration Related Events | FY-4A/AGRI
Improvement of De-stripping algorithm | 08/11/2019
reflective solar bands (RSB) calibration correction coefficients updates | 09/25/2019

## Slide 38
FY-2G/H IR Rad. Calibration Performance (2019)
 | IR1_11.0 (286K) | IR2_12.2 (285K) | IR3_6.9 (247K) | IR4_3.8 (285K)
Metop-A/IASI | -0.2593 | -0.7841 | -1.4897 | 1.1197
Metop-B/IASI | -0.2194 | -0.7426 | -1.4335 | 0.9641
 | IR1_11.0 (286K) | IR2_12.2 (285K) | IR3_6.9 (247K) | IR4_3.8 (285K)
Metop-A/IASI | -0.4519 | -1.0307 | -1.1022 | 2.9536
Metop-B/IASI | -0.4653 | -1.0320 | -0.9186 | 1.8630
FY-2G
FY-2H
IR1
IR2
IR3
IR4
IR1
IR2
IR3
IR4
Ref: IASI-A
Ref: IASI-A
Bias at window channels are less than 1k (FY-2G) and 1.5k (FY-2H)
FY-2G/H’s Tb bias at standard Tb show seasonal variation;

## Slide 39
FY-4A/AGRI IR Rad. Calibration Performance
 | CH8_3.8 (286K) | CH9_6.25 (237K) | CH10_7.1 (248.5K) | CH11_8.5 (283K) | CH12_10.8 (286) | CH13_12.0 (285) | CH14_13.5 (258)
Metop-A/IASI | -3.5927 | -0.2230 | 0.6527 | 0.3048 | -0.1227 | -0.1447 | -0.2635
Metop-B/IASI | -3.5148 | -0.2223 | 0.6303 | 0.2745 | -0.1419 | -0.1776 | -0.2756
*Average bias in 2019;
CH 9
CH 10
CH 11
CH 12
CH 13
CH 14
Tb bias are less than 0.7 k (operation phase);
Scene dependent is much more better than FY-2G/H;
No strong seasonal variation;

## Slide 40: Improvement of radiance consistency in different detectors
Wave Length (um) | Sensitivity | Stripe Noise
3.5L | 0.1K | 
5.8 | 0.09K | Visiable in image
6.9 | 0.12K | 
8.0 | 0.06K | Visialbe in products
10.3 | 0.07K | 
11.5 | 0.14K | 
13.2 | 0.6K | Visiable in image
Stripping in absorption channels are more obvious, main contribution from inconsistent SRFs.
The maximum equivalent noise can reach 2K, improved algorithm of adaptive wavelet filter has been preliminarily developed.
The requirement of quantification is getting higher, systematic design needs to be strengthened and the image quality needs to be improved continuously
13.2-13.8um

## Slide 41: Improvement of radiance consistency in different detectors
SST
Cloud Mask
Before de-stripping
After de-stripping

## Slide 42
FY-4A AGRI RSB
Monitoring and calibration updates using stable target
band | Wavelength (um) | Total attenuation rate(%) | Annual attenuation rate(%)
1 | 0.47 | 40.3 | 14.36
2 | 0.65 | 6.62 | 2.36
3 | 0.82 | -8.56 | -3.05
5 | 1.61 | 6.53 | 2.33
6 | 2.85 | 9.62 | 3.43
Operational Ref bias variation in 2 years;
Normalized response trend using Multi method;
Reflection of Ch1 at DCC and Multi station are consistent;

## Slide 43: DCC monitored reflectance of operational VS recalibrated
DCC reflectance (operational)
DCC reflectance (recalibrated)
15% fluctuation in Operational calibration results
Fluctuation was greatly decreased in recalibrated results

## Slide 44: Milestones of FY-4/GIIRS L1 Data (Operation, Distribution and Application)
2016.12~2017.10: Commissioning and Preliminary Validation
2017.11~2018.04: User Readiness (i.e. observation mode optimization, training)
2018.05~2018.11: Experimental Application (i.e. NWP and retrieval)
2018.12: Operational Application in GRAPES (direct radiation assimilation)
2019.01: V1 Data Distribution to International Users;
2019.08: V2 Data in Operation(QC，ZPD alignment)
2019.10: V2+ available (spectral coding error corrected)
2019.11.07: V3 Data in Operation (diurnal BT biases variation corrected)

## Slide 45
Key Improvements of GIIIRS L1 Data in V3
Abnormal Observations (bad graduals) Correction
Spectral Optimization
  Off-axis effects correction (for 32×4 detector array)
  Accurate spectral shift correction
Radiometric Optimization
  ZPD-aligning improvement
  New calibration model for diurnal-varying on GEO platform
Processing Efficiency Optimization
  Fast DFT for GIIRS utilization (increased by 8~10 times)
Optional Apodization upon L1 Data
  0813~0828: Hamming Apodization
  0829~ : Unapodized

## Slide 46
Bad granules occurred in V1 has been overcome completely: 11/350≈3%
V2/V3 V1

## Slide 47: FY4A/GIIRS spectral and radiometric asessment
ECMWF Assessments of V3 Radiance (O-B): channel7 (~100hPa)
V1
V3
Less than 1K for most channels in LW band
SSEC/UW Assessments of V3 Spectral Shifts
< 5ppm
< 10ppm

## Slide 48: Future work
Add GSICS monitoring of FY-4/GIIRS using GSICS inter-calibration/inter-comparison
  Bias at reference temperature
  Uncertainty of Tb bias at reference temperature
FY-4A/AGRI IR gsics correction products development
FY-4A/AGRI reflective solar bands (RSB) calibration monitoring.

## Slide 49: 2019 Annual GSICS Calibration Report for EUMETSAT
Tim Hewison, Sebastien Wagner
EUMETSAT

## Slide 50: Satellite/Instrument Summary - GEO
Satellite (status) |  | Location | Launch date | EO instruments |  |  | 
Meteosat-8 | Op | 41.5 E | 2002-08-28 | SEVIRI | GERB |  | 
Meteosat-9 | B | 3.5 E | 2005-12-21 | SEVIRI | GERB |  | 
Meteosat-10 | RSS | 9.5 E | 2012-07-05 | SEVIRI | GERB |  | 
Meteosat-11 | Op | 0.0 E | 2015-07-15 | SEVIRI | GERB |  | 
Major calibration relevant events in 2019
  2019-01-21/28 Meteosat-11 Decontamination
  EUMETSAT User Notification Service
Hyperlinks on instrument names navigate to the Calibration Landing Page
Satellite Status |  | 
 | Op = Operational | 
 | P = Pre-operational | 
 | B = Back-up, secondary | 
 | L = Limited availability | 
Instrument Status |  | 
 |  | Operational (or capable of)
 |  | Operational with limitations (or Standby)
 |  | Operational with Degraded Performance
 |  | Not Operational
 |  | Functional, Turned Off

## Slide 51
Channel Name |  | VIS0.6 | VIS0.8 | NIR1.6 | HRV | Units
Meteosat-8 | Mean Bias (DCC-SSCC) | +14.0 ± 2.3 |  |  |  | %
 | Annual Drift (DCC) | -0.61 ± 0.04 |  |  |  | %/yr
 | Annual Drift (SSCC) | -0.55 ± 0.03 | -0.56 ± 0.03 | -0.05 ± 0.03 | -0.53 ± 0.03 | %/yr
 | Annual Drift (LCS) | -0.58 ± 0.01 | -0.55 ± 0.01 | -0.04 ± 0.02 | -0.55 ± 0.02 | %/yr
Meteosat-9 | Annual Drift (SSCC) | -0.54 ± 0.08 | -0.58 ± 0.07 | -0.05 ± 0.06 | -0.56 ± 0.07 | %/yr
 | Annual Drift (LCS) | -0.57 ± 0.01 | -0.51 ± 0.01 | -0.01 ± 0.02 | -0.53 ± 0.02 | %/yr
Meteosat-10 | Annual Drift (SSCC) | -0.61 ± 0.11 | -0.63 ± 0.10 | -0.04 ± 0.09 | -0.67 ± 0.10 | %/yr
 | Annual Drift (LCS) | -0.80 ± 0.02 | -0.72 ± 0.02 | -0.05 ± 0.07 | -0.89 ± 0.08 | %/yr
Meteosat-11 | Mean Bias (DCC-SSCC) | +10.47 ± 1.6 |  |  |  | %
 | Annual Drift (DCC) | -0.43 ± 0.03 |  |  |  | %/yr
 | Annual Drift (SSCC) | -0.23 ± 0.28 | -0.32 ± 0.27 | -0.11 ± 0.26 | -0.39 ± 0.26 | %/yr
 | Annual Drift (LCS) | -0.57 ± 0.14 | -0.40 ± 0.13 | -0.21 ± 0.45 | -0.46 ± 0.36 | %/yr
Summary Statistics of Meteosat/SEVIRI VIS/NIR Calibration Performance (All Uncertainties are k=1)
Calibration Performance: Meteosat/SEVIRI Visible Bands 2019

## Slide 52
Mean Bias: Mean and SD of difference of DCC from operational (SSCC) calibration for all 2019 pentad results
Annual Drift: Mean gain drift and uncertainty calculated from DCC and operational (SSCC) over each satellite life
DCC: Demonstration GSICS Deep Convective Cloud inter-calibration, with respect to Aqua/MODIS
SSCC: SEVIRI Solar Channel Calibration System = vicarious calibration used operationally for SEVIRI
Calibration Performance: Meteosat/SEVIRI Visible Bands - 2019
Time Series of gains derived for Meteosat-8 (MSG1) and -11 (MSG4) VIS0.6 channel SSCC (red), DCC (green).

## Slide 53
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.59 | -0.18 | +0.35 | -0.02 | -0.12 | +0.01 | -0.02 | +0.22
Standard Deviation of Bias (K) | 0.03 | 0.09 | 0.09 | 0.05 | 0.08 | 0.04 | 0.04 | 0.07
Mean Drift Rate of Bias (K/yr) | -0.07 | -0.19 | -0.14 | -0.03 | -0.14 | -0.06 | -0.06 | -0.20
Summary Statistics of Meteosat-8/SEVIRI IR Calibration Performance in 2019
The statistics are derived from Meteosat-8/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-B/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Calibration Performance: Meteosat-8/SEVIRI IR Bands
Time series of Meteosat-8/ SEVIRI Tb biases w.r.t. Metop-B/IASI at standard radiance
Instrument Calibration Landing Page: https://www.eumetsat.int/website/home/Data/Products/Calibration/Instrumentstatusandcalibration/index.html#met8seviri

## Slide 54
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.08 | -0.13 | +0.12 | -0.05 | -0.07 | +0.00 | -0.02 | -1.73
Standard Deviation of Bias (K) | 0.05 | 0.15 | 0.17 | 0.04 | 0.09 | 0.05 | 0.04 | 0.10
Mean Drift Rate of Bias (K/yr) | -0.07 | -0.21 | -0.10 | +0.04 | -0.10 | -0.04 | -0.02 | -0.18
Summary Statistics of Meteosat-9/SEVIRI IR Calibration Performance in 2019
The statistics are derived from Meteosat-9/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-B/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Meteosat-9 operated in Rapid Scan Service during most of this period, which increases the bias uncertainties
Erroneous data introduced in April 2019 – not dedected by quality control – should be reprocessed!
Calibration Performance: Meteosat-9/SEVIRI IR Bands
Time series of Meteosat-9/ SEVIRI Tb biases w.r.t. Metop-B/IASI at standard radiance
Instrument Calibration Landing Page: https://www.eumetsat.int/website/home/Data/Products/Calibration/Instrumentstatusandcalibration/index.html#met9seviri

## Slide 55
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.58 | -0.23 | +0.09 | +0.03 | -0.03 | +0.03 | -0.02 | -0.86
Standard Deviation of Bias (K) | 0.03 | 0.04 | 0.06 | 0.07 | 0.09 | 0.05 | 0.04 | 0.09
Mean Drift Rate of Bias (K/yr) | +0.08 | -0.00 | -0.01 | -0.04 | -0.10 | -0.07 | -0.02 | -0.23
Summary Statistics of Meteosat-10/SEVIRI IR Calibration Performance in 2019
The statistics are derived from Meteosat-10/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-B/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Calibration Performance: Meteosat-10/SEVIRI IR Bands
Time series of Meteosat-10/ SEVIRI Tb biases w.r.t. Metop-B/IASI at standard radiance
Instrument Calibration Landing Page: https://www.eumetsat.int/website/home/Data/Products/Calibration/Instrumentstatusandcalibration/index.html#met10seviri

## Slide 56
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.03 | -0.06 | +0.22 | +0.00 | +0.17 | +0.09 | -0.03 | -0.22
Standard Deviation of Bias (K) | 0.01 | 0.05 | 0.04 | 0.07 | 0.04 | 0.04 | 0.03 | 0.17
Mean Drift Rate of Bias (K/yr) | -0.01 | +0.11 | -0.05 | +0.01 | +0.04 | -0.01 | -0.01 | -0.58
Summary Statistics of Meteosat-11/SEVIRI IR Calibration Performance in 2019
The statistics are derived from Meteosat-11/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-B/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Decontaminations introduce calibration jumps – most obvious in the IR13.4 channel due to ice contamination
Calibration Performance: Meteosat-11/SEVIRI IR Bands
Time series of Meteosat-11/ SEVIRI Tb biases w.r.t. Metop-B/IASI at standard radiance
Instrument Calibration Landing Page: https://www.eumetsat.int/website/home/Data/Products/Calibration/Instrumentstatusandcalibration/index.html#met11seviri

## Slide 57: IASI-A/B Double Differences
After IASI-A change (2019-09-30)
Warm Scenes
No significant trends
  But only 6 months
No significant differences (some statistically significant, but very small)
DD Trend= -0.044+/- 0.020 K/yr IR3.9 Delta(MetopB-A)=-0.023 +/- 0.004 K
DD Trend= -0.021+/- 0.044 K/yr IR6.2 Delta(MetopB-A)=-0.009 +/- 0.008 K
DD Trend= -0.103+/- 0.172 K/yr IR7.3 Delta(MetopB-A)=-0.017 +/- 0.020 K
DD Trend= -0.040+/- 0.027 K/yr IR8.7 Delta(MetopB-A)= 0.014 +/- 0.005 K
DD Trend= -0.038+/- 0.058 K/yr IR9.7 Delta(MetopB-A)= 0.003 +/- 0.010 K
DD Trend= 0.021+/- 0.024 K/yr IR10.8 Delta(MetopB-A)= 0.021 +/- 0.004 K
DD Trend= -0.003+/- 0.023 K/yr IR12.0 Delta(MetopB-A)= 0.021 +/- 0.004 K
DD Trend= -0.026+/- 0.034 K/yr IR13.4 Delta(MetopB-A)= 0.017 +/- 0.007 K

## Slide 58: IASI-A/B Double Differences
After IASI-A change (2019-09-30)
Cold Scenes
No significant trends
  But only 6 months
No significant differences
DD Trend= -1.003+/- 2.550 K/yr IR3.9 Delta(MetopB-A)=-0.419 +/- 0.285 K
DD Trend= -0.177+/- 0.212 K/yr IR6.2 Delta(MetopB-A)= 0.031 +/- 0.035 K
DD Trend= -0.686+/- 0.868 K/yr IR7.3 Delta(MetopB-A)= 0.037 +/- 0.112 K
DD Trend= -0.336+/- 0.389 K/yr IR8.7 Delta(MetopB-A)=-0.078 +/- 0.055 K
DD Trend= -0.222+/- 0.292 K/yr IR9.7 Delta(MetopB-A)=-0.037 +/- 0.041 K
DD Trend= -0.270+/- 0.433 K/yr IR10.8 Delta(MetopB-A)= 0.058 +/- 0.054 K
DD Trend= -0.319+/- 0.463 K/yr IR12.0 Delta(MetopB-A)= 0.073 +/- 0.055 K
DD Trend= -0.129+/- 0.253 K/yr IR13.4 Delta(MetopB-A)= 0.075 +/- 0.037 K

## Slide 59: IASI-A/B Double Differences
Before IASI-A change (2017-09-01/ 2019-09-01)
wrt Meteosat-11
Warm Scenes
No significant trends
Small, but significant differences:
~+0.03K at >9µm
<0.02K at <9µm
DD Trend= 0.004+/- 0.002 K/yr IR3.9 Delta(MetopB-A)=-0.010 +/- 0.001 K
DD Trend= 0.014+/- 0.015 K/yr IR6.2 Delta(MetopB-A)=-0.015 +/- 0.006 K
DD Trend= 0.002+/- 0.006 K/yr IR7.3 Delta(MetopB-A)=-0.003 +/- 0.004 K
DD Trend= -0.005+/- 0.006 K/yr IR8.7 Delta(MetopB-A)= 0.018 +/- 0.003 K
DD Trend= 0.004+/- 0.006 K/yr IR9.7 Delta(MetopB-A)= 0.040 +/- 0.003 K
DD Trend= -0.007+/- 0.006 K/yr IR10.8 Delta(MetopB-A)= 0.019 +/- 0.002 K
DD Trend= -0.005+/- 0.006 K/yr IR12.0 Delta(MetopB-A)= 0.023 +/- 0.002 K
DD Trend= -0.007+/- 0.007 K/yr IR13.4 Delta(MetopB-A)= 0.045 +/- 0.003 K

## Slide 60: IASI-A/B Double Differences
Before IASI-A change (2017-09-01/ 2019-09-01)
wrt Meteosat-11
Cold Scenes
No significant trends
Small, but significant differences:
~+0.2K at >9µm
DD Trend= 0.305+/- 0.131 K/yr IR3.9 Delta(MetopB-A)=-0.000 +/- 0.068 K
DD Trend= 0.040+/- 0.070 K/yr IR6.2 Delta(MetopB-A)=-0.039 +/- 0.027 K
DD Trend= -0.009+/- 0.040 K/yr IR7.3 Delta(MetopB-A)=-0.004 +/- 0.025 K
DD Trend= -0.060+/- 0.074 K/yr IR8.7 Delta(MetopB-A)= 0.068 +/- 0.039 K
DD Trend= 0.011+/- 0.024 K/yr IR9.7 Delta(MetopB-A)= 0.130 +/- 0.017 K
DD Trend= -0.059+/- 0.052 K/yr IR10.8 Delta(MetopB-A)= 0.197 +/- 0.025 K
DD Trend= -0.060+/- 0.065 K/yr IR12.0 Delta(MetopB-A)= 0.200 +/- 0.027 K
DD Trend= -0.064+/- 0.047 K/yr IR13.4 Delta(MetopB-A)= 0.199 +/- 0.023 K

## Slide 61: IASI-A/B Double Differences
Before IASI-B change (2015-04-02/ 2019-09-02)
wrt Meteosat-10
Warm Scenes
No significant trends
Small, but significant differences:
~-0.04K at >9µm
<-0.02K at <9µm
DD Trend= 0.005+/- 0.002 K/yr IR3.9 Delta(MetopB-A)=-0.014 +/- 0.001 K
DD Trend= -0.002+/- 0.004 K/yr IR6.2 Delta(MetopB-A)=-0.009 +/- 0.002 K
DD Trend= -0.002+/- 0.003 K/yr IR7.3 Delta(MetopB-A)=-0.006 +/- 0.002 K
DD Trend= 0.000+/- 0.002 K/yr IR8.7 Delta(MetopB-A)=-0.019 +/- 0.002 K
DD Trend= -0.002+/- 0.004 K/yr IR9.7 Delta(MetopB-A)=-0.047 +/- 0.002 K
DD Trend= -0.001+/- 0.002 K/yr IR10.8 Delta(MetopB-A)=-0.033 +/- 0.002 K
DD Trend= 0.002+/- 0.003 K/yr IR12.0 Delta(MetopB-A)=-0.037 +/- 0.002 K
DD Trend= 0.011+/- 0.005 K/yr IR13.4 Delta(MetopB-A)=-0.048 +/- 0.002 K

## Slide 62: IASI-A/B Double Differences
Before IASI-B change (2015-04-02/ 2019-09-02)
wrt Meteosat-10
Cold Scenes
No significant trends
Small, but significant differences:
~-0.1K at >8µm
DD Trend= 0.030+/- 0.083 K/yr IR3.9 Delta(MetopB-A)= 0.014 +/- 0.063 K
DD Trend= -0.002+/- 0.010 K/yr IR6.2 Delta(MetopB-A)=-0.006 +/- 0.006 K
DD Trend= 0.003+/- 0.028 K/yr IR7.3 Delta(MetopB-A)=-0.011 +/- 0.018 K
DD Trend= 0.026+/- 0.046 K/yr IR8.7 Delta(MetopB-A)=-0.179 +/- 0.030 K
DD Trend= 0.023+/- 0.026 K/yr IR9.7 Delta(MetopB-A)=-0.147 +/- 0.015 K
DD Trend= 0.002+/- 0.031 K/yr IR10.8 Delta(MetopB-A)=-0.111 +/- 0.020 K
DD Trend= 0.014+/- 0.036 K/yr IR12.0 Delta(MetopB-A)=-0.109 +/- 0.020 K
DD Trend= -0.000+/- 0.034 K/yr IR13.4 Delta(MetopB-A)=-0.103 +/- 0.020 K

## Slide 63: Summary of IASI-A/B Double Differences
Before IASI-B Change (2015/17):
  Warm ~-0.04K at >9µm
  Cold ~-0.1K at >9µm
After IASI-B Change (2017/19):
  Warm ~+0.03K at >9µm
  Cold ~+0.2K at >9µm
After IASI-A Change (2019/20):
  Warm: <+0.02K in all bands
  Cold: <±0.1K at >6µm
🡺 Best match now!
Chart: IASI-B-A at Standard Scene Tb (warm)
| IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Bv1-Av1 | -0.014 | -0.009 | -0.006 | -0.019 | -0.047 | -0.033 | -0.037 | -0.048
u(Bv1-Av1)
Bv2-Av1 | -0.01 | -0.015 | -0.003 | 0.018 | 0.04 | 0.019 | 0.023 | 0.045
u(Bv2-Av1)
Bv2-Av2 | -0.023 | -0.009 | -0.017 | 0.014 | 0.003 | 0.021 | 0.021 | 0.017
Chart: IASI-B-A at Tb=220K (cold)
| IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Bv1-Av1 | 0.014 | -0.006 | -0.011 | -0.179 | -0.147 | -0.111 | -0.109 | -0.103
u(Bv1-Av1)
Bv2-Av1 | 0 | -0.039 | -0.004 | 0.068 | 0.13 | 0.197 | 0.2 | 0.199
u(Bv2-Av1)
Bv2-Av2 | -0.419 | 0.031 | 0.037 | -0.078 | -0.037 | 0.058 | 0.073 | 0.075

## Slide 64: Discussion Points
Double Differences between references interesting, but:
  IASI-A discontinuity 2019-09-30
    Due to change in on-board processing - New version of GSICS products
    Split time series and statistics
  Started processing IASI-C 2019-08-08
    Cannot show full year time series
Are users interested in GSICS Correction uncertainties?
  Or instrument stability?
What time period to cover in report?
  D.GWG2019.3q.1: GSICS Annual Reports should contain the following information: Mean Bias & SD - 1 year (or shorter in special cases) & Drift and Time series plots - full operational lifetime.
Does it add value to show bias for other scene radiances?
  Considering discussion re: revising slope/offset – to be revisited
Can we combine results for all channels of each instrument?
  Which are key results? Bias? Trend? SD?
  Blend all RSB results? (Medium-term goal) – first close DCC
Can we automate the production of reports/slides/tables?

## Slide 65: Further Discussions
From Cheng-Zhi email 2020-04-07:
ITWG Climate Working Group Action 6:
  recent GSICS Executive Panel Meeting, from the climate reanalysis groups
  bias corrections applied to AIRS, IASI and CrIS assimilated in ERA5
  useful insights into performance of reanalysis
  with respect to hyperspectral sounder radiometric uncertainties.
  E.g. bias corrections applied to SNPP and NOAA-20 CrIS for most 15 μm temperature sounding channels < radiometric uncertainties at 3σ. (NEdT?)
  Good consistency check on mean state of reanalysis in the recent era,
  may provide an important tool in development of a ‘benchmark’ reanalysis.
  should be extended to other hyperspectral IR instruments
  but requires radiometric uncertainties for these sensors are documented and made available to users.
  Different agencies may have already provided these information in the instrument ATBDs. But it would be beneficial if the uncertainties were estimated in a consistent way across sensors, to facilitate uptake by users. Ideally, this would be made available in a single document, to enable easy cross-comparison of the methodologies.
This sounds like an excellent idea – to develop standard methods to define the radiometric uncertainties in the IR sounders and to compare those with the bias corrections applied operationally by NWP centres.

## Slide 66: IMD Agency Report 2020
AK Mitra
Kavita Navria
Rakesh Kumar
&
Virendra Singh
India Meteorological Department
16-Apr-2020

## Slide 67: 2019 Geo Calibration work in CMA
Imager Validation (Visible/TIR) with NOAA
INSAT3D Sounder and products validation
INSAT3D/3DR Cal/Val campaign Jan-2020
Major satellite/Instrument : INSAT3D and INSAT3DR calibration and its radiance assimilation.

## Slide 68
TIR1 validation is done between INSAT 3D, NOAA 19 and INSAT 3DR. For validation NOAA 19 TIR1 daily file is available and INSAT 3D/3DR files are being taken for 0300, 0600, 0900 and 1200 GMT.
Overall Comparison : Every collocated data is taken and RMSE, BIAS, CC are calculated. Difference of both data sets (data from two different satellites) is also calculated and plotted.
Clear sky cloudy sky comparison both performed.
INSAT3D INSAT3DR

## Slide 70
VISIBLE VALIDATION
INSAT 3D with NOAA 19
INSAT 3DR with NOAA 19

## Slide 71
INSAT-3D TPW and AIRS TPW retrievals 2018
Seasonal variation of TPW from the INSAT-3D satellite and AIRS retrievals

## Slide 72
INSAT-3D /3DR calibration campaign at Great Rann of Kutchh
03-08 January 2020
Bhuj

## Slide 73
INSAT3D spectral response function for VIS and SWIR channels

## Slide 76: 2020 Annual GSICS Calibration Report for JMA
Meteorological Satellite Center of JMA
Okuyama Arata, Kodera Kazuki
and Tanaka Hideaki

## Slide 77: Himawari-8 Calibration Events in 2020
Himawari-9 was non-operational during the maintenance period.
Satellite Status | 
 | Op = Operational
 | P = Pre-operational
 | B = Back-up, secondary
 | L = Limited availability
Satellite (status) |  | Location | Launch date | Operation Date
Himawari-8 | (Op) | 140.7 E | 07 Oct. 2014 | 07 Jul. 2015
Himawari-9 | (B) | 140.7 E | 12 Nov. 2016 | -
After the updating
Before the updating on 17 Dec. 2019
Major Calibration Related Events | Himawari-8 | Himawari-9
Update of the VNIR cal. Info. In L1B | 08 Jul. 2019 | -
Best detector select (BDS) map updating | 17 Dec. 2019 | -
🡨 Dust RGB imagery
21:50UTC 15 May 2019 to
04:00 UTC 17 Dec. 2019
Stripes for E-W direction due to an abnormal detector outputs appeared in Himawari-8/AHI band 11 (8.6 μm) data intermittently.

## Slide 78
Summary Statistics of Himawari-8/AHI VNIR Calibration Performance (All Uncertainties are k=1)
Mean Bias: monthly average and standard deviation of the daily results in January 2020
Annual Drift: calculated using Mean Bias from July 2015 to February 2020
Ray-matching: Spectral Band Adjustment Factors on NASA Langley website compensates Spectral diff. (ATBD)
Vicarious calibration uses optical parameters retrieved from Aqua/MODIS C6 L1B (Reference)
Calibration Performance: Himawari-8/AHI VIS/NIR Bands
BAND03 (0.64 μm)
BAND05 (1.6 μm)
Trend of the ratio of observation to reference computed using Ray-matching / Vicarious calibration approaches
BAND01 (0.47 μm)
Band name (central wavelength in mm) |  | Band 01 (0.47) |  |  | Band 02 (0.51) |  |  | Band 03 (0.64) |  |  | Band 04 (0.86) |  |  | Band 05 (1.6) |  |  | Band 06 (2.3) |  |  | Units
Ray-matching w/ SNPP/VIIRS | Mean bias | -2.6 | ± | 0.8 | +0.5 | ± | 1.0 | +0.4 | ± | 0.8 | -0.6 | ± | 0.7 | +5.6 | ± | 1.5 | -5.5 | ± | 1.0 | %
 | Annual drift | -0.34 | ± | 0.04 | -0.48 | ± | 0.04 | -0.76 | ± | 0.04 | -0.59 | ± | 0.04 | -0.25 | ± | 0.06 | -0.23 | ± | 0.05 | %/yr
Vicarious cal. using Aqua/MODIS + RTM | Mean bias | -2.7 | ± | 1.6 | -3.6 | ± | 1.5 | -0.9 | ± | 1.5 | +0.5 | ± | 1.3 | +3.7 | ± | 0.9 | -5.0 | ± | 0.8 | %
 | Annual drift | -0.52 | ± | 0.05 | -0.64 | ± | 0.05 | -0.88 | ± | 0.06 | -0.74 | ± | 0.05 | -0.21 | ± | 0.06 | -0.18 | ± | 0.07 | %/yr
Available at JMA/MSC Web page: https://www.data.jma.go.jp/mscweb/data/monitoring/gsics/vis/monit_visvical.html

## Slide 79
Summary Statistics of Himawari-8/AHI IR Calibration Performance in Jan. 2020 (All uncertainties are k=1)
The statistics are derived from Himawari-8/AHI GSICS Re-Analysis Correction (ATBD)
Standard Radiance: typical scene defined by GSICS for easy inter-comparison of sensors’ inter-calibration biases
Calibration Performance: Himawari-8/AHI Infrared Bands
Time series of Himawari-8/AHI Tb biases w.r.t. Metop-A/IASI at std. radiance
-0.3
-0.2
-0.1
0.0
+0.1
Brightness temperature bias [K]
 | Channel Name | BAND07 | BAND08 | BAND09 | BAND10 | BAND11 | BAND12 | BAND13 | BAND14 | BAND15 | BAND16
 | (Central Wavelength in um) | (3.9) | (6.2) | (6.9) | (7.3) | (8.6) | (9.6) | (10.4) | (11.2) | (12.4) | (13.3)
 | Std. Radiance as Tb (K) | 286.0 | 234.6 | 243.9 | 254.6 | 283.8 | 259.5 | 286.2 | 286.1 | 283.8 | 269.7
Metop-A IASI | Mean Bias (K) | -0.136 | -0.182 | -0.214 | -0.116 | -0.067 | -0.281 | 0.018 | 0.028 | -0.049 | 0.073
 | Stdv. of Bias (K) | 0.003 | 0.004 | 0.004 | 0.004 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003
Metop-B IASI | Mean Bias (K) | -0.136 | -0.174 | -0.208 | -0.107 | -0.076 | -0.291 | 0.008 | 0.016 | -0.069 | 0.053
 | Stdv. of Bias (K) | 0.004 | 0.004 | 0.004 | 0.004 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003
Aqua AIRS | Mean Bias (K) | -0.026 | - | -0.296 | -0.164 | - | -0.290 | 0.034 | 0.053 | -0.015 | 0.131
 | Stdv. of Bias (K) | 0.003 | - | 0.003 | 0.003 | - | 0.002 | 0.002 | 0.002 | 0.002 | 0.002
S-NPP CrIS | Mean Bias (K) | - | -0.166 | -0.235 | -0.116 | - | -0.257 | -0.037 | -0.029 | -0.112 | 0.033
 | Stdv. of Bias (K) | - | 0.004 | 0.004 | 0.004 | - | 0.003 | 0.003 | 0.003 | 0.003 | 0.003
Available at JMA/MSC Web page: https://www.data.jma.go.jp/mscweb/data/monitoring/gsics/ir/monit_geoleoir.html
vs. Metop-A/IASI

## Slide 80: Summary
Major calibration events
  Update of the VNIR cal. Info. In L1B: 08 Jul. 2019
  Best detector select (BDS) map updating: 17 Dec. 2019
VNIR
  Calibration performance estimated by the ray-matching w/ SNPP/VIIRS and vicarious calibration w/ Aqua/MODIS looks stable.
  B01-B04 show sensor sensitivity degradation trend with 0.3-0.9% / year. The trend is less in B05 and B06.
IR
  Biases at the std. radiance are -0.3 to 0.1 K for all IR bands. Estimated biases look consistent among reference sensors.
JMA GSICS landing page
  https://www.data.jma.go.jp/mscweb/data/monitoring/calibration.html
Himawari-8/9 AHI Event Log page
  https://www.data.jma.go.jp/mscweb/en/oper/event_H8.html
  https://www.data.jma.go.jp/mscweb/en/oper/event_H9.html

## Slide 81: Appendix: Double difference of the Tb biases @std. radiance
From Reanalysis Correction for Jan. 2020
DD = Tb biases@std.radiance(Ref.sensors) - Tb biases@std.radiance(Metop-A/IASI)
 | Channel Name | BAND07 | BAND08 | BAND09 | BAND10 | BAND11 | BAND12 | BAND13 | BAND14 | BAND15 | BAND16
 | (Central Wavelength in um) | (3.9) | (6.2) | (6.9) | (7.3) | (8.6) | (9.6) | (10.4) | (11.2) | (12.4) | (13.3)
 | Std. Radiance as Tb (K) | 286.0 | 234.6 | 243.9 | 254.6 | 283.8 | 259.5 | 286.2 | 286.1 | 283.8 | 269.7
Metop-A IASI | - | - | - | - | - | - | - | - | - | - | -
Metop-B IASI | DD of the mean bias with Metop-A/IASI [K] | 0.000 | 0.007 | 0.006 | 0.009 | -0.009 | -0.011 | -0.009 | -0.012 | -0.020 | -0.020
Aqua AIRS | DD of the mean bias with Metop-A/IASI [K] | 0.110 | - | -0.082 | -0.048 | - | -0.009 | 0.017 | 0.025 | 0.034 | 0.058
S-NPP CrIS | DD of the mean bias with Metop-A/IASI [K] | - | 0.015 | -0.021 | 0.000 | - | 0.023 | -0.055 | -0.056 | -0.063 | -0.040

## Slide 82: 2020 Annual GSICS Calibration Report - GEO
KMA

## Slide 83: GK2A,COMS Calibration Events in 2019
http://planet.rssi.ru
Satellite (status) |  | Current Location | Launch date | Operation Date
COMS | Back-up Since 2020-04-01 | 128.2E | 2010-06-26 | 2011-04-11
GK2A | (OP) | 128.2 E | 2018-12-04 | 2019-07-25
COMS/GK2A Calibration Events https://nmsc.kma.go.kr/enhome/html/bbs/listNotice.do?bbsCd=00026
  Provide calibration events and schedule : can check in Notice item
Major Calibration Related Events | COMS | GK2A
IR133 (13.3um) channel SRF update |  | 09/27/2019

## Slide 84: GK2A AMI VNIR Cal. Performance
GEO | Reference Instr. | B01 (0.47 μm) | B02 (0.51 μm) | B03 (0.64 μm) | B04 (0.86 μm) | B05 (1.37 μm) | B06 (1.61 μm)
GK2A AMI | Terra/MODIS | -1.08(±1.27) | -1.55(±2.27) | 3.06(±1.08) | 8.87(±2.18) | 6.45(±0.95) | 4.87(±0.97)
 | SNPP/VIIRS | -3.87(±1.71) | 3.14(±1.49) | 2.41(±1.41) | 1.53(±1.62) | -0.78(±0.69) | 6.88(±1.49)
The mean calibration difference between GK2A AMI and Terra/MODIS, SNPP/VIIRS from Oct. 1, 2019 – Dec. 31, 2019 (unit: %, all uncertainties k=1)
We are testing ray matching method using SNPP/VIIRS.
All the AMI Visible and Near-Infrared (VNIR) channels has very high bias and uncertainty.
That caused by seasonal variation.
We have to keep watching since over 1 year operations.
VIIRS
MODIS
AMI vs MODIS
AMI vs VIIRS

## Slide 85
Summary Statistics of COMS/MI IR Calibration Performance in 2019 (all uncertainties are k=1)
COMS IR Calibration Performance: Bias
The mean Tb bias at standard Tb is within 0.21K except for WV(6.8µm) channel as reference AIRS.
 | Channel Name (Central Wavelength in μm) | SWIR (3.8) | WV (6.8) | IR1 (10.8) | IR2 (12.0)
 | Std. Scene Tb (K) | 285.9 | 237.6 | 286.3 | 285.1
Metop-A/ IASI | Bias at Std. Scene radiance (K) | 0.17 (±0.05) | -0.02 (±0.03) | 0.20 (±0.08) | 0.08 (±0.06)
Metop-B/ IASI | Bias at Std. Scene radiance (K) | 0.21 (±0.05) | -0.04 (±0.03) | 0.13 (±0.07) | 0.02 (±0.05)
AQUA/ AIRS | Bias at Std. Scene radiance (K) | -0.07 (±0.08) | -0.31 (±0.10) | 0.11 (±0.16) | 0.14 (±0.1)
S-NPP/ CrIS | Bias at Std. Scene radiance (K) | - | -0.17 (±0.08) | 0.08 (±0.14) | 0.09 (±0.09)

## Slide 86
Summary Statistics of GK2A/AMI IR Calibration Performance in August-December 2019 (All uncertainties are k=1)
GK2A IR Calibration Performance: Bias
 | Channel Name (Central Wavelength in μm) | BAND07 (3.8) | BAND08 (6.3) | BAND09 (6.9) | BAND10 (7.3) | BAND11 (8.7) | BAND12 (9.6) | BAND13 (10.5) | BAND14 (11.2) | BAND15 (12.3) | BAND16 (13.3)
 | Std. Scene Tb (K) | 285.9 | 234.9 | 244.1 | 254.5 | 283.7 | 259.1 | 286.1 | 286.0 | 283.8 | 269.4
Metop-A/ IASI | Bias at Std. Scene radiance (K) | 0.04 (±0.07) | -0.06 (±0.01) | -0.12 (±0.01) | 0.01 (±0.01) | 0.03 (±0.01) | -0.05 (±0.02) | 007 (±0.02) | 008 (±0.02) | 0.06 (±0.02) | 0.01 (±0.01)
Metop-B/ IASI | Bias at Std. Scene radiance (K) | 0.08 (±0.08) | 0.06 (±0.01) | -0.10 (±0.01) | 0.01 (±0.01) | 0.02 (±0.03) | -0.08 (±0.02) | 0.04 (±0.02) | 0.05 (±0.02) | 0.03 (±0.02) | -0.01 (±0.02)
AQUA/ AIRS | Bias at Std. Scene radiance (K) | - | -0.03 (±0.01) | -0.21 (±0.01) | -0.05 (±0.01) | - | -0.07 (±0.01) | 006 (±0.02) | 007 (±0.02) | 006 (±0.02) | 0.06 (±0.02)
S-NPP/ CrIS | Bias at Std. Scene radiance (K) | -0.04 (±0.04) | 0.02 (±0.02) | -0.19 (±0.02) | -0.06 (±0.02) | 0.01 (±0.01) | -0.02 (±0.02) | 0.02 (±0.01) | 0.02 (±0.01) | 0.01 (±0.01) | -0.01 (±0.01)
NOAA-20/ CrIS | Bias at Std. Scene radiance (K) | 0.01 (±0.05) | 0.04 (±0.02) | -0.13 (±0.01) | -0.01 (±0.01) | 0.09 (±0.01) | -0.01 (±0.02) | 009 (±0.03) | 0.09 (±0.03) | 0.06 (±0.03) | -0.03 (±0.01)
GK2A AMI IR channels are in general well calibrated
GK2A AMI has relatively large bias around -0.1K~-0.2K for 6.9µm (WV level)
SRF(13.3µm) updated (shifted by -0.8cm-1) on 27 Sep. 2019

## Slide 97: NOAA 2020 Annual GSICS Calibration Report - GEO
GOES-R ABI

## Slide 98: GOES-16/17 Calibration Events in 2019
http://planet.rssi.ru
GOES-16/17 ABI Calibration Event Log:
https://www.star.nesdis.noaa.gov/GOESCal/goes_SatelliteAnomalies.php
Satellite (status) |  | Current Location | Launch Date | Operation Date
GOES-16 | (Op) | 75.2W (GOES-East) | 2016-11-19 | 2017-12-18
GOES-17 | (Op) | 137.2W (GOES-West) | 2018-03-01 | 2019-02-12
GOES-15 |  | storage orbit on 2020-03-02 |  | 
Major Calibration Related Events | GOES-16 | GOES-17
B02 (0.64um) solar cal. LUT update | 04/23/2019 | 04/27/2019
Predictive Calibration Algorithm Implementation |  | 07/25/2019
This is to provide the major calibration events the agency would like users to be aware.

## Slide 99: G16/17 B02 Solar Cal. LUT Updates
The update of the B02(0.64um) solar calibration LUT reduces the calibration difference to SNPP and NOAA-20 VIIRS
More information: https://www.star.nesdis.noaa.gov/GOESCal/G16_ABI_VNIR_InterCal_static.php
https://www.star.nesdis.noaa.gov/GOESCal/G17_ABI_VNIR_InterCal_static.php

## Slide 100: G17 IR pCal Implementation on 07/25/2019
The GEO-GEO inter-comparison shows that the GS update on July 25, 2019 significantly improves the G17 IR radiance accuracy at unstable FPM temperature time
More information at: https://www.star.nesdis.noaa.gov/GOESCal/G17_ABI_GEO_GEO_IR_daily.php
Before implementation
After implementation

## Slide 101: G16/17 ABI VNIR Cal. Performance
GEO | Reference Instr. | B01 (0.47um) | B02 (0.64um) | B03 (0.86um) | B04 (1.37um) | B05 (1.6um) | B06 (2.2um)
G16 | SNPP/VIIRS | 5.62(±2.44) | -0.46(±3.12) | 0.16(±3.10) | -2.16(±2.41) | 2.28(±3.06) | -1.70(±1.71)
G17 | SNPP/VIIRS | 1.52(±3.24) | 0.99(±4.45) | 0.00(±3.60) | -1.17(±7.97) | -0.97(±3.36) | -2.61(±2.86)
The mean calibration difference between G16/17 ABI and SNPP/VIIRS from Oct. 1, 2019 – Nov. 30, 2019 (unit: %, all uncertainties k=1)
All the ABI Visible and Infrared (VNIR) channels, except for G16 B01, are within 5% difference to SNPP/VIIRS from 10/01/2019-11/30/2019
  G16 B01 is brighter than SNPP/VIIRS by 5.6%
Slight scene radiance/reflectance dependent bias can be observed at some VNIR bands
  Uncertainty in SRF correction may contribute
G16/17 VNIR calibration is in general very stable since their operations, apart from the B02 LUT updates in April 2019. Long-term monitoring is available:
https://www.star.nesdis.noaa.gov/GOESCal/G16_ABI_VNIR_InterCal_static.php
https://www.star.nesdis.noaa.gov/GOESCal/G17_ABI_VNIR_InterCal_static.php

## Slide 102
 | Channel Name (Central Wavelength in μm) | BAND07 (3.9) | BAND08 (6.2) | BAND09 (6.9) | BAND10 (7.3) | BAND11 (8.6) | BAND12 (9.6) | BAND13 (10.4) | BAND14 (11.2) | BAND15 (12.4) | BAND16 (13.3)
 | Std. Scene Tb* | 286.0 | 234.5 | 244.0 | 254.5 | 284.0 | 259.5 | 286.0 | 286.0 | 283.5 | 269.5
Metop-A/ IASI | Bias at Std. Scene radiance (K) | -0.00 (±0.06) | -0.10 (±0.01) | -0.11 (±0.01) | -0.04 (0.01) | -0.03 (±0.02) | -0.07 (±0.01) | 0.00 (±0.03) | 0.05 (±0.03) | 0.05 (±0.03) | -0.11 (±0.03)
Metop-B/ IASI | Bias at Std. Scene radiance (K) | 0.01 (±0.05) | -0.09 (±0.01) | -0.10 (±0.01) | -0.04 (±0.01) | -0.03 (±0.02) | -0.08 (±0.01) | -0.03 (±0.02) | 0.03 (±0.03) | 0.02 (±0.03) | -0.14 (±0.03)
Metop-C/ IASI | Bias at Std. Scene radiance (K) | 0.01 (±0.06) | -0.09 (±0.01) | -0.10 (±0.01) | -0.05 (±0.01) | -0.03 (±0.02) | -0.05 (±0.02) | -0.02 (±0.03) | 0.03 (±0.03) | 0.03 (±0.03) | -0.13 (±0.03)
S-NPP/ CrIS | Bias at Std. Scene radiance (K) | - | - | -0.11 (±0.01) | -0.05 (±0.01) | - | -0.02 (±0.01) | -0.04 (±0.02) | 0.00 (±0.02) | -0.01 (±0.02) | -0.13 (±0.02)
NOAA-20/ CrIS | Bias at Std. Scene radiance (K) | - | - | -0.09 (±0.00) | -0.04 (±0.01) | - | -0.02 (±0.01) | -0.01 (±0.01) | 0.06 (±0.02) | 0.04 (±0.02) | -0.10 (±0.02)
Summary Statistics of GOES-16/ABI IR Calibration Performance in December 2019 (all uncertainties are k=1)
G16 IR Rad. Calibration Performance: Bias
Either table/figure can be used.
G16 ABI IR bands are well-calibrated. The mean Tb bias at standard radiance/Tb is within 0.15K for all bands.

## Slide 103
Summary Statistics of GOES-17/ABI IR Calibration Performance in Dec. 2019 at Gainset I Period (All uncertainties are k=1)
G17 IR Calibration Performance: Bias
 | Channel Name (Central Wavelength in μm) | BAND07 (3.9) | BAND08 (6.2) | BAND09 (6.9) | BAND10 (7.3) | BAND11 (8.6) | BAND12 (9.6) | BAND13 (10.4) | BAND14 (11.2) | BAND15 (12.4) | BAND16 (13.3)
 | Std. Scene Tb (K) | 286.0 | 234.5 | 244.0 | 254.5 | 284.0 | 259.5 | 286.0 | 286.0 | 283.5 | 269.5
Metop-A/ IASI | Bias at Std. Scene radiance (K) | 0.01 (±0.09) | -0.02 (±0.01) | 0.13 (±0.01) | 0.09 (±0.01) | 0.07 (±0.03) | -0.05 (±0.02) | 0.02 (±0.03) | 0.02 (±0.03) | 0.13 (±0.03) | 0.43 (±0.03)
Metop-B/ IASI | Bias at Std. Scene radiance (K) | 0.01 (±0.08) | -0.01 (±0.01) | 0.13 (±0.01) | 0.09 (±0.01) | 0.05 (±0.02) | -0.06 (±0.02) | -0.01 (±0.03) | -0.01 (±0.03) | 0.11 (±0.03) | 0.41 (±0.03)
Metop-C/ IASI | Bias at Std. Scene radiance (K) | 0.01 (±0.08) | -0.01 (±0.01) | 0.13 (±0.01) | 0.09 (±0.01) | 0.05 (±0.02) | -0.06 (±0.02) | -0.01 (±0.03) | -0.01 (±0.03) | 0.11 (±0.03) | 0.41 (±0.03)
S-NPP/ CrIS | Bias at Std. Scene radiance (K) | - | - | 0.14 (±0.03) | 0.08 (±0.04) | - | -0.03 (±0.04) | -0.04 (±0.08) | -0.08 (±0.09) | 0.05 (±0.10) | 0.46 (±0.11)
NOAA-20/ CrIS | Bias at Std. Scene radiance (K) | - | - | 0.16 (±0.03) | 0.09 (±0.03) | - | -0.02 (±0.05) | -0.02 (±0.08) | -0.04 (±0.09) | 0.08 (±0.10) | 0.48 (±0.10)
G17 ABI is in general well calibrated at the gain-set I period when the focal plane module (FPM) temperature is stable.
G17 B16 has relatively large bias at 0.4-0.5K
LWIR FPM Temperature
Gainset I

## Slide 104: G16/G17 Rad. Calibration Performance: Trending/Scatterplots
GOES-16 ABI IR calibration is very stable after the GS update on 06/19/2018.
GOES-17 ABI IR calibration is very stable during the stable FPM temperature period since its operation
No strong scene dependent bias at all IR bands
The different of the Tb bias to CrIS/IASI is within 0.1K
More information and plots are available at: https://www.star.nesdis.noaa.gov/GOESCal/G16_GSICS_ABI_IR_Bias_static.php
https://www.star.nesdis.noaa.gov/GOESCal/G17_GSICS_ABI_IR_Bias_static.php
GS update on 06/19/2018
Note: Trending can also be characterized with the GSICS correction bias, our traditional GSICS bias monitoring method.
The trending shown in this slide is calculated with the mean radiance difference converted to 300K. This is requirement for ABI.

## Slide 108
NOAA-20 and S-NPP VIIRS Calibration Report
Presented by Taeyoung (Jason) Choi
With contributions from NOAA VIIRS SDR Team
Changyong Cao, Sirish Uprety, Wenhui Wang, Slawomir Blonski,
Xi Shao, Yalong Gu, Bin Zhang, Khalil Ahmad
Date: 4/16/2020
GSICS Web Meeting

## Slide 109: Outline
VIIRS On-orbit Calibration
NOAA-20 VIIRS Calibration
  IDPS planetary ephemeris ancillary table error Jan 15-16, 2020
  Reflective Solar Band (RSB)
    SD and lunar F-factors
    Post processing check: DCC and SNO trending results
  Thermal Emissive Band (TEB)
S-NPP VIIRS RSB Calibration
  RSB
    Solar calibration anomaly Feb 2019
    SD and lunar F-factors
    Post processing check: DCC and SNO trending results
  TEB
Day Night Band (DNB) Calibration Updates
Summary

## Slide 110: VIIRS On-orbit Calibration
Source: VIIRS Radiometric ATBD.
Focal Plane Interface Electronics
Blackbody

## Slide 111: NOAA-20 and S-NPP VIIRS Anomaly
A major anomaly occurred in the operational JPSS IDPS processing on 01/16/2020 for both S-NPP and NOAA-20 VIIRS (first detected by NASA team)
The JPL planetary ephemeris ancillary file was corrupted in the binary LUT
The duplicated records led to a failure in indexing and time interpolation. 🡪 It was corrected and became normal.
Starting from 01/16, the modeled solar vector became abnormal

## Slide 112: NOAA-20 VIIRS RSB Status
The SD F-factor stability was improved with the H-factor update.
Normalized SD F-factors (lines) and lunar F-factors (symbols) are consistent within 1% level.
  Short wavelength bands (M1~M4) had lower SD F-factors than lunar F-factors.

## Slide 113: NOAA-20 VIIRS RSB Status
Post processing check.
  VIIRS bias trends are derived relative to AQUA MODIS, since no direct SNOs exists between VIIRS.
  Double differencing the two VIIRS bias trends indicates the VIIRS radiometric consistency.
  DCC time series showed upward trends in some bands (~0.3%/year in M1 and M2), but their magnitudes are similar to uncertainty levels
  NOAA-20 VIIRS operational F-factors has been remained in the same level.
    Since 4/27/2018.
NOAA VIIRS team is closely monitoring.

## Slide 114: NOAA-20 VIIRS TEB Status
TEB F-factors are very stable after the last bake-out event in 2018.
Blackbody reference temperature has been very stable
  No TEB calibration issues.
TEB WUCD bias correction has been successfully implemented in the NOAA operational processing since July 2019.
TEBs show larger than expected scan angle and scene temperature dependent biases.

## Slide 115: S-NPP VIIRS RSB Status
The S-NPP VIIRS has been performing well
The SD degradation (H-factor) is slow compared to the early lifetime after 2014
F-factor drops for bands M4 and M5 on 2/16/2018 were caused by a Data Acquisition Schedule (DAS) error during DNB calibration
  It continued until 3/7/2018

## Slide 116: S-NPP VIIRS RSB Status
Solar calibration anomaly on 2/24/2019
  SD signal dropped in SD and SDSM observations (~1%)
  The H factors dropped similarly
  The F factors also changed initially, but then returned to near the original levels after the updated H factors were applied
  SWIR bands (I3, M8-M11) still have the increased F factors (by about 0.5%)

## Slide 117: S-NPP VIIRS RSB Status
SD F-factor validation
  Short wavelength bands (M1~M4) showed mismatches in early lifetime.
  The SD and lunar F-factors are consistent within 1%.

## Slide 118: S-NPP VIIRS RSB Status
Post processing check.
  DCC trending results show very stable response from 2018 to 2020 in VISNIR bands.
  Comparing VIIRS reflectance trending over pseudo-invariant calibration sites (PICS) S-NPP VIIRS indicated stable responses.
    Bias relative to NOAA-20, S-NPP showed on the order of 2-4%
NOAA-20 / S-NPP

## Slide 119: S-NPP VIIRS TEB Status
The TEB F-factors show consistent trends in all bands.
  Band I5 shows largest degradation.
Warm-up-cool-down (WUCD) frequency has been changed from quarterly to yearly since last year.
Blackbody temperature is very stable around 292.6K.

## Slide 120: NOAA-20 & S-NPP VIIRS DNB Status
The VIIRS Day/Night Band (DNB) sensors onboard NOAA-20 and SNPP satellites are performing well, providing critical nighttime imagery of clouds, nocturnal lights, aurora etc.
DNB major calibration updates:
  Recent algorithm improvement for both S-NPP and NOAA-20 to address the residual striping and enhance the imagery quality over high aggregation zones due to nonlinearity.
  To synchronize with the improved DNB calibration algorithm, updated the monthly DNB stray light correction LUTs for SNPP and NOAA-20.
Major S-NPP DNB Anomaly
  Anomaly after the Flight Software (FSW) update on 01/08/2020 resulting in increased striping in nighttime SDRs (Figure).
  All aggregation zones affected, in particular the edge zones (29 ~ 32).
  Algorithm updated for dark offset calculation to resolve the anomaly.
Striping from anomaly
Striping removed after resolving anomaly

## Slide 121: NOAA-20 & S-NPP VIIRS DNB Status
Radiometric consistency (within 3-5% over ~2 years) between SNPP and NOAA-20 VIIRS DNB is demonstrated through long term monitoring of TOA reflectance derived over pseudo-invariant calibration sites (PICS):
  Nighttime nadir observation over two snow flats and three desert sites
  Lunar irradiance model from Miller and Turner, 2009 used to derive the TOA reflectance
Radiometric consistency between two VIIRS DNB is also demonstrated and validated with that from PICS using lunar illuminated Deep Convective Cloud (Cao et al., 2019)
Deserts
Polar snow
Radiometric consistency between S-NPP and NOAA-20 DNB

## Slide 122: Template for 2020 (GEO)
Major satellite/Instrument events relevant to calibration: 1 page for agency.
Radiometric calibration performance for GEO imagers using GSICS inter-calibration/inter-comparison approaches (1-2 pages/instrument)
  Table or Figure summarizing bias/unc: average of last one year or typical time period
  Time series chart of bias/unc: since operation start
  Scene Dependent Bias: Scatterplot of scene dependent bias
  IR Diurnal variation (recommended): GEO-LEO or GEO-GEO
Detailed information: referred to Calibration Landing Page/Calibration Event Log