## Slide 1
Monitoring SLSTR calibration using IASI: Updates
A. Burini I. Tomazic, T. Hewison

## Slide 2: Introduction
Aim
  To verify if SLSTR IR is meeting the performance requirements:
    The absolute radiometric accuracy for data acquired by the IR channels shall be smaller than 0.2K, traceable to ITS-90.
    As a minimum, this requirement shall be met in the blackbody temperature range (~250K - ~300K)
Objectives
  To intercompare SLSTR with a stable and characterized reference sensor:
    IASI is the GSICS reference sensor due to its stability and chracterisation
    To follow GSICS methodology (Hewison, 2013)
    Based on EUMETSAT study by University of Leicester: Radiometric Intercomparison of AATSR and IASI, 2013, C. Whyte, D. Moore and J. Remedios
Collaboration with FIDUCEO project (H2020), Merchant et al.

## Slide 3: Previous Methodology
Crossovers (SNO)
  SNO = simultaneous nadir overpasses
  based on orbital model prediction
  Each event last ~2 days with ~50 crossovers per SNO
Collocations (matchups)
  spatio/temporal/geometry
  Time: 5 min pixel time difference
  Spatial: within pixel
  Viewing angle: |Δsec(ϑ)/sec(ϑ)|<1% or |IASI SZA| < 20°
  IASI IFOV estimated as ellipse
Spectral convolution
  Convolve IASI radiance spectra with SLSTR SRF
  SLSTR SRF v2014
  S7 (3.7 µm) requires gap filling approach – incomplete IASI spectral coverage
Aggregate (average)
  SLSTR pixels in IASI FoV
Green – true collocation; blue – time of collocation + 3 min; red – time of collocation – 3 min
Limited to pole regions  temperature range ~200 K - 280 K

## Slide 4
EUM started to prototype a new multi-mission environment for the calibration and monitoring of Level1 products. MICMICS
SLSTR-IASI is the first branch to be prototyped and integrated in the new environment, where data access, processing and reporting are fully integrated
Objective:
  To solve the collocation problem in a general and fast way
  To create an infrastructure for the operational monitoring of IR sensor with IASI
  To extend the collocation criteria outside the polar region
  To ready for future missions
  To identify and test a “gap filling” method for S7 (extends beyond IASI shortwave limit of 2760cm-1)
SLSTR – IASI: MIMICS Development

## Slide 5: Data Access as a Service in MICMICS
SLSTR-A
SLSTR-B
OLCI-A
OLCI-B
IASI-A
IASI-B
IASI-C
Python DAM API
Mysql
MYSQL is doing the actual job of handling the temporal and geographical data type
Working Code for querying SLSTR data from fbf overpassing a user defined Region of Interest
DAM has 2 main options:
--init-catalogue: initiate the mysql tables
--update-catalogue: harvest and update the fbf repository
DAM is running 4 times a day

## Slide 6
Data Access as a service - MICMICS
Cataloguing of data
Daemon tool to perform cross query:
  Identification of Potential Candidates
  Overlap Criteria can be customized (percentage of overlapping polygons)
Tool Completely de-coupled from the processing:
  To speed up the pre-collocation process
  It can be re-used for other processes
Collocation Archive for SLSTR-A/ IASI-B

## Slide 7
A Generic Collocation Approach
To make re-use of well tested and broadly accepted libraries for geographic projection, aiming to minimize the distortion of data
Collocation between sounding sensors and Imaging sensor is then automatically achieved (same reference system) = DATA CUBE
The collocation is done at “granule” level (or at scenario level ) in order to be easily parallelized over several nodes. (it can still be applied in the GEO disk)
Projection in a common reference grid.
Orthographic projection
Oblique Mercator
Transversal Mercator

## Slide 8: Example: SLSTR-IASI [LEO-LEO]
Through the DAM, two overlapped granules of SLSTR and IASI have been selected (no true SNO, only geographical match)
IASI FOV is calculated (~2 sec/granule). Each FOV can be considered a “shape” in the GIS terminology.
For this particular case, the collocation problem can be summarized as “finding an efficient way of overlapping a shape (fov) over a raster (image). (this is a typical GIS application )
The first step is to have a common reference system between the two product
The processing steps can be summarized as:
IASI FOV Computation (~2s)
Projection of Master (SLSTR) [PROJ4 + pyresample] (~5s for 2500x2500 image)
Projection of Slave (IASI) [PROJ4 + shapely] (~1 s)
Rasterisation of Indices [rasterio] (~20s)
Extraction of statistics [numpy] (~10s)

## Slide 9: Example: SLSTR-IASI [LEO-LEO]
Target Scenario Projection [Oblique Mercator | Ortographic]
Once SHAPE and RASTER are projected onto a common reference space, it is easy to work directly in IMAGE COORDINATES (indices).
Based on [PROJ4 – Shapely (intersection)]
This process takes less than 10s.

## Slide 10: Example: SLSTR-IASI [LEO-LEO]
SLSTR Pixels within IASI FOV
SLSTR Pixels StdDev Value within IASI FOV
SLSTR Pixels Mean Value within IASI FOV
Original Indices are kept, so in principle it is still possible to perform the collocation directly in the original L1 grid. Tests are still on going.

## Slide 11: Analysis of Results
Status:
  Thresholds on several combination of parameters being tested
  Uncertainty-based metrics are being defined to optimise them
Possibility of analysis of data over land/sea and during night/day overpass
Collocations can be retrieved outside the tropical areas.
Filtering by land/sea mask is possible

## Slide 12: Status on the Analysis
dataset.reset_filter()
dataset.filter_data(field='solzen', operator='<', value=90)
dataset.filter_data(field='fov_stdev_bt', operator='<', value=0.4)
dataset.filter_data(field='time_diff', operator='<', value=600)
dataset.filter_data(field='ref_zen', operator='<', value=20)

## Slide 13: Status on the Analysis
dataset.reset_filter()
dataset.filter_data(field=land_sea_mask', operator=‘=', value=1)
dataset.filter_data(field='solzen', operator='<', value=90)
dataset.filter_data(field='fov_stdev_bt', operator='<', value=0.4)
dataset.filter_data(field='time_diff', operator='<', value=600)
dataset.filter_data(field='ref_zen', operator='<', value=20)

## Slide 14: Status on the Analysis
dataset.reset_filter()
dataset.filter_data(field=land_sea_mask', operator=‘=', value=0)
dataset.filter_data(field='solzen', operator='<', value=90)
dataset.filter_data(field='fov_stdev_bt', operator='<', value=0.4)
dataset.filter_data(field='time_diff', operator='<', value=600)
dataset.filter_data(field='ref_zen', operator='<', value=20)

## Slide 15: Conclusions
Prototype for monitoring SLSTR calibration with IASI as reference has been developed.
Analysis of results is still on-going, several filtering parameters are being evaluated
Analysis of Oblique view is possible, but not being assessed for the moment
Software is stable and producing results for SLSTR A/B vs IASI/A/B/C
Once a metric for results will be consolidated, the monitoring will be put into operations.
Future plans:
  to include the Geo Scenario
  Gap Filling to include S7 channel – The software has been designed to be used with gap filling method, once this will be consolidated.