## Slide 1: GSICS VIS/NIR 2021 annual meeting discussion
David Doelling
March 31, 2021

## Slide 2: GSICS recommends N20 VIIRS as the VIS/NIR calibration reference
See the GSICS quarterly winter 2021 issue
N20 VIIRS not recommended for its absolute calibration
  Need to wait for CLARREO to tie the VIS/NIR calibration to an SI traceable source
  The Aqua-MODIS and N20 VIIRS 0.65µm calibration difference is 3.7%
N20 VIIRS recommended because of its on-orbit performance
  Two active calibration teams monitoring the onboard calibration systems
  Well documented prelaunch characterization and continued documentation of instrument performance
  Level 1B (L1B) radiance data products are made publicly available in near real time in an easily readable format, and archived
  Archive facility capable of reprocessing the sensor record after calibration anomalies
  Preference given to multiple sensor copy missions, (N20, N21, N22, and N23), that are launched into the same orbit
  Preference given to sensor that are used for climate quality retrievals

## Slide 3: GSICS recommends N20 VIIRS as the VIS/NIR calibration reference
Both NASA and NOAA teams monitoring N20 VIIRS performance
For the VIIRS M5 band the bias between NOAA and NASA L1B datasets is <0.1 % and for other RSBs is <0.2% with almost no trend differences
Both the NOAA JPSS VIIRS SDR (order from NOAA CLASS) and the NASA VIIRS Characterization Support Team (VCST) JPSS VIIRS L1B (order from NASA LandSIPS) datasets contain the well calibrated NOAA-20 VIIRS RSB reflectances.
  Users may order either dataset as a matter of convenience
NOAA is currently reprocessing the NOAA-20 VIIRS record from the beginning of the mission using the latest advanced algorithms (Cao et al., 2021)
Users should document the source and version of the N20 VIIRS dataset in journal articles and other documents

## Slide 4: Discussion of future VIS/NIR web meetings
(1) Propose a bi-monthly (2-month), 1-day, 2-hour meeting
  Have them occur on the same weekday each month, for example every 2nd Thursday. May, July, September, November and January
  What day and time can we agree on
  Will the lunar group have their own schedule?
  Except for the month of the annual meeting
(2) OR a monthly (1-month), 1-day, 2-hour meeting?
  If there are insufficient presentations, we will cancel the meeting
(3) OR continue with existing method, of having to schedule in advance future meetings

## Slide 5: Agency GSICS VIS/NIR presentations for future web meetings
Name | Agency | Title
Ling Sun | CMA | A Fengyun consistent VIRR calibration record for inheritable solar bands
Jing Wang | CMA | Pre-launch analysis of Rapid Scan Imager aboard FY-4B from TVAC test
Tae Hyeong OH | KMA | Lunar calibration of AMI visible channels using GIRO
Eunkyu KIM | KMA | AMI visible calibration results using MODIS and VIIRS
Jae-Hyun AHN | KMA | System vicarious calibration for the Geostationary Ocean Color Imager (GOCI)
Kazuki and Tanaka | JMA | DCC analysis for MTSAT-1R/2 to Himawari-8
Kodera Kazuki | JMA | Ray-matching analysis for Himawari-8
Vincent Leroy | Rayference | Eradiate, a 3D open-source radiative transfer model to support CalVal activities
Sindy Sterckx | VITO | The Belharmony approach for harmonization of PROBA-V, Landsat-8 and Sentinel-2 timeseries
Sindy Sterckx | VITO | Investigation into the impact of in-orbit temperature variation on the PROBA-V Vicarious Calibration Results
Ben Scarino | NASA | SBAF out of band tool feature

## Slide 6: Future proposed VIS/NIR meetings
Follow up VIS/NIR meeting to allow presentations not presented at the annual meeting
Agency ray-matching methodology meeting to compile best practices
Rayleigh scattering methodology meeting joint with the UV group
DCC extension to the NIR and SWIR bands
PICS or Earth invariant target (desert) calibration methodology to compile best practices
Journal paper on the DCC method and to promote DCC method from demonstration to operational mode