## Slide 1: Annual GSICS Calibration Report – Way forward
Masaya Takahashi (JMA), Xiuqing Hu (CMA) and Dohyeong Kim (KMA) with great supports of GRWG members of GEO operating agencies

## Slide 2: Background (1/2)
CGMS member agencies have been reporting their spacecraft status using the same format (text-format document).
We could also make reports for CGMS on instrument performance based on GSICS inter-calibration approaches.

## Slide 3: Background (2/2)
Action at GSICS-EP-18 (2017)
Draft template and report example for GEO imagers
  Developed by GRWG/GDWG and reported at GSICS-EP-19
  EP’s point: information on scene dependent biases (if exists) and accuracies of reference instruments by Double Difference approaches would also be useful
GSICS-EP plans to submit the report to CGMS-47 (May 2019) as
“First Annual State of Global Observing System”
  We need to finalize the report template (contents) for operational GEO imager
Reference | Action Description | Actionee | Due date
EP-18.A03 | GDWG and GRWG to develop an approach for an Annual GSICS report on the State of the Observing System with respect to Instrument Performance and Inter-comparisons with GSICS Reference Instruments | GDWG and GRWG | EP-19 (Jun 2018)

## Slide 4: Concepts of Annual Report (Discussion Points Today)
Target audience: satellite data users + operators (incl. non calibration experts)
Keeping report contents SIMPLE for GSICS members’ minimum efforts
  Satellite/Instrument events relevant to calibration: 1 page for agency
  Radiometric calibration performance for GEO imagers
  1-2 page / instrument Using GSICS inter-calibration approaches
  Table summarizing bias/unc: for one year? snapshot for a certain month of year?
  Time series chart of bias/unc: for one year? days since operation start?
Detailed information: referred to Calibration Landing Page
Adopting existing formats as possible
  Color chart on NOAA satellite status, visualization tools (e.g. GSICS Plotting Tool)
Comments by GSICS-EP
  Scene dependent bias and reference instruments performance by double difference
  Should we (all agencies) include in the report?

## Slide 5
The following slides: 2018 reports for operational GEO imagers – thanks for your cooperation
EUMETSAT (Tim Hewison and Sebatien Wagner)
NOAA (Fred Wu, Fangfang Yu, and Hyelim Yoo)
JMA (Masaya Takahashi, Yusuke Yogo)
KMA (Dohyeong Kim, Minju Gu, and Eunkyu Kim)
ROSHYDROMET (Alexey Rublev and Alexander Uspensky)

## Slide 6: 2018 Annual GSICS Calibration Report for EUMETSAT
Tim Hewison, Sebastien Wagner
EUMETSAT

## Slide 7: Satellite/Instrument Summary - GEO
Satellite (status) |  | Location | Launch date | EO instruments |  |  | 
Meteosat-8 | Op | 41.5 E | 2002-08-28 | SEVIRI | GERB |  | 
Meteosat-9 | B | 3.5 E | 2005-12-21 | SEVIRI | GERB |  | 
Meteosat-10 | RSS | 9.5 E | 2012-07-05 | SEVIRI | GERB |  | 
Meteosat-11 | Op | 0.0 E | 2015-07-15 | SEVIRI | GERB |  | 
Major calibration relevant events in 2018
  2018-02-05/13 Meteosat-11 moved 3.4°W to 0°E
  2018-02-08/27 Meteosat-10 moved 0°E to 9.5°E
  2018-02-21/03-05 Meteosat-9 moved 9.5°E to 3.5°E
  2018-02-20 Meteosat-11 Operational 0° prime
  2018-03-13 Meteosat-10 Operational 9.5°E RSS
  2018-03-13 Meteosat-9 to Backup
  2018-12-03/08 Meteosat-10 Decontamination
  UNS Technical Bulletin
Hyperlinks on instrument names navigate to the Calibration Landing Page
Satellite Status |  | 
 | Op = Operational | 
 | P = Pre-operational | 
 | B = Back-up, secondary | 
 | L = Limited availability | 
Instrument Status |  | 
 |  | Operational (or capable of)
 |  | Operational with limitations (or Standby)
 |  | Operational with Degraded Performance
 |  | Not Operational
 |  | Functional, Turned Off

## Slide 8: Meteosat Data Availability

## Slide 9
Channel Name |  | VIS0.6 | VIS0.8 | NIR1.6 | HRV | Units
Meteosat-8 | Mean Bias (DCC-SSCC) | +13.6 ± 2.5 |  |  |  | %
 | Annual Drift (DCC) | -0.54 ± 0.08 |  |  |  | %/yr
 | Annual Drift (SSCC) | -0.56 ± 0.03 | -0.55 ± 0.03 | -0.04 ± 0.03 | -0.52 ± 0.03 | %/yr
 | Annual Drift (LCS) | -0.57 ± 0.01 | -0.53 ± 0.01 | -0.02 ± 0.02 | -0.55 ± 0.02 | %/yr
Meteosat-9 | Annual Drift (SSCC) | -0.54 ± 0.08 | -0.57 ± 0.07 | -0.04 ± 0.07 | -0.55 ± 0.08 | %/yr
 | Annual Drift (LCS) | -0.57 ± 0.01 | -0.52 ± 0.01 | -0.06 ± 0.03 | -0.52 ± 0.03 | %/yr
Meteosat-10 | Annual Drift (SSCC) | -0.66 ± 0.14 | -0.63 ± 0.11 | -0.02 ± 0.11 | -0.71 ± 0.12 | %/yr
 | Annual Drift (LCS) | -0.84 ± 0.03 | -0.71 ± 0.02 | -0.01 ± 0.08 | -0.98 ± 0.08 | %/yr
Meteosat-11 | Mean Bias (DCC-SSCC) | +10.0 ± 0.8 |  |  |  | %
 | Annual Drift (DCC) | -0.13 ± 0.11 |  |  |  | %/yr
 | Annual Drift (SSCC) | -0.30 ± 0.38 | -0.25 ± 0.36 | -0.08 ± 0.34 | -0.32 ± 0.36 | %/yr
 | Annual Drift (LCS) | -0.60 ± 0.07 | -0.42 ± 0.05 | +1.18 ± 0.20 | -0.75 ± 0.08 | %/yr
Summary Statistics of Meteosat/SEVIRI VIS/NIR Calibration Performance (All Uncertainties are k=1)
Calibration Performance: Meteosat/SEVIRI Visible Bands
Mean Bias: Mean and SD of difference of DCC from operational (SSCC) calibration for all 2018 pentad results
Annual Drift: Mean gain drift and uncertainty calculated from DCC and operational (SSCC) over each satellite life
DCC: Demonstration GSICS Deep Convective Cloud inter-calibration, with respect to Aqua/MODIS
SSCC: SEVIRI Solar Channel Calibration System = vicarious calibration used operationally for SEVIRI

## Slide 10
Mean Bias: Mean and SD of difference of DCC from operational (SSCC) calibration for all 2018 pentad results
Annual Drift: Mean gain drift and uncertainty calculated from DCC and operational (SSCC) over each satellite life
DCC: Demonstration GSICS Deep Convective Cloud inter-calibration, with respect to Aqua/MODIS
SSCC: SEVIRI Solar Channel Calibration System = vicarious calibration used operationally for SEVIRI
Calibration Performance: Meteosat/SEVIRI Visible Bands
Time Series of gains derived for Meteosat-8 (MSG1) and -11 (MSG4) VIS0.6 channel SSCC (red), DCC (green).

## Slide 11
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.57 | -0.16 | +0.35 | +0.00 | -0.07 | +0.04 | +0.01 | +0.37
Standard Deviation of Bias (K) | 0.03 | 0.05 | 0.06 | 0.05 | 0.07 | 0.03 | 0.03 | 0.08
Mean Drift Rate of Bias (K/yr) | -0.05 | -0.11 | -0.12 | -0.05 | -0.18 | -0.05 | -0.05 | -0.21
Summary Statistics of Meteosat-8/SEVIRI IR Calibration Performance in 2018 (All uncertainties are k=1)
The statistics are derived from Meteosat-8/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-A/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Decontaminations introduce calibration jumps – most obvious in the IR13.4 channel due to ice contamination
Calibration Performance: Meteosat-8/SEVIRI IR Bands
Time series of Meteosat-8/SEVIRI Tb biases w.r.t. Metop-A/IASI at standard radiance

## Slide 12
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.21 | -0.14 | +0.07 | -0.01 | -0.03 | +0.02 | +0.00 | -1.55
Standard Deviation of Bias (K) | 0.08 | 0.17 | 0.30 | 0.07 | 0.20 | 0.04 | 0.05 | 0.16
Mean Drift Rate of Bias (K/yr) | -0.21 | -0.42 | -0.63 | -0.09 | -0.40 | -0.07 | -0.08 | -0.35
Summary Statistics of Meteosat-9/SEVIRI IR Calibration Performance in 2018 (All uncertainties are k=1)
The statistics are derived from Meteosat-9/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-A/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Meteosat-9 operated in Rapid Scan Service during most of this period, which increases the bias uncertainties
Calibration Performance: Meteosat-9/SEVIRI IR Bands
Time series of Meteosat-9/SEVIRI Tb biases w.r.t. Metop-A/IASI at standard radiance

## Slide 13
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.10 | -0.30 | +0.21 | +0.04 | +0.05 | +0.01 | +0.02 | -1.94
Standard Deviation of Bias (K) | 0.10 | 0.05 | 0.13 | 0.12 | 0.15 | 0.06 | 0.05 | 0.41
Mean Drift Rate of Bias (K/yr) | +0.07 | -0.07 | +0.11 | +0.05 | -0.02 | -0.00 | -0.05 | +0.22
Summary Statistics of Meteosat-10/SEVIRI IR Calibration Performance in 2018 (All uncertainties are k=1)
The statistics are derived from Meteosat-10/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-A/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Decontaminations introduce calibration jumps – most obvious in the IR13.4 channel due to ice contamination
Calibration Performance: Meteosat-10/SEVIRI IR Bands
Time series of Meteosat-10/SEVIRI Tb biases w.r.t. Metop-A/IASI at standard radiance

## Slide 14
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.03 | -0.06 | +0.22 | +0.00 | +0.17 | +0.09 | -0.03 | -0.22
Standard Deviation of Bias (K) | 0.01 | 0.05 | 0.04 | 0.07 | 0.04 | 0.04 | 0.03 | 0.17
Mean Drift Rate of Bias (K/yr) | -0.01 | +0.11 | -0.05 | +0.01 | +0.04 | -0.01 | -0.01 | -0.58
Summary Statistics of Meteosat-10/SEVIRI IR Calibration Performance in 2018 (All uncertainties are k=1)
The statistics are derived from Meteosat-11/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-A/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Decontaminations introduce calibration jumps – most obvious in the IR13.4 channel due to ice contamination
Calibration Performance: Meteosat-11/SEVIRI IR Bands
Time series of Meteosat-11/SEVIRI Tb biases w.r.t. Metop-A/IASI at standard radiance

## Slide 15: 2018 Annual GSICS Calibration Report for NOAA
Fred Wu, Fangfang Yu, and Hyelim Yoo
NOAA

## Slide 16: Satellite/Instrument Summary - GEO
Satellite (status) |  | Current Location | Launch Date | Operation Date
GOES-15* | (Op) | 128W | 2010-03-04 | 2011-12-06
GOES-16 | (Op) | 75.2W (GOES-East) | 2016-11-19 | 2017-12-18
GOES-17 | (Op) | 137.2W (GOES-West) | 2018-03-01 | 2019-02-12
http://planet.rssi.ru
GOES-16/17 ABI Calibration Event Log:
https://www.star.nesdis.noaa.gov/GOESCal/goes_SatelliteAnomalies.php
* GOES-15 drifted from 135W on 2018-10-23 and arrived the new operating location of 128W on 2018-11-07. GOES-17 and GOES-15 will operate in tandem for 6 months from their respective locations of 137.2W and 128W.

## Slide 17
 | Channel Name (Central Wavelength in m) | BAND07 (3.9) | BAND08 (6.2) | BAND09 (6.9) | BAND10 (7.3) | BAND11 (8.6) | BAND12 (9.6) | BAND13 (10.4) | BAND14 (11.2) | BAND15 (12.4) | BAND16 (13.3)
 | Std. Scene Tb (K) | 286.0 | 234.5 | 244.0 | 254.5 | 284.0 | 259.5 | 286.0 | 286.0 | 283.5 | 269.5
Metop-A/ IASI | Bias at Std. Scene(K) | -0.03 | -0.11 | -0.12 | -0.05 | -0.05 | -0.05 | -0.03 | 0.04 | 0.03 | -0.10
 | Stdv. of Bias (K) | 0.08 | 0.06 | 0.07 | 0.08 | 0.11 | 0.08 | 0.12 | 0.12 | 0.12 | 0.12
Metop-B/ IASI | Bias at Std. Scene(K) | -0.00 | -0.12 | -0.14 | -0.07 | -0.04 | -0.10 | -0.02 | 0.05 | 0.03 | -0.12
 | Stdv. of Bias (K) | 0.18 | 0.13 | 0.08 | 0.09 | 0.19 | 0.13 | 0.21 | 0.21 | 0.22 | 0.20
S-NPP/ CrIS | Bias at Std. Scene(K) | - | - | -0.14 | -0.09 | - | -0.05 | -0.07 | -0.01 | -0.03 | -0.15
 | Stdv of Bias (K) | - | - | 0.03 | 0.04 | - | 0.04 | 0.06 | 0.06 | 0.07 | 0.06
NOAA-20/ CrIS | Bias at Std. Scene(K) | - | - | -0.11 | -0.06 | - | -0.04 | -0.01 | 0.05 | 0.03 | -0.11
 | Stdv of Bias (K) | - | - | 0.03 | 0.03 | - | 0.04 | 0.06 | 0.06 | 0.06 | 0.07
Summary Statistics of GOES-16/ABI IR Calibration Performance in December 2018 (All uncertainties are k=1)
Calibration Performance: GOES16/ABI Infrared Bands
GOES-16 ABI IR calibration is very stable.
The mean Tb bias to CrIS/IASI less than 0.15K after the operational update on 06/19/2018.
No significant scene dependent Tb bias to the reference instruments for all the IR channels
Metop-B/IASI update
G16 ABI updates

## Slide 18
Reference Instrument Performance: Double Difference Using G16 ABI as the Transfer
N20/CrIS, NPP/CrIS, Metop-A/IASI and Metop-B/IASI are all stable within the study period.
The calibration difference is less than 0.1K among the four reference instruments
N20/CrIS is slightly warmer than NPP/CrIS.
Double Difference between N20 and NPP CrIS
Double Difference between NPP/CrIS and IASI-B
Double Difference between IASIA and IASIB
N20/CrIS is slightly warmer than NPP/CrIS
Metop-A/IASI and Metop-B/IASI is in general within ~±0.05K
Metop-B/IASI and SNPP/CrIS is in general within ~±0.1K

## Slide 19: 2018 Annual GSICS Calibration Report for JMA
Masaya Takahashi, Yusuke Yogo
Japan Meteorological Agency

## Slide 20: Satellite/Instrument Summary - GEO
Satellite Status |  | 
 | Op = Operational | 
 | P = Pre-operational | 
 | B = Back-up, secondary | 
 | L = Limited availability | 
Instrument Status |  | 
 |  | Operational (or capable of)
 |  | Operational with limitations (or Standby)
 |  | Operational with Degraded Performance
 |  | Not Operational
 |  | Functional, Turned Off
Satellite (status) |  | Location | Launch date | EO instruments |  |  | 
Himawari-8 | (Op) | 140.7 E | 2014-10-07 | AHI |  |  | 
Himawari-9 | (B) | 140.7 E | 2016-11-02 | AHI |  |  | 
Major calibration relevant events in 2018
  2018-02-14: Himawari-8 maintenance (backup operation by Himawari-9 for about 2 days)
Hyperlinks on instrument names navigate to the Calibration Landing Page

## Slide 21
Channel Name (Central Wavelength in m) |  | BAND01 (0.47) | BAND02 (0.51) | BAND03 (0.64) | BAND04 (0.86) | BAND05 (1.6) | BAND06 (2.3) | Units
Ray-matching w/ S-NPP/VIIRS | Mean Bias | -3.6 ± 2.6 | -2.0 ± 1.6 | +1.1 ± 2.1 | -0.4 ± 1.8 | +5.8 ± 1.2 | -5.5 ± 1.5 | %
 | Annual Drift | -0.38 ± 0.08 | -0.50 ± 0.07 | -0.77 ± 0.05 | -0.57 ± 0.04 | -0.22 ± 0.07 | -0.23 ± 0.05 | %/yr
Vicarious Cal. using Aqua/MODIS + RTM | Mean Bias | -1.1 ± 1.6 | -2.3 ± 1.6 | +0.51 ± 1.7 | +1.6 ± 1.6 | +4.4 ± 0.9 | -4.1 ± 1.0 | %
 | Annual Drift | -0.48 ± 0.10 | -0.68 ± 0.10 | -1.04 ± 0.10 | -0.86 ± 0.10 | -0.20 ± 0.07 | -0.17 ± 0.10 | %/yr
Summary Statistics of Himawari-8/AHI VNIR Calibration Performance (All Uncertainties are k=1)
Mean Bias: monthly average and standard deviation of the daily results in January 2018
Annual Drift: calculated using Mean Bias from July 2015 to January 2019
Ray-matching: Spectral Band Adjustment Factors on NASA Langley website compensates Spectral diff. (ATBD)
Vicarious calibration uses optical parameters retrieved from Aqua/MODIS C6 L1B (Reference)
Calibration Performance: Himawari-8/AHI VIS/NIR Bands
BAND03 (0.64 μm)
BAND05 (1.6 μm)
Trend of the ratio of observation to reference computed using Ray-matching / Vicarious calibration approaches
BAND01 (0.47 μm)

## Slide 22
 | Channel Name (Central Wavelength in m) | BAND07 (3.9) | BAND08 (6.2) | BAND09 (6.9) | BAND10 (7.3) | BAND11 (8.6) | BAND12 (9.6) | BAND13 (10.4) | BAND14 (11.2) | BAND15 (12.4) | BAND16 (13.3)
 | Std. Radiance as Tb (K) | 286.0 | 234.6 | 243.9 | 254.6 | 283.8 | 259.5 | 286.2 | 286.1 | 283.8 | 269.7
Metop-A/ IASI | Mean Bias (K) | -0.149 | -0.184 | -0.223 | -0.127 | -0.062 | -0.239 | 0.036 | 0.047 | -0.036 | 0.106
 | Stdv. of Bias (K) | 0.006 | 0.009 | 0.008 | 0.020 | 0.012 | 0.012 | 0.020 | 0.020 | 0.017 | 0.016
S-NPP/ CrIS | Mean Bias (K) | -0.223 | -0.163 | -0.245 | -0.152 | N/A | -0.249 | -0.019 | -0.012 | -0.0097 | 0.039
 | Stdv/ of Bias (K) | 0.438 | 0.015 | 0.021 | 0.040 | N/A | 0.010 | 0.017 | 0.017 | 0.019 | 0.017
Summary Statistics of Himawari-8/AHI IR Calibration Performance in 2018 (All uncertainties are k=1)
The statistics are derived from Himawari-8/AHI GSICS Re-Analysis Correction (ATBD)
Standard Radiance: typical scene defined by GSICS for easy inter-comparison of sensors’ inter-calibration biases
Calibration Performance: Himawari-8/AHI Infrared Bands
Time series of Himawari-8/AHI Tb biases w.r.t. Metop-A/IASI at std. radiance

## Slide 23: 2018 Annual GSICS Calibration Report for KMA
Dohyeong Kim, Minju Gu, and Eunkyu Kim
Korea Meteorological Administration

## Slide 24: Satellite/Instrument Summary - GEO
Satellite Status |  | 
 | Op = Operational | 
 | P = Pre-operational | 
 | B = Back-up, secondary | 
 | L = Limited availability | 
Instrument Status |  | 
 |  | Operational (or capable of)
 |  | Operational with limitations (or Standby)
 |  | Operational with Degraded Performance
 |  | Not Operational
 |  | Functional, Turned Off
Satellite (status) |  | Location | Launch date | EO instruments |  |  | 
COMS | (Op) | 128.2E | 2010-06-26 | MI |  |  | 
GK-2A | (P) | 128.2 E | 2018-12-04 | AMI |  |  | 
Major calibration relevant events in 2018
  2018-08-31 : relocation of COMS for preparation of GK-2A/2B collocation
  2018-12-04 : launch and start of commissioning GK-2A
Hyperlinks on instrument names navigate to the Calibration Landing Page

## Slide 25
Channel Name |  | Visible (0.675μm)
Ray-matching (DCC) / MODIS(Terra) | Mean Bias[%] | -12.7 ± 5.5
 | Annual Drift[%/yr] | -1.60 ± 0.12
KMA DCC / RTM(SBDART) | Mean Bias[%] | -12.0 ± 6.5
 | Annual Drift[%/yr] | -1.30 ± 0.10
GSICS DCC / MODIS(Aqua) | Mean Bias[%] | -14.7 ± 9.2
 | Annual Drift[%/yr] | -1.38 ± 0.16
Calibration Performance: COMS/MI Visible Band
Summary Statistics of COMS/MI VIS Calibration Performance from 2011 to 2018 (All uncertainties are k=1)
Mean Bias: monthly average and standard deviation of the daily results from April 2011 to December 2018.
Annual Drift: calculated using Mean Bias from April 2011 to December 2018.
Ray-matching: GEO-LEO Inter-calibration method using MI(COMS) and MODIS(Terra) based on DCC condition
KMA DCC: Comparison MI and RTM(SBDART).
GSICS DCC: Using Hu BRDF Model.
Trend of the ratio of observation to reference computed using Ray-matching / KMA DCC / GSICS DCC approaches

## Slide 26
Calibration Performance: COMS/MI Infrared Bands
Summary Statistics of COMS/MI IR Calibration Performance in 2018 (All uncertainties are k=1)
The statistics are derived from COMS/MI Operational GSICS Re-Analysis Correction vs. Metop-A/IASI, Metop-B/IASI, Aqua/AIRS, SNPP/CrIS
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
 | MetOp-A/IASI |  |  |  | MetOp-B/IASI |  |  | 
Channel Name | IR3.8 | IR6.8 | IR10.8 | IR12.0 | IR3.8 | IR6.8 | IR10.8 | IR12.0
Std Rad as Tb (K) | 286 | 238 | 286 | 285 | 286 | 238 | 286 | 285
Mean Bias (K) | 0.16 | -0.03 | 0.15 | 0.03 | 0.18 | -0.03 | 0.10 | -0.01
Stdv of Bias (K) | 0.03 | 0.05 | 0.05 | 0.03 | 0.03 | 0.04 | 0.05 | 0.03
Mean Drift Rate of Bias (K/yr) | +0.18 | -0.05 | +0.16 | +0.05 | +0.17 | -0.04 | +0.05 | -0.04
 | Snpp/CrIS |  |  |  | Aqua/AIRS |  |  | 
Channel Name | IR3.8 | IR6.8 | IR10.8 | IR12.0 | IR3.8 | IR6.8 | IR10.8 | IR12.0
Std Rad as Tb (K) | 286 | 238 | 286 | 285 | 286 | 238 | 286 | 285
Mean Bias (K) | - | -0.20 | -0.02 | -0.02 | -0.19 | -0.29 | 0.02 | 0.04
Stdv of Bias (K) | - | 0.10 | 0.13 | 0.08 | 0.06 | 0.09 | 0.15 | 0.09
Mean Drift Rate of Bias (K/yr) | - | -0.19 | -0.04 | -0.03 | -0.18 | -0.29 | -0.01 | +0.02

## Slide 27: 2018 Annual GSICS Calibration Report for ROSHYDROMET
Alexey Rublev, Alexander Uspensky
ROSHYDROMET

## Slide 28
Satellite/Instrument Summary - LEO

## Slide 29
Calibration Performance: MSU-MR
IR channels vs SEVIRI/Meteosat-10 (-11)
Shortwave channels vs AVHRR/Metop-A
N= 1,2,3, A—the spectral brightness coefficient
Calculated SBAF for reflectance between MSU-MR and AVHRR ̴1.0 for each pair of channels

## Slide 30
Satellite/Instrument Summary - GEO
The MSU-GS instrument is functional with limitations (12 m channel is absent).
Absolute calibration is completing.

## Slide 31
Calibration Performance of MSU-GS: Visible/Near-Infrared Channels
Inter-calibration of MSU-GS shortwaves channels
versus the VIIRS/Suomi NPP
Comparison above
deep convective clouds
over the Indian Ocean
± 20° North/South and East/West of Elektro-L #2 sub-satellite point (76E)
Calculated SBAF between
MSU-GS and VIIRS ~1.0
for each pair of channels

## Slide 32: Concepts of Annual Report (Discussion Points Today)
Target audience: satellite data users + operators (incl. non calibration experts)
Keeping report contents SIMPLE for GSICS members’ minimum efforts
  Satellite/Instrument events relevant to calibration: 1 page for agency
  Radiometric calibration performance for GEO imagers
  1-2 page / instrument Using GSICS inter-calibration approaches
  Table summarizing bias/unc: for one year? snapshot for a certain month of year?
  Time series chart of bias/unc: for one year? days since operation start?
Detailed information: referred to Calibration Landing Page
Adopting existing formats as possible
  Color chart on NOAA satellite status, visualization tools (e.g. GSICS Plotting Tool)
Comments by GSICS-EP
  Scene dependent bias and reference instruments performance by double difference
  Should we (all agencies) include in the report?

## Slide 33: {Year} Annual GSICS Calibration Report
{Name}
{Agency}
Report Template - Proposal

## Slide 34
Satellite (status) |  | Location | Launch date | EO instruments (operation start date) |  | 
{Satlelite#1} | {Status} | {SSP} | YYYY-MM-DD | {Instrument#1} (YYYY-MM-DD) |  | 
{Satellite#2} | {Status} | {SSP} | YYYY-MM-DD | {Instrument#1} (YYYY-MM-DD) | {Instrument#2} (YYYY-MM-DD) | 
Major calibration relevant events in {Year}
  YYYY-MM-DD: XXXXXXXX
  YYYY-MM-DD: YYYYYYYY
Satellite Status |  | 
 | Op = Operational RSS = Rapid Scanning Service | 
 | P = Pre-operational | 
 | B = Back-up, secondary | 
 | L = Limited availability | 
Instrument Status |  | 
 |  | Operational (or capable of)
 |  | Operational with limitations (or Standby)
 |  | Operational with Degraded Performance
 |  | Not Operational
 |  | Functional, Turned Off
{Year} Satellite/Instrument Summary
Please add hyperlinks over instrument names which navigate to agency’s Calibration Landing Page
Legends for satellite/instrument status
Report Template - Proposal

## Slide 35
Reference: {Satellite}/{Instrument} | Channel Name (m) | CH XX (XXX) | CH XX (XXX) |  |  |  |  | Units
{Method#1} | Mean Bias (unc.) |  |  |  |  |  |  | 
 | Annual Drift (unc.) |  |  |  |  |  |  | 
{Method#2} | Mean Bias (unc.) |  |  |  |  |  |  | 
 | Annual Drift (unc.) |  |  |  |  |  |  | 
Summary Stats of {Satellite}/{Instrument} VIS/NIR Calibration Performance in {Year}
Stats derived from {Satellite}/{Instrument} GSICS Re-Analysis Correction ( {Link to ATBD} )
{Description on inter-calibration methods#1}
{Description on inter-calibration methods#2}
{Notes on validation results (if any) }
(All uncertainties are k=1)
Report Template for VIS/NIR - Proposal
Monitored Instrument Gain
[W/m2/sr/um]
Time series of gains derived for {Satellite}/{Instrument} CH XXX w.r.t. {Reference}

## Slide 36
 | Channel Name (m) | CH XX (XXX) | CH XX (XXX) |  |  |  |  |  |  |  | 
 | Std. Rad. as Tb (K) |  |  |  |  |  |  |  |  |  | 
{Reference#1} | Mean Bias (K) |  |  |  |  |  |  |  |  |  | 
 | Stdv. of Bias (K) |  |  |  |  |  |  |  |  |  | 
{Reference#2} | Mean Bias (K) |  |  |  |  |  |  |  |  |  | 
 | Stdv. of Bias (K) |  |  |  |  |  |  |  |  |  | 
Summary Stats of {Satellite}/{Instrument} IR Calibration Performance in {Year}
Stats derived from {Satellite}/{Instrument} GSICS Re-Analysis Correction ( {Link to ATBD} )
Standard Radiance: typical scene defined by GSICS for easy inter-comparison of sensors’ inter-calibration biases
{Notes on validation results (if any) }
(All uncertainties are k=1)
Report Template for IR - Proposal
Time series of {Satellite}/{Instrument} Tb biases w.r.t. {Reference} at std. radiance