## Slide 1: Review of atmospheric radiative transfer models suitable for vicarious calibration
2019 GSICS Data and Research Working Groups Annual Meeting
Yves Govaerts & Vincent Leroy
Rayference
ESRIN, Frascati, 4 – 8 March 2019

## Slide 2: Overview
Radiative transfer models play a critical role for vicarious calibration;
Instruments like S2/MSI have proven to have a radiometric accuracy close to 2-3%;
What is the expected simulation accuracy with current 1D RTMs over CEOS calibration sites: 1%, 3% or 5%?
    RTM numerical accuracy
    Input parameter accuracy
Notes: Target of choice: water – appears dark in all 8 bands Sentinel 2 doesn’t make observations over open waters Open waters may appear too dark Coastal waters may appear brighter due to the presence of suspended matter
2

## Slide 3: Concept
Physics is based on two fundamental pillars
OBSERVATION
THEORY

## Slide 4: Concept
Physics is based on two fundamental pillars
OBSERVATION
THEORY
MEASUREMENT DEVICE
MATHEMATICAL MODEL

## Slide 5: Concept
Physics is based on two fundamental pillars
OBSERVATION
THEORY
SATELLITE RADIOMETER
RADIATIVE TRANSFER MODEL

## Slide 6: Experimental Setup
Acquisition of TOA BRF over Libya-4 acquired by (PICSCAR)
  Envisat/MERIS
  AQUA/MODIS
  S2A/MSI
  L8/OLI
Simulation of these TOA BRFs with 3 different RTMs fed with the same surface and aerosol properties (Govaerts et al., 2004, 2013)
Estimation of the mean bias between observation and simulation
Code | RTE solver | Gas | Surface | Aerosol
6S-V | Successive order | Hitran96 | RPV 4P | Customised
LibradtranV2 | Monte Carlo | Hitran2012 | RPV 4P | Customised
RTMOM | Matrix Operator | Hitran96 | RPV 4P | Customised

## Slide 7: S2A/MSI
All SZA values

## Slide 8: S2A/MSI

## Slide 9: S2A/MSI

## Slide 10: S2A/MSI
All SZA values

## Slide 11: L8/OLI
All SZA values

## Slide 12: S2A/MSI
All SZA values

## Slide 13: L8/OLI

## Slide 14
ZSA < 30
SIXS-V
Libradtran
RTMOM
MERIS 412 band

## Slide 15
ZSA < 30
SIXS-V
Libradtran
MERIS 885 band
RTMOM

## Slide 16: Typical RTM functionalities
Man-Machine Interface
Collects the input information concerning the
Spectral range and resolution;
Atmospheric vertical composition;
Cloud and aerosol concentration;
Surface properties;
Type of “measurements”
  Up/down
  Flux, radiance reflectance transmittance
  Elevation

## Slide 17: Typical RTM functionalities
Driver
Converts the input information into data that can be understood by the RTE solver at a given wavelength, i.e. for each atmospheric layer:
The phase function
The single scattering albedo
The molecular transmittances
It provides the lower boundary conditions.
It also performs the vertical rescaling of molecular concentration if needed.

## Slide 18: Typical RTM functionalities
Driver
Converts the input information into data that can be understood by the RTE solver at a given wavelength, i.e. for each atmospheric layer:
The phase function
The single scattering albedo
The molecular transmittances
The lower boundary conditions (if needed)
It also performs the vertical rescaling of molecular concentration if needed.
RTMs without a versatile Driver should not be considered for operational vicarious calibration because there are too cumbersome to operate.

## Slide 19: Typical RTM functionalities
RTE Solver
Solves the radiative transfer equation in each scattering element (e.g. atmospheric layers) with a specific numerical methods:
Successive Order of Scattering
Discrete ordinate
Adding/doubling
Matrix Operator
Spherical harmonic
Monte Carlo

## Slide 20: Review of existing models
1D plane parallel atmosphere
  Vertical structure of the atmosphere
  No 3D cloud effects (e.g. for DCC)
  Only flat surface
  Not accurate for large sun and viewing angles because of the plane parallel approximation.
3D plane parallel atmosphere
  The atmosphere is divided into regular voxels
  Each voxel might have different optical properties
  RTE solver : discrete ordinate or Monte Carlo

## Slide 21: Toward a 1% RTM accuracy
Surface BRF : accounting for topography (e.g., oriented sand dunes);
Molecular absorption: account for species like O4;
Rigorous calculation of the coupling between:
  Surface reflectance and atmosphere scattering;
  Aerosol scattering and molecular absorption;
Polarization, non flat earth for large zenith angles;
Improvement of the surface and atmospheric property characterization;

## Slide 22: The Eradiate RTM
New open source 3D RTM specifically dedicated to Cal/Val activities;
Based on most advanced 3D Monte Carlo Ray Tracing rendering techniques;
Not limited to only one (atmospheric) community;
Will include 3D representation of land / ocean / atmospheric / cryosphere in a single framework;
Will allow the simulation of
  BRF field at the infinity;
  Satellite images;
  Ground observations.

## Slide 23: Development Phases

## Slide 24: Phase 1 : Planned Scene Elements
1D Atmosphere
  Plane-parallel (“flat-Earth”)
  Layered spheroids (“round-Earth”)
Surface
  Standard empirical BRF models (e.g. RPV, Ross-Li, Hapke)
  Microfacet models (e.g. semi-discrete, Oren-Nayar, Torrance-Sparrow, Cox-Munk)
  Including parameter texturing
  3D scenes with detailed typography and objects (e.g. Libya-4, RadCalNet, Dome-C, …)
Illumination
  Infinitely distant collimated
  Finite-size solar disc (uncollimated)
Sensors
  Flux & radiance meters
  Ideal detector (pinhole camera)
  BRF at finite or infinite distance

## Slide 25: The Eradiate RTM
www.eradiate.eu
Please register to the Eradiate newsletter (under contact) to be updated on Eradiate latest developments.
Yearly Eradiate workshops are organised at the JRC, Ispra site (IT). The next (third) one will take place on Nov 26th - 27th 2019 (save the date!).
Our sponsors (for this presentation)