## Slide 1: KMA GSICS Agency Report 2022
Jiyoung Kim,
Eunkyu Kim, and Minju Gu
KMA/NMSC

## Slide 2: Presentation Overview
Summary of Agency’s GSICS Activities, Actions, and Achievements
Agency’s Support to GDWG Activities
Agency’s Support to GRWG Activities
Agency’s Calibration Stand-up Items

## Slide 3: Summary of KMA’s GSICS Activities, Actions, and Achievements
Current Status of KMA activities
  Generation of GSICS product for IR
    Demonstration phase of GK2A/AMI IR channel with IASI/CrIS for NRTC and RAC
  GK2A AMI lunar calibration for 6 VIS/NIR channel
Achievements Summary
  Develop the additional satellite (NOAA-20/VIIRS) for ray matching method and DCC based NASA algorithm in VNIR calibration

## Slide 4: Support to GDWG Activities
Summary of the tasks of KMA’s supports in the GDWG
  Set up and operate a GitHub project for GDWG activities
  Building a plotting tool development environments in KMA
  Review GPRC websites
Overview of the resources and time taken for this support
  Eunkyu Kim

## Slide 5
Summary of the tasks of KMA’s supports in the GRWG
  Monitoring of GEO-LEO using MetOp-B, -C/IASI, SNPP and NOAA20/CrIS for IR
    Application of gap-filling method to inter-calibrate with CrIS
    Demonstration phase for NRTC and RAC data (MetOp-B, -C/IASI, SNPP and NOAA20/CrIS)
  Develop GEO-GEO direct comparison for both IR and visible channel
    Long-term analysis AMI vs AHI (application of SBAF)
  Develop and update calibration approaches
    Lunar calibration
    Ray matching method and GSICS DCC with NOAA-20/VIIRS
Overview of the resources and time taken for this support
  Jiyoung Kim, Eunkyu Kim(VNIR), Minju Gu*(IR)
  * leave of absence
Issues
  GK2A AMI VNIR channels seasonal variation
Support to GRWG Activities

## Slide 6: KMA’s Calibration Stand-up Items (IR)
Reference Satellite |  | Bias (Uncertainty) |  |  |  |  |  |  |  |  | 
 |  | SW038 (3.8㎛) | WV063 (6.3㎛) | WV069 (6.9㎛) | WV073 (7.3㎛) | IR087 (8.7㎛) | IR096 (9.6㎛) | IR105 (10.5㎛) | IR112 (11.2㎛) | IR123 (12.3㎛) | IR133 (13.3㎛)
CrIS | NOAA-20 | 0.01 (±0.06) | 0.06 (±0.02) | -0.13 (±0.02) | -0.01 (±0.01) | 0.06 (±0.06) | -0.01 (±0.02) | 0.08 (±0.03) | 0.08 (±0.03) | 0.06 (±0.02) | -0.03 (±0.02)
 | S-NPP | -0.09 (±0.07) | 0.05 (±0.02) | -0.15 (±0.01) | -0.04 (±0.02) | -0.01 (±0.06) | -0.03 (±0.02) | 0.01 (±0.02) | 0.01 (±0.02) | -0.00 (±0.02) | -0.06 (±0.02)
IASI | Metop-B | 0.01 (±0.09) | 0.05 (±0.03) | -0.13 (±0.02) | -0.00 (±0.02) | -0.00 (±0.03) | -0.12 (±0.03) | 0.04 (±0.03) | 0.04 (±0.02) | 0.03 (±0.02) | -0.08 (±0.03)
 | Metop-C | 0.02 (±0.08) | 0.05 (±0.02) | -0.12 (±0.02) | 0.00 (±0.01) | 0.02 (±0.03) | -0.06 (±0.02) | 0.06 (±0.03) | 0.06 (±0.03) | 0.05 (±0.02) | -0.04 (±0.03)
Standard Temp.(K) |  | 285.9 | 234.9 | 244.1 | 254.5 | 283.7 | 259.1 | 286.1 | 286.0 | 283.8 | 269.4
January - December 2021
IR133

## Slide 7: KMA’s Calibration Stand-up Items (VNIR)
Reference Satellite | Mean Bias (Uncertainty) |  |  |  |  | 
 | VI004 (0.47 μm) | VI005 (0.51 μm) | VI006 (0.64 μm) | VI008 (0.86 μm) | NR013 (1.37 μm) | NR016 (1.61 μm)
NOAA-20/ VIIRS | -2.23 (±1.91) | 2.17 (±1.21) | 4.17 (±1.07) | 2.53 (±1.16) | 2.11 (±0.66) | 9.15 (±0.98)
S-NPP/ VIIRS | -3.59 (±2.11) | -0.39 (±1.06) | 2.13 (±0.95) | 0.62 (±1.00) | -2.26 (±0.69) | 5.39 (±0.93)
Stable radiance histogram over DCC
January - December 2021

## Slide 8: Additional Slides Not Presented
Introduce/Confirm the Agency’s Personnel Supporting GSICS
  GRWG members/GDWG members
  Other Key Agency Personal
Agency’s GSICS activities to be discussed in this joint meeting
  GSICS agenda items that are especially of interest to the agency
  Agency’s activities that may be of interest to the GSICS community

## Slide 9: Introduce the KMA’s Personnel supporting GSICS
EP
Dohyeong Kim
GRWG
Jiyoung Kim, Eunkyu Kim, and Minju Gu*
(*leave of absence)
GDWG
Eunkyu Kim
Member | GRWG | GDWG | GEO-LEO | DCC RTM | Moon | GEO-GEO
Jiyoung Kim (Mr.) | Y |  | Y | Y | Y | Y
Minju Gu (Ms.) | Y |  | Y |  |  | Y
Eunkyu Kim (Mr.) | Y | Y |  | Y | Y | 

## Slide 10: KMA’s GSICS activities to be discussed in this joint meeting
GRWG
  VIS Sub-Group
    GK2A AMI visible calibration results (Eunkyu Kim)