## Slide 1: Validation of a model of the disk-integrated lunar radiance in the thermal ir channels
Presenter: Martin burgdorf, universität hamburg
CrIS observations of Moon: yong cheN, nOOA
Model of moon: Thomas Müller, MPI extraterrestrische physik
HIRS observations of Moon: constanze seibert, esa

## Slide 2: Introduction
Recently models of spectral irradiance of the Moon in vis. And MW spectral range were presented (Kieffer, 2022, Yang & Burgdorf, 2022)
To be complemented with a model for the thermal infrared (Müller et al., 2021)
Many disk-integrated infrared observations of the Moon became available
What use for (inter-)calibration offers such a model?

## Slide 3: Available infrared observations of the moon
Thousands of spectra with CrIS on SNPP and NOAA-20 (3.9 - 4.6, 5.7 – 8.3, 9.1 – 15.4)
123 photometric observations with HIRS on 18 satellites (3.8 - 15, Seibert 2022, master thesis)
248 events with more than half part of the Moon in AHI (Nishiyama et al., 2022)
Many events with the whole Moon in SEVIRI
Observations with IASI…

## Slide 4: Lunar radiance – division by solid angle
Data missing for MW, similar phase angle
… but different observing time matters
Salisbury et al. (1997)

## Slide 5: Comparison of cris with model
Are features real? Not relevant for stability
Modelling of reflected sunlight to be improved?
Salisbury et al. (1997)

## Slide 6: Results from comparing obs. And model
Model in good agreement with SW and MW part of spectrum
The same is true for the comparison with HIRS observations (phase 90, master thesis Seibert)
Possible features in lunar spectrum affect only certain wavelengths
Difference of OBS/MOD = 0.6% - 0.8% for observations one month apart (not LW)
Difference of OBS/MOD = 1.1% for observations more than seven years apart (not LW)
Uncertainty of 1% of a single spectrum, detect calibration trends of a few 10-4/decade
10-4 corresponds to 3 mK at 250 K, smaller than UTH trends

## Slide 7: Cross calibration with geostationary satellites?
Dayside saturated, nightside poor SNR
Observe close to New Moon
Obs/Mod increases with wavenumber (model valid for phase )
AHI has Moon always close to Earth => abs. in atm.
Use planets instead?
Nishiyama et al., (2022)

## Slide 8: Summary and perspectives
A model of the IR irradiance of the disk-integrated Moon is available.
It takes distance of Moon from weather satellite and Sun, phase angle, and center of disk into account.
Agreement with observation checked with two instruments and comparable with vis and MW models.
Well suited for stability check and comparison S-NPP – NOAA-20
Can be shared with GSICS like irradiance models for other wavelengths
Next steps -
  check presence of spectral features in lunar spectrum
  Compare model to IASI spectra of the Moon
  Extend lunar model to larger range of phase angles

## Slide 9: Additional slides (not presented)

## Slide 10: CROSS-TRACK INFRARED SOUNDER SCAN PATTERNS
9 FOVs with 2 sweep directions.
The 9 FOVs form one FOR.
3 wavenumber ranges: 650 – 1095 cm-1, 1210 – 1750 cm-1, 2155 – 2550 cm-1
3 x 3 14 km (0.96IFOV, sampling distance: 16 km.
A typical CrIS lunar event has several observations in two to four FOVs.
From Yong Han et al. (2014)

## Slide 11: Lunar flux density measured with cris
Wiggles in LW (interference?), Christiansen Feature in MW?
Flux received depends on diameter, distance, and phase angle
Salisbury et al. (1997)

## Slide 12: Mercury and venus with ahi at 11.2 microns
Mercury smaller than pixel => gaps/overlaps relevant
Venus larger than AHI pixel, but has atmosphere
Use Venus for inter-calibration (differences)
SEVIRI with Moon for cross-calibration and model tuning
Nishiyama et al., (2022)