## Slide 1: Lunar Reflectance model developed from SELENE/SP data for Lunar Calibration
Toru Kouyama
Supported by SELENE/SP Team
HISUI calibration WG

## Slide 2: SELENE(KAGUYA) and SP
SELENE:
Polar orbit (non sun-synchronous)
Altitude: 100 km
Grand track repeat cycle: ~ 30 days
Mission period: 2007 – 2009 (1.5 years)
Observation with various solar incident angle condition.

## Slide 3: SELENE(KAGUYA) and SP
SP: Spectral Profiler
Sensor type: Spectrometer
Spectral range:
500-2600 nm
Spectral resolution:
6 nm (VNIR 520-960 nm)
8 nm (NIR-SWIR > 900 nm)
Observation swath
500 m

## Slide 4: SELENE(KAGUYA) and SP
SP: Spectral Profiler
http://global.jaxa.jp/press/2007/12/20071214_kaguya_e.html

## Slide 5: SELENE(KAGUYA) and SP
http://l2db.selene.darts.isas.jaxa.jp/index.html.en
At this time, SP Lunar reflectance model has not been distributed from this archive.

## Slide 6: Key persons
Yokota et al., 2011,Icarus, 215, 639-660:
Lunar photometric properties at wavelengths 0.5–1.6 lm acquired by SELENE
Spectral Profiler and their dependency on local albedo and latitudinal zones
PI
横田康弘
Yoshihiro Yokota
松永恒雄
Tsuneo Matsunaga

## Slide 7
Wavelength [nm]
Reflectance
SELENE/SP
Lunar Reflectance map
[Yokota et al., 2011]
Spectral range:
512 – 1650 nm (160 channels)
Δλ = 6 nm(VNIR) & 8 nm (SWIR)
1˚ x 1˚ resolution: published
0.5˚ x 0.5˚: to be published
Also including the lunar surface photometric properties depending on incident, emission and phase angles.
0.5x0.5: Corresponding to ~40 μrad resolution viewing from Earth
@ nadir
Hyper spectral reflectance map
Newkur data

## Slide 8
Model equations
XL: Lunar lambert function
f: Empirical function of phase angle dependencies
After Yokota et al., 2011, Eq (11)
B: Shadow hiding opposition effect
P: Regolith phase function
h, c, g, B0: Model coefficients
Correction terms for Limb darkening effect
Reflectance to be calculated
i: incident angle
e: emission angle
α: phase angle
Notes: c1=-0.019, c2=0.242x10-3, c3=-1.46x10-6

## Slide 9
Model equations
B: Shadow hiding opposition effect
P: Regolith phase function
h, c, g, B0: Model coefficients
After Yokota et al., 2011, Eq (11)
High land, mare and medium albedo
Reflectance to be calculated
XL: Lunar lambert function
f: Empirical function of phase angle dependencies
Correction terms for Limb darkening effect
i: incident angle
e: emission angle
α: phase angle

## Slide 10
Model equations
After Yokota et al., 2011, Eq (11)
B: Shadow hiding opposition effect
P: Regolith phase function
h, c, g, B0: Model coefficients
Reflectance to be calculated
XL: Lunar lambert function
f: Empirical function of phase angle dependencies
Correction terms for Limb darkening effect
i: incident angle
e: emission angle
α: phase angle

## Slide 11
Incident angle
Emission angle
Input geometry data
Estimation of Lunar radiance
Highland, mare and middle albedo region map
Lunar radiance map at the observation time
Reflectance map (30,0,30)
Phase angle at observation timing
+ Solar Irradiance model

## Slide 12
Chart: 
| 0.48 | 0.48399999999999999 | 0.48799999999999999 | 0.49199999999999999 | 0.496 | 0.5 | 0.504 | 0.50800000000000001 | 0.51200000000000001 | 0.51600000000000001 | 0.52 | 0.52400000000000002 | 0.52800000000000002 | 0.53200000000000003 | 0.53600000000000003 | 0.54 | 0.54400000000000004 | 0.54800000000000004 | 0.55200000000000005 | 0.55600000000000005 | 0.56000000000000005 | 0.56399999999999995 | 0.56799999999999995 | 0.57199999999999995 | 0.57599999999999996 | 0.57999999999999996 | 0.58399999999999996 | 0.58799999999999997 | 0.59199999999999997 | 0.59599999999999997 | 0.6 | 0.60399999999999998 | 0.60799999999999998 | 0.61199999999999999 | 0.61599999999999999 | 0.62 | 0.624 | 0.628 | 0.63200000000000001 | 0.63600000000000001 | 0.64 | 0.64400000000000002 | 0.65 | 0.66 | 0.67 | 0.68 | 0.69 | 0.7 | 0.71 | 0.72 | 0.73 | 0.74
Band 1 | 0 | 0.0069 | 0.0078 | 0.0073 | 0.0107 | 0.058 | 0.125 | 0.2911 | 0.4567 | 0.6717 | 0.8392 | 0.9381 | 0.9906 | 1 | 0.9662 | 0.89 | 0.876 | 0.8959 | 0.9029 | 0.9263 | 0.9184 | 0.9387 | 0.9501 | 0.954 | 0.9606 | 0.9528 | 0.9058 | 0.8687 | 0.774 | 0.6795 | 0.5206 | 0.2972 | 0.151 | 0.0918 | 0.052 | 0.0355 | 0.0098 | 0.0046 | 0.0037 | 0.0056 | 0.0037 | 0.0014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Band 2 | 0.0038 | 0.0032 | 0 | 0.0019 | 0.0031 | 0.0006 | 0.005 | 0.0049 | 0.0018 | 0.0136 | 0 | 0.1529 | 0.3429 | 0.5998 | 0.8024 | 0.9709 | 1 | 0.9758 | 0.9696 | 0.975 | 0.943 | 0.9077 | 0.9396 | 0.9426 | 0.9226 | 0.91 | 0.8935 | 0.8427 | 0.8031 | 0.7917 | 0.7702 | 0.7487 | 0.6619 | 0.5544 | 0.4596 | 0.4258 | 0.3708 | 0.2991 | 0.2166 | 0.1247 | 0.0623 | 0.0442 | 0.028 | 0.0118 | 0.0105 | 0.0054 | 0.0041 | 0.0007 | 0 | 0 | 0 | 0
Band 3N | 0.0022 | 0 | 0.0093 | 0.0258 | 0.048 | 0.0509 | 0.098 | 0.1907 | 0.3353 | 0.6379 | 1 | 0.9786 | 0.8982 | 0.9148 | 0.9778 | 0.9942 | 0.9783 | 0.9624 | 0.9355 | 0.9713 | 0.982 | 0.9976 | 0.9895 | 0.9751 | 0.9874 | 0.9694 | 0.9542 | 0.9489 | 0.9247 | 0.9609 | 0.9489 | 0.942 | 0.9297 | 0.8366 | 0.6943 | 0.4813 | 0.2958 | 0.1763 | 0.09 | 0.0547 | 0.0318 | 0.0258 | 0.0204 | 0.0075 | 0.0074 | 0.0049 | 0.0024 | 0.0024 | 0 | 0 | 0 | 0
SRF convolution
Simulated hyperspectral images
Simulated band image

## Slide 13
Observed
ASTER/Band 2 (660 nm)
April 14, 2003
Simulated

## Slide 14
April 13, 2003
April 15
April 18
Simulating Moon observations

## Slide 15
Band 1
Observed radiance
(W/m2/μm/str)
Frequency
Brightness Comparison: ASTER vs SELENE/SP
Band 2
Band 3N
Simulated radiance (W/m2/μm/str)
 | Band 1 | Band 2 | Band 3
Observed / Simulated (= Bias) | 1.20 | 1.01 | 0.95
Correlation Coefficient | 0.992 | 0.993 | 0.993
Standard deviation | 0.03 | 0.03 | 0.04
Standard error | 0.0002 | 0.0002 | 0.0002

## Slide 16
Known problems
Large bias
Worse model accuracy in high emission angle and high latitude regions
This model requires estimating where each pixel looks at on the moon surface (= LOS ray tracing).
=> Pixel registration error should be considered.
In SP observation, emission angle was basically ~0 degree because of nadir viewing.
Yokota recommends using only the region where emission angle is less than 45 degrees.
Model
ASTER

## Slide 17
Summary
Lunar reflectance model based on SELENE/SP hyper-spectral data has been developed. Using the model, we can simulate/predict any moon observation.
This model describes surface contrast and phase angle dependencies well.
=> The model can be used for evaluating relative degradations of sensors.
Large brightness bias exits.
Some limitations (emission angle and latitude dependences, etc..) should be considered.
Collaboration of ROLO/GIRO is very important
phase angle dependence, bias, etc..

## Slide 20
Modeled radiance (W m-2 str-1 μm-1)
Observed radiance (W m-2 str-1 μm-1)
ASTER (Band 1) Large bias
Observed / Model
Relative Frequency
Mean (Obseｒved/Model) = 1.20
SD = 0.04
SE (= SD/√Number of pixels used) = 0.0002
ASTER@2003.04.14 vs Model (SELENE/SP)

## Slide 21
In shorter wavelength region, SP tends to describe Moon reflectance darker than other sensors
(Ohtake et al., 2010 & 2013)
Ohtake,M. et al., Deriving the Absolute Reflectance of Lunar Surface Using SELENE (Kaguya) Multiband Imager Data, 2010, Space Sci. Rev., 154, 57-77
Ohtake,M. et al., One Moon, Many Measurements 3: Spectral reflectance, 2013, Icarus., 226, 364-374
SP’s reflectance

## Slide 22
Hyperspectral Imager
Multispectral Imager
HISUI
Panchromatic
Stereo Camera
ALOS-3
(JAXA)
Hyperspectral
Image “Cube”
The hyperspectral imager:
Contiguous and high resolution spectral information from visible to short-wave IR
The multispectral imager:
4 Bands observation with a high spatial resolution by a wide swath

## Slide 23
Band 1
Band 2
Band 3
1.0
0.7
0.9
0.8
0
3000
Day since launch

## Slide 24
[Kouyama et al., 2014, LPSC]

## Slide 25
April 13, 2003
April 15
April 18
Simulating Moon observations

## Slide 26
Model equations
r: reflectance using i=30, e=0, α=30 as the basis condition [Yokota et al.,2011] (11)
i: incident, e: emission, α: phase anlge
Fsun: Sun light Flux (W/m2/um)
S: SRF
From SP model
f: Empirical function of phase angle dependencies
XL: Empirical function of sun-light scattering

## Slide 27: Hayabusa-2
Japanese satellite for exploring a small asteroid
Successfully launched Yesterday !