## Slide 1: Inter-Sensor Comparison for Soumi NPP CrIS
Likun Wang1, Yong Han2*, Denis Tremblay3, Fuzhong Weng2, and Mitch Goldberg4
1. CICS/ESSIC/University of Maryland, College Park, MD; wlikun@umd.edu
2. NOAA/NESDIS/STAR, College Park, MD
3. Earth Resources Technology, Inc., Laurel, MD
4. NOAA/NESDIS/JPSS Program Office, Greenbelt, MD
* CrIS SDR Team Lead
2013 GSICS User Workshop, 8 April 2013,College Park, MD

## Slide 2: Motivation
Hyperspectral IR sounders have served as benchmark measurements for the GSICS community.
  Polar orbiting sensor: HIRS, AVHRR, AATSR
  Geostationary : Imagers and Sounders
With more hyperspectral IR sounders on-orbit, are there any radiometric and spectral differences among them?
  Now: AIRS →Metop-A/IASI → NPP/CrIS → Metop-B/IASI
  Future: JPSS-1/CrIS and MetOp-C/IASI ….
If so, we need to understand the root causes of the differences based on sensor physics.
  Benefit for each sensor’s calibration
  Basis for climate data records

## Slide 3: Instrument and Spectral Characteristics
From Hank Revercomb
Spectral Coverage and Resolution of
AIRS, IASI, and CrIS
IASI-A: 2006
IASI-B:2012

## Slide 4: Approach
Direct comparison
  CrIS versus IASI/AIRS
Indirect comparison:
  Through the third sensor, CrIS-VIIRS versus IASI-VIIRS
Objectives
  Reduce uncertainties caused by the methodology
  Identify the differences at the sensor calibration level
  Understanding the root causes of these differences
VIIRS
CrIS

## Slide 5: Simultaneous Nadir Overpass (SNO)
IASI
CrIS
All data are from IDPS.
Only nadir and uniform scenes were selected.
Using the same collocation algorithms to collocate CrIS/IASI with VIIRS.
Time Difference: <= 120 Sec
FOV distance difference: <=(12+14)/4.0 km = 6.5 km
Angle Difference: ABS(cos(a1)/cos(a2)-1) <= 0.01
From Changyong Cao

## Slide 6: Collocating CrIS/IASI with VIIRS: Accurately computing FOV Shape
Satellite Direction
CrIS Scan Direction
VIIRS Scan Direction
EP V35 Upload
VIIRS Geolocation errors
M6.3x released, code bugs were fixed
The method based on the algorithm
can detect the VIIRS geolocation errors

## Slide 7: Collocate VIIRS with CrIS/IASI
50%
CrIS/IASI FOV Spatial Response
VIIRS Pixels
CrIS FOV footprint
Histogram of VIIRS M16 radiances in CrIS FOV

## Slide 8: Scene Uniformity Effects

## Slide 9: Resample IASI to CrIS
Fourier Transform
Inverse Fourier Transform
De-Apodization
2) Truncation
3) Apodization
CrIS – IASI
Re-sampling error very small

## Slide 10: IASI and CrIS SNO Spectra
Average Spectra
North (339)
South (431)
South (133)
North (153)
Metop-A IASI and CrIS
Metop-B IASI/ and CrIS
SNOs in 03/2013
SNOs in 10/2012, 12/2012, and 02/2013

## Slide 11: CrIS vs. IASI: CrIS Band 1
Metop-A
IASI
Metop-B
IASI
North Pole
South Pole
CrIS
IASI
CrIS-IASI
North Pole
South Pole

## Slide 12: CrIS vs. IASI: CrIS Band 2
Metop-A
Metop-B
North Pole
South Pole
CrIS
IASI
CrIS-IASI
North Pole
South Pole

## Slide 13: CrIS vs. IASI: CrIS Band 3
North Pole
South Pole
CrIS
IASI
CrIS-IASI
Metop-A
Metop-B

## Slide 14: How about CrIS/IASI versus VIIRS?
CrIS/IASI spectra are overlapped with VIIRS SRFs for M13, M15, and M16, and I5
10.8 µm
12.0 µm
4.05 µm

## Slide 15: Be careful for out-of-band response!
CrIS Band 1 end point
Center wavenumber and band correction coefficients are calculated using the above SRFs.

## Slide 16: OOB effects in BTs
M15
This relationship is used to compensate
CrIS convolution results.
M16
M15
M13
M16
IASI-IASI2CrIS vs. IASI2CrIS

## Slide 17: CrIS/IASI versus VIIRS
M15
M16
M15
M16
Metop-A
Metop-B
CrIS-VIIRS
IASI-VIIRS
Notes: CrIS is warmer than all the sensors, Band 15 have more large scene-dependence than M16
IASI seems close to VIIRS and doesn’t show scene dependence bias.
CrIS and IASI

## Slide 18: Conclusion Remarks
Inter-comparison of CrIS with IASI indicate that the consistency between CrIS and IASI is around 0.1-0.2 K at most spectral regions.
Given current consistency level (0.1-0.2K), it is very hard to find the root causes of the differences. However, in order to generate long-term climate data records, some issues still need further investigation:
  CrIS is warmer than IASI at the longwave band, especially for cold scenes
  CrIS-VIIRS scene-dependent features at M15
  Spectral inconsistency for shortwave sharp transition regions between CrIS and IASI
Investigation is now undergoing to understand these differneces.

## Slide 19: Thank you

## Slide 20: AIRS vs. CrIS
AIRS
CrIS
CrIS-AIRS
: North Pole SNOs