## Slide 1: PATMOS-x solar reflectance channel calibration – use of global mean reflectance
Andrew Heidinger
NOAA/NESDIS/STAR@CIMSS
JPSS Cloud Team Lead

## Slide 2: Outline
Analysis of Global Mean Reflectance from MODIS AQUA
Application to VIIRS M5 comparisons
Application to AVHRR Ch1
PATMOS-x Calibration Update

## Slide 3: Why Do This
NCEI asked the PATMOS-x team to monitor the calibration of the AVHRR.
While doing this we noted it was very stable and decided to pursue it as another calibration data source.
It has the benefit of
  available every day in real-time
  Independent of atmospheric correction, angular adjustments and cloud mask.
  Could be important for the pre-EOS AVHRR data.

## Slide 4: Stability of the Global Reflectance for AQUA/MODIS Ch1
So over 15 years, MODIS AQUA dropped about 1%.

## Slide 5: Stability of the Annual Cycle in Global Mean Reflectance
Variability of Global Mean Reflectance is comparable to that scene with clear-sky stable targets.

## Slide 6: Application VIIRS

## Slide 7: VIIRS M5 Issues
We continually see the cloud optical depths being higher from VIIRS than MODIS. (Both derived from NOAA Enterprise Algorithms).
Similar difference to that seen on Sunny Sun-Mack’s poster (CERES-VIIRS).
Cloud optical depth is highly non-linear with reflectance and calibration errors.
We think a 2-3% error accounts for this difference.

## Slide 8: STAR ICVS VIIRS M5 and M7 Bias
These results are after the adjustment for spectral response differences

## Slide 9: Spectral Conversion from MODIS Ch1 to VIIRS M5 and AVHRR Ch1
NASA Langley (Ben Scarino) runs a very nice site where SCHIMACHY-derived spectral conversions are available for many sensors and many surface regions including global. These plots are from that site.
Based on SCHIMACHY, VIIRS M5 should be 3.5% larger then MODIS Ch1 for a global mean reflectance
Based on SCHIMACHY, AVHRR Ch1 should be 1% smaller then MODIS Ch1 for a global mean reflectance

## Slide 10: Applying Global Reflectance Analysis to VIIRS M5.
VIIRS M5 after adjustment is 1.5% higher than MODIS Ch1
Very similar to STAR ICVS value
More than the computed degradation in MODIS Ch 1 (1%)
Less than we expected from the cloud optical depth analysis (2%)

## Slide 11: Application AVHRR Solar Channels

## Slide 12: Application to AVHRR for Inclusion in PATMOS-x
Day of Year (1 – 365)
Time of Day (13:30 – 18:00 Z)
NOAA-18 AVHRR CH 1
Since NOAA-18 has drifted so far, can we use it as a reference for the other AVHRR sensors?

## Slide 13: Method for Application AVHRR
Compute mean global count from any AVHRR
Compute mean global scaled radiance from the NOAA-18 table for a given day-of-year and the equator crossing time.
Generate a calibration slope.

## Slide 14: NOAA-18 Ch1 Results
Since NOAA-18 is the reference, we expect NOAA-18 to agree perfectly with the PATMOS-x calibration.
patmos-x
mitram
Blue dots are calibration slopes from the technique
Local equator crossing time

## Slide 15: Application to NOAA-16 Ch1
Method appears to work well with NOAA-16 over its 2 hours of drift from 2001 to 2007.

## Slide 16: Application to NOAA-14 Ch1
Issues arise after 2000 when the drift exceeds 3 hours.

## Slide 17: Conclusions
Mean global reflectance from a sun-synchronous polar orbiter is very stable. Warrants a look as a GSICS monitoring tool.
We can use this to compare MODIS and VIIRS. VIIRS M5 appears to be 1.5% too high.
Our optical depth analysis indicated VIIRS M5 is 2% too high relative to MODIS AQUA Ch1.
Long term analysis shows MODIS AQUA Ch1 gradually dropped 1%.
Application to AVHRR, which drifts, also shows promise.
PATMOS-x would like to use this as an independent monitoring tool and may use it in the calibration.
PATMOS-x owes an AVHRR calibration update to NCEI in September.