## Slide 1
Assessment of the calibration performance of satellite visible channels using cloud targets: Application to Meteosat-8/9 and MTSAT-1R
Seung-Hee Ham and B.J. Sohn Seoul National University, Korea
SPIE Asia Pacific Remote Sensing, Incheon, South Korea, 11-14 October 2010
Atmos. Chem. Phys., 10, 11131–11149, 2010
Notes: 1

## Slide 2
Method 1: Ray-Matching Technique
Meteosat-8/9 and MTSAT-1R visible channels are inter-calibrated using collocated and ray-matched MODIS 0.646-μm measurements.
Method 2: Use of MODIS cloud products as inputs to RTM
Meteosat-8/9 and MTSAT-1R visible channel reflectances are simulated using collocated MODIS-derived cloud parameters.
Method 3: Use of deep convective clouds (DCCs)
Meteosat-8/9 and MTSAT-1R visible channel reflectances are simulated for optically thick cloud targets.
Three Calibration Methods
2

## Slide 3
3
Method 1: Ray-Matching Technique
MODIS 0.646-μm Reflectance
Ocean only
0.5°х 0.5° Grid Format
SEVIRI 0.640-μm Reflectance
0.5°х 0.5°Grid Format
“Reference”
Ray-matching
∆(Viewing zenith angle; VZA) ≤ 5°
∆(Viewing azimuth angle; VAA) ≤ 15°
VZA ≤ 40°, SZA ≤ 40°
Spectral correction
Matching Time & Location
∆Time ≤ 5 minutes
Land Mask
Inter-Satellite Calibration
MODIS-Equivalent
SEVIRI Reflectance

## Slide 4
● Due to different spectral regions, measured reflectances by MODIS, Meteosat-8/9, and MTSAT-1R may be different.
● Therefore, spectral correction is achieved before comparing two channels (MODIS vs. Meteosat, or MODIS vs. MTSAT-1R).
4
Sensor Response Function

## Slide 5
Radiative simulation is performed to obtain relation between two channels.
- Cloud phase = ice (Baum) and water (Mie)
- Cloud particle size (re) = 10, 20, and 30 μm
- Cloud optical thickness (COT) = 0 to 100
- Solar zenith angle (SZA) = 0 to 40°
- Viewing zenith angle (VZA) = 0 to 40°
- Relative azimuth angles (RAA) = 0 to 180°
5
Spectral Correction between Two Channels
Conversion Equation
RMET8 = 0.9944 RTERRA + 0.0005
RMET8 = 0.9949 RAQUA + 0.0005
RMET9 = 0.9943 RTERRA + 0.0006
RMET9 = 0.9948 RAQUA + 0.0006
RMTSAT = 1.0213 RTERRA – 0.0038
RMTSAT = 1.0218 RAQUA – 0.0038
Relation between two channel reflectances
“Various inputs”

## Slide 6
6
Results of Meteosat-8/9 from Method 1
Regression slope = 0.93–0.94, Intercept < 0.01
 “6–7%” of low bias of SEVIRI measurements
Convert MODIS-measured reflectance into SEVIRI channel reflectance
6~7% bias

## Slide 7
7
Results of MTSAT-1R from Method 1
Measurement biases are shown to depend on reflectance magnitude. (+5% at reflectance=0.1, –20% at reflectance=1)
Considerable regression offset implies that incorrect space count may be currently used in MTSAT-R calibration.
Large scattered patterns are due to problems in scan method?
Negative bias
Positive bias

## Slide 8
8
Method 2: Use of MODIS Cloud Products
0.5°х 0.5° Grid Format
SEVIRI 0.640-μm Reflectance
MODIS
Cloud Products
0.5°х 0.5°Grid Format
“Reference”
Thresholds of Cloud Targets
Over ocean regions
Overcast clouds
5 ≤ Cloud optical thickness (COT)
Simulated Reflectance
Using SBDART
Matching Time & Location
∆Time ≤ 5 minutes
Examining SEVIRI Measurements
RTM Inputs
Surface – Ocean BRDF
Atmosphere – Tropical profile
Cloud – MODIS COT, particle size (re), Cloud altitude Mie scattering model for CTT ≥ 273 K
Baum scattering model for CTT ≤ 227 K
3D Radiative
Effects

## Slide 9
Two types of simulation biases associated with 3D effects
(1) Plane-parallel homogeneous (PPH) bias
The bias occurred by ignoring horizontal (subgrid) variation
(2) Independent column approximation (ICA) bias
The bias occurred by neglecting horizontal radiative interaction (e.g., cloud shadow, cloud illumination)
9
3D Radiative Effects in Cloud Simulation
RPPH
RICA
Cloud shadow
Cloud illumination
Columnar reflectance cannot be computed alone because the reflectance is influenced by surrounding columns due to radiative interaction (e.g., cloud shadow or illumination).

## Slide 10
10
Plane-Parallel Homogeneous (PPH) Bias
● PPH bias increases with grid size and subgrid variability.
● To minimize PPH bias, homogeneous cloud targets are used by applying STD(R0.6) ≤ 0.1.
● Lognormal (LN)-ICA method (Oreopoulos and Davies, 1998) is adopted to resolve subgrid variability.
“Subgrid variability”
LN function to describe COT distribution
Numerical integration of subgrid reflectance
Homogenous clouds

## Slide 11
11
Independent Column Approximation (ICA) Bias
Case study for quantifying ICA bias
Cloud vertical structures are described from CloudSat measurements
For the given cloud shapes, full 3D modeling (which considers cloud shadow-illumination) and ICA modeling (which ignores radiative interaction) are performed.
By comparing ICA modeling results with full 3D modeling results, ICA bias can be estimated.
ICA bias for CS1, CS2, CS3, and CS4
CS2
CS1
CS4
CS3
Four chosen cases among CloudSat measurements

## Slide 12
12
Independent Column Approximation (ICA) Bias
From the case study, we can minimize ICA bias in the calibration by
● Choosing cases with small SZA (≤ 40°) because the fluctuation of ICA bias increases with SZA.
● Taking spatial or temporal average because ICA bias is randomly distributed (i.e. their spatial mean is always close to zero regardless of case and SZA).
● Using homogeneous cloud targets only because large-scale homogeneous clouds (CS1 and CS4) represent smaller fluctuation of ICA biases compared to small-scale multilayered clouds (CS2 and CS3).
STD(R0.6) ≤ 0.1
Estimated ICA biases of four CloudSat cases with two SZAs (0 and 40°)

## Slide 13
13
Results of Meteosat-8/9 from Method 2
Regression results from Methods 1 and 2 are similar.
——— Regression from Method 1 ——— Regression from Method 2
 “6–7%” of low bias of SEVIRI measurements
6~7% bias

## Slide 14
14
Results of MTSAT-1R from Method 2
——— Regression from Method 1 ——— Regression from Method 2
Negative bias
Positive bias

## Slide 15
15
Method 3: Use of DCCs
SEVIRI 0.640-μm Reflectance and
11-μm Brightness Temperature
“Reference”
Thresholds of DCCs
TB11 ≤ 190 K
STD(TB11) ≤ 1 K
STD(R0.6)/Mean(R0.6) ≤ 0.03
Simulated Reflectance
Using SBDART
Examining SEVIRI Measurements
RTM Inputs
Surface – Ocean BRDF
Atmosphere – Tropical profile
Cloud properties
COT = 200, particle size (re) = 20 μm
Baum scattering model
3D Radiative
Effects
3D Effects
PPH bias
Can be ignored because of small pixel size, and almost linearity of reflectance w.r.t. COT for optically thick clouds (COT > 100).
ICA bias
Can be minimized from temporal averaging (daily mean) and two homogeneity checks. .
Investigating Optical Properties of DCCs with MODIS Data

## Slide 16
Optical Properties of DCC Targets
16
TB11 ≤ 190K
Chosen DCC Targets
(1) Cold cloud condition to select clouds overshooting tropopause layer
(2) Homogeneity checks to exclude cloud boundary pixels
R0.6: Visible reflectance
TB11: Brightness Temp. at 11-μm band
re≈20μm
COT≥100
 For the simulation, optical properties of DCC targets are assumed as COT = 200 and re = 20 μm.
DCC Properties from MODIS products

## Slide 17
Sensitivity of Input Parameters
to DCC Simulation
17
DCC targets
Input Parameters |  | Surface Reflectance | Atmospheric Profiles | AOT at 0.55 μm | Cloud Properties |  |  | 
 |  |  |  |  | COT at 0.646 μm | Effective Radius | CTH | Cloud Depth
Reference Value |  | Oceanic BRDF | Tropic | 0 | 200 | 20 μm | 15 km | 14 km
Input Range |  | 0 – 0.4 | MLS | 0 – 3 | 100 – 400 | 10 – 30 μm | 12 – 18 km | 10 – 14 km
Maximum Uncertainty (%) | SZA = 0° | 0.09% | 1.29% | 0.14% | 4.79% | 1.64% | 0.15% | 0.24%
 | SZA = 40° | 0.08% | 1.30% | 0.13% | 4.41% | 3.02% | 0.21% | 0.23%
~5% of simulation error by fixing cloud parameters
Simulation uncertainty by each RTM input parameter
COT=100
COT=200
COT=400
Diff. <5%
Diff. <5%

## Slide 18
Terra
Aqua

## Slide 19
Evaluation of Method 3 by Applying to Well-Calibrated MODIS Visible Channel
The accuracy of Method 3 seems to be better than 5%.
19

## Slide 20
Method 3 produces different results compared to Method 1 or 2.
The degree of discrepancy is “2 ~ 3%.”
20
Results of Meteosat-8/9 from Method 3
———Method 1 ———Method 2 X Method 3

## Slide 21
Methods 1, 2, and 3 are shown to produce consistent results.
21
Results of MTSAT-1R from Method 3
———Method 1 ———Method 2 X Method 3

## Slide 22
Summary of Three Calibration Results of Meteosat-8/9
and MTSAT-1R Visible Channels
–– Method 1: Inter-calibration
Method 2: Calibration using MODIS cloud products
× Method 3: Calibration using DCC targets ---- One-to-one match
All three methods generally show good agreement, with less than 3% differences.
When high reflectances are absent in inter-calibration, Method 2 and Method 3 can be used for improvement of calibration accuracy.

## Slide 23
Conclusions
Meteosat-8/9 SEVIRI 0.640-μm channel measurements are underestimated by 6–7%, and larger measurement biases are expected at the high end.
Consistent results of MTSAT-1R 0.724-μm channel are derived from three methods; i.e. MTSAT-1R measurements is positively biased at near-zero reflectances, while the bias is negative up to –20% at the bright side. Update of correct space offset count is required.
23
SEVIRI Reflectance
SEVIRI Digital Count
Reference
reflectance
6~7%
Method 1 &
Method 2
Measured reflectance
Method 3
MTSAT-1R Reflectance
MTSAT-1R Digital Count
Reference
reflectance
17~19%
Measured reflectance
Method 3
Methods 1 &
Method 2



## Slide 24
Thank you
Notes: 24