## Slide 1
Inter-Calibration of
COMS Infrared and Visible channels
Joint meeting of GRWG and GDWG
Korea Meteorological Administration
National Meteorological Satellite Center

## Slide 2
S-/L-/Ka-Band Comm
Meteo Imager
Ocean Color Imager
Solar array
Bus
Communication, Ocean, and Meteorological Satellite (COMS)
8-year program (2003 – 2010)
Launch date : June 26, 2010 (French Guiana Kourou)
Location : 128.2E
Mass : 2,500kg
Design life time : 7 years
Contractor : EADS Astrium (ITT for MI)
COMS
channel | Wave length(㎛)
Visible | 0.67
Shortwave IR(IR4) | 3.7
Water Vapor(IR3) | 6.7
IR1 | 10.8
IR2 | 12.0

## Slide 3
First Visible Image (2010.7.12 1115 KST)

## Slide 4
IR1 (11m)
IR2 (12m)
First IR Image (2010.8.11 1914 KST)

## Slide 5
SWIR (3.5m)
WV (6.7m)
First IR Image (2010.8.11 1914 KST)

## Slide 6
2010 4th Typhoon DENMU

## Slide 7
Full Disk : every 3 hr
NH : every 15 min
Korea : ~ 8 min
FD
LA
ENH
Observation Schedule

## Slide 8: Previously
IR inter-calibration system for GEO with MODIS
  Test using MTSAT-1R data: ~2010
GEO-LEO IR radiation Calibration with AIRS/IASI
  MTSAT(both 1R/2) during 2009-2010
COMS (1-Vis, 4-Irs)
  10.8, 12.0, 6.7, 3.7
  launch date: Jun. 26, 2010
  In-orbit test: July 10, 2010 ~ January 2011
  Operation: April 2011~
Notes: This is current GSICS activity of KMA. Implement IR inter-calibration system for COMS with MODIS. Test with MTSAT-1R data instead of COMS. Installation of GSICS GEO-LEO AIRS IR radiation calibration Software. Test with MTSAT-1R data during 2007.

## Slide 9: Currently
IR inter-calibration system for COMS with MODIS
  Using COMS after 2011
GEO-LEO IR radiation Calibration with AIRS/IASI
  COMS after January 2011
VIS vicarious Calibration
  Moon Calibration: 2011~
Notes: This is current GSICS activity of KMA. Implement IR inter-calibration system for COMS with MODIS. Test with MTSAT-1R data instead of COMS. Installation of GSICS GEO-LEO AIRS IR radiation calibration Software. Test with MTSAT-1R data during 2007.

## Slide 10
Polar orbital
Satellite
(AIRS/IASI)
Geostationary
Satellite
(COMS)
  Observation time difference
  - Maximum time difference is within 15 min
  Target
  - Selection clear or homogenous target
  Spatial resolution difference
  - hyper sounder: 12km, COMS: 4km
  - radiances over a box of 3x3 pixels
  Viewing angle (VA) difference
  - The viewing angle difference changes
  the effect of atmosphere
  - Data are selected within 50° of satellite viewing angle from nadir (M. König, 1999)
  - Maximum viewing angle difference is within 5°
Match-up Conditions
IR Calibration monitoring

## Slide 11
COLLOCATED IN SPACE
COLLOCATED IN TIME
ALIGNED IN LINE-OF-SIGHT
UNIFORM ENVIRONMENT (9x9 )
NORMAL GEO FOV
SPATIAL AVERAGING
SPECTRAL FILLING
Spectral filling method
Convolution method
  Linear interpolation using only US profile
  Proposed by NESDIS
Constraint method
  Least square method using 8-profile
  Proposed by JMA
GEO(COMS) vs. LEO(AIRS) IR Calibration
GEO: COMS
LEO: IASI
LEO: AIRS
Valid channel
Missing channel
SRFs of COMS (red), METEOSAT-8 (green) and GOES-12 (blue) IR channels

## Slide 12
GEO vs. LEO constraint method(IR Calibration)
AIRS
IASI

## Slide 13
TB vs. TB(COMS-AIRS) (IR Calibration)

## Slide 14
TB vs. TB(COMS – IASI) (IR Calibration)

## Slide 15
Time series of TB (IR Calibration)
Notes: SWIR 채널에 대한 오차분석은 진행중에 있으나 해결하지 못함. 다방면으로 분석중에 있으며 진행상황에 대해서 지속적으로 보고할 예정임.

## Slide 16
KMA/NMSC web

## Slide 17
COMS IR channels have low-bias except IR1
Difference between COMS TB and AIRS/
IASI TB shows positive bias in the cold
scenes while negative bias in the warm
scenes (except IASI IR4)
AIRS comparisons have larger bias and rmse than IASI
Need long-term monitoring
Preliminary Results (IR Calibration)

## Slide 18
Moon Calibration of COMS visible (1/3)
COMS has observed moon monthly for moon calibration since Feb. 2011.
KMA has used its own Moon Processing system in IMPS(Image Processing Subsystem) for Moon Calibration.
For observing moon, KMA choose two kind of moon observation method by using Local Area Observation for moon and Full disk Observation with moon.

## Slide 19
Moon Calibration of COMS visible (2/3)
To measure the total degradation of the instrument visible channel
Comparison between the Moon signal and ROLO model of USGS – as a Function of Phase angle(Sun-Moon-Earth)
Imager Response
Where
is the Moon irradiance as measured by the Imager
is the Moon irradiance computed from the ROLO model,
under the same conditions
All Imager responses are linearly trended over the various Moon images with the ratio expressed in percentage.

## Slide 20
Moon Calibration of COMS visible (3/3)
The results from Feb. 2011 to Jan. 2012.
Chart: Trend of Absolute Accuracy
| '11.2. | '11.3. | '11.4. | '11.5. | '11.6. | '11.7. | '11.8. | '11.9. | '11.10. | '11.11. | '11.12. | '12.1.
 | 0.019366 | 0.016756 | 0.02059 | -0.016186 | 0.0043202 | 0.016609 | 0.0067775 | 0.0033643 | 0.013964 | -0.00049657 | 0.0058184 | 0.031155
(1-measured/model)×100(%)
TIME(month)
Maximum absolute accuracy for last 1 year is less than 4%.
1-K on month(%)
TIME(month)
Irradiance with Earth
1-K on month(%)
TIME(month)
Irradiance without Earth
y = ax+b
a = 2.6769
b = -27.92045
bias = -13.1976
Rmse = 32.6
y = ax+b
a = 0.0077
b = -0.5024
bias = -0.4602
Rmse = 1.42
Since the rectangle, in which moon irradiance is calculated, can contain earth(red circle), count values of earth part in this rectangle should be replaced space values.
Notes: 달 관측 분석을 위해서 특정한 크기의 직사각형을 분석하는데 경우에 따라서 달만이 아닌 지구가 이 직사각형속에 포함되는 경우가 있어, 이 경우는 값이 매우 이상한 값으로 나타나기에 지구의 값을 제거하고 우주배경값으로 이를 대신하여 채워서 계산하게 되면 왼쪽 그래프에서 처럼 매우 터무니 없는 값이 오른쪽 그림과 같이 제거 됨.
이렇게 제거를 하고 난 후 ROLO 모델과의 차이는 4% 이내로 정확도를 가지게 됨
전체적으로 2011년동안 달을 이용한 가시채널 검정 결과는 완벽하게 분석이 되지는 않았으나 일정한 경향을 나타내고 있지는 않음. y절편을 0으로 두었을때 기울기가 약 3% 정도로 나타나고 있음. 하지만 오차와의 값이 크게 차이가 나지않아, 이를 가시채널의 센서가 퇴화되었다고 판단하기는 이른 것으로 생각됨.

## Slide 21: Any comments or questions?

## Slide 22
Trends from Feb. 2011 to Jan. 2012.
y = ax+b
a = 7.397574212
b = 0
y = ax+b
a = 0.443393249
b = 0
Irradiance with Earth
Irradiance without Earth
y = ax+b
a = 1.789828731
b = 0
y = ax+b
a = 0.300893607
b = 0
Irradiance with Earth except May 2011 data
Irradiance without Earth except May 2011 data
1-K on month(%)
1-K on month(%)
1-K on month(%)
1-K on month(%)