## Slide 1: Report on the NIST Lunar Calibration Workshop to GRWG
Fangfang Yu

## Slide 2: NIST Lunar Calibration Workshop
Goal: establish the Moon as an absolute calibration standard , SI traceable for satellite sensor calibration target through the inter-agency efforts with the cut-edge technologies.
Where: NIST, Gaithersburg, MD
Time: May 14-15, 2012
http://www.nist.gov/pml/div685/sc/lunar_workshop.cfm

## Slide 3: Representatives
Government agencies: NASA/NIST/NOAA/USGS
Institutions: UMBC, University of New Mexico, Dartmouth College, University of Wisconsin at Madison, JPL etc.
>15 talks on the satellite, ground-based, balloon and aircraft measurements of the Moon, as well as the NIST stars from the astronomy community – current technologies and achievements, ongoing goals and the challenges for the SI traceable for the climate studies

## Slide 4: Day One Talks & Discussions – (1)
Theme: What are the calibration needs?
Talk 1: Overview of lunar calibration by Kurt Thome (NASA)
  Calibration needs for commercial sensors, operational sensor and climate studies.
  Why on orbit & vicarious calibrations
  Why the Moon?
  How well is needed – better than we do now
    Commercial sensors – <5% (k=2) absolute calibration uncertainty; 1-2 processing during the mission
    Operational sensors – precision <0.1% variability with absolute calibration uncertainty <3%
    Climate study – precision <0.1%(k=2) and abs. <0.2%
  Future lunar calibration should be integrated pieces – meet the requirements for multiple types of sensors
  Discussion: why not the stars? Star is more stable than the Moon (from the astronomy community). It is pointed out that not all the satellite sensors can view the star (from the satellite agencies).

## Slide 5: Day One Talks & Discussions – (2)
The current state of lunar calibration and the ROLO model by Tom Stone (USGS)
  The USGS ROLO irradiance model is very useful in sensor trending; <1% in the mean absolute fitting residual over all 32 bands.
    Oversampling correction is the key factor
  Absolute calibration uncertainty 5-10%, mainly due to measurement uncertainty of Vega (stellar image processing), atm. Opacity correction, PSF etc.
  Use of 32 bands to interpolate the satellite sensor SRFs
  Need >3 years of observations to simulate the libration impact.

## Slide 6: Day One Talks & Discussions – (3)
Lunar calibrations in remote sensing and climate sciences
  Overview by James Bulter (NASA)
  MODIS & VIIRS
  SeaWiFS
  GOES-R
  Lunar photometry
  GOES
SeaWiFS, MODIS/VIIRS results show that ROLO model is very useful in trending at certain phase angles, yet significant phase angle dependent uncertainty >1% can be observed at some phase ranges which can be observed at both MODIS and SeaWiFS sensors.
Jim Bulter as a member in the GSICS Executive panel pointed out the need of ROLO model in the international GEO satellite inter-calibration. Tom Stone then mentioned the use of ROLO model in the foreign satellites should go through certain channel as the model development is supported by the US government agencies.
In the GOES-R ABI talk, in addition to the inter-comparisons between Hyperion, ROLO, GOES and model simulations, some examples of lunar calibration at thermal IR spectral ranges were also demonstrated.
Fred and me gave the talk of GOES lunar calibration at NOAA in which the motivation of lunar calibration in GSICS was included and presented. It is pointed out that GEO can view the moon at a large variety of phase angles and many of the unscheduled moon images are clipped. Therefore, an radiance model will be very useful. The practical effort to anchor the absolute calibration uncertainty <3% will significantly improve the operational GEO calibration. Fred also put the request to extend the spectral range to UV down to 300 or 320nm.
Hubble – space telescope for SI traceable for Vega measurement

## Slide 7: Day Two Talks & Discussions –(1)
Ground-based lunar calibrations and atmospheric monitoring
  NIST lunar calibration
  Lidar for atmospheric extinction
  Stellar photometry and the atmosphere
Aerosol effect is the key issue
Goal: abs. accuracy <0.5% (k=1) with spectral resolution ~0.3%
Current: 2-3% (k=1) of abs. accuracy, disployment at Mt. Hopkins

## Slide 8: Day Two Talks & Discussions –(2)
Measurements above the atm.
  Balloon-borne optical sources
  Balloon-borne telescopes
  The aircraft platform
Above ~95% of atm.
Goal is for 1% abs. , current 3% abs. accuracy

## Slide 9: Discussions, Suggestions & Conclusions
ROLO model should be maintained and improved
Turn ROLO model into institutional standard
Gate-keepers for the future lunar model, ITAR issue, version control, written documentations
Extend irradiance model to radiance model at certain level of accuracy
Extend the spectra to UV and Thermal IR range
NOAA as the operational agency will use whatever the existing resource while the institutional agencies will explore the new technology for the goals.
NIST should lead the inter-agency effort to improve the lunar model to meet the SI traceable absolute calibration accuracy goal.
The workshop report will be available in 3 months