## Slide 1: GOES-R Program Cal/Val Annual GSICS GRWG & GDWG Meeting March 4, 2013
Bob Iacovazzi, Jr.
GOES-R Program Systems Engineering (PSE) Cal/Val Lead
Notes: To-Do:

## Slide 2: Instrument Overview
Spare
Visual & IR Imagery
Lightning Mapping
Space Weather Monitoring
Solar Imaging
Advanced Baseline Imager (ABI)
Geostationary Lightning Mapper (GLM)
Space Environment in-Situ Sensor Suite (SEISS)
Magnetometer
Solar Ultra-Violet Imager (SUVI)
Extreme UV/X-Ray Irradiance Sensors (EXIS)
GOES-R supports NOAA mission to provide forecasts and warnings for the United States, its territories, and adjacent waters for the protection of life and property and the enhancement of the national economy.
GOES-R is the next generation of GOES satellites that will provide a major improvement in quality, quantity, and timeliness of data collected.
Earth Pointing
Sun Pointing
In-Situ
New and improved capabilities for:
  increased lead times for severe weather warnings
  better storm tracking capabilities
  solar, space weather, and climate analyses
  advanced products for aviation, transportation, commerce
Notes: To-Do:

## Slide 3: GOES-R Data and Product Overview
GOES-R Products
Radiances* | Cloud and Moisture Imagery (KPP)
Solar Imagery: X-ray* | Rainfall Rate / QPE
Energetic Heavy Ions* | Legacy Vertical Moisture Profile
Magnetospheric Electrons and Protons: Low Energy* | Legacy Vertical Temperature Profile
Magnetospheric Electrons and Protons: Medium and High Energy* | Derived Stability Indices
Solar and Galactic Protons* | Total Precipitable Water
Geomagnetic Field* | Clear Sky Masks
Solar Flux: EUV* | Downward Shortwave Rad.: Surface
Solar Flux: X-Ray* | Fire / Hot Spot Characterization
Lightning Det: Events, Groups, Flashes* | Land Surface (Skin) Temperature
Aerosol Detection (including Smoke & Dust) | Sea Surface Temperature (skin)
Aerosol Optical Depth | Reflected Shortwave Rad.: TOA
Volcanic Ash: Detection & Height | Snow Cover
Cloud Optical Depth | Derived Motion Winds
Cloud Particle Size Distribution | Hurricane Intensity
Cloud Top Phase | Cloud Top Pressure
Cloud Top Height | Cloud Top Temperature
ABI | GLM
SEISS | EXIS
SUVI | Magnetometer
 | * Included in GRB
Chart: 
| GOES-R | GOES I-P
IMAGER | 2
SOUNDER | 0.032
SXI | 0.4
EUV/XRS | 0.05
ABI | 67
GLM | 5.5
Space Wx | 3.62
Fill | 29.88
GLM
ABI
Space Wx
Fill Packets
Mbps
ABI provides 3x spectral, 4x coverage, and 5x temporal resolution of current imager
GOES-R product requirements drive instrument performance requirements, which often are the same as, or more strict than, heritage GOES.
GOES-R Raw Data Throughput
L1b
L2+ Products are remainder outside of oval
Notes: To-Do:

## Slide 4: Importance of Calibration & Validation
Calibration: The process to determine factors for converting and correcting raw detector measurements into science data units (e.g., radiance) with the specified level of accuracy.
  Calibration is applied to GOES-R raw instrument data to transform them into L1b measurements … the fundamental building blocks for all L2+ products.
  Validation provides user confidence that GOES-R data can be used for their intended purpose, e.g., weather forecasting or numerical weather prediction.
Validation: The process of determining that the deliverable item satisfies its intended use in its intended environment.
GOES-R cal/val requirements are integrated into mission requirements!
Notes: To-Do:

## Slide 5: GOES-R Cal/Val Scope
  Pre-launch calibration/L1B validation
    Observe, and validate results of, pre-launch instrument-level calibration tests
    Evaluate instrument performance risks and waiver requests
    Provide subject matter expert (SME) review of L1b algorithm design and implementation
    Develop Cal/Val related Post-Launch Test (PLT) planning
    Develop tools for post-launch validation and anomaly resolution of L1b science data quality
  Validate expected results from pre-launch system level testing of L1b algorithm using synthetic L0 data
  Analyze PLT cal/val data results and provide SME support of science data anomaly resolution
  Coordinate cal/val activities through PLT and Handover
  Prepare NOAA satellite calibration scientists and engineers for monitoring, analyzing and maintaining GOES-R series instrument calibration and product integrity after Handover
GOES-R cal/val enhances understanding of data quality, and encourages “Day-1” operational readiness and long-term user confidence.
Notes: To-Do:

## Slide 6: GOES-R Cal/Val Collaborators
Collaborator | Main Responsibilities | Cal | L1b Prod Val | L2+ Prod Val
Flight Project | Oversee SC/Instr. Design, Fabr., Integ., and Test |  |  | 
SC/Instr Vendors | SC/Instr. Design, Fabr., Integ., and Test |  |  | 
Ground Segment (GS) Project | Oversee GS Design, Fabr., Integ., and Test |  |  | 
GS Vendor | GS Design, Fabr., Integ., and Test |  |  | 
Mission Ops Support Team | Gov’t SC/Instr/GS Test |  |  | 
Data Ops Support Team | Gov’t GS Test |  |  | 
Cal Working Group (CWG) | PSE Technical Support to GOES-R Instr. Cal & L1b Val |  |  | 
Algorithm Working Group (AWG) | L2+ Product Dev and V&V |  |  | 
NESDIS Office of Satellite and Product Operations (OSPO) | Ops Support to Cal/Val |  |  | 
All Collaborators participate in the Cal Coordination Team to manage GOES-R cal/val activities.
Notes: To-Do:

## Slide 7: GOES-R Cal/Val Organization
Program Systems Engineering Lead
Instr./L1b Verification
Cal Working Group
Cal/Val Technical
Cal Coordination Team
Cal/Val Management
FP Mission Ops Support Team (MOST)
Gov’t Satellite Tests
GOES-R Chief Scientist
L1b Science Validation
GS Vendor
Instr. Vendors
GSP L1b Integ. Project Team
FP
Instr. Managers
GSP Prod and Algorithm Lead
GOES-R Program Manager
Ground Segment Project (GSP)
Manager
Flight Project (FP) Manager
GSP Data Ops Support Team (DOST)
Gov’t GS Tests
Cal/Val Collaborators
Algorithm Working Group - L2+ Product Cal/Val Technical
Notes: To-Do:

## Slide 8
GOES-R Program Cal/Val Documents
Calibration and Product Validation Strategy
Cal/Val Plan Vol. 1: L1b Data
Cal/Val Plan Vol 2: L2+ Product Val
All documents at CDR-level - Scope defined, technical methods mature, organizational role and responsibilities and processes defined, resources allocated, and schedules defined.
Cal/Val Methods and Processes
Scope, Organizations & Working Groups, Roles & Responsibilities, Resources, and Schedules
Notes: To-Do:

## Slide 9: GOES-R Cal/Val Resources
Resource | Pre-Launch | Post-Launch Testing | Mission Operations
Data and Tools |  |  | 
Cal/Val, L0, L1b Data Archive/Storage |  |  | 
Models/Analysis Tools |  |  | 
GOES-R Portal and Web Sites |  |  | 
Facilities and Equipment |  |  | 
Vendor Offices, Manufacturing Centers, Test Labs/Equipment |  |  | 
NIST Test Labs/Equipment |  |  | 
NASA Offices & Test Labs/Equipment |  |  | 
NOAA Offices |  |  | 
Independent Test Facilities (e.g., Mass General Hospital) |  |  | 
Field Campaign Assets (e.g. SURFRAD, ARM) |  |  | 
Notes: To-Do:

## Slide 10: GOES-R Cal/Val Current Status/Updates
  Instrument testing support:
    Attending instrument Pre-Environmental Review and Pre-ship Review meetings
    Cal-related testing activities:
      Observing select ABI, SEISS, and EXIS testing
      Analyzing vendor CDRL074 test results
      Resolving discrepancies found in CDRL074 test results with respect to analysis performed by the vendor
  Supporting L1b Algorithm and Instrument Cal Data Implementation
  Preparations for Post-Launch Testing (PLT):
    Creating “deep-dive” cal/val analysis tools
    Assessing MSFC, NGDC, and STAR agency computing infrastructure needed to support post-launch GOES-R cal/val
    Developing cal-related PLT Short Forms in collaboration with the MOST
Preparations for pre-launch system-level testing and PLT
  Developing a GOES-R Cal/Val CONOPS, based on Harris GS design presentations and program-level cal/val plans
  Developing a GOES-R Cal/Val OPSCON that describes processes needed to assess and maintain product integrity
  Creating a cal-related PLT implementation tracking spreadsheet, based on GOES-R Cal/Val Plan Volume 1: L1b Data
Notes: To-Do:

## Slide 11: Instr Cal and Cal Test Report Review: ABI
CWG conducted detailed data analysis on pre-launch tests for proto-type model (PTM)
Emissive (top) and Reflective (bottom) channel calibration test arrangement
Anomalies caused by not using actual scan mirror reflectance value
Reflective and emissive channel calibration
Coherent noise
Irradiance calibration
MTF-Focus-Registration
Emissive (left) and reflective (right) channel calibration test results - ratio of CWG to Exelis cal coefficient
Coherent noise test results
Exelis
CWG
Government analysis of vendor cal testing reports scrutinizes reproducibility of results and provides valuable feedback to the testing process.

## Slide 12: Instr Cal and Cal Test Report Review: NIST support for ABI and EXIS
Witness filter characterization (ongoing)
Reflective channel radiance scale validation via visible transfer radiometer (VXR) (planning)
FEL-based irradiance scale validation: uniformity test (completed)
Spectral response and irradiance characterization via SIRCUS (completed for PTM)
Characterization of external blackbody via thermal transfer radiometer (TXR) (completed)
EXIS testing at Synchrotron Ultraviolet Radiation Facillity-III (ongoing)
Traveling SIRCUS (Spectral Irradiance and Radiance Responsivity Calibration Using Uniform Sources)
Spatial uniformity results at three distances, z.
Spatial uniformity setup
0.1% contours
NIST testing provides independent validation of instrument performance and in some cases traceability to international standards.

## Slide 13: Cal/Val Roadmap to Launch
Continue …
  Cal testing and test report review and analysis
  Ensuring proper implementation of L1b algorithms, Instrument Cal Data and operational monitoring
  Creating “deep-dive” cal/val tools
  Coordinating cal/val efforts between projects and with external operational cal/val support agencies
Cal/Val Related Post-Launch Test (PLT) Preparations
  PLT detailed test planning will continue with CWG participation
Pre-launch System-level Testing Activities
  Ensure ability to process data that have been collected during End-to-End Test III
  Ensure correct cal parameter files are verified and are in place
  Inspect and analyze data associated with instrument testing
  Test out functionality of L1b “deep-dive” tools
Notes: To-Do:

## Slide 14
Post-launch Testing On-orbit Checkout
GOES-13 Hemispheric Image Tiles
KPP product quality evaluation
Calibration input parameter evaluation
GOES-10 Ch. 4A Corrected and uncorrected Radiance vs. scan angle. (Beaucom et al., Proceedings of SPIE, 1999)
On-board calibration system evaluation
Instrument Noise, Blackbody Temp and Cal Slope Monitoring
LEO Hyperspectral Sounder vs. GEO Inter-comparison (Courtesy of Wu et al.)
Radiance [mW/(m^2-sr-cm^-1)]
Notes: To-Do:

## Slide 15
Post-launch Anomaly Resolution
GOES-13 Eclipse Season Stray Light
GOES-13 Eclipse Season Stray Light Before Fix (Top) and After Fix (Bottom) (Courtesy of J. Paul Douglas, OSPO)
Stray Light
Strongly coordinated efforts between Cal Collaborators will be essential to success of post-launch instrument and L1b performance anomaly resolution efforts.

## Slide 16
Post-Launch Testing Environmental Calibration Initialization
GEO-LEO ABI and GLM Radiometric Cal and INR
Vicarious Calibration
Moon ABI Radiometric Cal, MTF and Band-to-band Registration
Desert and Instrumented Sites ABI Radiometric Cal
White Sands Missile Range
Sonora Desert
Deep Convective Clouds ABI and GLM Radiometric Cal
Satellite Inter-Calibration
Stars ABI Radiometric Cal
Activity near the end of PLT for L1b validation and creating a “state-of-the-cal” snapshot for long-term calibration trending
GEO-GEO ABI and GLM Radiometric Cal and INR
ARM and SURFRAD

## Slide 17
Mission-life sensor parameter and derived product trending
GOES-10
Application of ABI Long-term Radiometric Performance tool to GOES-10. (Wu et al., GSICS Monthly Web Seminar, Dec. 2011, https://gsics.nesdis.noaa.gov/wiki/ Development/20111213)
Tropical Rainfall Measurement Mission Lightning Imaging Sensor (LIS)
Application of GLM Long-term Radiometric Performance tool to LIS (Buechler et al., Atmos. Res., 2012)
Application of ABI Co-Registration Validation tool to the GOES Imager. (Grotenhuis, Proc. SPIE 8510, 85101T 2012.)
Cal activities required during GOES-R acquisition enables long-term monitoring, analysis and maintenance of GOES-R product quality after Handover.

## Slide 18: Summary
GOES-R has a comprehensive cal/val program to ensure product integrity
  Cal/Val Strategy
  Cal/Val Plans
  Cal/Val CONOPS&OPSCON
GOES-R leveraging diverse complementary technical capabilities and resources
Provide life cycle cal/val support for a successful GOES-R program
Notes: To-Do:

## Slide 19
Development Integration and Testing
GOES-R Pre-Launch Milestones
Program/System |  |  | 
Flight Segment |  |  | 
Ground Segment |  |  | 
System Design Review complete
All instruments have passed CDR
100 % delivery of baseline product algorithms
Spacecraft
Instruments
S/C SDR complete
ABI Delta CDR complete
Core GS PDR completed
Antenna System PDR completed
GS Project PDR complete
 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Mission PDR Part I
Mission PDR Part II
S/C PDR complete
S/C CDR
ABI Delivery
SEISS Delivery
EXIS Delivery
SUVI Delivery
GLM Delivery
Mission CDR
Antenna System CDR
GS Project CDR
ESPDS CDR
CLASS CDR
RBU/NSOF/WCDAS installation
WCDAS complete
Launch Readiness Oct. 2015
RBU complete
NSOF complete
Core GS CDR
MAG Delivery
Notes: To-Do: