## Slide 1: CLARREO RSS: Reference Inter-calibration on Orbit
Annual GRWG+GDWG Meeting 2013, Williamsburg, VA
C. Lukashin, C. Roithmayr, P. Speth, B. Wielicki, D. Young, C. Currey
NASA LaRC, Hampton, VA
K. Thome
NASA GSFC, Greenbelt, MD
W. Sun
SSAI, Hampton, VA

## Slide 2: Presentation outline
  CLARREO RSS Inter-calibration approach, mission requirements, and on-orbit matched-data sampling.
  CLARREO RSS inter-calibration approach to sensor’s sensitivity to polarization, estimates for resulting radiometric uncertainty.
  Multi-Instrument Inter-Calibration (MIIC) framework.

## Slide 3: CLARREO Reflected Solar Spectrometer (RSS) Science Implementation Strategy
  1) CLARREO will create benchmark climate data records using two complementary approaches:
    (a) Direct benchmark observations by CLARREO RSS: spectral
    fingerprinting techniques.
    (b) Enabling Climate Benchmark using CLARREO for reference
    inter-calibration of existing operational sensors.
  2) CLARREO Reference Inter-calibration (RI) will be used to determine
  and correct operational sensors for:
    - Sensor offset and gain (effective).
    - Spectral response function change on orbit.
    - Sensitivity to Polarization.
    - Non-linearity.
3) CLARREO RSS RI goal: uncertainty contribution ≤ 0.15% (k=1)
over autocorrelation time period ≤ 0.8 year (Wielicki et al., BAMS 2013)

## Slide 4: CLARREO RSS Mission Requirements
(1) CLARREO RS accuracy 0.15% (k=1) for measuring reflected radiation.
B. Wielicki et al. (BAMS, 2013)
(3) Uncertainty contribution from
RI method: ≤ 0.15% (k=1) over
climate autocorrelation time
period 0.8 year.
RI error is considered to be
random (data matching noise).
(2) High Priority RI Targets:
Sensors: CERES & VIIRS/JPSS,
AVHRR/Metop, Landsats,
ESA Sentinels (optical),
GEO imagers, TEMPO.
Surface: Dome C, Desert sites.
Space: Lunar Irradiance.

## Slide 5: CLARREO RSS Reference Inter-calibration Objectives
  RI Method: Sensor measurements compared to high accuracy reference on orbit (CLARREO RSS
  observations). The method is statistical , approach is different from sensor to sensor
  depending on its calibration model.
1) CLARREO RSS Inter-Calibration Objectives: Broadband Radiometers (CERES)
Parameter | Time scale | Variable | RI Error, k=1 (%) | N Samples
Effective Offset | monthly | Scan angle | ≤ 0.45 | 2.5 ✕ 103
Effective Gain | monthly | Scan angle | ≤ 0.45 | 2.5 ✕ 103
RSR Degradation | seasonally | Scene Type | ≤ 0.25 | 30 ✕ 103
Non-Linearity | Validation Annually, RI Error 0.15% (k=1) |  |  | 
Sensitivity to Polarization | Not Sensitive, Validation Annually, RI Error 0.15% (k=1) |  |  | 
2) CLARREO RSS Inter-Calibration Objectives: Imaging Radiometers (VIIRS)
Parameter | Time scale | Variable | RI Error, k=1 (%) | 
Effective Offset | monthly | Scan angle, DOP, HAM | ≤ 0.45 | 7 ✕ 103
Effective Gain | monthly | Scan angle, DOP, HAM | ≤ 0.45 | 7 ✕ 103
Sensitivity to Polarization | seasonally | Scan Angle(7), DOP, χ (9), HAM | ≤ 0.25 | 1.2 ✕ 106
RSR CW Shift | Validation Annually, RI Error 0.15% (k=1) |  |  | 
Non-Linearity | Validation Annually, RI Error 0.15% (k=1) |  |  | 
  Requirement: On-orbit matched data sampling is required to reduce random noise from data
  matching by averaging. Data matching in Time & Viewing geometry in orbit.
  Note: Requirements are set for limiting data matching noise to 1% (k=1).

## Slide 6: Simulation Study: CERES RSR Degradation SCIAMACHY data: Clear ocean (N = 1800) and marine clouds scenes (N = 7000)
CERES RSR Degradation:
α = 9.8155 (D=0.999 @ λ=0.7 μm)
Top: CERES – CLARREO difference versus CLARREO signals (%).
Middle: CERES – CLARREO difference versus CLARREO signals (%) with 1% matching noise.
Bottom: Relative difference between
CLARREO and CERES signals with noise reduced by averaging.
FIT RESULTS: |  | 
Scene | OFFSET (Wm-2sr-1) | GAIN (%)
CLRO | -0.183 ± 0.028 | -0.31 ± 0.18
MCLD | 0.021 ± 0.108 | -0.73 ± 0.10
* CLRO: Offset error (k=1) = 0.10%
* MCLD: Offset error (k=1) = 0.05%

## Slide 7: CLARREO RSS Requirement - 2D Pointing Ability
Studies by CLARREO Engineering Team, K. Thome, and C. Lukashin
Comments:
- Yaw & Roll pointing option
is preferred from RI point of view:
RAZ is matched accurately,
matching with GEO imagers
is more effective.
Hyperspectral image has
directional definition of swath:
RAZ (or Yaw).
Pitch & Roll pointing option
may be preferred for Lunar &
Solar measurements.
1) Yaw & Roll pointing: roll +/- 55o, and yaw +/- 84o range.
Requirement:
Ability to provide RI coincident data, matched in both RAZ and VZA angles.
Requirement implies at least 2D pointing ability in orbit.
2) Pitch & Roll pointing: roll +/- 55o, and pitch +/- 55o range.

## Slide 8
CLARREO RSS On-Orbit Pointing Operations
CLARREO RSS 2D pointing option:
1) Yaw (azimuth angle) match = constant (matching within 0.4o).
2) Continuous Gimbal Roll (scan angle) match  a function of time.
 JPSS
CLARREO

Note: yaw could also be varied continuously

## Slide 9
CLARREO RSS in Polar 90o Orbit – Orbital Modeling
Goal:
- Time/space/angle matching to obtain ensemble of
samples with data matching noise ≤ 1%
Wielicki et al., IGARSS 2008
Matching requirements:
Within +/- 5 min of the JPSS passing.
VZA match within 1.4° (CLARREO RSS 100 km swath).
SZA < 75o.
At least 10 km effective width of swath.
Figure: CLARREO RSS boresight
locations, which matched JPSS
cross-track data over one year time period.
Inter-calibration with sensors on the JPSS

## Slide 10
Sampling Estimates and Restrictions
Sampling for VIIRS/AVHRR is nadir equivalent 10×10 km area in angular space,
1o CLARREO elevation angle. To estimate number of samples with independent
spatial noise 1 km shift (0.1o in elevation angle ) is required from one sample to
the next in both spatial directions (along and perpendicular to the ground
track). With CLARREO spatial resolution of 0.5×0.5 km the 1 km shift ensures
that only 2 boundary pixels are common.
- This approach to CLARREO/VIIRS RI sampling does not allow the inter-
calibration on detector-by-detector basis. Relative calibration of VIIRS
detectors to each other requires the use of VIIRS data alone, and would
be performed using common histogram equalization, or overlapping field-of-
view methods.
For CERES sampling is estimated taking into account CERES FOV size of 25 km
at nadir (from JPSS orbit, 2.5o in CLARREO elevation angle), and data acquisition
rate 330/180 = 1.8 footprints per degree of scan angle every 3.3 seconds.
General Restrictions:
- SZA < 75o;
- CLARREO RSS effective swath > 10 km (VIIRS), and > 25 km (CERES).
- VZA difference < 1.4o.

## Slide 11: CLARREO RSS / Target Sensor - RI Sampling
VIIRS
CERES
Summary: Monthly (top) and seasonal (bottom) RI sampling (RAAN = 0o)
Red Lines: Required number
of samples for RI monthly error contribution 0.45% (k=1)
Red Lines: Required number
of samples for RI seasonal error contribution 0.25% (k=1)
NOTES: - The number of RI samples is derived under assumption of uniform
sampling distribution in relevant parameters to VIIRS sensitivity
to polarization: DOP and polarization angle.
- The sampling estimate for VIIRS derived for 670 nm wavelength.
- 1% noise : variability of noise due to time matching is averaged.

## Slide 12: CLARREO RSS / GEO Imager – Inter-calibration Sampling
Summary: Daily (left) and monthly (right) RI sampling (CLARREO orbit RAAN = 0o)
GEO: GOES-East (longitude = 75o W)
Note on time matching: future GEO imagers will have shorter duty cycle (about 10 min).

## Slide 13: CLARREO RSS on ISS / Target Sensor - RI Sampling
Summary: Monthly and seasonal RI sampling (CLARREO on ISS)
CLARREO RSS boresight
locations matching JPSS
cross-track data over one year time period.
Estimated inter-calibration
sampling for VIIRS and CERES on the JPSS, AVHRR on the MetOP.

## Slide 14: Summary on CLARREO RSS Inter-Calibration Sampling
(1) CLARREO RSS instrument radiometric accuracy at 0.15% (k=1).
(2) CLARREO RSS 2-D data matching on-orbit (azimuth and elevation):
constant in azimuth and varying in elevation within matching tent.
(3) All reference inter-calibration goals are feasible from sampling point of view
CLARREO RSS instrument in polar 90o inclination orbit or the ISS orbit provides
adequate sampling monthly, seasonally and annually for inter-calibration of
sensors on the JPSS, MetOP, and in GEO satellites.
References:
C.M. Roithmayr, and P.W. Speth, Chap. 13, “Analysis of Opportunities for Intercalibration between
Two Spacecraft," Advances in Engineering Research, Vol. 1, edited by V. M. Petrova, Nova Science
Publishers, Hauppauge, NY, 2012, pp. 409 - 436.
C.M. Roithmayr, C. Lukashin, P.W. Speth, K. Thome, B.A. Wielicki, D.F. Young, “CLARREO Approach
for On-Orbit Reference Inter-Calibration of Reflected Solar Radiance Sensors,” submitted to IEEE
Tran. Geo. Rem. Sensing, February, 2013.
C.M. Roithmayr, C. Lukashin, P.W. Speth, K. Thome, D.F. Young, B.A. Wielicki, “Opportunities to
Intercalibrate Radiometric Sensors from International Space Station,” in preparation for submission
to JTECH, March, 2013.

## Slide 15
3
CLARREO RSS Approach to Account for Imager Sensitivity to Polarization on Orbit
(a) Polarization factors for Aqua band 8.
(b) Detector-averaged polarization factors for Aqua.
Sun and Xiong: "MODIS Polarization-Sensitivity Analysis”,
IEEE Trans. on Geo. and Rem. Sensing, v. 45, n. 9, 2007.
Objective: Take into account MODIS/Terra/Aqua & VIIRS/JPSS sensitivity to polarization in orbit
by providing Polarization information on as function of viewing geometry and
scene type.
Impact: Accuracy of Level-1B data (intercal), Ocean Color and Level-2 Aerosol data products.

## Slide 16: Imager Calibration Model (MODIS as an example)
MODIS calibration model, reflectance factor (Xiong et al., 2003, 2006)
θEV - solar zenith angle
m1 - factor from solar calibration (SD and SD Monitor)
dnEV - detector response to earth radiance
dES - sun-to-earth distance
kinst - temperature correction coefficient
ΔT - temperature difference from reference value
RVSEV - response versus scan angle
Simplified RI Imager calibration model with polarization factor in:
m - sensitivity to polarization, it is function of θ and χ
ρ0 = ρEV (not-polarized reflectance)
Consistent with
Sun and Xiong 2007.

## Slide 17: CLARREO RSS RI: Polarization Parameters
Degree of linear polarization (P or DOP):
Polarization angle, defined relative to viewing plane
(PARASOL definition, range from -45o to 135o):
Note: The χ should be 90o for scattering in principle plane

## Slide 18: Polarization Data from PARASOL (2006.04.01)
PARASOL data:
Simulated cross-track sampling,
1o ✕ 1o lon/lat grid,
670 nm wavelength.
Cumulative sampling for
PARASOL Polarization bands

## Slide 19: Examples of Empirical PDMs (12 days of PARASOL data)
40o < SZA < 50o, 670 nm wavelength.
a) Clear-sky ocean:
WS < 2.5 m/s
b) Overcast water clouds over ocean:
5 < OD < 10
c) Overcast ice clouds over ocean:
5 < OD < 10
Note: DOP patterns are strongly
dependant on scene type, but the
Polarization angle is very similar.
DOP:
Polarization angle:

## Slide 20: Examples of Theoretical PDMs (clear-sky ocean)
The total reflectance and DOP at the principal plane calculated with the ADRTM
at a wavelength of 670 nm. Pristine clear atmosphere with the mid-latitude summer
atmospheric profile is assumed. The solar zenith angle is 33.3o. Wind direction is at 0o.
Wind speeds are 5.0 m/s, 7.5 m/s, 10.0 m/s, and 15.0 m/s, respectively.
Calculations by Wenbo Sun

## Slide 21: CLARREO RSS / Imager Inter-Calibration Formalism
Constraints for CLARREO/Imager RI samples on orbit:
CLARREO/Imager reflectance difference (scalar and linear terms):
A0 and G0 - for samples with not polarized reflectance
Ap and Gp - for samples with polarized reflectance
Let us call A’s and G’s reference inter-calibration offset and gain…

## Slide 22: CLARREO RSS Inter-Calibration: Imager Sensitivity to Polarization
RI gain difference for non-polarized and polarized
reflectance is attributed to sensitivity to polarization
Imager sensitivity to polarization on orbit
Relative uncertainty of sensitivity
to polarization on orbit
- First term is relative uncertainty of RI gain
difference (RI sampling).
- Second term is relative uncertainty of the PDMs.

## Slide 23: CLARREO/Imager Inter-Calibration: Resulting Radiometric Uncertainty
For fixed θ and χ values, assuming no correlation, reflectance variance:
Then, relative radiometric uncertainty:
First term is uncertainty for
non polarized reflectance.
Second term is from polarization
effects.
The first term is combined accuracy of CLARREO, RI random error, and remaining
Imager uncertainty (e.g. month-to-month stability).

## Slide 24
Inputs for calculation:
m = 3% (k=1)
σpdm = 5%, 10%, 15% (k=1)  Uncertainty in Polarization
σg0 = 0.10% (k=1)
σgp = 0.15% (k=1)
σclarreo = 0.15% (k=1)
σresidue = 0.10% (k=1)
Numerical Estimates of Inter-Calibrated
Imager Uncertainty:
Single measurement of m on orbit

## Slide 25: Numerical Estimates: Imager Sensitivity to Polarization Single measurements of m on orbit
Inputs for calculation:
m = 3%, 5%, 10%
σpdm = 5%
σg0 = 0.10%
σgp = 0.15%
σclarreo = 0.15%
σsensor = 0.10%

## Slide 26
(1) CLARREO RSS instrument radiometric accuracy at 0.15% (k=1).
(2) CLARREO RSS 2-D data matching on-orbit (azimuth and elevation): constant in azimuth and varying in elevation within matching tent.
(3) Polarization Distribution Models are required for inter-calibrating
sensor’s sensitivity to polarization, and further its stand-alone
operation. A global all-sky set of models should be built for DOP
and polarization angle χ .
Summary on CLARREO RSS Polarization Approach
References:
C. Lukashin, B.A. Wielicki, D.F. Young, K. Thome, Z. Jin, and W. Sun, “Uncertainty Estimates for Imager
Reference Inter-Calibration With CLARREO Reflected Solar Spectrometer”, IEEE TGRS, Special Issue on
Instrument Inter-calibration, DOI: 10.1109/TGRS.2012.2233480, 2012.
Wenbo Sun, B.A. Wielicki, D. F. Young, and C. Lukashin, “Modeling polarized solar radiation from
ocean-atmosphere system for CLARREO inter-calibration applications,” in preparation for submission
to Journal of Geophysical Research, 2013.
C. Lukashin, Z. Jin, D.G. Macdonnell, K. Thome, W. Sun, B.A. Wielicki, D.F. Young , “Requirement for
Instrument Sensitivity to Polarization for Climate Observing System in Reflected Solar,” in preparation
for submission to Journal of Geophysical Research, 2013.

## Slide 27
(1) Climate quality measurements require accurate instrument calibration.
Inter-calibration ties the calibration of one instrument to a more accurate
reference instrument.
(2) The MIIC Framework predicts near co-incident measurements with matched viewing geometries for instruments on separate spacecraft and efficiently acquires these data from remote data servers using OPeNDAP and server-side functions.
(3) New server-side functions will complement those now in place for format translation and subset selection to minimize the computation and network demands placed on instrument teams that perform multi-instrument inter-calibration in the distributed and heterogeneous context of the NASA Earth Science ACCESS infrastructure.
(4) The current MIIC project will demonstrate LEO-GEO and LEO-LEO
inter-calibrations use cases.
Multi-Instrument Inter-Calibration (MIIC) Framework
The MIIC Framework Objectives:
C. Currey (PI, NASA LaRC), A. Bartle, C. Lukashin, D. Doelling, C. Roithmayr

## Slide 28
Client-side (local) filtering and science algorithm processing:
- Web interface to allow users to optimize matching criteria.
- Automatically executes inter-calibration plans.
  - Computes inter-calibration coefficients and persists to database.
  - Persists matched radiances on client-side for further processing.
  - Develop science library for inter-calibration and comparative analysis.
The MIIC Framework Features
Intelligent Event Prediction software (including sensor’s operation mode):
  Based on SGP4 orbit propagator (Java implementation).
  Predict when/where footprint viewing geometries match criteria – geolocate pointing
  vectors in sensor’s scan plane (+/- 50°), calculate viewing angle relative to both -
  spacecraft and the sun.
  - Identifies data filenames and Lat-Lon bounding boxes for events (IC plan).
Efficient access to remote data based on the OPeNDAP:
- Develop OPenDAP server-side functions (gridding, spectral & spatial convolution).
- Using OPeNDAP Hyrax server.
- Using OPeNDAP Freeform and HDF4 handlers.
- Significant reduction in data volume by transferring gridded data.

## Slide 29
The MIIC Framework Architecture