## Slide 1: NOAA GPRC Report
2013 GSICS Annual Meeting
Williamsburg, VA
03/04/2013-03/08/2013

## Slide 2: Outline
Operation
Research
Actions
Outlook

## Slide 3: Operations
GOES Imager GEO-LEO IR correction products promoted to pro-operational status
Product access
Bias monitoring
Retro-processing status report
DCC calibration

## Slide 4: Product promotion
GOES Imager GEO-LEO IR correction product promoted in pre-operational status
  Progress in 2012:
    End-to-end and system levels of uncertainty analyses traceable to Metop-A/IASI, following Hewison (2013, TGRS)
    Implemented the version control for the softwares

## Slide 5: GEO-LEO Inter-Calibration Products
Pre-operation GEO-LEO correction products download server:
  http://gsics.nesdis.noaa.gov/thredds/nesdisResults.html
  Near Real-time Correction – update everyday
  Re-analysis Correction – updated once per month
Product monitoring wiki-website:
  https://gsics.nesdis.noaa.gov/wiki/GPRC/WebHome
  Add the monitoring of GOES-15 Imager IR correction

## Slide 6
MTSAT-1R/MTSAT-2
FY-2D
Aqua/AIRS
Metop-A/IASI
GOES-13
GOES-12
Aug2003
Jun2007
Aug08
Meteosat-7
GOES-15
GOES-14
Meteosat-9
Aug08
Ongoing NOAA GPRC GEO-LEO inter-calibration
Aug08
FY-2C
Apr 2010
GOES-11
Dec 2011
Dec 2011
Meteosat-10
Jan2013
Jan2013
Aug08
Apr2011
Apr2011

## Slide 7
GEO-LEO Retro-Processing (CIMSS/University of Wisconsin)
Satellite | Begin Date (year/jday) | End Date (year/jday) | Total number (Days) | Status
GOES-8 | 2002/224 | 2003/090 | 143 | Completed
GOES-9 | 2003/113 | 2005/321 | 854 | Completed
GOES-10 | 2002/224 | 2009/334 | 2350 | 95% Completed
GOES-11 | 2006/152 | 2011/340 | 1975 | Completed
GOES-12 | 2003/016 | 2010/364 | 2746 | 95% Completed
Meteosat-9 | 2007/101 | 2011/364 | 1464 | 95% Completed
GEO vs. AIRS Collocations

## Slide 8: DCC Calibration for GOES-13 Imager
GEO satellite | Aqua-MODIS (%) | Calibration Transfer (%) | Trend (%) | SBAF (%) | Total Uncertainty (%)
GOES-13 | 1.64 | 1.2 (?) | 0.5 | 0.27 (GOME) 0.30 (SCI)A | 2.2
GOES-15 | In-sufficient DCC pixels. Need multiple months of DCC pixels for a robust DCC histogram |  |  |  | 
Uncertainty components (from D. Doelling, DCC ATBD)

## Slide 9: Research
GOES calibration anomaly investigation
GOES Imager band-to-band co-registration error correction
GOES vs. AIRS/CrIS/IASI
Desert-based vicarious calibration for GOES Imager (to be presented later)
Lunar calibration – ROLO vs. M-T model
Combined vicarious calibration method
METOP-A/B AVHRR vis (Chang) (to be presented later)

## Slide 10: GOES Calibration Anomaly Investigation
GOES-15 Sounder LW radiance anomaly, 29/09/2012-01/10/2012
  GSICS GEO-GEO inter-comparison showed the radiance anomaly only occurred at LW channels, Jumped suddenly at ~00:00z – 12:00z on 29/10/12. The diurnal anomaly reduced and back to normal at 01/10/12.
  Root cause: pre-mature change of calibration mode
Patch temperature change/variation
Calibration Anomaly

## Slide 11: GOES Imager band-to-band co-registration error correction
Accuracy of Spatial calibration is essential for meaningful interpolation of geophysical parameters and radiance inter-comparison
Band-to-band co-registration error out of specification can be observed at certain time of day at some GOES Imager instruments due to diurnal heating variation of the optics’ components
Operational correction algorithm is being implemented.
“False” fog products, courtesy of U. Wisc.
Diurnal co-registration errors at G8 thru G15 (by M. Grotenhuis, NOAA/NEDIS/STAR)

## Slide 12
GOES vs. AIRS/CrIS/IASI Inter-Calibration – long-term monitoring
Notes: Consistent diurnal Tb difference in between AIRS and CrIS
The difference among AIRS/CrIS/IASI in general is less than 0.2K
AIRS is slightly warmer than CrIS at ~0.2K at Ch6.5um
AIRS is slightly warmer than CrIS at Ch10.3um, however, the Tb difference seems smaller at Jun-July than Apr-May at night-time data
Among the three GOES IR channels, Tb difference between AIRS and CrIS is smallest at Ch13.3um
CrIS overall radiometric calibration accuracy is very stable and comparable with AIRS/IASI during the study period

## Slide 13: GOES vs. AIRS/CrIS/IASI Inter-Calibration – Diurnal Variation
Data: 04/18/2012 – 05/28/2012
Notes: Consistent diurnal Tb difference in between AIRS and CrIS
The difference among AIRS/CrIS/IASI in general is less than 0.2K
AIRS is slightly warmer than CrIS at ~0.2K at Ch6.5um
AIRS is slightly warmer than CrIS at Ch10.3um, however, the Tb difference seems smaller at Jun-July than Apr-May at night-time data
Among the three GOES IR channels, Tb difference between AIRS and CrIS is smallest at Ch13.3um
CrIS overall radiometric calibration accuracy is very stable and comparable with AIRS/IASI during the study period

## Slide 14
GOES vs. AIRS/CrIS/IASI Inter-Calibration – day/night difference
Chart: Ch4(10.7um) AIRS-CrIS
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.5 | 19 | 19.5 | 20 | 20.5 | 21 | 21.5 | 22 | 22.5 | 23 | 23.5
Apr-May | 0.13402 | 0.1496 | 0.0815 | 0.22083 | 0.13064 | 0.1526 | 0.04037 | 0.18814 | 0.21527 | 0.26377 | 0.00519 | 0.1387 | 0.04722 | 0.04289 | 0.13064
Jun-Jul | -0.03035 | 0.053 | 0.12483 | 0.04329 | 0.12461 | 0.06644 | 0.1549 | 0.04906 | 0.17119 | 0.15012 | 0.0256 | -0.0627 | 0.05711 | 0.07146
Chart: Ch6(13.3um) AIRS-CrIS
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.5 | 19 | 19.5 | 20 | 20.5 | 21 | 21.5 | 22 | 22.5 | 23 | 23.5
Apr-May | -0.04639 | 0.00608 | -0.02261 | -0.1231 | -0.01374 | -0.00484 | -0.09146 | 0.06556 | -0.07278 | 0.04941 | 0.00834 | 0.01199 | 0.0627 | -0.06058 | 0.0202 | -0.08661 | -0.08034 | -0.10928
Jun-Jul | 0 | -0.06646 | -0.05042 | -0.10803 | -0.07128 | -0.04222 | -0.06234 | -0.10891 | -0.01279 | -0.13873 | 0.01571 | 0.0211 | -0.00022 | -0.11418 | -0.02869 | -0.06833 | 0.07084 | -0.09254 | -0.10782 | -0.0253
Chart: Ch3(6.5um) AIRS-CrIS
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.5 | 19 | 19.5 | 20 | 20.5 | 21 | 21.5 | 22 | 22.5 | 23 | 23.5
Apr-May | 0.06436 | 0.15457 | 0.11383 | 0.11658 | 0.1049 | 0.12828 | 0.15422 | 0.18501 | 0.07287 | 0.12942 | 0.10335 | 0.12718 | 0.10677 | 0.12109 | 0.12637 | 0.14327 | 0.13493 | 0.17808 | 0.12354 | 0.12941
Jun-Jul | 0.10608 | 0.11523 | 0.09387 | 0.1319 | 0.11401 | 0.13279 | 0.1723 | 0.08718 | 0.0434 | 0.12704 | 0.14054 | 0.1282 | 0.12249 | 0.09956 | 0.1443 | 0.10207 | 0.10323 | 0.17772 | 0.09041
Notes: Consistent diurnal Tb difference in between AIRS and CrIS
The difference among AIRS/CrIS/IASI in general is less than 0.2K
AIRS is slightly warmer than CrIS at ~0.2K at Ch6.5um
AIRS is slightly warmer than CrIS at Ch10.3um, however, the Tb difference seems smaller at Jun-July than Apr-May at night-time data
Among the three GOES IR channels, Tb difference between AIRS and CrIS is smallest at Ch13.3um
CrIS overall radiometric calibration accuracy is very stable and comparable with AIRS/IASI during the study period

## Slide 15: Desert Calibration
[32.05N-32.35N, 114.4W-114.7W]
25 pixels
Seasonal variability
GOES image

## Slide 16: Lunar Calibration: MT vs. ROLO model
Miller-Turner model, an independent lunar irradiance model (Miller and Turner, TGRS, Vol. 47(7), 2009)
  Hyperspectral, covering 0.2-2.8um with 1nm resolution
  Benchmarked against observation and ROLO model
  Publically available
  Relative calibration
  Doesn’t account for lunar libration impact
Chart: Moon Irradiance (mM/m^2/um)
| 2003-12-04T14:16:40. | 2004-08-30T18:10:03.
Measurement | 1.9501 | 4.9753
ROLO | 1.936 | 4.724
Miller-Turner | 1.8638 | 4.802
Difference between MT and ROLO model <5%

## Slide 17: Obs-MT vs Obs-ROLO
Two moon images observed on 02/14/2006 at ~1 hour difference (in the dark circles)
  The MT Irr./ROLO Irr. ratios at the two observations are identical (right)
  The consistent large obs/simulation ratios with both simulations (left) indicate that the ratio difference comes from the observation variation, most likely due to the impacts of incident angle dependent scan mirror reflectance and variation in space background.
Trending uncertainty using the 20 observations
  MT: 2.5%, data with phase angle (>5o and <60o) excluded.
  ROLO: 1.3% , all the 20 data.
Notes: 1. Confirmed that the relative large variation of the obs/simulation ratios at the one-hour-different-observation-pairs is attributed to the uncertainty in the GOES measurements.
2. GOES Trending uncertainty with current MT model result is larger than that of ROLO results (2.5% vs 1.3%, k=1)
3. Confirmed that when phase angle (>5 and <60) excluded, MT and ROLO irradiance difference is within 5%, however, the difference seems phase-angle dependent.

## Slide 18: MT vs. ROLO
Confirmed that the MT and ROLO model irradiance difference is <5% if abs(phase angle) is within the range of [5 , 60]
In this case, the difference seems phase angle dependent

## Slide 19: Combined Vicarious Calibration Algorithm
 | Valid # | Total # | Usage Frequency | trending uncertainty
DCC | 54 | 96 | 56.25% | 1.277%
Desert | 26 | 87 | 29.86% | 2.129%
Moon | 4 | 27 | 14.82% | 2.050%
MODIS | 11 | 25 | 44.00% | 1.127%
Star | 28 | 56 | 50.00% | 0.974%
Combined method |  |  |  | 0.484%
average the daily degradation at monthly scale
Recursive filtering algorithm to remove the outliers
Anchor the smoothed trending with one GOES-MODIS inter-calibration result
Fit with a quadratic function

## Slide 20: Metop-A/B AVHRR VNIR Calibration
Details presented by Dr. T. Chang on 03/04/2013

## Slide 21: Actions
Actions
  GOES instrument information (Action…)
Action Ref | Description | Due Date | State/Update
GRWG06_16 | Compile a list a existing activities concerning composite satellite imagery | Jun 2011 | No activity
GRWG06_17 | GEO satellite overlap time overlaps | Dec 2011 | https://gsics.nesdis.noaa.gov/wiki/Development/InstrumentInformation; closed
Joint07_05 | Reports on what events can be made available from legal point of view | Mar 2013 | Open, had some email discussions
EP-12.05 | Each GPRC to consider implementing NRT distribution of calibration correction information at Level1B data | Sept 2012 | Closed. NOAA cannot do it.
Joint06_01 | Recommend a signal AIRS flag file to be adopted by all AIRS users | Dec 2011 | Need clarification for this action
Joint07_09 | Check and provide comments to provide shortlist of instrument events to be logged | Mar 2013 | Open, had some email discussions with action lead and GDWG chair

## Slide 22: Outlook
GOES-R ABI
  To be launched in 2015
  ABI covering 16 spectral channels, 6 VNIR + 10 IR, onboard calibration for solar reflective channel, improved spatial resolution
NPP/JPSS instruments
  CrIS  Aqua
  VIIRS  MODIS
Metop-B/IASI  Metop-A/IASI
Challenging
  Bridging the multiple references

## Slide 23: Summary
Operation status
  normal
  Looking forward to the operation for the GOES GEO-LEO IR products
MT model is valuable to validate the ROLO results
Combined method can improve the relative calibration accuracy better than 0.5%.
Need to continue to work on the absolute calibration (traceable to Aqua MODIS) of current existing vicarious calibration methods
NPP and Metop-B provide more opportunities.
  Distractions – bridging over the multiple reference requires thoroughly understand the calibration differences on all-sky data at various temporal scales, from diurnal to long-term scales.