## Slide 1: Uncertainty evaluation of GSICS MTSAT-IASI correction products
Masaya Takahashi
Meteorological Satellite Center/
Japan Meteorological Agency

## Slide 2: Contents
Background
Methodology of uncertainty evaluation
Results
Systematic error
Summary and future plan

## Slide 3: Background
Current status of MTSAT-1R/-2 IR GSICS correction
Demonstration phase, started in July 2010
Reference sensor: Metop-A/IASI and Aqua/AIRS
Still in the “demonstration phase” beyond the maximum period: 365-days
GSICS Web meeting in Apr 2012
JMA MTSAT Imager GEO-LEO IR product
  Need the traceability /uncertainty analysis documentation
  So far have two reviewers’ comments on the ATBD and data usability and reliability.
From the presentation by F. Yu

## Slide 4: MTSAT-2 Brightness Temperature Difference against IASI and AIRS
3.8um(IR4)
6.8um(IR3)
10.8um(IR1)
12.0um(IR2)
0 5 10 15 20 (UTC) 0 5 10 15 20 (UTC)
30 minutes mean brightness temperature differences between MTSAT-2 and IASI/AIRS (Feb. 2012)
IASI
AIRS
The midnight blackbody calibration correction (MBCC) is active for MTSAT-2 in eclipse season.
Internal user’s feedback: “Midnight calibration error (MCE) strongly contaminated SST products produced by MSC/JMA. If hourly inter calibration become available by GSICS, MCE will be corrected more effectively.”

## Slide 5: Methodology of uncertainty evaluation
Follows the method described in Hewison (2013) for the SEVIRI-IASI product, Yu and Wu (2012) for GOES-IASI product.
Hewison, T. J., 2013: An Evaluation of the Uncertainty of the GSICS SEVIRI-IASI Inter-Calibration Products", IEEE TGRS., vol. 51, no. 3.
F. Yu and X. Wu: “GSICS GEO-IASI Inter-calibration Uncertainty Evaluation”, version dated on 2012-08-17.
L： Radiance of monitored sensor (GEO)
L^：Radiance of reference sensor (LEO)
Obtain a different corrected radiance from a regression using radiance w/ each perturbation
L： Radiance
i：each collocation
j: each process
GSICS correction g(L) :
sensitivity of the radiances in each collocation to perturbations in each variable
Typical differences in sampling variables between the monitored (MTSAT) and reference (IASI) instruments ( ) are estimated for each process of the inter-Cal.
Uncertainty on Li due to process j:

## Slide 6: Systematic error
: Recalculated GSICS correction w/ the perturbation from (1)
: GSICS correction
: Systematic errors introduced by process j
Temporal mismatch
Longitudinal and latitudinal mismatch
Geometric mismatch
Spectral mismatch between GEO and LEO
Spectral calibration of reference sensor
Processes to be considered
L： Radiance
i：each collocation
j: each process

## Slide 7: Results: systematic error’s perturbations and sensitivities
 | Δx | Sensitivity ∂Lj/∂x (mW/m^2/sr/cm^-1/Δx) |  |  | 
 |  | IR4 (3.75um) | IR3 (6.75um) | IR1 (10.8um) | IR2 (12.0um)
Temporal mismatch | -12 sec | -0.01009 | -0.00059 | 0.1458 | 0.19811
Longitudinal mismatch | 0.96 km | -0.00005 | 0.00017 | 0.00055 | 0.00055
Latitudinal mismatch | 1.56 km | 0.00002 | 0.00020 | 0.00319 | 0.00350
Geometric mismatch | -0.0018 | ongoing |  |  | 
Spectral mismatch | 1 | ongoing |  |  | 
Spectral calibration | 2 ppm | ongoing |  |  | 
MTSAT-2 – IASI systematic error’s perturbations and sensitivities

## Slide 8: Temporal mismatch
01 03 05 07 09 11 13 15 17 19 21 23
01 03 05 07 09 11 13 15 17 19 21 23
01 03 05 07 09 11 13 15 17 19 21 23
01 03 05 07 09 11 13 15 17 19 21 23
Time series of mean of radiance change (2013/02/07)
Δt | -12 sec
3.75um | -0.01009
6.75um | -0.00059
10.8um | 0.1458
12.0um | 0.19811
Sensitivity
(mW/m^2/sr/cm^-1/Δx)
Δt: Calculated from collocation data
Radiance change calculated from MTSAT-2 observation in successive data
Diurnal variation
12-11UTC difference as a sensitivity of temporal mismatch

## Slide 9: Longitudinal and Latitudinal Mismatches
http://mscweb.kishou.go.jp/landmark_b/seq03.htm
MTSAT-2 Navigation error
Calculate from navigation monitoring data at MSC/JMA
Average from the start of the operation (1 Jul, 2010) to 31 Dec. 2012
Longitudinal error: 0.37 km
Latitudinal error: 1.76 km
IASI L1C geolocation accuracy
2km (Blumstein et al., 2004)
Δlon = (0.37+2)/√2/√3 = 0.96 km
Δlat = (1.76+2)/√2/√3 = 1.56 km
MTSAT navigation monitoring website
: mean of radiance difference between adjacent pixels of MTSAT-2 observation (Feb. 28, 2013 1200UTC data are used)
 | 3.75um | 6.75um | 10.8um | 12.0um
Lon | -0.00005 | 0.00017 | 0.00055 | 0.00055
Lat | 0.00002 | 0.00020 | 0.00319 | 0.00350
(mW/m^2/sr/cm^-1/Δx)

## Slide 10: Summary and future plan
Current status of MTSAT-1R/-2 IR GSICS correction
Demonstration phase, started in July 2010
Reference sensor: Metop-A/IASI and Aqua/AIRS
Additions and modifications to the netCDF conventions have been done
Internal user’s feedback
Toward the implements to Pre-Operational phase
Completion of uncertainty evaluation
Documentation

## Slide 11: Backup slides

## Slide 12: GEO-LEO Spectral mismatch