## Slide 1
On the Use of Infrared Spectral Band Adjustment Factors
To Extend IASI to Archived Data
Patrick Minnis1, Ben Scarino2, Arun Gopalan2, Dave Doelling1
1NASA Langley Research Center, Hampton, VA
2SSAI, Hampton, VA USA
GSICS Annual Meeting, Williamsburg, VA USA
4-8 March

## Slide 2
Objectives
• Develop an empirical spectral response function (SRF) radiance data base for each satellite imager channel & create spectral band adjustment factors for each potential pair of imager channels
- solar channels, Ref: Sciamachy (see Scarino talk)
- infrared channels, Ref: IASI, AIRS
• Complete the construction of a satellite inter-calibration algorithm suite
• Apply the algorithms to inter-calibrate meteorological and research satellite imager channels taken since 1976 using the Aqua MODIS as a calibration standard

## Slide 3
Background
• ISCCP IR calibration: straight transfer of a LEO-to-GEO satellite 11 µm temperature, TGEO = TLEO = a T’GEO + b, with no spectral correction
• Reference LEO imager calibration adjusted using 10th & 90th Percentile mean temperatures
Current GOAL
• Transfer IASI calibration via MODIS to AVHRR and to earlier GEOs
• Retain spectral characteristics of each imager
- “true temperature”, not AVHHR equivalent
• Use trends in various parameters (e.g., percentiles, DCC) to monitor older AVHRRs

## Slide 6
Approach
• Derive pseudo-radiances LDl for each target satellite channel SRF RDl from either SCIAMACHY, IASI, CrIS, or AIRS spectral radiance Ll depending on the satellite channel and time period
LDl = S Rli Lli’ (li - li-1) / S Rli’ (li - li-1)
• Determine spectral band adjustment factors (SBAF) relative for a target imager, t, to a particular reference, r, from pseudo-radiances
Tlt = SBAFlrt(Tlr) = a Tlr + b
• Apply NSRT method to matched imager data from reference and target satellite imagers for entire overlap period, ‘ indicates data
Tlt = SBAFltr(Tlt) = (a T’lr + b) = a’ Tlt’ + b’
Force fits denote b and b’ forced to zero

## Slide 7
Examples of Pseudo-radiance Sets
Aqua MODIS
NOAA-18 AVHRR
GOES-11 Imager

## Slide 8
Spectral Response Functions on IASI Mean Footprint Radiance Spectrum
10 – 12 µm Channels, All Sky Tropical Ocean

## Slide 9
Pseudo-radiances from IASI, 12-µm Channels, GOES-11/MODIS

## Slide 10
Pseudo-radiances from IASI, 12-µm Channels, GOES-11/NOAA-18

## Slide 11
Pseudo-temperatures from IASI, 12-µm Channels, GOES-11/MODIS

## Slide 12
Pseudo-temperatures from IASI, 12-µm Channels, GOES-11/NOAA-18

## Slide 13
Spectral Response Functions on IASI Mean Footprint Radiance Spectrum
3.7 – 3.9 µm Channels, Night, All Sky Tropical Ocean
AVHRR
MODIS
GOES-11
Use model calculations for fill?

## Slide 14
Pseudo-radiances from IASI, 3.8-µm Channels, GOES-11/MODIS

## Slide 15
Pseudo-radiances from IASI, 3.8-µm Channels, GOES-11/NOAA-18

## Slide 16
Pseudo-temperatures from IASI, 3.8-µm Channels, GOES-11/MODIS

## Slide 17
Pseudo-temperatures from IASI, 3.8-µm Channels, GOES-11/NOAA-18

## Slide 18
Testing Use of SBAFs & Cross-Calibrations to Extend Record Into Archive
• Three or four way cross calibration, apply SBAF or use raw data only
1) intercalibrate satellites 1 and 2
2) intercalibrate satellites 2 and 3 after first step
3) intercalibrate satellites 1 and 3
4) compare results of steps 1 and 3, does SBAF improve agreement?
• Start with modern satellites, then older imagers, MODIS as reference

## Slide 19
Channel | MODIS / GOES-11 | GOES-11 / NOAA-18 | MODIS / NOAA-18 (approx.) | MODIS / NOAA-18 (direct) | Difference | Difference (No SBAF)
12 μm | 1.0005 1.0019* | 0.99851 | 0.9990 | 0.9996 1.0020 | 0.06% | 0.07%
11 μm | 1.0013 0.9989 | 0.99804 | 0.9993 | 1.0011 0.9991 | 0.18% | 0.18%
3.8 μm | 0.99803 0.99810 | 0.99986 | 0.9980 | 1.0008 0.9991 | 0.28% | 0.28%
MODIS / GOES-11
direct
MODIS / NOAA-18
direct
GOES-11 / NOAA-18
Force Slope Comparisons
Using SBAFs to extend calibrations: MODIS to N-18 AVHRR; 3 satellites
12-µm channel, night, June 2008
*SBAF slope

## Slide 20
Channel | MODIS / NOAA-18 | NOAA-18 / GOES-11 | GOES-11 / NOAA-16 | MODIS / NOAA-16 (approx.) | MODIS / NOAA-16 (direct) | Difference | Difference (No SBAF)
12 μm | 0.9988 | 1.0022 | 0.99825 | 0.9992 | 1.0033 1.0021* | 0.41% | 0.41%
11 μm | 1.0002 | 1.0026 | 0.99705 | 0.9998 | 1.0055 0.9996 | 0.57% | 0.57%
3.8 μm | 0.9997 | 1.0005 | 0.99784 | 0.9980 | 1.0094 0.9983 | 1.13% | 1.13%
Force Slope Comparisons (numbers are for SBAF application)
GOES-11 / NOAA-16
MODIS / NOAA-16
Direct
MODIS / NOAA-18
Direct
NOAA-18 / GOES-11
Using SBAFs to extend calibrations: MODIS to N-16 AVHRR; 4 satellites
11 µm channel, night, July 2006
*SBAF slope

## Slide 21
• SBAF corrections for modern IR channels small
- ~0.2%
- ~0.5K
• Satellite to satellite transfer errors larger than SBAF corrections
- 0.06 – 0.28% error for one generation transfer
- 0.4 – 1.1% error for second generation transfer, 1K error
• Errors can probably be reduced by taking longer time periods to increase sampling
• What about older satellites?
Summary of Preliminary Results

## Slide 22
Spectral Response Functions on IASI Mean Footprint Radiance Spectrum
11 Channels, Night, All Sky Tropical Ocean
Meteosat-7
GOES-7
Meteosat-9
GOES-7
• Broader bands on older GEOs

## Slide 23
GOES-7 vs. NOAA-11
Meteosat-7 vs. NOAA-11
Pseudo-temperatures from IASI, 11-µm Channels
GOES-7/NOAA-11, Meteosat-7/NOAA-11

## Slide 24
GMS-3 vs. NOAA-11
Pseudo-temperatures from IASI, 11-µm Channels
GMS-3/NOAA-11
Older Satellites
• SBAF difference nearly double that for 2nd generation GEOS
- ~0.4%
- ~1.2 K
• transfer errors will likely be larger also due to navigation, resolution, etc.

## Slide 25
Future Work
• Develop SBAFs using larger datasets to determine if there are seasonal or diurnal changes
- fill in AVHRR 3.7-µm spectrum
• Test using multiple months of modern data to establish transfer errors
• Perform tests using year or two of 1st generation matched data
• Determine trend correction method for older satellites
- percentiles, DCC, SSTs?
- GSICS reference?
• Perform normalizations, clean up short term variations