## Slide 1
GRWG Web Meeting
2013-10-15
Scoring Scheme to Select Reference Instrument
Agenda
Tim Hewison (EUMETSAT) – A statement of the Problem
Dave Smith (RAL) – Thoughts on Selecting a Reference – in absentia
Bertrand Fougnie (CNES) - A Vision of How to Select the Reference – in absentia
Tim Hewison (EUMETSAT) – A Proposed Scoring Scheme
Group Discussion

## Slide 2: GRWG Minutes 2013-03-05
The discussion then turned to how these factors can be quantified. It was suggested that an error budget for each application would allow the impact of changing each variable to be ascertained - even the operational lifetime, in the case of generating FCDRs from multiple instruments. However, it was recognised that this is a relatively cumbersome process. So it was suggested that we could review the existing uncertainty assessment for the GEO-LEO IR products to assign a weighting to each factor, based on the sensitivity of the resulting GSICS Correction to the likely range of each variable. Each potential reference instrument could then be scored in comparison to IASI and the scores combined in some way, as yet to be determined.
Action: Tim Hewison to draft proposal for a simple scoring scheme based on the uncertainty analysis for GEO-LEO IR and review this at a web meeting by 1 March 2014.

## Slide 3: Application to Other Products
Developed for GEO-LEO IR
Is this applicable to other inter-calibration types?
  LEO-LEO SNO?
    SBAFs, ...
  Pseudo Invariant Targets?
  Other?

## Slide 4: Choice of Reference Instrument (from TGARS Overview paper)
In general, inter-calibration involves the comparison of observations from one monitored instrument to another, defined to be the reference instrument. Observations from these reference instruments provide the common scale on-orbit, against which other instruments are inter-calibrated. The key feature of any reference instrument is its radiometric stability as it defines the calibration’s datum. However, many other factors need to be considered when defining an instrument as an inter-calibration reference. Most obviously, it must be operated concurrently to allow observations to be made which can be directly compared, but their satellite orbits must also allow coverage of the same geographic areas, ideally at the same time. The reference instrument’s spectral coverage also needs to be considered, as ideally it would cover the channels of the monitored instrument and be well-matched such that minimal errors are introduced by the SBAF. For example, a hyperspectral reference instrument can allow full representation of the monitored instruments’ SRF. The reference instrument itself must also be accurately calibrated consistent with other instruments and well characterized to allow better traceability.

## Slide 5: Choice of Reference Instrument (from TGARS Overview paper)
Currently, GSICS is using the Infrared Advanced Sounding Interferometer (IASI) aboard the Meteorological Operational Satellite (Metop)-A satellite as an inter-calibration reference for GSICS products [34]. This is complemented by the Advanced Infrared Sounder (AIRS) onboard Aqua as a transfer standard to expand the inter-calibration opportunity into the time of the day not covered by Metop underpasses [32]. A document has been prepared to demonstrate the suitability of these hyperspectral spectrometers as inter-calibration references [49]. It has been shown that IASI can be used as an excellent inter-calibration reference because it has been well characterized pre-launch and its calibration has proven to be stable in-orbit and consistent with the AIRS with uncertainties ~0.1K (k=1) [50]. This methodology is currently being extended to develop counterpart Geostationary Earth Orbit (GEO) - Low Earth Orbit (LEO) infrared products for historical dataset of geostationary radiances observed before suitable hyperspectral reference instruments were available. The HIRS is being considered as a candidate reference instrument because it has been operated in various incarnations on NOAA and Metop platforms since 1978 [28]. This requires the development of SBAFs to account for the different SRFs of the monitored GEO and reference HIRS instruments. For the RSB, the MODIS sensor provides an excellent spectral coverage and stability, and it has a robust onboard calibration strategy. Since the Aqua MODIS is more stable better calibrated than Terra MODIS [51], [52], it has been selected by GSICS as the current reference for channels in the RSB. In the longer term, reference sensors capable of establishing SI traceability onboard together with appropriate sampling and SRF characteristics are desired to underpin a climate observing system [16].

## Slide 6: A Statement of the Problem
GSICS products need an inter-calibration reference
Inter-calibration  Reference is one instrument
  Other instruments may be used as transfer references
We need a way to select the reference
From a list of candidates
Started asking “How good is it as a Reference?”
  Impact on overall uncertainty
  Score scheme
But first question should be: “Is it good enough?”

## Slide 7: State Your Requirements
Requirements for a Reference come from
Requirements for Inter-Calibration Product
For particular application: NRTC, RAC, ARC, ...
  Date Range
  Geographic Coverage
  Dynamic Range
  Spectral Range
  Geometric Range
  Diurnal Coverage
  ...Others?...
  Total Uncertainty
Threshold Values
  - Below which product not useful
Beneficial Range
  - Above which product benefit increases
Saturation Threshold
  - Above which no additional benefit

## Slide 8: Equate Product Requirements to Reference Requirements
For Each Requirement:
Define Threshold for Usefulness
Define Threshold for Saturation
Define Relative Importance  Weighting
  In terms of Total Uncertainty for Inter-Cal Product

## Slide 9: Assess Candidate References
Assess candidate References against Requirements
Do they meet minimum thresholds?
How do they ‘score’ on sliding scale?

## Slide 10: Other Factors affecting Total Uncertainty
Availability/Sampling
Data Availability!
Date Range
  Continuity!
Geographic Coverage
  Latitude, Longitude
Dynamic Range
Spectral Range
Geometric Range
  VZA, VAA, SZA, SAA, Polarisation
Diurnal Coverage
# Collocations
Instrument Characteristic
Geolocation Accuracy
Polarisation Knowledge
Radiometric Stability
Orbital Stability
Radiometric Noise
Spectral Resolution (incl SRF)
Absolute Accuracy (?)
  Inter-Channel?
Calibration Traceability
Documentation – Validation, Characterisation, etc

## Slide 11: Points from Dave Smith (RAL)
I’m afraid I can’t make it to this meeting due to another meeting. I would like to have joined this as there are some interesting issues to discuss. Some points I would like to raise are:
What is the requirement for the intercalibration? Note that an intercomparison may require consistency between sensors of the same series so absolute calibration may not be the priority.
What are the spectral range and resolution of the reference? Note if a sensor is a filter radiometer – e.g. MERIS, MODIS, AVHRR etc… then it becomes necessary to make adjustments for different sensors.
What is the availability of data for the reference sensor? i.e. is the data easy to get hold of?
How well the sensor is characterised – and are the characterisation data available?
What is the stability of the reference sensor? – Is there documented evidence that said reference is stable?

## Slide 12: Points from Bertrand Fougnie (CNES)
For the today's meeting,
I think the goal is to draw an exhaustive list of points to be considered.
If possible, cross-calibration method(s) has(ve) to be identified for each of these points,
and finally a cross-calibration example with a couple of sensors.
After that, on a second step, points must be sorted, perhaps not scored in the first approach, but at least classified as (for example) :
  mandatory regarding GSICS goals
  nice to have
  not crucial

## Slide 13: Application to Other Products
Developed for GEO-LEO IR
Is this applicable to other inter-calibration types?
  LEO-LEO SNO?
    SBAFs, ...
  Pseudo Invariant Targets?
  Other?