## Slide 1: In-orbit Calibration of The Total Ozone Unit on FY-3B(FY-3B/TOU)
Weihe Wang (wangwh@cma.gov.cn)
Yuan Li (liyuan@cma.gov.cn)
National Satellite Meteorological Center(NSMC)
China Meteorology Administration(CMA)
Inaugural Meeting of GSICS/UV Subgroup, November 13, 2013

## Slide 2: Experience
Research: Spaceborne UV ozone instrument calibration and retrieval algorithm development;
Missions:
Total Ozone Unit (TOU): Total ozone mapper on FY-3A (May 27, 2008 - ), FY-3B (November 5, 2010 - ) and FY-3C (September 23,2013-);
Solar Backscatter Ultraviolet Sounder(SBUS): Nadir profiler on FY-3A(failed in Dec. 2008 due to chopper failure), FY-3B and FY-3C;
Ozone Monitoring Suite: Hyperspectral ozone instrument suite including total ozone mapper, nadir profiler and limb profiler onboard FY-3E(2017-)
Publications:
W. Wang, X. Zhang, X. An, Y. Zhang, F. Huang, Y. Wang, et al., “Analysis for retrieval and validation results of FY-3 Total Ozone Unit (TOU),” Chinese Science Bulletin, vol. 55, pp. 3037–3043, 2010.
W. Wang, X. Zhang, Y. Wang, Y. Wang, Z. ZHANG, L. Fu, et al., “Introduction to the FY-3A Total Ozone Unit(FY-3A/TOU): instrument, performance and results,” International Journal of Remote Sensing, vol. 32, pp. 4749-4758, 2011.
Weihe Wang, Lawrence Flynn, Xingying Zhang et al, Cross-Calibration of the Total Ozone Unit (TOU) With the Ozone Monitoring Instrument (OMI) and SBUV/2 for Environmental, IEEE Transactions on Geoscience and Remote sensing, 50(12): 4943-4955

## Slide 3: Current work on FY-3B/TOU Calibration
Degradation rates of the diffusers;
Instrument degradation estimated from solar irradiance observations;
Degradation rate of the detector estimated from nadir radiance observation of channel 6;
Cross-track dependence correction;
Examples of product;

## Slide 4: Degradation of The Diffusers
Periodical oscillation degradation

## Slide 5: Periodical oscillation degradation
Causes: the difference of the illumination angle of diffusers and other unknown reasons.
Strategy:
  Calculate the periodical formula of oscillation by nonlinear least-squares
    f=f1*f2
    f1(x)=p(1)*power(t,4)+p(2)*power(t,3)+p(3)*power(t,2)+p(4)*power(t,1)+p(5)
    t=x-T*t0
    x0=360,t0=365.25,T＝ceil((x-x0)/t0)
    f2=lp(1)*x^2+lp(2)*x+lp(3)
  Angle correction, need to built a model because of the unknown angle of diffuse plane to the satellite plat.(next work)

## Slide 6: The periodical oscillation corretion
p(1) | p(2) | p(3) | p(4) | p(5)
5.3635E-11 | -3.7256E-08 | 9.5554E-06 | -1.0989E-03 | 1.0396E+00
Coefficients of 4 orders least squares polynomial curve fitting of f1
lp(1) | lp(2) | lp(3)
1.74E-05 | -0.0307 | 110.2324
Coefficients of 2 orders fitting of f2(A2r CH6)

## Slide 7: Ocean vicarious calibration
Latitude: S 30 ~ N30 Longitude: E 160~ W 120
Trend of observation radiance
Trend of the radiance ratio of observation and model
The TOMRAD was used and the total ozone assumed to be 300

## Slide 8: 3 years data analysis (13-Nov-2010 to 17-Jul-2013)

## Slide 9: Monthly minimum and 2 order polynomial curve fitting
Chart: 
| Diffuser (A2/CH6) | Observation radiance | Ratio or observation and model
r^2 | 0.97301 | 0.77806 | 0.90534
Chart: 
| Diffuser (A2/CH6) | Observation radiance | Ratio or observation and model
D | 0.12953 | 0.13914 | 0.12874
The detector degradation monitored by diffusers and ratio is close(0.61%)
Consistency hint the degradation of diffuser A3 is small

## Slide 10: Cross track dependence correcction
The Cross track dependence of radiance is corrected by comparing the observed clear–sky radiances with RTM predicted radiances over the tropical Pacific Ocean, with the GOME-2 L3 (DOAS) ozone products as input. The clear-sky FOVs are chosen by taking the minimum radiometrically equivalent cloud fraction.

## Slide 11: Effect of cross-track dependence
Top left: before correction
Bottom left: after correction
FY-3B was launched on Nov. 15, 2010, the diffusers didn’t have apparent degration.

## Slide 12: FY-3B/TOU Total ozone Product
FY-3B/TOU global ozone product is provided to WOUDC from Aug. 12, 2013 via the web:
http://www.wmo.int/pages/prog/www/WIS/
The FY-3B/TOU Global ozone products can be downloaded from the following link:
http://wisportal.cma.gov.cn:8080/nsmc/FY3B.P_TOUXX_GBAL_L2_TOZ_MLT_GLL_POAD_110KM_MS_TXT.BAWX/
Parent Directory
201308/
201309/
201310/
201311/

## Slide 13: Thanks