## Slide 1: Implementation of DCC at JMA and comparison with RTM
Meteorological Satellite Center of JMA
Keita Hosaka

## Slide 2: Contents
Implementation for JMA Systems
Results
Comparison with RT simulation
Summary

## Slide 3: Contents
Introduction
Comparison of DCC selection between NASA and JMA
Results of JMA processing frameworks
Threshold dependency
PDF stability
Summary and future plan

## Slide 4
Introduction
Histograms are
completely overlapped!
First time for JMA to apply NASA’s algorithm to MTSAT-2/Imager
a
Deep gratitude to NASA for providing DCC verification package!
a
At first, we checked the package and got good results ⇒
JMA

## Slide 5
NASA DCC method for MTSAT-2/Imager
DCC selection thresholds: same as Doelling et al. (2013) except for homogeneity check for MODIS
Presentation by R. Bhatt at the DCC Part I web meeting
5km sub-sampled MODIS L1B (MYD02SSH) are used in this analysis instead of the nominal data (MYD021KM)
DCC domain:
20 S < latitude < 20 N
125 E < longitude < 165 E
SBAF (Spectral Band Adjustment Factor): 0.9376
From web meeting 2012/10
Doelling et al., 2013: The Characterization of Deep Convective Clouds as an Invariant Calibration Target and as a Visible Calibration Technique. IEEE TGRS , 51, 1147-1159.

## Slide 6: JMA processing sequences
MYD02SSH
Collect Data
Download MODIS Data from CLASS
Make working environment
DCC Selection
Roughly → Accurately
Archive Data
Monthly/
Rolling Average
MTSAT-2
HRIT
Archive Statistic Data
Put Products to EUMETSAT Server
Future Plan in Demonstration Phase
Real-time Comparison
*Don’t use cremate data

## Slide 7
Comparison of DCC selection between NASA and JMA
MTSAT-2 11μm channel TB [K]
MTSAT-2 11μm channel TB [K]
NASA DCC verification package
JMA’s own processing program
MTSAT-2 DCC detection at 04UTC 1 July 2012
Thresholds of JMA processing framework:
- Same values in NASA’s DCC verification data document (latitudinal range: N20[deg] ～ S20[deg])
Similar results, but some differences are found because of:
- Data coverage (latitudinal range of the package: -16[deg] < lat < 16[deg])

## Slide 8
Monthly Histogram Comparison
Our results:
- About twice as many DCC pixels
- Mode: almost the same
- Mean: slightly lower
a
a
Angular corrected DN/radiances by Hu DCC BRDF are used in this presentation
latitudinal range: N20[deg] ～ S20[deg]

## Slide 9
TB threshold for DCC detection and PDF bin size
TB threshold
MTSAT-2 visible channel PDF of angular corrected DCC on July 2012
Bin size
Parameters described in the ATBD (TB threshold:205K, Bin size:5) are reasonable
In this study, recommended parameters by NASA are used
(Probability Density Function)

## Slide 10
MTSAT-2/Imager PDF variation with time
Monthly PDFs
Time series of mode and mean of DCC pixels
mode
mean
Consistent results with the ATBD or those of other GEO satellites
Seasonal variation (mode is more stable than mean)
Small sample size or NO observation from October to December every year, due to MTSAT’s ground system maintenance
(Probability Density Function)

## Slide 11
Aqua/MODIS PDF Stability
Input: 5km sub-sampled data (MYD02SSH, Collection 5)
  - IR/VIS spatial homogeneity checks are not applied.
Thresholds for DCC detection: almost same as those for MTSAT-2/Imager
Consistent results with Doelling et al. (2013)
Doelling et al., 2013: The Characterization of Deep Convective Clouds as an Invariant Calibration Target and as a Visible Calibration Technique. IEEE TGRS , 51, 1147-1159.
Monthly PDFs
Time series of mode and mean of DCC pixels
mode
mean
Same as the RT simulation

## Slide 12
Monthly Gain
SBAF for MTSAT-2: 0.9376 (Described in Dave’s presentation in October 2012 GSICS web meeting)
a
Need to compare with the results based on our RT simulation method ⇒
a
Presentation by D. Doelling at the web meeting @ 2012/10

## Slide 13: Summary and future plans
Summary
Implementation of NASA’s DCC method to MTSAT-2/Imager
Preliminary results: good agreement with the ATBD
Issue of MODIS data archive at JMA: difficult to archive nominal Aqua/MODIS data (MYD021KM) due to our disk space and downloading speed
Needs to consider proper thresholds for homogeneity check using 5km sub-sampled data (MOD02SSH)
Future plans
Investigate the impact of BRDF and SBAF on the calibration results
Comparison of the results using nominal Aqua/MODIS data and those using 5km sub-sampled data
Comparison of the results with those based on RT simulation method
Uncertainty evaluation
Creation of netCDF intermediate data which contain selected DCC pixels for replication (and GSICS Correction netCDF)

## Slide 14: Contents
NASA DCC method for MTSAT-2
Vicarious calibration using RT simulation
Comparison of gain between NASA DCC method and RT simulation method
Summary / toward demonstration phase

## Slide 15
Results of Real-Time DCC method
Time series of mode and mean of DCC pixels
mode
mean
Good agreements with the ATBD or those of other GEO satellites
Seasonal variation (mode is more stable than mean)
mode
mean
MTSAT-2/Imager
Aqua/MODIS

## Slide 16: Data Correcting Span for the Demonstration Phase Product
Monthly Mean
Moving Average 30 Days
Data loss mainly due to maintenances of the antenna

## Slide 17: Reanalysis: MODIS 3-year Average

## Slide 18
Vicarious calibration using RT simulation
Method: Comparison of observed and simulated radiance for some targets (collaboration research with the University of Tokyo)
Target: Wide range of radiances
Cloud-free ocean / land, liquid water cloud, and DCC
Radiative transfer calculation:
RSTAR (Nakajima and Tanaka [1986,1988])
Input data: Independent from GEO data
JMA Re-Analysis atmos. profiles (JRA-25/JCDAS)
Aerosol/Cloud optical thickness retrieved from MODIS L1B (MYD02SSH)
MODIS BRDF (MCD43C2) for land target
Aura/OMI total column ozone, …
Result of MTSAT-2 in Feb. 2011
Simulated reflectivity
Observed reflectivity

## Slide 19
Target selection for the RT simulation
 | Ocean | Land | Liquid cloud | DCC
Standard deviation of digital counts (5x5km mean) | < 6 | < 3 | < 12 | < 15
Optical thickness Aerosol for sea and land Cloud for cloud and DCC | < 0.3 | < 0.3 | > 10 & < 40 | > 150
TBB of 10.8um ch. | >273K | > 273K | > 273K | < 205K
Thresholds used in the target selection for MTSAT-2/Imager
Spatially uniform scene
Small standard deviation of digital counts in a target area
Geometrical condition
Solar/satellite zenith angle < 60
Exclude data around sun-glint area
Ice crystal shape for DCC simulation: Hexagonal column (Yang et al. 2000)
To minimize the uncertainty, cloud with large optical thickness are used.

## Slide 20
Comparison of gain between NASA DCC method and RT simulation method
Gains by RSTAR simulation are derived from direct comparisons between observation and RT simulation
Similar trends, but large variance (seasonal variation) in results of the vicarious method
Time series of monthly visible channel gain
NASA DCC method
Vicarious method using RT simulation

## Slide 21: Properties of RT Simulation & It’s Statistics
In the statistics of RT simulation, the offset of liner regression is variable.
  But if we change offset to 0, the regression slopes may change little. Because there are cloud-free oceans in low levels of both reflectivities.
We tried to use only DCC target in RT simulation, but results have larger variance.
  Because there are one group which has the comparable levels and large variance.
  There are same problems in retrievals of cloud ices in DCC. For the optical depths of DCC, we use nearly fixed values, in contrast with optical depths of water cloud which are retrieved from MODIS data.
Notes: explain

## Slide 22: Summary / Toward demonstration phase
Summary
Implementation of NASA’s DCC method to MTSAT-2/Imager
we used real-time comparison for estimating the gains.
Comparison of NASA DCC method with vicarious method on RT simulation
Similar gain trend
Need to improve vicarious method
Toward demonstration phase
MODIS DCC selection / data archiving
Difficult to get/archive nominal Aqua/MODIS data (MYD021KM) due to downloading speed. Alternatively, we used 5km sub-sampled data.
Very useful if NASA creates the DCC-selected data (e.g., MTSAT-IASI/AIRS IR collocation NetCDF data on EUMETSAT THREDDS server).
GSICS product (NetCDF) format
What attributes/variables should be contained?
Application for Himawari-8/AHI for the AHI operational phase (starting at 2015/Apr.~2016/Mar.).

## Slide 23: Thanks for your attentions!

## Slide 24: AHI VIS/NIR Calibration Strategy