## Slide 1: NOAA Operational Implementation of DCC Correction
Fangfang Yu and Xiangqian Wu
NOAA/NESDIS/STAR

## Slide 2: Outlines
Operational implementation
  Routine daily DCC pixel identification for GOES-13 and GOES-15 since Dec. 2011
  Issue of GOES-13 DCC reflectance in 2013 and possible resolving option
Sensitivity analyses
  Mode vs. median reflectance
  BRDF model: CNES, Hu, and CNES
Proposed DCC correction parameters in netCDF file

## Slide 3: DCC Correction
DCC pixel identification
  Routine DCC pixel identification for GOES-13 and GOES-15 since late December 2011
Absolute reference reflectance
  Long-term or monthly reference reflectance
  MODIS vs. VIIRS
DCC reflectance
  Mode vs. median
BRDF model
  Hu, CERES, CNES PLODER, MODIS and BJ Sohn models
Trending of monitored instrument degradation
  Polynomial function
Correction coefficients and the uncertainty variables in the netCDF

## Slide 4
Image from: http://noaasis.noaa.gov/NOAASIS/ml/genlsatl.html
GOES-15
GOES-13
Routinely archive the daily DCC pixels from the near real-time data server since late December 2011
All the routine earth scan frames within the DCC temporal and spatial domains
Identified with community- agreed DCC identification criteria
DCC Pixel Identification

## Slide 5: GOES-15, Hu’s ADM Correction

## Slide 6: GOES-13, Hu’s ADM Correction
Anomaly on May 22, 2013
Data outage: May 22, 2013- Jun 6, 2013
Anomaly on Sept 12, 2013
Data outage: Sept. 12, 2013 – Oct. 18, 2013

## Slide 7: Comparisons with Results of other methods
No apparent change of GOES-13 degradation trending was observed in 2003 from the ray-matching and desert methods
Ratio between the Terra/MODIS and GOES collocated cloud pixels (ray-matching)
Time-series of Sonoran TOA reflectance (desert target)
GOES DCC Reflectance

## Slide 8: Time-series of Monthly DCC Reflectance
GOES-12 was GOES-East
Monthly Aqua MODIS C6 DCC reflectance
No significant long-term trending
Apparent Annual variation
Root causes to the variation are unknown yet
  Land/ocean surface?

## Slide 9: Possible solution – Determination of the reference reflectance
Semi-annual/annual variation in DCC reflectance
  Climate (water vapor, precipitation, radiation, etc) variation in tropics has semi-variation that can often be stronger than annual cycle
  Continent viewed by GOES-East (GOES-13) may complicate this situation
Long-term mean reflectance
  May result in relatively large uncertainty, especially in the first several years of operation.
Monthly reference reflectance
  Allows for the seasonal variation
  How to handle the months with insufficient DCC pixels? Use the long-term value?

## Slide 10: Minimum pixels for a robust DCC reflectance
Median reflectance
Mode Reflectance
Both methods need at least thousands of DCC pixels for a robust result
Less variation with median reflectance

## Slide 11: Mode vs. Median Reflectance
Less variations with median values in the time-series of DCC reflectance
The bias between the median and mode reflectance is less than 0.4% (0.21% for GOES-12, 0.34% for MODIS data)
Calibration coefficient difference between median DCC and desert method is less than 1%

## Slide 12
 | Hu | CERES | CNES
Bias, using Hu’s model result as the reference | - | 0.27% | 0.11%
CNES BRDF model Band 670nm solar range =30-40o
BRDF Models
Hu, CERES, and CNES models
Different angular resolutions
  CNES: 10 (szn) x2 (vzn) x ~2(raz) degrees (6 x 31 x 61 grid)
  CERES: 10 (szn) x 10*(vzn)x10(raz)
  Hu: 10 (szn) x 10*(vzn)x10(raz)
CNES model, probably due to its high angular resolution, has relatively large variation
Impact of the long-term trending is very small (<0.3%)

## Slide 13: Correction Coefficients
Re-analysis product
  Linear correction
  Polynomial fitting for GOES Imager visible
Near real-time product
  Latency for a reliable DCC product
  D. Doeling et al. 2014: Aqua Collection 6 and VIIRS Land PEATE 0.65 channel DCC calibration results.

## Slide 14: Variables in the correction product netCDF file
Monthly correction
Global attributes
  Band information (satellite and instrument names, central wavelength etc)
  Reference instrument information
  DCC Data duration
  Application validity period
  SBAF and the standard error (SCIAMACHY-derived)
  Solar constant uncertainty
  Trending function equation
  ….
Variables
  Reference reflectance and uncertainty
  Fitting coefficients and uncertainty
  Correction coefficients and combined uncertainty
  BRDF model uncertainty
  …..

## Slide 15: Conclusions
In addition to slight seasonal variation, DCC reflectance over the GOES-East position seems to have some annual reflectance variation in certain years.
  Determination of reference reflectance
  Affect the calibration latency for the near real-time product
While median reflectance can result in slightly lower standard error than mode reflectance, the resulted correction coefficients between these methods is very small (<0.4%)
  Median reflectance is recommended
  Impact on the degradation fitting (systematic error) is very small
Three BRDF models were tested.
  Different standard error
  Impacts on the degradation fitting (systematic error) are very small (<0.3%) with long-term re-analysis data