## Slide 1: An Integrated Vicarious Calibration Method to Improve the GOES Imager Radiometric Calibration Accuracy
Fangfang Yu1 and Xiangqian Wu2
1: ERT, Inc@NOAA/NESDIS/STAR
2: NOAA/NESDIS/STAR
2014 GSICS Annual Meeting, Darmstadt, Germany

## Slide 2: Outline
GOES Imager vicarious calibration methods
  Desert based method
  Deep Convective Cloud (DCC)
  Ray-matching
  Lunar calibration
  Star calibration
Integrated method
  relative calibration
  absolute calibration
Conclusions

## Slide 3: GOES Imager Visible Vicarious Calibration Methods
Reference targets:
  Sonoran desert
  Deep Convective Cloud (DCC)
  Aqua MODIS – collocated cloud pixels
  Moon
  Stars
GOES-10 (GOES-West, 135W) and GOES-12 (GOES-East, 75W) as examples
Earth surface targets,
Absolute calibration
Direct sensor inter-calibration,
absolute calibration
Extra-terrestrial objects, relative calibration

## Slide 4: Sonoran Desert
Trending of clear pixel pre-launch reflectance
  Removal of contaminated pixels is important to reduce the uncertainty
  BRDF and seasonal atmospheric variations are simulated with two sine terms
  Periodic deviations (e.g. ENSO events)
Transfer the GOES calibration to Aqua MODIS standard for absolute calibration
  BRDF correction of different solar zenith angle and relative azimuth angle between GEO and LEO measurements
  Hyperion data for the spectral correction

## Slide 5: Deep Convective Cloud
Stable, spectrally flat, high reflectance and common to all the satellites
Trending of DCC
  Seasonality
  Occasional insufficient DCC pixels may lead to large deviation
GOES-West
GOES-East

## Slide 6: Ray-matching
Direct inter-comparison
Collocations at sub-satellite regions: nadir lat/lon ±8o
  Large uncertainty of spectral correction for GOES-12
Wu et al. IGARSS 2011
GOES-West
GOES-East

## Slide 7: Lunar Calibration
Extremely stable, slight spectral variation at different phase angles
Relative Calibration available with comparison to the USGS ROLO model

## Slide 8: Star Calibration
Extremely stable
  A variety of bright stars.
  Subject to instrument diurnal/seasonal sensor optical variation
  Each star has observation gap in a year
Relative calibration

## Slide 9: Normalization of the Pre-launch Reflectance
Normalized to the estimated Day1 reflectance
Removal of contaminated pixels
Trending fitting
Monthly average reflectance

## Slide 10: Combined Vicarious Calibrations
Comparable relative calibration accuracy
Similar degradation patterns over different reference targets indicate that the impact of spectral response function variation, if any, is small and possibly negligible on the pre-launch calibration reflectance

## Slide 11: Integrated Vicarious Calibration
Where is the truth of sensor degradation?
  The truth should have higher possibility of observations where results of most methods converge
Recursive filtering to remove the observations away from the “truth” - the fitting curve

## Slide 12: From Relative to Absolute Calibration
Use of desert and DCC methods as example to calculate the absolute calibration correction coefficients
Re-construct the pre-launch reflectance from the integrated calibration result.

## Slide 13: Absolute Calibration Correction
Sonoran Desert:
DCC :
The systematic difference between desert and DCC method is less than 1%

## Slide 14: Conclusions
The integrated algorithm is able to increase the relative calibration accuracy
It can be used to evaluate the absolute calibration difference between different vicarious methods
Other integrated method should be explored
instr. Refl.
Reference refl.