## Slide 1: Migrating References, Double Differences, Delta Corrections, Archive Re-Calibration, Blending References
Tim Hewison
(EUMETSAT) (GRWG Chair)
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:

## Slide 2: Intro
Discussion framed in terms of creating delta-corrections
  to migrate from IASI-A to –B as Reference,
  using double differences
But generically applicable
  Even for single difference
  Met7-IASIA as example (because it’s bad)
For NRTC & RAC
  Thinking ahead to Archive Re-Calibration Corrections

## Slide 3: Time Series of Meteosat7/MVIRI Bias wrt IASI
Just an example time series
Meteosat7/MVIRI “WV” and “IR”
GSICS Re-Analysis Correction
Evaluated Standard Bias for Standard Scene radiance
Expressed as Tb
5 year long time series
WV: strong yearly cycle
IR: twice-yearly cycle
  + long-term drift
Time Series of Standard Biases for “WV” and “IR” channels of Meteosat7/MVIRI calculated with reference to Metop-A/IASI.

## Slide 4: Characterise Biases in Available Data
In general, time series include: x=f(t)+...
  Random Noise – White noise α
  Systematic Bias β
  Random Drift – 1/f noise
  Systematic Drift – linear, polynomial...
  Periodic Variations – diurnal/seasonal
  Random sporadic outliers – can be filtered

## Slide 5: Characterise Biases in Available Data
In general, time series include: x=f(t)+... }
  Random Noise – White noise α }
  Systematic Bias β } All can
  Random Drift – 1/f noise } Change
  Systematic Drift – linear, polynomial... }Abruptly
  Periodic Variations – diurnal/seasonal }
  Random sporadic outliers – can be filtered }
We should characterise biases from available data!
Use this to determine nature of Δ Correction

## Slide 6: In case of Jumps in Ref1/2
Any time series parameter can jump
Comparison of Double Differences can identify which time series has jumped
Treat as a discontinuity
Process segments independently
Tie segments together using double-differences
  Need to work example

## Slide 7: Delta Corrections’ Time Period
At 2014 GRWG meeting:
  Agreed to generate Delta Corrections for RACs & NRTCs
  Based on double differences over same time periods
But this makes Delta Corrections redundant
  Δ=(Mon-Ref1)-(Mon-Ref2)
  (Mon-Ref2)+Δ=(Mon-Ref1) – Identical if same period
  So users will keep using (Mon-Ref1) until they can’t
  Then what?

## Slide 8: What happens after Metop-A?
Monitor IASIb-a DD
  during overlap period
Characterise relative bias
and uncertainty
Extrapolate trend?
  Only if significant?
  Dangerous!
Extrapolate uncertainty
  Need >1 year overlap
Time
Delta Correction

## Slide 9: After Ref1 is gone – 3 Options
Just use most recent ΔRAC?
  Does not capture any drift - Extrapolation dangerous!
  periodicity e.g. Season cycle
  or increased uncertainty - Would be constant in time??
Use whole overlap period?
  Could account for drift - in terms of increased uncertainty
  Could model periodicity - Risks aliasing different periods
  Could model uncertainty as a function of time
Use overlap period of integer number of periods (years)
  As 2, but cancels out periodic variations

## Slide 10: Schematic Example
First month: ΔTb = -1.90 ± 0.05 K
Time Series of Standard Biases for “IR” channel of Meteosat7/MVIRI calculated with reference to Metop-A/IASI.

## Slide 11: Schematic Example
First month: ΔTb = -1.90 ± 0.05 K
First 3 months: ΔTb = -2.00 ± 0.10 K
Time Series of Standard Biases for “IR” channel of Meteosat7/MVIRI calculated with reference to Metop-A/IASI.

## Slide 12: Schematic Example
First month: ΔTb = -1.90 ± 0.05 K
First 3 months: ΔTb = -2.00 ± 0.10 K
First 6 months: ΔTb = -2.00 ± 0.05 K
Time Series of Standard Biases for “IR” channel of Meteosat7/MVIRI calculated with reference to Metop-A/IASI.

## Slide 13: Schematic Example
First month: ΔTb = -1.90 ± 0.05 K
First 3 months: ΔTb = -2.00 ± 0.10 K
First 6 months: ΔTb = -2.00 ± 0.05 K
First 12 months: ΔTb = -2.05 ± 0.07 K
Time Series of Standard Biases for “IR” channel of Meteosat7/MVIRI calculated with reference to Metop-A/IASI.

## Slide 14: Schematic Example
First month: ΔTb = -1.90 ± 0.05 K
First 3 months: ΔTb = -2.00 ± 0.10 K
First 6 months: ΔTb = -2.00 ± 0.05 K
First 12 months: ΔTb = -2.05 ± 0.07 K
First 24 months: ΔTb = -2.15 ± 0.10 K
Time Series of Standard Biases for “IR” channel of Meteosat7/MVIRI calculated with reference to Metop-A/IASI.

## Slide 15: Schematic Example
First month: ΔTb = -1.90 ± 0.05 K
First 3 months: ΔTb = -2.00 ± 0.10 K
First 6 months: ΔTb = -2.00 ± 0.05 K
First 12 months: ΔTb = -2.05 ± 0.07 K
First 24 months: ΔTb = -2.15 ± 0.10 K
First 36 months: ΔTb = -2.25 ± 0.15 K
Time Series of Standard Biases for “IR” channel of Meteosat7/MVIRI calculated with reference to Metop-A/IASI.

## Slide 16: Schematic Example
First month: ΔTb = -1.90 ± 0.05 K
First 3 months: ΔTb = -2.00 ± 0.10 K
First 6 months: ΔTb = -2.00 ± 0.05 K
First 12 months: ΔTb = -2.05 ± 0.07 K
First 24 months: ΔTb = -2.15 ± 0.10 K
First 36 months: ΔTb = -2.25 ± 0.15 K
First 48 months: ΔTb = -2.35 ± 0.20 K
Time Series of Standard Biases for “IR” channel of Meteosat7/MVIRI calculated with reference to Metop-A/IASI.

## Slide 17: Schematic Example
First month: ΔTb = -1.90 ± 0.05 K
First 3 months: ΔTb = -2.00 ± 0.10 K
First 6 months: ΔTb = -2.00 ± 0.05 K
First 12 months: ΔTb = -2.05 ± 0.07 K
First 24 months: ΔTb = -2.15 ± 0.10 K
First 36 months: ΔTb = -2.25 ± 0.15 K
First 48 months: ΔTb = -2.35 ± 0.20 K
First 60 months: ΔTb = -2.50 ± 0.25 K
Time Series of Standard Biases for “IR” channel of Meteosat7/MVIRI calculated with reference to Metop-A/IASI.

## Slide 18: Schematic Example
First month: ΔTb = -1.90 ± 0.05 K
First 3 months: ΔTb = -2.00 ± 0.10 K
First 6 months: Cyclic Period ΔTb = -2.00 ± 0.05 K Min Uncert.
First 12 months: ΔTb = -2.05 ± 0.07 K
First 24 months: ΔTb = -2.15 ± 0.10 K Define fn
First 36 months: Increasing ΔTb = -2.25 ± 0.15 K Uncertainty
First 48 months: ΔTb = -2.35 ± 0.20 K
First 60 months: ΔTb = -2.50 ± 0.25 K
Time Series of Standard Biases for “IR” channel of Meteosat7/MVIRI calculated with reference to Metop-A/IASI.

## Slide 19: Extrapolate Uncertainty, not Bias
Time Series of Standard Biases for “IR” channel of Meteosat7/MVIRI calculated with reference to Metop-A/IASI.

## Slide 20: Variograms for Meteosat-7/MVIRI “WV” and “IR”
“WV” and “IR” channels of Meteosat/MVIRI
Variograms increase with time interval 1-29d
  Averaging period used in GSICS Correction
“WV” Minimum at Δt=1yr:
  (2γt)1/2=65±4 mK
“IR” Minimum at Δt=1yr:
  (2γt)1/2=187±12 mK
Higher “nugget values”
  More collocation noise
Higher “sill values”
  Faster calibration drift
See poster for details
Temporal variograms [(2γt)1/2] calculated as RMS differences in Standard Biases for “WV” and “IR” channels of Meteosat-7/MVIRI calculated with reference to Metop-A/IASI. Vertical lines show periods of 29d and 1yr.
Low Pass Filter
Long-term Drift
6-Month Cycles
Low Pass Filter
Long-term Drift
Annual Cycles

## Slide 21: Time Series of Standard Biases – Updated! Full year (Met10/SEVIRI-MetopA/IASI)
^ Decontaminations ^
^ Decontaminations ^
Unsmoothed Daily Results 3-sigma filter
– not necessarily same days!

## Slide 22: Single-Difference Variograms for (MSG3-IASIB) RACs
Low Pass Filter
Long-timescale minima (Decontaminations)
Long-term Drift

## Slide 23: Time Series of Standard Biases – Updated! Full year (Met10/SEVIRI-MetopB/IASI) & (Met10/SEVIRI-MetopA/IASI)
Unsmoothed Daily Results 3-sigma filter
– not necessarily same days!

## Slide 24: Time Series of Double Differences (Met10/SEVIRI-MetopB/IASI)-(Met10/SEVIRI-MetopA/IASI)
Unsmoothed Daily Results – only selecting matched days!
No Significant Trend in DD for Tb=std or 220K, 290K,...
No Significant Trend in DD for slope or offset

## Slide 25: Double-Difference Variograms for (MSG3-IASIB)-(MSG3-IASIA) RACs
Low Pass Filter
No Long-term Drift
No annual cycle

## Slide 26: Diurnal Cycles w/ multiple References
Metop-A/IASI
Metop-B/IASI
Aqua/AIRS
S-NPP/CrIS
Meteosat-9/SEVIRI
ΔIASIB-IASIA - Tie 9:30am/pm Time series together }
ΔAIRS-CrIS - Tie 1:00am/pm Time series together }-Combine -> Blended Ref*
ΔAIRS-IASIA - Characterise diurnal cycle }
* Blending could be just ‘averaging’ – susceptible to calibration differences
Or after bias adjustment = traceable to Metop-A/IASI

## Slide 27: Blending References
Metop-A/IASI
Metop-B/IASI
Meteosat-9/SEVIRI
ΔIASIB-IASIA - 50-50 Blend* of References during whole overlap
* Blending could be just ‘averaging’ – susceptible to calibration differences
Or after bias adjustment = traceable to Metop-A/IASI
Weight
0% 100%
Time

## Slide 28: Blending References
Metop-A/IASI
Metop-B/IASI
Meteosat-9/SEVIRI
ΔIASIB-IASIA - 50-50 Blend* of References after initial delay
  E.g. 1yr to evaluate Double Differences and develop Delta Correction
* Blending could be just ‘averaging’ – susceptible to calibration differences
Or after bias adjustment = traceable to Metop-A/IASI
Weight
0% 100%
Delay
Time

## Slide 29: Blending References
Metop-A/IASI
Metop-B/IASI
Meteosat-9/SEVIRI
ΔIASIB-IASIA - Tapering Blend* of References after initial delay
  E.g. 1yr to evaluate Double Differences and develop Delta Correction
* Blending could be just ‘averaging’ – susceptible to calibration differences
Or after bias adjustment = traceable to Metop-A/IASI
Weight
0% 100%
Delay
Time

## Slide 30: Conclusions
Need to generate double differences for all overlap period
Analyse these to characterise reference differences
Should probably not extrapolate trends
  But could reconstruct them from multiple references
May not need Delta Corrections until current reference instrument dies
But then Delta Corrections will be needed instantly
  For continuity of RACs, NRTCs
  To trace them back to previous references
So need to start generating double differences asap
  And define Delta Corrections to be ready when needed

## Slide 31: Questions
Should we extrapolate periodic cycles?
  If we can model/understand them & they are significant
  Or use last n whole years
Is it OK to extrapolate uncertainty like this for NRTC/RAC?
  For Delta Correction, keeping constant DD bias after Ref1 is dead
Is there any point in generating Delta corrections for current RAC/NRTC using the same smoothing period?
  Or should we calc DD over whole overlap period? (or n years?)
Is this concept applicable to other GSICS Products?
  DCC, Lunar, ...
Can we make blended reference for Archive Re-Cal/RACs?
  With or without bias adjustment?

## Slide 32: Urgent Questions
How to characterise diurnal calibration variability?
  Do we need to include this in RAC/NRTC netCDF or document it?
How to define Delta Corrections for IASI-B->A?
  Just from double difference of RAC & NRTC – same periods (As agreed in 2014 GRWG Meeting) - No added value
  Average of all RACs/NRTCs over overlap period? (Correlated)
  Average of selected RACs/NRTCs every 29/14d? (Uncorrelated)
  Calculate Variograms from RACs/NRTCs over 30d-Nyquist
  Recalculate regression from all collocations in overlap period?
    Need more data – Any advantages?
  As 2, 3 or 4, but for only the most recent n years (avoids aliasing seasonality e.g. from n.5 years)