## Slide 1: An Integrated Calibration Method to Improve the GOES Visible Calibration Accuracy
Fangfang Yu and Xiangqian Wu
GSICS VNIR Subgroup Webmeeting
10/22/2014

## Slide 2: Background
Multiple vicarious methods are usually available for the VNIR channels
  Different stable reference used for each method
  Independently evaluate the sensor performance & cross verifications
GSICS VNIR inter-calibrations
  Two common references: DCC & Moon
  Other options: Desert, Rayleigh scattering, Ray-matching, star, sun-glint …
  Absolute calibration vs. Relative calibration: no method can excel to the others
How to combine the multiple vicarious calibration methods?
  Can we improve the calibration accuracy from the combined results?
  Improved absolute calibration accuracy: long-term climate change studies
  Improved relative calibration accuracy: early change (trending) detection
Applications:
  GSICS VNIR products
  Verification of AHI/ABI on-orbit calibration accuracy & early warning of on-orbit calibration anomaly

## Slide 3: Objectives
Evaluate the individual vicarious calibration method implemented in-house for GOES Imager visible channel at NOAA/NESDIS
Integrate the different vicarious calibration methods to improve the calibration accuracy
  Improve the relative calibration accuracy
  Evaluate the difference between different absolute calibration results
Manuscript on the research method was submitted to Remote Sensing of Environment for peer-review purpose on July 22, 2014. Received positive feedbacks from two anonymous reviewers with many constructive comments on Oct. 13, 2014.

## Slide 4: GOES Imager Visible Vicarious Calibration Methods
Reference targets:
  Stars – relative cal.
  Ray-matching – relative cal.
  Sonoran desert – absolute cal.
  Deep Convective Cloud (DCC) – absolute cal.
  Moon – to be implemented with GSICS Implemented ROLO (GIRO) model
Absolute calibration accuracy was achieved by calibrating the GOES Imager visible data traceable to Aqua MODIS Band 1 C6 standard
  Recommended by the GSICS VNIR sub-group
GOES-15 (GOES-West, 135W) and GOES-12 (GOES-East, 75W) as examples
In-house implemented algorithms

## Slide 5: Spectral Response Functions & Desert/Clouds/Vegetation/Water Spectra
GOES-E
GOES-W

## Slide 6: Sonoran Desert
Target is long-term radiometrically, spatially and spectrally stable at GOES viewing geometries.
Challenges:
  Impact of seasonal variation of solar zenith angle
  Impacts of daily dynamic atmospheric components and periodic climatic variations e.g. ENSO events
  Different SRFs
  No strict GEO-LEO ray-matching pixels for absolute cal.
Absolute Calibration:
  Quadratic fitting for sensor degradation + two sine functions for the impacts of seasonal changes of solar zenith angle and atmospheric components.
  Hyperion data for the spectral correction
  One year of satellite measurements to develop the BRDF model to transfer the Aqua MODIS data to GOES viewing geometries
Yu, F. et al. (2014) JGR doi:10.1002/2013JD020702
[32.05N-32.25N, 114.7W-114.4W]
GOES-East
GOES-West

## Slide 7: Reference reflectance of Sonoran Desert
 | GOES-12 (East) | GOES-15 (West)
Desert MODIS long-term reflectance (%) | 32.59 | 34.29
SBAF (GOES/MODIS, Hyperion data derived) | 0.949 | 0.929
Desert Reference Reflectance, traceable to Aqua MODIS
Daily median MODIS reflectance
Removal of contaminated pixels
Average the daily clear-sky pixel reflectance at monthly interval
Trend fitting
Yu, F. et al. (2014) JGR doi:10.1002/2013JD020702

## Slide 8: Ray-matching
Direct satellite-to-satellite inter-comparison to minimize the impacts of BRDF and different atmospheric components
  Doelling, D. et al. (2004)
Challenges
  Lack of coincident hyper-spectral radiometric measurements in result in large uncertainty in spectral correction
  Few collocations with same relative azimuth angles - BRDF
Relative Calibration
  Collocations at sub-satellite regions within ±10o lat/lon
  Viewing angle difference < 1%
  High reflectance cloud collocations: MODIS reflectance > 50%
  Reflectance ratio for sensor trending purpose
  Statistically stable ratio with sufficient high reflectance cloud pixel #
GOES-East
GOES-West
Yu, F. and X. Wu (2014) Remote Sensing of Environment, Submitted
MODIS reflectance
GOES-MODIS Refl.
Wu, X. et al. (2011)IGARSS
GOME-2 Simulated G14 and MODIS Refl.

## Slide 9: Deep Convective Cloud (DCC)
Stable, spectrally flat, high reflectance and common to all the satellites
  Doelling, D. et al. (2004)
  Reflectance is represented with monthly identified DCC pixels
Challenges
  Slight variation in reflectance
  Occasional insufficient DCC pixels may lead to relatively large reflectance deviation for GOES-West Satellites
Absolute Calibration
  Use mode or median reflectance of the monthly DCC pixels to represent the DCC reflectance
  At least 2,000 DCC pixels are needed to generate a statistically reliable monthly DCC reflectance value
  Use Ray-matching collocated DCC pixels to determine the reference reflectance
Courtesy of D. Doelling
Yu, F. and X. Wu (2014) Remote Sensing of Environment, Submitted

## Slide 10: Reference Reflectance of DCC
 | GOES-12 (East) | GOES-15 (West)
DCC MODIS long-term reflectance (%) | 88.87 | 90.38
SBAF (GOES/MODIS) | 0.9911 | 0.9942
DCC Reference Reflectance, traceable to Aqua MODIS
Time-series of monthly MODIS DCC reflectance for GOES-12
DCC Reference Reflectance Derived from Ray-matching Collocated MODIS DCC Pixels
1: SCIAMACHY data derived provided by D. Doelling, 2: GOME-2 data derived
Histogram of MODIS DCC Reflectance for GOES-15 (Dec 2011 – March 2014)
Yu, F. and X. Wu (2014) Remote Sensing of Environment, in review

## Slide 11: Combination of the Different Vicarious Calibration Results
Normalized to the estimated Day1 reflectance
Trending fitting
Monthly average reflectance
Combine the Normalized Data

## Slide 12: Integrated Vicarious Calibration
Where is the truth of sensor degradation?
  The truth should exist where most observations converge
Recursive filtering to remove the observations away from the “truth” - the fitting curve
Similar degradation patterns over different reference targets may indicate that the spectral response function degradation, if any, is very small and negligible
ENSO effects?
*Relative calibration accuracy improved to 0.41% when only ray-matching and DCC methods are combined

## Slide 13: “Recursive Fitting” Residual Distribution

## Slide 14: Absolute Calibration Correction Comparisons
Sonoran Desert:
DCC :
where,
Yu, F. and X. Wu (2014) Remote Sensing of Environment, in review
Co-occurrence of the monitored and reference data period to determine the reference reflectance!

## Slide 15: Possible Causes to the Bias
Reference reflectance, especially at Day1 ,is critical to determine the absolute calibration correction coefficients
  Need long-term desert observation to ensure the accurate desert Day1 reflectance value
  Co-occurrence of the monitored and reference data period to determine the reference reflectance
Possible reflectance difference between overall DCC pixels (±20ofrom sub-satellite point) and subset DCC pixels (±10ofrom sub-satellite)
  Slight Land/ocean DCC difference?
  Slight difference at different viewing angle, residual of DCC ADM correction?
Impact of GOES scan mirror reflectivity between nadir (DCC) and off-nadir (Sonoran desert) observations.
X
X
Yu et al. (2013), GSICS QL
GOES-East
GOES-West
nadir

## Slide 16: Time-Series of G12 Error Budget
Yu, F. and X. Wu (2014) Remote Sensing of Environment, in review
Integrated method uncertainty
Integration of DCC and Ray-matching results as the “truth”

## Slide 17: Discussions - 1
Anchoring date
  Day 1
    Pros: consistent, valuable to detect the potential SRF shift and/or reference target change/variation
    Cons: relatively larger uncertainty
  Median date over the period
    Pro: possible reduced uncertainty
    Cons: dynamic median dates at different time (days after operation).
  Suggestion
    Re-analysis: median date as the anchors. Trendings anchored at Day1 used to evaluate the potential SRF shift and/or reference target
    Near real-time: anchored at day 1
Sensitivity of DCC/Ray-matching minimum pixels for reliable monthly data
  Current values randomly selected
  Should not be critical

## Slide 18: Discussions - 2
Can it be used for on-board calibration verification like ABI and MODIS
  yes
Relative calibration: how to handle with rapid change like VIIRS early in orbit period
  Rapid change relies on the on-board calibration
  Improved relative calibration to reduced latency time for the warning
Degradation fitting function
  Accurate degradation function is another key to the success!
  Suggestion using different fitting function once the rapid change occurs, or when necessary
Absolute calibration vs. relative calibration accuracy
  This method can improve the relative calibration accuracy, not the absolute calibration accuracy
  Therefore useful to provide early warning for the on-board calibration anomaly
  Provide more robust result to distinguish the abs. calibration difference

## Slide 19: Conclusions
The integrated method can improve the relative calibration accuracy for the GOES Imager visible channels (GOES-East)
  Maximum overall uncertainty is about 2% in the first one year with long-term stability <0.5%
  After about 2 years, calibration accuracy is generally stable at <1%
  Similar error budget assessment is needed for the GOES-West satellites
For the GOES-West satellites, the stellar calibration is expected to play a critical role to improve the relative calibration accuracy
  Especially in the early stage of the satellite mission life
For the GOES-East satellites, the ray-matching and DCC results play almost equally important roles in the integrated method
  The stellar observations are expected to further improve the relative calibration accuracy
The difference between desert- and DCC- based absolute calibration accuracy is less than 1%
  Bias may be reduced with the correction of scan angle dependent reflectivity
Tools and knowledge/experience will continue evolving and will be applied to verify radiometric calibration accuracy of GOES-R ABI solar reflectance channels.