## Slide 1
Inter-calibration using DCCs and seasonality
Sébastien Wagner (EUMETSAT)
Notes: EUM/STG-SWG/36/14/VWG/15

## Slide 2
Moved from month-to-month analysis to a GEO-LEO IR approach with a rolling window to derive:
  Daily Near-Real-Time Corrections
  Re-analysis Corrections
  Effect of the saturation of MET-09/VIS0.6 over DCCs on the end results
  Results without the saturated pixels are smoother (saturation adds a peak at Spring time)
  Saturation disappears in time (degradation helps us )
  Attempts to change the size of the rolling window for NRTC (30 days or 15 days)
  Start looking into seasonality
  Variograms
Short summary of the 2014 GSICS Annual Meeting...

## Slide 3
NRTC – 30 days
MODE
MODE – No saturation
MEAN
MEAN – No saturation
SKEWNESS + smoothed over 30 days
Number of DCCs
K-K0
KURTOSIS + smoothed over 30 days

## Slide 4
NRTC – 15 days
K-K0
MODE
MODE – No saturation
MEAN
MEAN – No saturation
SKEWNESS + smoothed over 30 days
Number of DCCs
KURTOSIS + smoothed over 30 days

## Slide 5: Effect of the saturation MET-9/VIS0.6
Effects of saturation decreases with time  Instrument degradation helps us!

## Slide 6: Variogram analysis of the time series
Variogram
30 days (interval used for the NRT product)
 | Mode | Mean | Mode (no saturation) | Mean (no saturation)
Drift Stability | 0.1538 | 0.1110 | 0.1374 | 0.1046

## Slide 7: Original time series – NRTC 30 days – Mode – No saturation

## Slide 8: Deseasonalizing the time series
Choice of a model  Multiplicative: Seasonalized = Deseasonalized * Seasonal factors
Calculation of a smooth version of the time series:
  Each daily point is the centred average over 365 days (see variograms).
  Beginning and endings points: various methods to take care of the missing data (replacing the missing points by as many time the last available value as necessary)
Estimation of the seasonal indices:
  Ratio between the mode time series and the smoothed data.
  Calculating the seasonal indices:
    For each day of the year, average all the ratio values (Step A) for that day across the years (for leap years I adjust it to 365 equivalent)  year of seasonal indices. However, average value  1.
    Normalization of the ratios by the mean value over the year è 365 seasonal indices.
Deseasonalization of the time series by dividing each value from the original time series by the seasonal indices
Linear regression of the deseasonalized time series.
Consistency check: multiplying the trend by the seasonal indices and visual check.

## Slide 9: Original time series + yearly-smoothed time series

## Slide 10: Deseasonalizing the time series
Choice of a model  Multiplicative: Seasonalized = Deseasonalized * Seasonal factors
Calculation of a smooth version of the time series:
  Each daily point is the centred average over 365 days (see variograms).
  Beginning and endings points: various methods to take care of the missing data (replacing the missing points by as many time the last available value as necessary)
Estimation of the seasonal indices:
  Ratio between the mode time series and the smoothed data.
  Calculating the seasonal indices:
    For each day of the year, average all the ratio values (Step A) for that day across the years (for leap years I adjust it to 365 equivalent)  year of seasonal indices. However, average value  1.
    Normalization of the ratios by the mean value over the year è 365 seasonal indices.
Deseasonalization of the time series by dividing each value from the original time series by the seasonal indices
Linear regression of the deseasonalized time series.
Consistency check: multiplying the trend by the seasonal indices and visual check.

## Slide 11: Adjusted seasonal factors

## Slide 12: Adjusted seasonal factors

## Slide 13: Deseasonalizing the time series
Choice of a model  Multiplicative: Seasonalized = Deseasonalized * Seasonal factors
Calculation of a smooth version of the time series:
  Each daily point is the centred average over 365 days (see variograms).
  Beginning and endings points: various methods to take care of the missing data (replacing the missing points by as many time the last available value as necessary)
Estimation of the seasonal indices:
  Ratio between the mode time series and the smoothed data.
  Calculating the seasonal indices:
    For each day of the year, average all the ratio values (Step A) for that day across the years (for leap years I adjust it to 365 equivalent)  year of seasonal indices. However, average value  1.
    Normalization of the ratios by the mean value over the year è 365 seasonal indices.
Deseasonalization of the time series by dividing each value from the original time series by the seasonal indices
Linear regression of the deseasonalized time series.
Consistency check: multiplying the trend by the seasonal indices and visual check.

## Slide 14: Deseasonalized time series

## Slide 15: Deseasonalizing the time series
Choice of a model  Multiplicative: Seasonalized = Deseasonalized * Seasonal factors
Calculation of a smooth version of the time series:
  Each daily point is the centred average over 365 days (see variograms).
  Beginning and endings points: various methods to take care of the missing data (replacing the missing points by as many time the last available value as necessary)
Estimation of the seasonal indices:
  Ratio between the mode time series and the smoothed data.
  Calculating the seasonal indices:
    For each day of the year, average all the ratio values (Step A) for that day across the years (for leap years I adjust it to 365 equivalent)  year of seasonal indices. However, average value  1.
    Normalization of the ratios by the mean value over the year è 365 seasonal indices.
Deseasonalization of the time series by dividing each value from the original time series by the seasonal indices
Linear regression of the deseasonalized time series.
Consistency check: multiplying the trend by the seasonal indices and visual check.

## Slide 16: Deseasonalized time series + drift
 | Drift | Offset | Error
Seasonalized | -0.4447% yr-1 | 880.16 | 7.587
Deseasonalized | -0.4325% yr-1 | 879.74 | 7.591

## Slide 17: Deseasonalizing the time series
Choice of a model  Multiplicative: Seasonalized = Deseasonalized * Seasonal factors
Calculation of a smooth version of the time series:
  Each daily point is the centred average over 365 days (see variograms).
  Beginning and endings points: various methods to take care of the missing data (replacing the missing points by as many time the last available value as necessary)
Estimation of the seasonal indices:
  Ratio between the mode time series and the smoothed data.
  Calculating the seasonal indices:
    For each day of the year, average all the ratio values (Step A) for that day across the years (for leap years I adjust it to 365 equivalent)  year of seasonal indices. However, average value  1.
    Normalization of the ratios by the mean value over the year è 365 seasonal indices.
Deseasonalization of the time series by dividing each value from the original time series by the seasonal indices
Linear regression of the deseasonalized time series.
Consistency check: multiplying the trend by the seasonal indices and visual check.

## Slide 18: Verification of the seasonal model

## Slide 19
  ATBD is ready
  Seasonal signal removed upon availability of ancillary data
  Similar analysis being applied to the reference time series for sake of consistency (still on going)
  Still to be done:
    Define the smoothing parameters to try to reduce the noise
    Apply the current seasonal indices to other SEVIRI instruments as prior information
  Questions:
    Can we think of “Level 3 product” (after NRTC and RAC)?
    Any other better way of taking care of the seasonality?
    Can we detect jumps in the instrument response?
    What about other bands?
Conclusion

## Slide 20
MODIS data as extracted by JMA (data provided by JMA)

## Slide 21: Extending the DCC method to other bands

## Slide 22
  MODIS DCC analysis – Mean and Mode for 0.6m and 0.8m

## Slide 23
  SEVIRI DCC analysis – Mean and Mode for 0.6m, 0.8m and 1.6 m

## Slide 24
  SEVIRI DCC analysis – Mean and Mode for 0.6m, 0.8m and 1.6 m

## Slide 25
  SEVIRI DCC analysis – Mean and Mode for 0.6m, 0.8m and 1.6 m

## Slide 26: Detecting jumps in the instrument sensitivity

## Slide 27: Time series for SEVIRI – Meteosat 9 - MODE

## Slide 28: Time series for SEVIRI – Meteosat 9 - MEAN

## Slide 29: Time series for SEVIRI – Meteosat 9 – MODE – After removing the seasonal signal

## Slide 30: Time series for SEVIRI – Meteosat 9 – MEAN – After removing the seasonal signal

## Slide 31: How are we capable to detect jumps? Testing varying integration periods for the PDFs and adding sharp changes…