## Slide 1: Proposal of L1 requirement sharing in three GSICS sever center
Xiuqing Hu, Zhe Xu
National Satellite Meteorological Center, CMA
Thank to Peter Miu and Tim Hewison for their great help to CMA IASI/GOME-2 L1 sharing from EUMETSAT
March 16-20, 2015, New Deli, India

## Slide 2: Background
Traditional way of GSICS L1 data acquirement for reference instrument is public website order and downloading in general when these reference data is not provided by theirselves. This leads to heavy time delay and operational instability and even frequently restricted because of security consideration and internet bandwidth occupation.
Three THREDDS severs in CMA, EUMETSAT and NOAA were setting down and provide the opportunity to share more data for GSICS operation, especially these data of their own reference instruments and target sensors for other GPRCs.
Current status of isolated data acquirement way in all GPRCs under GSICS community reveals weak organization, little collaboration, large unbalance between all GPRCs. This is disadvantageous to strengthen our voice and authority in EOS.
EUMETSAT GDWG have done a good demonstration in L1 sharing for CMA GSICS operation in L1 IASI.nc (for FY-2-IASI) requirement and is testing the provision of GOME-2 for FY-2 VIS inter-calibration.

## Slide 3: Scope of GSICS L1 sharing
Reduce the time delay of GSICS operational processing based on L1 public website order procedure (2~3 days1day) between different agencies and also reduce data volume transfer(by crop)
Keep operation stability of GEO-LEO and LEO-LEO GSICS processing in all GPRCs, especially NRTC products
Push GEO-GEO comparison such as FY-2-MTSAT/Himawari, FY-2-MSG , MSG-GOES for long term
VIS/NIR Inter-calibration and reference transfer based on global PICS sites (desert, snow and barren ocean)
Support other GSICS researches such as SBAF, BRDF

## Slide 4: What kinds of L1 Data sharing
GSICS Reference instruments
  Hyper-spectral : IASI, CrIS, GOME-2, HIRAS(FY-3D)
  Imager: MODIS, VIIRS
  Sounder : ATMS, AMSR-E, GMI, HIRS
Target instruments for GSICS operation
  GEO imagers: MSG, GOES, FY-2, MTSAT, Himawari, COMS, INSAT
  LEO imagers: AVHRR , MERSI
  LEO sounders: MWTS, MWHS, IRAS
LEO PICS sites granule L1
  MODIS, VIIRS, GOME-2, SCIAMACHY, Hyperion

## Slide 5: Provision and setting
L1 Data generation automatically by instrument operator
ROI Regional or Granule for spatial coverage for cutting data volume
Format and name following GSICS convention : HDF, NetCDF
Time delay: Near real time
Ready Notification
User feedback to the instrument operator or GCC

## Slide 6: Current Status of GSICS THREDDS severs
3 Collaboration Servers available
GSICS Collaboration Server | Server URL
EUMETSAT GSICS Server (Europe) | http://gsics.eumetsat.int/thredds/catalog.html
NOAA GSICS Server (Americas) | http://gsics.nesdis.noaa.gov/thredds/catalog.html
CMA GSICS Server (Asia) | http://gsics.nsmc.cma.gov.cn/thredds/catalog.html

## Slide 7: EUMETSAT L1 Source Data For CMA
Satellite: MetopA MetopB
Instrument: IASA GOME
Server: EUMETSAT GSICS Thredds
Timeline: Near real time
Spatial: Cropped for FY-2
Format:
  IASA: NetCDF
  GOME: HDF 5.0
    GOME NC demo data is being investigated by CMA now
We hope IASI and GOME-2 is also provided for FY-3 SNO collocation in the next step instead of our order from CLASS.

## Slide 8: What is next?
Who is willing to do this provision job?
What kind of the convention and format?
Where has the hardware resource and disk space or public Cloud?
Can we do more step by step for establishing GSICS data sharing center or data collaboration platform

## Slide 9: Summary
Requirement of L1 data sharing in collaboration servers for GSICS operation is necessary.
Could GDWG begin to investigate this kind of specific requirements in all GPRCs?
Should we incorporate L1 data sharing into the future Working Plan of GDWG?

## Slide 10: Thanks