## Slide 1: Selection of Reference Instrument - Review Requirements
Tim Hewison
(EUMETSAT) (Outgoing GRWG Chair)
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:

## Slide 2: Overview
Report on Reference Sensor Traceability and Uncertainty
Review Reference Instrument Requirements
Scoring scheme for Reference Instruments
OSCAR rule-based selection

## Slide 3: Previously on this channel...
GRWG_15.63 | Tim to provide to Manik a list of parameters from his scoring proposal to include them into the expert system. | TimHewison | 29 Feb 2016
Web Meeting 2013-10-15
2015 GRWG Meeting: Agenda Item 7a: Scoring scheme for reference instruments
Action:

## Slide 4: Overview
Report on Reference Sensor Traceability and Uncertainty
Review Reference Instrument Requirements
Scoring scheme for Reference Instruments
OSCAR rule-based selection

## Slide 5: Report on Reference Sensor Traceability and Uncertainty
Report on Reference Sensor Traceability and Uncertainty
Collaborative document in Google Drive
  Aims
To support the choice of IASI as a reference instrument for GSICS
To provide traceability to other community reference instruments (AIRS, CrIS)
By consolidating pre-launch test results and various in-flight comparisons
  Limitations
No new results, just expressing results of existing comparisons in a common way, reformating where necessary, to allow easy comparisons.

## Slide 6: Report on Reference Sensor Traceability and Uncertainty
Error Budget & Traceability
  AIRS - Pagano?
  IASI - Jouget+Jacquette
  CrIS - Tobin
Inter-comparisons
  Polar SNOs - Jouglet, Tobin, Wang?
  Quasi-SNOs - Jouglet
  GEO-LEO Double Differencing - Hewison (with input from JMA, ISRO, NOAA)
  NWP Double-Differencing - Wu, Coppens?, CNES/LMD?, Strow?
  Massive Means - Tulpin?
Aircraft Double-Differences - Tobin, Newman?, Revercomb?

## Slide 7: Section on Inter-Comparisons
In this section, we will ask contributors to generate statistics using common conditions, where possible. These are to be agreed at the offset, but could include:
Biases with respect to MetopA/IASI
With standard uncertainties (k=1)
At full spectral resolution - in which channel-space? How to convert?
Averaged over specific spectral bands - e.g. SEVIRI, AHI, HIRS, …, pseudo, ?
With specific SRFs - rectangular?
Converted into Brightness Temperatures
For specific radiance scenes - e.g. 200K, 220K, 240K, 260K, 280K, 300K (not all ranges will be available for all methods in all spectral ranges)
For specific viewing angles - e.g. nadir±10⁰
Over specific period - e.g. Beginning of sensors’ operational life to end 2014? Noting any significant changes with time
Scene Homogeneity

## Slide 8: Overview
Report on Reference Sensor Traceability and Uncertainty
Review Reference Instrument Requirements
Scoring scheme for Reference Instruments
OSCAR rule-based selection

## Slide 9: Must Have Requirements
Most basic requirements are essential properties:
  Is it available for the date in question?
  Does it cover at least part of the spectral range?
  Does it generate sufficient collocations?
  Is it’s calibration sufficiently stable?
Already some basic requirements are subjective
Different answers for different applications
  Near Real-Time, Archive Re-Calibration, Monitored instruments

## Slide 10: Nice to Have Requirements
Additional desirable requirements reflect reduced uncertainties in inter-calibration:
  Does it cover the full spectral range?
  At sufficiently high spectral resolution?
  Is it’s calibration sufficiently stable?
Already some basic requirements are subjective
But no improved uncertainty beyond saturation
Different answers for different applications
  Near Real-Time, Archive Re-Calibration, Monitored instruments

## Slide 11: One Size Fits All?
Can we select one Primary reference for all GSICS products in one class?
e.g. All IR channels of current GEO imagers?
GEO sounders?
Historic imagers?
Future imagers? ...

## Slide 12: Spectral Coverage
Essential (Threshold) Requirement:
  Reference instrument has channels covering at least nominal wavelength of all channels on all monitored instruments in class
Desirable (Saturation) Requirement:
  Reference instrument has channels covering the full SRF of all channels on all monitored instruments in class
  At sufficiently high spectral resolution to introduce negligible uncertainty from spectral convolution
Can be defined
  Per channel equivalent (e.g. IR3.9, WV, 13.3m)
  Per sub-band (e.g. SWIR, MWIR, LWIR)
  For whole spectral band (even empty spectral regions)
  In wavelength or wavenumber!

## Slide 13: IR Channels on Current GEO Imagers
 | Meteosat/SEVIRI |  |  | GOES-12-15/Imager |  |  | MTSAT-2/Imager |  |  | FY-2F/S-VISSR |  |  | COMS-1/MI |  |  | INSAT-3D/Imager |  |  |  | Essential |  | Desirable |  | Number
 | lmin | lnom | lmax | lmin | lnom | lmax | lmin | lnom | lmax | lmin | lnom | lmax | lmin | lnom | lmax | lmin | lnom | lmax |  | lmin | lmax | lmin | lmax | 
SWIR | 3.48 | 3.92 | 4.36 | 3.80 | 3.90 | 4.00 | 3.50 | 3.75 | 4.00 | 3.50 | 3.75 | 4.00 | 3.50 | 3.75 | 4.00 | 3.80 | 3.90 | 4.00 |  | 3.75 | 3.92 | 3.48 | 4.36 | 6
(3.50-5.00) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MWIR | 5.35 | 6.25 | 7.15 | 5.80 | 6.55 | 7.30 |  |  |  |  |  |  |  |  |  |  |  |  |  | 6.25 | 7.35 | 5.35 | 7.85 | 7
(5.00-8.26) | 6.85 | 7.35 | 7.85 |  |  |  | 6.50 | 6.75 | 7.00 | 6.30 | 6.95 | 7.60 | 6.50 | 6.75 | 7.00 | 6.50 | 6.80 | 7.10 |  |  |  |  |  | 
LWIR | 8.30 | 8.70 | 9.10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8.70 | 13.40 | 8.30 | 14.40 | 14
(8.26-15.50) | 9.38 | 9.66 | 9.94 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 9.80 | 10.80 | 11.80 | 10.20 | 10.70 | 11.20 | 10.30 | 10.80 | 11.30 | 10.30 | 10.80 | 11.30 | 10.30 | 10.80 | 11.30 | 10.30 | 10.80 | 11.30 |  |  |  |  |  | 
 | 11.00 | 12.00 | 13.00 |  |  |  | 11.50 | 12.00 | 12.50 | 11.50 | 12.00 | 12.50 | 11.50 | 12.00 | 12.50 | 11.50 | 12.00 | 12.50 |  |  |  |  |  | 
 | 12.40 | 13.40 | 14.40 | 13.00 | 13.35 | 13.70 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 14: IR Channels on Current GEO Imagers
 |  | Threshold |  | Saturation |  | 
 | Unit | Min | Max | Min | Max | Weight
Spectral Range | µm | 3.75 | 13.40 | 3.50 | 14.40 | 10
Spectral Range SWIR | µm | 3.75 | 3.92 | 3.48 | 4.36 | 2.2
Spectral Range MWIR | µm | 6.25 | 7.35 | 5.35 | 7.85 | 2.6
Spectral Range LWIR | µm | 8.70 | 13.40 | 8.30 | 14.40 | 5.2

## Slide 15: Example of Channel Scorecard
 | Metop/IASI |  |  |  |  | Aqua/AIRS |  |  |  |  | SNPP/CrIS (in FSR mode) |  |  |  |  | NOAA/HIRS/2 |  |  |  | 
 | Min | Max | OK? | Perfect | Score | Min | Max | OK? | Perfect | Score | Min | Max | OK? | Perfect | Score | Min | Max | OK? | Perfect | Score
Spectral Range | 3.62 | 15.50 | Pass | 99% | 9.9 | 3.62 | 15.38 | Fail | 99% | 9.9 | 4.44 | 15.38 | Fail | 100% | 10.0 | 3.76 | 14.95 | Fail | 100% | 10.0
Spectral Range SWIR | 3.62 | 5.00 | Pass | 74% | 1.6 | 3.74 | 4.61 | Pass | 52% | 1.2 | 3.92 | 4.64 | Fail | 50% | 1.1 | 3.69 | 4.59 | Pass | 61% | 1.4
Spectral Range MWIR | 5.00 | 8.26 | Pass | 100% | 2.6 | 6.20 | 8.22 | Pass | 53% | 1.4 | 5.71 | 8.26 | Pass | 80% | 2.1 | 6.40 | 7.44 | Fail | 9% | 0.2
Spectral Range LWIR | 8.26 | 15.50 | Pass | 100% | 5.2 | 8.80 | 15.38 | Fail | 50% | 2.6 | 9.13 | 15.38 | Fail | 50% | 2.6 | 9.59 | 14.98 | Fail | 50% | 2.6

## Slide 16: Other Requirements
 |  | Threshold |  | Saturation |  | 
 | Unit | Min | Max | Min | Max | Weight
Date Range | Year | 2015 | 2015 | 2006 | 2030 | 10
Geographic Coverage: Lat | deg | -10 | 10 | -90 | 90 | 1
Geographic Coverage: Lon | deg | -10 | 10 | -180 | 180 | 1
Dynamic Range | K | 270 | 300 | 180 | 330 | 2
Geometric Range: VZA | deg | 5 | 15 | 0 | 90 | 2
Geometric Range: VAA | deg |  |  |  |  | 0
Geometric Range: SZA | deg |  |  |  |  | 0
Geometric Range: SAA | deg |  |  |  |  | 0
Geometric Range: Pol | deg |  |  |  |  | 0
Diurnal Coverage | hr | 9 | 10 | 0 | 12 | 10
Field of View | km |  | 300 |  | 3 | 1
Number of obs/day | /d |  |  |  |  | 0
Number of Collocations | /d | 1 |  | 10000 |  | 4
Spatial resolution | km |  | 100 |  | 10 | 0
Spatial sampling | km |  | 100 |  | 10 | 1
Geolocation accuracy | km |  | 10 |  | 0.1 | 5
Polarisation knowledge | deg |  |  |  |  | 
Radiometric Stability | K/yr |  | 1 |  | 0.001 | 10
Orbital Stability | hr/yr |  | 12 |  | 0.1 | 0
Radiometric Noise | K |  | 10 |  | 0.1 | 1
Uncertainty from SBAF | K |  | 1 |  | 0.01 | 10
Spectral Resolution | cm-1 |  | 100 |  | 0.5 | 0
Spectral Stability | cm-1/yr |  | 2 |  | 0.01 | 0
SBAF Uncertainty | K |  | 1 |  | 0.001 | 10
Absolute Calibration Acc | K |  | 1 |  | 0.001 | 10
Inter-channel calibration | K |  |  |  |  | 2
Your thoughts on these requirements? ...

## Slide 17: Overview
Report on Reference Sensor Traceability and Uncertainty
Review Reference Instrument Requirements
Scoring scheme for Reference Instruments
OSCAR rule-based selection

## Slide 18: Scoring Criteria
Select reference meeting most essential requirements
Select reference meeting most desirable requirements
Define weighting for all requirements and score each reference against all criteria
Some hybrid of the above?

## Slide 19: Reference Score wrt Saturation

## Slide 20: Alternative Approaches
Just define the uncertainty on the resulting inter-calibration products!
Problem:
  Current uncertainty analysis assumes the Primary GSICS Reference is the Truth
  It does not contribute to the uncertainty
Solution?
  Analyse uncertainties of Delta Corrections
  As part of process of generating Prime GSICS Corrections

## Slide 21: Draft Scorecards
Online Spreadsheet in Microsoft OneDrive
for 2014 GEO Imagers
And 2020 GEO Imagers
Anyone want to try sounders?
Any thoughts on other spectral bands?

## Slide 22: Overview
Report on Reference Sensor Traceability and Uncertainty
Review Reference Instrument Requirements
Scoring scheme for Reference Instruments
OSCAR rule-based selection

## Slide 23
Thank You
Notes: 23