## Slide 1: Selecting a GSICS reference instrument
Manik Bali, Tim Hewison and Lawrence E Flynn
July, 09, 2015 ( Web meeting)

## Slide 2: Outline
Introduction
  Introduction to OSCAR and ICVS
  GSICS Ref Instrument
  GSICS Reference Instrument
Selection of References – Classical Monitoring
Selection of References – Future needs
Process to identify GSICS reference Instrument.
  Tim Hewison Scoring Scheme
  Application of Process ( Example-1, Example-2)
Summary and Conclusion.

## Slide 3: Introduction
Introduction- OSCAR/ NCC /ICVS
OSCAR [ Observing System Capability Anaysis and Review Tool]
OSCAR is a resource developed by WMO in support of Earth Observation applications, studies
and global coordination. (IASI , CrIS )
Web pages are static. ( can act as a starting point but not complete input for selecting Ref Instrument)
National Calibration Center (NCC)
Resulted from joint NOAA and NIST collaboration.
Info on NCC instrument that is more relevant to Cal/Val community
ICVS [ Integrated Calibration Validation System ] ( other similar systems can be explored)
On-orbit and prelaunch instrument characterization and long-term monitoring of instrument performance. Web pages give dynamic info on key cal/val parameters of the instrument
Do we have similar public websites for IASI that provide its trending?

## Slide 4: Introduction-GSICS References
GSICS Reference Instruments are at the Center of instrument Monitoring and GSICS Product Generation.
Stability and accuracy (over time) of reference instrument are vital parameters for ensuring good quality of GSICS inter-calibration monitoring.
GSICS Reference Instruments
IR Products
Vis Products
MW
UV
AIRS
IASI
MODIS
GSICS Aims [Ref: WMO website ]
Monitoring instrument performances,
Operational inter-calibration of satellite instruments- GSICS Products
Tying the measurements to absolute references and standards, and recalibration of archived data
Preoperational 8 products [4 EUMETSAT, 4 NOAA]
Demonstration 27 products [4 EUMETSAT, 13 NOAA, 6 JMA]

## Slide 5
Initial years of GSICS ….handled problems of lower complexity ….
Monitored broad band GEO /LEO sensors by inter comparing with hyper spectral LEO.
Needed a reference instrument that is stable enough be able to monitor GEO/LEO instruments and reveal expected measurements biases ( and variations in them) .
The MODIS instrument has high calibration accuracy and can track its own radiometric changes due to the inclusion of an onboard calibration system for the VIS/NIR spectral region [MCST].
Stated Accuracy better than 1 K.
AIRS ( Afternoon orbit) and IASI ( Morning orbit ) Hyper-spectral Instruments
Radiances span main IR channels of broad band instruments i.e 11 12 13 Micron
AIRS and IASI routinely monitored and long term monitoring of three way comparisons exist ( CrIS IASI and AIRS).
Added confidence Comparisons of IASI and AIRS with Climate Instruments (ATSR2 and AATSR) reveal better than 0.1 K accuracy and pre-launch like behavior of AIRS and IASI.
In-orbit reference Instrument noise not fully known
Used a simple selection criterion for selecting reference instrument
Focused on monitoring IR and VIS bands using a limited number of reference instruments
MODIS
IASI
AIRS
AVHRR
MTSAT
GOES
SEVIRI
For In-orbit Inter-calibration we broadly needed
An algorithm that can perform the inter- comparison
[ e.g.. DCC, SNO baseline algorithm]
Well calibrated in-orbit References [ stability, accuracy ]
Selection of Reference Instruments-Classical Monitoring

## Slide 6
New In-Orbit Inter-comparison methods have been developed [ For eg VIS cross calibration using DCC, Direct SNO and Ray Matching]
Advances in GSICS MW Subgroup ( GPM-X, need reference , developed FCDR )
New Hyper-spectral IR instruments that ( some of legacy make such as IASI-B/C and some new like CrIS) can be good candidates for being used as a reference.
Prime Correction product ( such as developed at EUMETSAT) is being developed. This product attempts to give a single reference radiance that combines several high quality instruments (references).
GSICS Requirements have grown.
We wish to monitor VIS, MW UV in addition to classical IR Instruments
We now have a better understanding of in-orbit behaviour of reference instruments ( parameters such as in-orbit spectrum, temperature, geo-locational and temporal ) biases and instrument noise are being monitored. Monitored on ICVS and documented on OSCAR, NCC and other pages maintained by agencies).
With newer and better instruments, User gets the opportunity to make a selection for reference from a wider range of instruments.
Recent Developments
Selection of Reference Instruments-Future Monitoring

## Slide 7
GRWG
IR
MW
UV
VIS
AIRS
IASI A/B/C
Primary Ref*
CrIS*
GP-X *
ATMS*
MSU AMSU
SSMI*
OMI*
GOME-2*
Aqua Modi+ DCC
Monitored instrument overlaps with spectrum of hyper-spectral instruments
MW spectrum is large and not spanned by a single reference instrument.
Multiple broad band instruments can be candidates.
Complexity of in-orbit Inter - comparision enhanced as by surface reflectance Solar Zenith Angle. viewing geometry impact A-B .
Stability of Transfer targets such as DCC, Desert kicks in instrument monitoring algo.
Diverse requirements across subgroups ( even within subgroups )
GSICS Need to adopt a process to identify references.
Selection of Reference Instruments-Future Monitoring
Notes: tore

## Slide 8
GSICS Subgroups are the center of GSICS Cross Calibration Research and product generation.
Selection of Reference instruments should be made by the GSICS group level.
Selection criterion could depend on……
The instrument and Channels sub group wishes to monitor.
The method/s they would employ to monitor( eg. single or blended references, use transfer target or not stability criterion).
In addition consider scoring proposed by Tim ( if there are more than 1 candidate instruments).
Comparison of Instrument design specification ( Pre-launch testing) with In-orbit behavior.
May consider if in-orbit status of key parameters of Candidate Ref instrument are monitored and available to users ( eg. ICVS).
Take inputs from Info ( global coverage, eq. cross time etc) related to instrument available ( eg OSCAR)
Selection should be based on sub group (user) requirements .
GRWG
IR
MW
UV
VIS
Selection of Reference Process

## Slide 9
Source: Tim Hewison
Scoring Scheme

## Slide 10
A very simple scheme
The proposed scoring scheme can be summarized by the definition of the following for each class of GSICS product:
Variables describing required performance of Reference.
Minimum thresholds for each variable required for inter-calibration to be useful.
Maximum thresholds (optimal values) for each variable above which no further improvement will be realized
Weighting for each variable (to align with contributions to overall uncertainty)
Tim Proposed Scoring Scheme-Overview
Curtsey Tim Hewison

## Slide 11
Selection Process Reference for MW
A sub-group meeting is organized to identify instrument to be monitored.
Group wishes to monitor GPM satellites spread over a range of roughly 25S to 25N ( for eg GMI)
Group evaluates ATMS and SAPHIR.
Group considers that SAPHIR are the first radiometers in the 183 GhZ in low inclination orbit ( Wilheit)
Despite not presenting global observations SAPHIR also scores higher because the intended goal is to inter-calibrate low inclination instruments. In addition input from scoring is considered.
On the other hand if goal would have been to monitor Polar instruments ATMS could have been a better choice.
Both SAPHIR and ATMS can score the same marks
OSCAR provides limited but critical information on instruments. (spectral, temporal and geographical coverage)
Detailed information is obtained via ATBD
Instrument info on OSCAR and NRT monitoring on ICVS is considered
Application of Process- Example-1

## Slide 12: Example-2
Reference for IR
A sub-group meeting is organized to identify instrument to be monitored.
Group wishes to monitor 11 and 12 and 13 Micron Channels of a GEO instrument.
Group evaluates IASI and CrIS
Group considers that both the instruments span the Monitored instrument channels
OSCAR page reveals that noise levels in the 10- 13 Micron range are comparable.
Monitoring at ICVS reveals key calibration parameters within spec.
.
Both instruments can act as references .
Application of Selection Process - Example-2

## Slide 13: Summary and Conclusions
Process by which reference instrument could be selected in GSICS has been proposed here.
It is proposed that the main decision to identify a reference instrument should rest with the subgroup.
Evaluation of OSCAR for the purpose of Ref selection reveals that while some information about candidate reference instruments could be obtained via the WMO OSCAR however OSCAR pages are static and a complete info about instrument should be obtained from the agency maintaining the instrument. Special caution to be applied when considering noise levels ( NeDT) stated at OSCAR.
More useful input could be provided by instrument monitoring done by the agency ( such as ICVS, NCC).
Scoring scheme for reference instrument can be a vital input in deciding which instrument to use as a reference.
Summary and Conclusions

## Slide 14: Thank You

## Slide 15
Web Meeting 2013-10-15
2015 GRWG Meeting: Agenda Item 7a: Scoring scheme for reference instruments
Action:
GRWG_15.63 | Tim to provide to Manik a list of parameters from his scoring proposal to include them into the expert system. | TimHewison | 29 Feb 2016

## Slide 16
Spectral Characteristics of CrIS
Spectral Characteristics of IASI
OSCAR page reveals that noise levels in the 10- 13 Micron range are comparable.
Both instruments can act as references