## Slide 1: GRWG Web Meeting: Best Practice for defining SBAFs
Tim Hewison
(EUMETSAT) (Outgoing GRWG Chair)
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:

## Slide 2: Agenda
Tim Hewison (EUMETSAT) - Introduction
Ben Scarino (NASA) - NASA SBAF web page
Ben Scarino (NASA) - The use of IASI to define SBAFs for IR channels
Tom Stone (USGS) – How ROLO accounts for different Spectral Response Functions
Sebastien Wagner (EUMETSAT) – GIRO SBAFs
Tim for Viju John - Meteosat-HIRS SBAFs
All - Discussion on whether we can recommend standard methods to define SBAFs and their uncertainties

## Slide 3: Introduction to SBAF Definition - Can we define a Best Practice?
Tim Hewison
(EUMETSAT) (Outgoing GRWG Chair)
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:

## Slide 4: Revised Vision for GSICS in 2020s
Action: GRWG Chair to set up an additional web meeting on SBAF determination
Other SBAF actions:
GWG_13.26 | Ben Scarino to analyse SBAFs for each GEO imager and supply to GPRCs, together with the uncertainty due to DCC variation - due by 2nd DCC web meeting. | BenScarino? | 01 Jun 2013
GRWG_15.52 | Tim to provide SBAF tool to support the analysis of GEO-GEO double-differences | TimHewison | 29 Feb 2016

## Slide 5: Background
Comparisons with Hyperspectral references
  Can synthesise any SRF
  With negligible uncertainty*
  Need no SBAFs
*Confirmed by uncertainty analysis

## Slide 6: Background
Comparisons with Hyperspectral references
  Can synthesise any SRF
  With negligible uncertainty
  Need no SBAFs
Comparisons with Broad-band reference instruments
  Different SRFs
  Different sensitivity to scene radiance spectral
  Need SBAF to project between channel spaces
MET
HIRS -2
HIRS-3/4

## Slide 7: Motivation for Systematic SBAF Definition
Now starting to generate GSICS products using broadband reference instruments
  VIS/NIR: DCC and Lunar Using Aqua/MODIS
  Microwave
  IR: GEO-HIRS
SBAFs can be defined in many ways
Can we define a generic procedure as a best practice to define the SBAF?

## Slide 8: Basic Approaches
Regression using training dataset
  Radiances from monitored and reference instruments
  What form of regression?
  Linear – between pairs of channels
  Multiple – between combinations of channels
    What combinations?
  Weighted?
  Non-linear?
  In radiance/reflectance/brightness temperature?

## Slide 9: Training Datasets
Synthetic }
Empirical }- Observations from monitored and reference instruments
Semi-synthetic}
Need to cover full range of target inter-calibration
  Radiances
  Viewing geometry
  Atmospheric conditions LARGE!
  Geographic (lat, lon, surface type, ...)

## Slide 10: Synthetic Training Datasets
Synthetic
  E.g. Radiative Transfer Models
  Need to include atmosphere (clear, cloud, aerosol, ppt)
  And Surface (sea/land/ice,...)
  From Radiosondes/NWP
  May include model biases
  Difficult to ensure representative
  Estimate uncertainties by perturbing inputs (e.g. Monte Carlo method)

## Slide 11: Empirical Training Datasets
Observational
  E.g. Pairs of collocated observations
  Need to account for instrumental biases
  Can ensure representative using large real dataset
  Estimate uncertainties from regression statistics

## Slide 12: Semi-Synthetic Training Datasets
From Hyperspectral Observations
  Convolved with SRFs of monitored and reference instruments
  May include inter-band instrumental biases? Small?
  Can ensure representative using large real dataset
  Estimate uncertainties from regression statistics

## Slide 13: Uncertainties
Need to estimate uncertainty
Error propagation difficult
Using validation dataset
  Independent from training dataset

## Slide 14: Agenda
Tim Hewison (EUMETSAT) - Introduction
Ben Scarino (NASA) - NASA SBAF web page
Ben Scarino (NASA) - The use of IASI to define SBAFs for IR channels
Tom Stone (USGS) – How ROLO accounts for different Spectral Response Functions
Sebastien Wagner (EUMETSAT) – GIRO SBAFs
Tim for Viju John - Meteosat-HIRS SBAFs
All - Discussion on whether we can recommend standard methods to define SBAFs and their uncertainties

## Slide 15: Can we recommend standard methods to define SBAFs and their uncertainties?
Tim Hewison
(EUMETSAT) (Outgoing GRWG Chair)
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:

## Slide 16: Is one approach the best?
How to select best approach:
  Just compare uncertainties?
  Try each approach and perform independent validation?
  How?
Repeat for different inter-calibration classes
  GEO-LEO IR/VIS/NIR
  LEO-LEO?

## Slide 17: Next Steps?
Do we take this further?
If so, how?
Who to lead?
Timescale?