## Slide 1: Lunar Calibration based on SELENE/SP data
Toru Kouyama (AIST)
Matsunaga, Nakamura, Yamamoto, Yokota and Ishihara
SELENE/SP Team
・SP lunar reflectance model
・Basic characteristics of SP model
・Our recent lunar calibration activities using SP model

## Slide 2
Using Moon for Radiometric calibration
Extremely Photometrical stable (1% change  1 Myr)
[Kieffer, 1997]
Moon is an ideal target for radiometric calibration
No atmospheric and aerosol absorption and scattering
Earth
Reliable Lunar reflectance model is important, and SELENE/SP team has tried to develop such a reliable reflectance model.
Notes: “Photometrical properties” do not change in any Moon observation.
Lunar calibration is one of ideal calibration methods

## Slide 3: SELENE(KAGUYA) and SP
SELENE:
・Size: 2 x 2 x 5m, 14 science instruments
・Orbit: Polar orbit (non sun-synchronous)
Altitude: 100 km
Ground track repeat cycle: ~ 30 days
・Mission period: 2007 – 2009 (finished)
Observing lunar surface
with various solar incident and phase angle conditions.
(Spectral Profiler)

## Slide 4: SELENE(KAGUYA) and SP
(Spectral Profiler)
Spectral
Sensor type: Spectrometer
Point sensor
http://www.kaguya.jaxa.jp/en/equipment/tc_e.htm
Multi-band Imager
Terrain Camera
Notes: Sensor type: Spectrometer
Spectral range:
500-2600 nm
Spectral resolution:
6 nm (VNIR 520-960 nm)
8 nm (NIR-SWIR > 900 nm)
Observation swath
500 m

## Slide 5: SELENE(KAGUYA) and SP
http://global.jaxa.jp/press/2007/12/20071214_kaguya_e.html
(Spectral Profiler)
SP Data
MI image and SP footprints
Wavelength
Notes: During the mission, SP obtained this kind of data globally and repeatedly.

## Slide 6
Spectral range:
512 – 1650 nm (160 channels)
Δλ = 6 - 8 nm
1˚ x 1˚ grid interval: published
0.5˚ x 0.5˚: to be published
Reflectance spectrum
SP Lunar Reflectance model (Yokota et al., 2011)
Reflectance map (758nm, i=30, e=0, α=30°)
Integrating 70 million observation data covering whole lunar surface with various phase angle conditions
Including incident, emission and phase angle dependencies using empirical functions
Notes: Including incident, emission and phase angle dependencies using empirical functions

## Slide 7
April 13, 2003
April 15
April 18
Simulating Moon observations

## Slide 8: SELENE(KAGUYA) and SP
Sensitivity stability of SP during mission
The degradation of SP was not significant over the mission period (variation: up to 1 %) [Yamamoto et al., 2011].
Comparison of four observations of
Apollo 16 landing site [Yamamoto et al., 2011]
Nov. 19, 2007
Mar. 12, 2009
Notes: Sensor stability during the mission

## Slide 9
・SP model characteristics
Terra / ASTER
Comparing with actual Moon observation data

## Slide 10
ASTER/Band 2 (660 nm)
April 14, 2003
Simulated*
Observed
ASTER vs SELENE/SP
*Integrated with ASTER Band2
Spectral response function (SRF)
[Kouyama et al., Inpress, Icarus]

## Slide 11
Brightness Comparison: ASTER vs SELENE/SP
 | Band 1 (520-600 nm) | Band 2 (630-690nm) | Band 3 (760-860nm)
Correlation Coefficient | 0.992 | 0.993 | 0.993
・SP model describes lunar surface contrast very well
Good for measuring sensitivity deviation among pixels
and relative degradation of a sensor

## Slide 12
Brightness Comparison: ASTER vs SELENE/SP
 | Band 1 (520-600 nm) | Band 2 (630-690nm) | Band 3 (760-860nm)
Correlation Coefficient | 0.992 | 0.993 | 0.993
Mean ratio (= Bias): Observed / Simulated | 1.27 | 1.01 | 0.95
Standard deviation of ratio (= Precision of each pixel) | 0.05 | 0.04 | 0.04

## Slide 13
SP reflectance has a steeper profile
(cf. Ohtake et al., 2010 & 2013)
SP’s reflectance
・More investigation for absolute accuracy of SP model is required
for measuring absolute degradation
[Ohtake et al., 2013]
In shorter wavelength region, SP model tends to describe lunar brightness darker than actual.
SP calibration issue
Notes: This plot shows a comparison of observation results among many sensors at a same place
SP reflectance shows a steeper profile than those
As a result… In shorter wavelength region, SP tends to describe Moon reflectance darker.
感度偏差: sensitivity deviation

## Slide 14
Correction with other lunar reflectance model (ex. ROLO)
Brightness ratio of Band 1
1.27 → 1.09
Fitted curve as a correction curve for SP model
Measuring ROLO irradiance is from Kieffer and Stone, 2005
Ratio (ASTER/SP)
[Kouyama et al., Inpress, Icarus]
Lunar Irradiance
SP calibration issue
Good Solution?

## Slide 15
Lunar calibration for planetary explorers
©JAXA
©JAXA
Hayabusa
Hayabusa2

## Slide 16
Observation
Simulation (Higher resolution)
Hayabusa
(AMICA)
Hayabusa2
(ONC-T)
2004.05.17
2015.12.05
Visible band (~550nm)
Visible band (~550nm)
observed mainly the far side of the Moon

## Slide 17
Irradiance comparison
Hayabusa/AMICA vs SP model
Corrected SP model with ROLO
SP model
Hayabusa/AMICA
AMICA’s irradiance is measured with calibration parameters reported in Ishiguro et all., 2011.

## Slide 18
Summary
Lunar reflectance model based on SELENE/SP hyper-spectral data
has been developed. Using the model, we can simulate/predict
any moon observation.
SP model describes lunar surface contrast very well.
The model can be used for evaluating relative degradations of
sensors.
However…
Large brightness bias exists between SP model and actual Moon
observations.
Correction using other models may be a possible solution for improving absolute accuracy of SP model.
Collaboration with ROLO/GIRO is very important.
We can simulate not only the near side of the Moon, but also the far side!
Notes: 論理の飛躍: leap in logic

## Slide 19
Supplement slides

## Slide 20
Incident angle
Emission angle
Geometry data
Highland, mare and middle albedo region map
Lunar radiance map
Reflectance map (i=30,e=0,α=30)
Phase angle at observation time
x Solar Irradiance

## Slide 21
Other Known calibration issues
Model accuracy tends to be worse in high emission angle and high latitude regions
Using this model requires estimating the location where each pixel looks at on the moon surface (=ray tracing calculation).
=> Error from uncertainty of pixel registration should be considered.
Model
ASTER

## Slide 22
Deference of phase angle dependency: ROLO vs SP

## Slide 23
[Kouyama et al., 2014, LPSC]

## Slide 24
Definition of three albedo groups of Moon surface

## Slide 25
Modeled radiance (W m-2 str-1 μm-1)
Observed radiance (W m-2 str-1 μm-1)
ASTER (Band 1) Large bias
Observed / Model
Relative Frequency
Mean (Obseｒved/Model) = 1.27
SD = 0.05
SE (= SD/√Number of pixels used) = 0.0002
ASTER@2003.04.14 vs Model (SELENE/SP)

## Slide 26
Band 1
Band 2
Band 3
1.0
0.7
0.9
0.8
0
3000
Day since launch
ASTER/VNIR degradation curves

## Slide 27
Moon observation conducted by ASTER is only once (April, 2003).
We are proposing the second Moon observation by ASTER to NASA/Terra.
Time
14 April, 2003
?
?
?
Degradation ratio
EOM
2016 or 2017
ASTER Moon observation:

## Slide 28
Chart: 
| 0.48 | 0.48399999999999999 | 0.48799999999999999 | 0.49199999999999999 | 0.496 | 0.5 | 0.504 | 0.50800000000000001 | 0.51200000000000001 | 0.51600000000000001 | 0.52 | 0.52400000000000002 | 0.52800000000000002 | 0.53200000000000003 | 0.53600000000000003 | 0.54 | 0.54400000000000004 | 0.54800000000000004 | 0.55200000000000005 | 0.55600000000000005 | 0.56000000000000005 | 0.56399999999999995 | 0.56799999999999995 | 0.57199999999999995 | 0.57599999999999996 | 0.57999999999999996 | 0.58399999999999996 | 0.58799999999999997 | 0.59199999999999997 | 0.59599999999999997 | 0.6 | 0.60399999999999998 | 0.60799999999999998 | 0.61199999999999999 | 0.61599999999999999 | 0.62 | 0.624 | 0.628 | 0.63200000000000001 | 0.63600000000000001 | 0.64 | 0.64400000000000002 | 0.65 | 0.66 | 0.67 | 0.68 | 0.69 | 0.7 | 0.71 | 0.72 | 0.73 | 0.74
Band 1 | 0 | 0.0069 | 0.0078 | 0.0073 | 0.0107 | 0.058 | 0.125 | 0.2911 | 0.4567 | 0.6717 | 0.8392 | 0.9381 | 0.9906 | 1 | 0.9662 | 0.89 | 0.876 | 0.8959 | 0.9029 | 0.9263 | 0.9184 | 0.9387 | 0.9501 | 0.954 | 0.9606 | 0.9528 | 0.9058 | 0.8687 | 0.774 | 0.6795 | 0.5206 | 0.2972 | 0.151 | 0.0918 | 0.052 | 0.0355 | 0.0098 | 0.0046 | 0.0037 | 0.0056 | 0.0037 | 0.0014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Band 2 | 0.0038 | 0.0032 | 0 | 0.0019 | 0.0031 | 0.0006 | 0.005 | 0.0049 | 0.0018 | 0.0136 | 0 | 0.1529 | 0.3429 | 0.5998 | 0.8024 | 0.9709 | 1 | 0.9758 | 0.9696 | 0.975 | 0.943 | 0.9077 | 0.9396 | 0.9426 | 0.9226 | 0.91 | 0.8935 | 0.8427 | 0.8031 | 0.7917 | 0.7702 | 0.7487 | 0.6619 | 0.5544 | 0.4596 | 0.4258 | 0.3708 | 0.2991 | 0.2166 | 0.1247 | 0.0623 | 0.0442 | 0.028 | 0.0118 | 0.0105 | 0.0054 | 0.0041 | 0.0007 | 0 | 0 | 0 | 0
Band 3N | 0.0022 | 0 | 0.0093 | 0.0258 | 0.048 | 0.0509 | 0.098 | 0.1907 | 0.3353 | 0.6379 | 1 | 0.9786 | 0.8982 | 0.9148 | 0.9778 | 0.9942 | 0.9783 | 0.9624 | 0.9355 | 0.9713 | 0.982 | 0.9976 | 0.9895 | 0.9751 | 0.9874 | 0.9694 | 0.9542 | 0.9489 | 0.9247 | 0.9609 | 0.9489 | 0.942 | 0.9297 | 0.8366 | 0.6943 | 0.4813 | 0.2958 | 0.1763 | 0.09 | 0.0547 | 0.0318 | 0.0258 | 0.0204 | 0.0075 | 0.0074 | 0.0049 | 0.0024 | 0.0024 | 0 | 0 | 0 | 0
SRF convolution
Simulated hyperspectral images
Simulated band image

## Slide 29
Model equations
r: reflectance using i=30, e=0, α=30 as the basis condition [Yokota et al.,2011] (11)
i: incident, e: emission, α: phase anlge
Fsun: Sun light Flux (W/m2/um)
S: SRF
From SP model
f: Empirical function of phase angle dependencies
XL: Empirical function of sun-light scattering

## Slide 30
Model equations
XL: Lunar lambert function
f: Empirical function of phase angle dependencies
After Yokota et al., 2011, Eq (11)
B: Shadow hiding opposition effect
P: Regolith phase function
h, c, g, B0: Model coefficients
Correction terms for Limb darkening effect
Reflectance to be calculated
i: incident angle
e: emission angle
α: phase angle
Notes: c1=-0.019, c2=0.242x10-3, c3=-1.46x10-6

## Slide 31
Model equations
After Yokota et al., 2011, Eq (11)
B: Shadow hiding opposition effect
P: Regolith phase function
h, c, g, B0: Model coefficients
Reflectance to be calculated
XL: Lunar lambert function
f: Empirical function of phase angle dependencies
Correction terms for Limb darkening effect
i: incident angle
e: emission angle
α: phase angle

## Slide 32
Model equations
B: Shadow hiding opposition effect
P: Regolith phase function
h, c, g, B0: Model coefficients
After Yokota et al., 2011, Eq (11)
High land, mare and medium albedo
Reflectance to be calculated
XL: Lunar lambert function
f: Empirical function of phase angle dependencies
Correction terms for Limb darkening effect
i: incident angle
e: emission angle
α: phase angle

## Slide 33
http://l2db.selene.darts.isas.jaxa.jp/index.html.en
SELENE(KAGUYA) and SP

## Slide 34
Hyperspectral Imager
Multispectral Imager
HISUI
Panchromatic
Stereo Camera
ALOS-3
(JAXA)
Hyperspectral
Image “Cube”
The hyperspectral imager:
Contiguous and high resolution spectral information from visible to short-wave IR
The multispectral imager:
4 Bands observation with a high spatial resolution by a wide swath
HISUI mission

## Slide 35: Hayabusa-2
Japanese satellite for exploring a small asteroid