## Slide 1: JAXA Calibration Activities of GCOM-C/SGLI
Hiroshi Murakami and Masahiro Hori
JAXA/EORC
2016 GSICS Data & Research Working Groups Meeting
Mini Conference, 29 Feb. 2016

## Slide 2
Evaluation of model outputs and process parameterization
EarthCARE/CPR
3-D structure of
cloud and aerosol
Aerosol
radiative forcing change
Cloud
GCOM-C
Global/horizontal distribution of cloud and aerosol
Monitoring and process knowledge of
cloud and aerosol by GCOM-C & EarthCARE
1. GCOM-C/SGLI: Mission targets
Long-term observation about radiation budget and carbon cycle
Global environmental change
(irradiance, temperature,
CO2, precipitation）
Feedback
Change of atmosphere CO2
Photosynthesis production
Vegetation index
Leaf area index
Primary production
Above-ground biomass
Land cover/use
Soil respiration
Photosynthesis production
Phytoplankton chl-a
Sea surface temperature
PAR
Dissolved organic matter
CO2 solution, pH
Sedimentation
CO2 increase and
Global warming
Land
Ocean
Ecosystem
CO2 sink and pool
Global coverage
Many parameters
Long-term data
GCOM-C
Launch
GCOM-C2
GCOM-C3
5 years
~13 years
JFY 2016

## Slide 3
Solar calibration window
Earth view
window
FOV: 80-deg
Deep space
window
approx. 1.4m
approx. 0.6m
Visible and Near-infrared Radiometer
(SGLI-VNR)
VNR-NP
Non-polarization tree telescopes
Each has the same 11 channels
Solar diffuser
approx. 1.7m
approx. 1.3m
GCOM-C
satellite
Total FOV: 70deg
= 24deg  3 telescopes
(~1150km@nadir)
Earth direction
Earth
Earth
45deg along-track slant observation
VNR-POL
Polarization two (670nm and 865nm) telescopes
Each has tree polarization-angle filters
Scan mortar
Black body
SWIR detector
TIR detectors
Optical bench
Earth
mechanical cooler
FOV: 55deg
(~1150km@45deg along-track slant)
Orbit
Orbit
Orbit
Orbit
InfraRed Scanner
(SGLI-IRS)
45deg
1. GCOM-C/SGLI: Satellite/Sensor system
Internal lamp (PD)
GCOM-C SGLI characteristics | 
Orbit | Sun-synchronous (descending local time: 10:30), Altitude: 798km, Inclination: 98.6deg
Launch Date | JFY 2016
Mission Life | 5 years (3 satellites; total 13 years)
Scan | Push-broom electric scan (VNR: VN & P) Wisk-broom mechanical scan (IRS: SW & T)
Scan width | 1150km cross track (VNR: VN & P) 1400km cross track (IRS: SW & T)
Spatial resolution | 250m, 500m, 1km
Polarization | 3 polarization angles for POL
Along track tilt | Nadir for VN, SW and TIR, & +/-45 deg for P
SGLI/VNR daily coverage
Notes: The Second-generation Global Imager (SGLI) on the Global Change Observation Mission -Climate (GCOM-C) is a multi-band optical imaging radiometer in the wavelength range from 380nm to 12000nm.
It consists of two main components, the Visible and Near Infrared Radiometer (SGLI VNR) and the Infrared Scanning Radiometer (SGLI IRS).

## Slide 4
(a) 250m Sagami-Bay (2 May 2015, CHL by LCI)
(b) 1km Sagami-Bay (2 May 2015, CHL by LCI)
250m resolution to detect finer structure in the coastal area such as river outflow, regional blooms, small current, and redtide
250m SGLI products simulated by Landsat image on 2 May 2015
1. GCOM-C/SGLI:
SGLI 250m Visible-SWIR observation
250m
1km
1-km resolution
250-m resolution
Redtide

## Slide 5
1-km resolution
250-m resolution
1. GCOM-C/SGLI:
SGLI 250m Thermal infrared observations
Simulated by LANDSAT-8/TIRS 11m 100m data on 23 Jan. 2014
Kelvin
Arakawa Riv.
Edogawa Riv.
Tama Riv.
Obitsu Riv.

## Slide 6
Along-track 45deg modes will be planned for polarization observation of the atmospheric scattering
Along track slant obs
45deg
Satellite direction
Polarization filter
0/60/120
670nm
865nm
Orbit direction
45deg
~2min
45deg
1. GCOM-C/SGLI:
SGLI slant-view polarization observation
~1150km @ 45 slant view
FOV=55deg(27.5deg)
Global aerosol optical thickness in June 2003 using POLDER-2 polarization reflectance (provided by T. Sano, Kinki Univ.)
Aerosol optical thickness

## Slide 7
Land | 
Surface reflectance | Precise geometric correction
 | Atmospheric corrected reflectance
Vegetation and carbon cycle | Vegetation index
 | Above-ground biomass
 | Vegetation roughness index
 | Shadow index
 | Fraction of Absorbed Photosynthetically available radiation
 | Leaf area index
Temp. | Surface temperature
Application | Land net primary production
 | Water stress trend
 | Fire detection index
 | Land cover type
 | Land surface albedo
Atmosphere | 
Cloud | Cloud flag/Classification
 | Classified cloud fraction
 | Cloud top temp/height
 | Water cloud optical thickness /effective radius
 | Ice cloud optical thickness
 | Water cloud geometrical thickness
Aerosol | Aerosol over the ocean
 | Land aerosol by near ultra violet
 | Aerosol by Polarization
Radiation budget | Long-wave radiation flux
 | Short-wave radiation flux
Cryosphere | 
distribution | Snow and Ice covered area
 | Okhotsk sea-ice distribution
 | Snow and ice classification
 | Snow covered area in forest and mountain
Surface properties | Snow and ice surface Temperature
 | Snow grain size of shallow layer
 | Snow grain size of subsurface layer
 | Snow grain size of top layer
 | Snow and ice albedo
 | Snow impurity
 | Ice sheet surface roughness
Boundary | Ice sheet boundary monitoring
Common | 
Radiance | TOA radiance (including system geometric correction)
Ocean | 
Ocean color | Normalized water leaving radiance
 | Atmospheric correction parameter
 | Photosynthetically available radiation
 | Euphotic zone depth
In-water | Chlorophyll-a conc.
 | Suspended solid conc.
 | Colored dissolved organic matter
In-water | Inherent optical properties
Temp. | Sea surface temp.
Application | Ocean net primary productivity
 | Phytoplankton functional type
 | Redtide
 | multi sensor merged ocean color
 | multi sensor merged SST
Blue: standard products
Red: research products
1. GCOM-C/SGLI: GCOM-C Observation Products
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
All standard products (L1, L2, L3) will be distributed by the internet (released to the public one year after the launch)
Free for both science and commercial purposes

## Slide 8: 2. GCOM-C/SGLI development: Spectral bands
Characteristics of SGLI spectral bands |  |  |  |  |  | 
CH |  |  | Lstd | Lmax | SNR@Lstd | IFOV
 | nm |  | W/m2/sr/m K: Kelvin |  | - K: NET | m
VN1 | 380 | 10 | 60 | 210 | 250 | 250 /1000
VN2 | 412 | 10 | 75 | 250 | 400 | 250 /1000
VN3 | 443 | 10 | 64 | 400 | 300 | 250 /1000
VN4 | 490 | 10 | 53 | 120 | 400 | 250 /1000
VN5 | 530 | 20 | 41 | 350 | 250 | 250 /1000
VN6 | 565 | 20 | 33 | 90 | 400 | 250 /1000
VN7 | 673.5 | 20 | 23 | 62 | 400 | 250 /1000
VN8 | 673.5 | 20 | 25 | 210 | 250 | 250 /1000
VN9 | 763 | 12 | 40 | 350 | 1200* | 250 /1000*
VN10 | 868.5 | 20 | 8 | 30 | 400 | 250 /1000
VN11 | 868.5 | 20 | 30 | 300 | 200 | 250 /1000
POL1 | 673.5 | 20 | 25 | 250 | 250 | 1000
POL2 | 868.5 | 20 | 30 | 300 | 250 | 1000
SW1 | 1050 | 20 | 57 | 248 | 500 | 1000
SW2 | 1380 | 20 | 8 | 103 | 150 | 1000
SW3 | 1630 | 200 | 3 | 50 | 57 | 250 /1000
SW4 | 2210 | 50 | 1.9 | 20 | 211 | 1000
TIR1 | 10800 | 700 | 300K | 340K | 0.2K | 250/500/1000
TIR2 | 12000 | 700 | 300K | 340K | 0.2K | 250/500/1000
Multi-angle obs. for 674nm and 869nm
Uchikawa, T., K. Tanaka, Y. Okamura, S. Tsuida, and T. Amano, "Proto Flight Model (PFM) performance and development status of Cisible and Near Infrared Radiometer (VNR) on the Second-generation Global Imager (SGLI)", SPIE Asia-Pacific Remote sensing, Beijing, China, 9264-27, 2014.
Tanaka, K., Y. Okamura, T. Amano, T. Hosokawa, and T. Uchikita, "The development status of Second Generation Global Imager Infrared Scanning Radiometer (SGLI-IRS)", SPIE Asia-Pacific Remote sensing, Beijing, China, 9264-15, October, 2014.
VNR-POL
VNR-NP
SGLI-IRS
high-gain bands
POL bands

## Slide 9
Yoshihiko Okamura ; Kazuhiro Tanaka ; Takahiro Amano ; Koichi Shiratama and Tamiki Hosokawa, " Development and pre-launch test status of Second Generation Global Imager (SGLI) ", Proc. SPIE 9639, Sensors, Systems, and Next-Generation Satellites XIX, 96390I (October 12, 2015); doi:10.1117/12.2193387
2. GCOM-C/SGLI development: Radiometric tests
specification
Results
low NEdT is better
high SNR is better

## Slide 10
3. SGLI calibration: raiometric calibration system
solar irradiance
SST
fixed-point
blackbody furnace
integration
sphere
AIST
NIST
SGLI VN/SWR
diffuser BRDF
radiometer
internal lamp
SGLI TIR
radiometer
standard blackbody
onboard
blackbody
radiometer
LST
Cloud
Ocean
Desert
Snow
Other satellite sensors
GIRO
(GSICS/ROLO)
in-situ radiometer
buoy SST
Solar spectrum
2%
1%
<2%
Post-launch Level-1 calibration will be based on the onboard calibration
Vicarious calibration will be used for
  confirmation of the onboard calibration,
  more accurate calibration (adjustment) required for the L2 algorithms
Cross calibration
Vicarious calibration
Onboard calibration
Ground characterization
in-situ
radiometers
once/month
at the same phase angle
Moon
launch shift
longtime change

## Slide 11
SGLI Operation Concept (SPIE, Incheon, Oct. 13, 2010)
3. SGLI calibration: VNR onboard calibration

## Slide 12
SGLI Operation Concept (SPIE, Incheon, Oct. 13, 2010)
3. SGLI calibration: IRS onboard calibration

## Slide 13
SGLI Operation Concept (SPIE, Incheon, Oct. 13, 2010)
3. SGLI calibration: Calibration Maneuver

## Slide 14
Forward calculation from surface measurements by Radiative Transfer model: SST, land/snow surface reflectance, Ocean color..
Iteration from satellite radiance by modifying correction coefficients: Land surface temperature, Ocean Color..
4. Vicarious/cross calibration
In-situ or reference BRDF  sBRF
RT or LUT by RT with RSR
r, g , a(, Model), tg, t0, t1, T0, T1, Sa
In-situ aerosol or reference sensor/band TOA
Simulated TOA
Ancillary (Pres, O3, H2O, WS)
SGLI TOA
TOA /tg  r + t0t1 g + a +
T0T1  sBRF
1  Sa  s
Corrected TOA
SGLI TOA
Inversion algorithm
Product
In-situ or other satellite product
gvc
(A) Forward
(B) Iteration
gvc

## Slide 15
4. Vicarious/cross calibration: products and methods
Target product | Vicarious calibration method
Ocean color and aerosol | (A & B) MOBY and BOUSSOLE (A & B) Aeronet-OC (confirmation) (A & B) Rrs ship measurements (confirmation)
Ocean color and aerosol (geometrical and FOV dependency) | (A) Other satellite Rrs
Sea surface temperature (SST) | NOAA iQuam data base +RT (A) AIRS, IASI + RT
Land-Surface Temperature (LST) | (B) LST measurements (desert sits) and iteration with LST algorithm
Snow properties | (A) Snow in-situ albedo (by PIs) + RT
Land vegetation products | (A) 500m-scale vegetation sites +RT
Ocean color, aerosol, and cloud (inter band) | (A) Sunglint in the offshore (+ multi-angle)
Ocean color and aerosol (Cross calibration, stability) | (A) Cross calibration over offshore ocean with Rayleigh scattering
land, snow, and cloud (Cross calibration, stability) | (A) Cross calibration over desert, snow sites, and high water cloud

## Slide 16
4. Vicarious/cross calibration: Fixed Area Extraction
Equal lat-lon grid from GCOM-C LTOA tile data (250m and/or 1km resolution)
1deg x 1deg area (wide areas for the ocean stable areas)
Site locations (TBD): CEOS sites, other Sentinel-3 sites, and some val sites in the Asia-Pacific
Sites can be changed by modify list file: lut/cvsites.list
Format: HDF5 (TBD)

## Slide 17: 5. Calibration of in-situ instruments
In-situ radiometer calibration by JAXA integration sphere (MS-720, Dr. Kajiwara, Chiba Univ.)
Sensor vendor calibration
  Support and schedule yearly calibration
Radiance and wavelength of some sensors are calibrated by integration spheres and calibration lamps in JAXA (about twice per month)
  wide angle radiometers need special consideration
JAXA/GCOM-C science team has prepared some in-situ observation instruments for the satellite algorithm development and validation
e.g., Skyradiometer (POM-02), MS700 spectroradiometer (irradiance), Microtops-II sunphotometer, FieldSpec spectroradiometer, TriOS spectroradiometer (ocean), multi-band profiling radiometer (PRR2600, C-OPS), ocean optical backscatter sensor (HydroScat-6P), etc.

## Slide 18
6. Summary
The mission targets of GCOM-C are contribution to the climate system researches, the carbon cycle and the radiative forcing.
  It has 250-m resolution and along-track slant-view polarization observation
  Stable calibration: on-board diffuser with monthly moon observation
GCOM-C/SGLI will be launched in Japanese Fiscal Year 2016.
Proto-flight tests of GCOM-C satellite-system are on-going in JAXA Tsukuba Space Center
  The radiometric tests (SNR, dynamic range, linearity, gain stability, etc.) are carried out using integrating spheres
  Preliminary results of SNR meet the specification with some margin
Post-launch calibration of SGLI will be conducted by using on-board diffusers supported by lamp, moon and vicarious/cross calibration (e.g., cross calibration with AHI and through AHI)
In-situ instrument calibration is comfirmed by JAXA integration spheres