## Slide 1: Calibration Activities of GOSAT and GOSAT-2
Kei Shiomi
Japan Aerospace Exploration Agency
shiomi.kei@jaxa.jp
GSICS Meeting 2016
TKSC, Tsukuba, Japan
February 29, 2016

## Slide 2: GOSAT TANSO-FTS and CAI
Cloud and Aerosol Imager (CAI)
Thermal And Near infrared Sensor for carbon Observation (TANSO)
Fourier Transform Spectrometer (FTS)
Fourier Transform Spectrometer (FTS) | 
Mission | GHGs measurements
Band | SWIR-0.76µm, 1.6µm, 2.0µm bands with P/S polarization (O2-A, CO2, CH4, H2O band)
 | TIR-5.5~14.3µm (CO2, CH4, O3 band)
SPC Res. | 0.2cm-1
Swath | 750km(3 points every 260km)
IFOV | 10.5km
Cloud and Aerosol Imager (CAI) | 
Mission | Cloud detection and aerosol correction within FTS IFOV
Band | Nadir view 0.38, 0.67, 0.87, 1.60µm band
Swath | 750-1000km
Footprint | 0.5 and 1.5km
GOSAT on orbit since 2009
666km altitude
3 days revisit

## Slide 3: GOSAT on orbit since 2009
CAI L1B radiances
(0.38, 0.67, 0.87, 1.60 um)
and L2 cloud flag
FTS L1B spectra
with high spectral resolution and SNR
L4 CO2 and CH4 flux inversion with uncertainty estimate
L2 XCO2 and XCH4 distributions
with high precisions ~0.5% and 0.7%

## Slide 4: GOSAT operation summary
 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 -
Milestone | * launch |  |  |  |  | * * Solar paddle accident Unstable Pointing | * Switching Pointing mechanism
Nominal Pointing Pattern |  |  |  |  |  |  | 
Pointing system |  |  |  |  |  |  | 
FTS interferogram |  |  |  |  |  |  | 
V161.160 |  |  |  |  |  |  | 
V201.201 |  |  |  |  |  |  | 
5p-CT
3p-CT
3p-CT
1 &3 p-CT
The primary
Back up
No bias
800 fringes bias
Latest
Latest version
Re-processing (no geometry correction)
Re-processing (pointing error, biased interferogram corrected)
Latest version
GOSAT is operated with fully observations over 7 years since 2009, currently in extended operation phase.
GOSAT survived after overcoming two big events, satellite solar paddle accident (stop one of 2 paddles) and switching to redundancy pointing mechanism of FTS after unstable pointing of the primary one.
The latest 2 versions (currently v161.160 and v201.201) can be delivered to users.

## Slide 5: FTS and CAI observation on June 5 2015
Amazon dithering
West US targeted
LA, Oil field, RRV
Island tracing
3-point grid observation over land
Glint observation over ocean (extended high latitudes)
Challenging operation to get more effective observation points

## Slide 6: GOSAT calibrations
 | FTS |  |  |  | CAI |  |  | 
 | B1P/S 0.76um | B2P/S 1.6um | B3P/S 2um | B4 5.5-14.3um | B1 0.38um | B2 0.67um | B3 0.87um | B4 1.6um
Radiance | Vicarious calibration (1/year) Solar calibration （backside: 1/month） Lunar calibration (2/year) |  |  | Vicarious calibration (1/year) Inter-comparison (AIRS) | Vicarious calibration（1/year） Lunar calibration (2/year) Dark (Night observation: 1/month) |  |  | 
Spectral features | Fraunhofer line (spectral shift) ILS calibration (B2P/S: 1/month) |  |  | - | - |  |  | 
Geometry | FTS onboard-camera image is validated by using AVNIR-2. |  |  |  | Validated by using GSHHS |  |  | 
CAI
FTS onboard-camera
ILS cal.
Night obs.
FTS-TIR obs.
FTS-SWIR obs.
CAI obs.
Lunar cal.
Solar cal. (radiance, Fraunhofer)
Solar diffuser plate onboard FTS

## Slide 7: Status of GOSAT calibration
(1) TIR radiometric calibration (The latest FTS L1B v201)
Blackbody (BB) and Deep Space (DS) views for onboard calibration (2-time in dayside, 4-time in nightside)
Polarization correction (mirrors, beamsplitter, dichroic filters)
BB emissivity (EM evaluated by heated halo method at UW-Madison)
Sensor background temperature estimation
Vicarious calibration field campaign (with UW-Madison), Inter-comparison with AIRS
(2) UV-SWIR radiometric calibration (Radiometirc degradation factor)
Onboard solar diffuser monitoring per month
Vicarious calibration field campaign (with NASA/OCO-2, Ames), Lunar calibration (2009-2015)
FTS L1B v201 is added the best-estimated radiance considered with degradation
(3) Geometric correction
Pointing location evaluated by onboard IFOV camera
Best-estimated geolocation data in FTS L1B v201
Pointing offset angle for FTS observation plan is affected after the accessment

## Slide 8: Vicarious calibration campaign at Railroad Valley
Surface Spectral Reflectance
BRDF
Path 37
from West
Path 36
from East
19.9deg
19deg
33.0deg
25deg
Surface and Profile
of Pressure, Temperature, Humidity
Surface Thermal radiation
Variability
Aerosol Optical Thickens
TOA Spectral radiance
Surface
CO2 CH4
High altitude
Vertical
CO2 CH4
Horizontal
CO2 CH4
8

## Slide 9: Radiometric evaluation of FTS SWIR and CAI at RRV
Kuze et al., AMTD, 2016
FTS radiance
CAI radiance

## Slide 10: FTS SWIR solar diffuser monitoring
PM-B

## Slide 11: FTS TIR radiometric monitoring
Blackbody calibration
Deep space view calibration
PM-B Standby
PM-B
One solar paddle stop
After stopping one solar paddle, TIR sensitivity decreased 80%.
After switching to PM-B, there was no significant change.

## Slide 12: FTS TIR inter-comparison
The GOSAT TIR spectra are compared with Aqua/AIRS at Simultaneous Nadir Observations (SNOs).
- This work is collaborated with SSEC, Univ. Wisconsin-Madison.
The coincidences are located at mid-latitudes for AIRS. The spectral difference is evaluated in 0.5 K.

## Slide 13: FTS TIR long-time inter-comparison with AIRS
1
0
-1
-2
-3
-4
-5
-6
GOSAT v161 -AIRS dT [K] at CO2 689.5 cm-1
2009 2010 2011 2012 2013 2014 2015 2016
Solar paddle stop
Also TIR power down
Collaborated with SSEC, Univ. Wisconsin-Madison

## Slide 14: FS TIR long-time stability evaluated using SST
Night
Daily mean stdev (GOSAT-SST-iQuam) [Night]
stdev
SST Residual (GOSAT SST- iQuamSST)
2009/03/03~2015/03/16
Nighttime
Long-time stability

## Slide 15: Lunar calibration for GOSAT
Radiometric onboard calibration for FTS SWIR and CAI
For FTS, gazing the moon by the satellite pointing with half IFOV
For CAI, scanning the moon by the satellite pitch motion
Once a year (also with backup, i.e. total twice)
Bright and stable target with observation phase angle of 7 degrees near full-moon
FTS-SWIR band
(TIR off)
CAI
Phase ~7 deg near full-moon
North
South

## Slide 16: CAI lunar calibration result
Band4
CAI lunar observation on 28 April 2010. Images are oversampled in along-track direction.
12 pixels
4 pixels
R:Band1
G:Band2
B:Band3
Band4 IFOV is broader than the identical. It might not be well-evaluated.
Band1-3 radiometric trends are evaluated well.
Raw image
Resampled

## Slide 17: GOSAT-2 TANSO-2 FTS-2 and CAI-2
Cloud and Aerosol Imager -2 (CAI-2)
Fourier Transform Spectrometer -2 (FTS-2)
Thermal And Near infrared Sensor for carbon Observation -2 (TANSO-2)
GOSAT-2 on orbit in early 2018
Fourier Transform Spectrometer -2 (FTS-2) | 
Mission | GHGs measurements
Band | SWIR-0.76µm, 1.6µm, 2.0-2.3µm bands with P/S polarization (O2-A, CO2, CH4, H2O, CO band)
 | TIR-5.5-8.4, 8.4-14.3µm (CO2, CH4, O3 band)
SPC. Res. | 0.2cm-1
Swath | 850km with all targeted observations every 4sec
IFOV | 9.7km
Cloud and Aerosol Imager -2 (CAI-2) | 
Mission | Cloud and aerosol properties
Band | 2 off-nadir sights (+20 and -20deg) 0.34/0.38, 0.44/0.55, 0.67/0.67, 0.87/0.87, 1.64/1.64µm band
Swath | 1000km
IFOV | 0.5 and 1.0km
613km altitude
6 days revisit

## Slide 18: GOSAT-2 calibrations
 | FTS-2 |  |  |  | CAI-2 |  |  |  | 
 | B1P/S 0.76um | B2P/S 1.6um | B3P/S 2-2.3um | B4 5.5-8.4, 8.4-14.3um | B1/B6 0.34/ 0.38um | B2/B7 0.44/ 0.55um | B3/B8 0.67um | B4/B9 0.87um | B5/B10 1.64um
Radiance | Vicarious calibration (1/year) Solar calibration （backside: 1-2/month） Lunar calibration (1 / 2month) |  |  | Vicarious calibration Inter-comparison Lunar calibration BB thermistor evaluation | Vicarious calibration（1/year） Lunar calibration (1 / 2month) - Radiance by AT, PRNU by CT scan Dark (Night observation: 1/month) |  |  |  | 
Spectral features | Fraunhofer line (spectral shift) ILS calibration (B1P/S,B2P/S: 1/month) |  |  | - | - |  |  |  | 
Geometry | FTS-2 onboard-camera image is validated |  |  |  | Validated by using GSHHG |  |  |  | 
FTS-2
*SWIR for radiometry
*TIR signal output (upgrade)
*AT scan for radiometry
*CT scan for PRNU correction (upgrade)
CAI-2
GOSAT-2 lunar cal.
ILS cal.
Night obs.
FTS-2-TIR obs.
FTS-2 -SWIR obs.
CAI-2 obs.
Lunar cal.
Solar cal. (radiance, Fraunhofer)

## Slide 19: Summary
GOSAT is operated with fully observations of FTS SWIR and TIR bands and CAI over 7 years.
Calibration activities in 7 years
  TIR inter-comparison by Simultaneous Nadir Observations (SNOs) with AIRS
  SWIR vicarious calibration field campaign with in-situ measurements and aircraft over-flight collaborated with NASA OCO-2 and Ames.
Ongoing work
  Simultaneous Off-Nadir Observations (SONOs) for scan angle dependency evaluation
  Simultaneous observation at Railroad Valley with GOSAT and OCO-2
  GOSAT-2 calibration plan is under preparation based on GOSAT.

## Slide 21: GOSAT-2 specification
 |  |  | GOSAT-2 | GOSAT
Main body Size(m) X*Y*Z |  |  | 5.8 x 2.0 x 2.1 （Wing Span 16.5m） | 3.7 x 1.8 x 2.0 （Wing Span 13.7m）
Total Mass |  |  | 1800kg | 1750kg
Total Power |  |  | 5.0 kW(EOL) | 3.8 kW (EOL)
Life Time |  |  | 5 years | 5 years
Orbit |  |  | sun synchronous | sun synchronous
 | Local time |  | 13:00+/-0:15 | 13:00+/-0:15
 | Altitude |  | 613km | 666km
 | Inclination |  | 98deg | 98deg
 | Repeat |  | 6 days (89 revol.) | 3 days (44 revol.)
Launch |  | Vehicle | H-IIA | H-IIA
 |  | Schedule | JFY2017 | 23 Jan., 2009
TANSO-2 FTS-2
TANSO-2 CAI-2
TANSO-CAI
TANSO-FTS
GOSAT-2
GOSAT

## Slide 22
TANSO-FTS-2 Specifications
Items | GOSAT-2 TANSO-2 FTS-2 | GOSAT TANSO FTS
Measurement Gases | CO2，CH4，O3，H2O，CO | CO2，CH4，O3，H2O
Footprint size (FOV) | 9.7 kmf (15.8mrad) | 10.5 kmf (15.8mrad)
Spectral Ranges (mm)(cm-1) | band 1 : 0.75-0.77 (12,950-13,250) band 2: 1.56-1.69 (5,900-6,400) band 3: 1.92-2.33 (4,200-5,200) band 4: 5.5-8.4 (1,188-1,800) band 5: 8.4-14.3 (700-1,188) | band 1: 0.75-0.77 (12,900-13,200) band 2: 1.56-1.72 (5,800-6,400) band 3: 1.92-2.08 (4,800-5,200) band 4: 5.5-14.3 (700-1,800)
SNR | band 1: >400 (S@13,050cm-1) band 2: >300 (S@6,200cm-1) band 3: >300 (S@5,000cm-1) >250 (S@4,250cm-1) band 4: >300 (@1,300cm-1) band 5: >300 (@700cm-1) | band 1: >300 (345) band 2: >300 (322) band 3: >300 (412) band 4: >300 (304)
Observation Mesh | 160km (5 points in the CT direction) | 160km (5 points in the CT direction)
Scan duration | 4 seconds / interferogram | 4, 2, 1.1 seconds / interferogram
Sampling resolution | 0.2cm-1 | 0.2cm-1
Effective Aperture size | Φ73mm | Φ64mm
Gain steps | 16 | 2
Avoidance of the cloud | Intelligent pointing | -------

## Slide 23
TANSO-CAI-2 Specifications
Items | GOSAT-2 TANSO-2 CAI-2 |  | GOSAT TANSO-CAI
Spectral Ranges (nm) | Forward Viewing (+20 deg) b 1 : 333-353 b 2 : 433-453 b 3 : 664-684 b 4 : 859-879 b 5 : 1585-1675 | Backward Viewing (-20deg) b 6 : 370-390 b 7 : 540-560 b 8 : 664-684 b 9 : 859-879 b 10: 1585-1675 | Nadir Viewing band 1 : 370-390 band 2 : 664-684 band 3 : 860-880 band 4 : 1555-1645
Spatial Resolution nadir | except band 5, 10 band 5, 10 460m (700mrad) 920m(1,400mrad) |  | Band 1-3 Band 4 500m(750mrad) 1,500m(2,250mrad)
swath/FOV | every points on the earth to be observed at least twice a recurrent cycle |  | Band 1-3 Band 4 1,002 km / 72 deg 786km / 60 deg
SNR (@spectral-radiance/albedo) (W/m2/sr/mm) | b 1 : >200 (45/0.158) b 6 : >200 (48/0.152) b 2 : >200 (79/0.144) b 7 : >200 (65/0.125) b 3 : >200 (46/0.106) b 8 : >200 (46/0.106) b 4 : >200 (30/0.112) b 9 : >200 (30/0.112) b 5 : >200 (7/0.101) b 10 : >200 (7/0.101) |  | b 1 : >200 (47/0.149) b 2 : >200 (45/0.104) b 3 : >200 (29/0.108) b 4 : >200 (7/0.101)

## Slide 24: GOSAT-2 lunar calibration plan
TANSO-FTS-2
TANSO-CAI-2
On orbit in early 2018
Upgrade specifications from GOSAT | 
FTS-2 | Adding CO channel (2.3 mm)
CAI-2 | 2 off-nadir sights (+ 20deg and – 20deg) Adding 3 bands (0.34, 0.44, 0.55 mm) 0.5 and 1.0 km spatial resolutions
FTS-2
CAI-2
*AT scan for radiometry
*CT scan for PRNU correction (upgrade)
GOSAT-2 lunar cal
*SWIR for radiometry
*TIR signal output (upgrade)

## Slide 25
ILS cal.
Night obs.
FTS-TIR obs.
FTS-SWIR obs.
CAI obs.
Lunar cal.
Solar cal. (radiance, Fraunhofer)
Solar diffuser plate onboard FTS
ILS cal.
Night obs.
FTS-2-TIR obs.
FTS-2 -SWIR obs.
CAI-2 obs.
Lunar cal.
Solar cal. (radiance, Fraunhofer)

## Slide 26: Summary
GOSAT has operated lunar calibration around April and July every year since 2009 for radiometric calibration.
GOSAT targets the moon with observation phase angle around 7 deg.
CAI observes the moon with a linear array sensor of 0.38-1.6 microns by pitch (along-track) scan operation.
FTS observes the moon with a half size of the IFOV of 0.78-2.0 microns in high resolution. (not shown here)
GOSAT-2 will be upgraded in FTS-2 by adding 2.3micron channel, while CAI-2 by extending to 0.34 micron.
CAI-2 will also examine the photo response non-uniformity (PRNU) by yaw (cross-track) scan operation.