## Slide 1: Calibration activities of TRMM & GPM Radars
Takeshi Masaki, Kinji Furukawa, Takuji Kubota, Kaya Kanemaru,
Riko Oki*1,Toshio Iguchi ,Hiroshi Hanado, *2
Naofumi Yoshida *3
*1: Japan Aerospace Exploration Agency
*2: National Institute of Information and Communications Technology
*3:Remote Sensing Technology Center of Japan
February 29th, 2016 Annual Meeting of GRWG+GDWG at JAXA/TKSC

## Slide 2: Outline
1. Introduction
2. DPR Algorithm status
3. Calibration status
4. Summary

## Slide 3: Global Precipitation Measurement (GPM) mission status
GPM is an international mission consisting of the GPM Core Observatory and Constellation Satellites for high accurate and frequent global precipitation observation.
Dual-frequency Precipitation Radar (DPR)
  It was developed by JAXA and NICT
  The DPR is composed of two radars: KuPR & KaPR
GPM Core Observatory was successfully launched on 28 Feb. 2014 (JST).
The DPR has observed steadily.
All GPM standard products were released on September 2014.
New version products will be released in March 2016.
KuPR: 13.6GHz radar (phased array)
KaPR: 35.5GHz radar (phased array)
GMI (Microwave Imager)
Core
Observatory by NASA-JAXA
Constellation
Satellites by international partners
GPM Core Observatory
1. Introduction
Notes: GPM is an international mission consisting of the GPM Core Observatory and Constellation Satellites for high accurate and frequent global rainfall observation.
- Core Observatory: developed under NASA and JAXA equal partnership.
- Constellation satellites: provided by international partners (includes GCOM-W1)
Dual-frequency Precipitation Radar (DPR)
- developed by JAXA and NICT
- the most sophisticated precipitation radar
- 3D structure of rainfall
- simultaneous dual-frequency observation to detect even weak rainfall and snowfall.
GPM Core Observatory will be launched in early 2014.

## Slide 4
Completion of Precipitation Radar (PR) Normal Mission Operation on 7th October 2014, due to lack of fuel. Completion of PR extra operation on 1st April 2015.
Completion of TRMM Microwave Imager (TMI) on 8th April 2015.
The TRMM spacecraft re-entered the Earth’s atmosphere on June 15, 2015 over the South Indian Ocean
Launch | 28 Nov. 1997 (JST)
Altitude | About 350km (since 2001, boosted to 402km to extend mission operation）
Inc. angle | About 35 degree, non-sun-synchronous orbit
Design life | 3-year and 2month (completed on April 2015)
Instruments | Precipitation Radar (PR) TRMM Microwave Imager (TMI) Visible Infrared Scanner (VIRS) Lightning Imaging Sensor (LIS) CERES (not in operation)
US-Japan joint mission Japan: PR, launch
US: satellite, TMI, VIRS, CERES, LIS, operation
1. Introduction
Tropical Rainfall Measuring Mission (TRMM)

## Slide 5
Foot print size about 5km
Swath
KuPR：245km
KaPR：125km
Inclination
65 degrees
GPM/DPR
DPR (and PR) can observe three dimensional structure of precipitation.
Frequency
KuPR: 13.6 GHz
KaPR: 35.5 GHz
Fight
direction
Range resolution
KuPR：250m
KaPR：250/500m
Altitude
about 407km
1. Introduction
DPR specification

## Slide 6
2.4m
2.4m
0.6m
1.0m
0.6m
1.4m
450kg
330kg
At JAXA
KaPR
KuPR
Photograph of the DPR
1. Introduction

## Slide 7: GPM Core Observatory was successfully launched on 28 Feb. 2014 (JST).
Launch from the JAXA Tanegashima Space Center by the H-IIA F23 rocket
Separation of the spacecraft
NASA
JAXA
JAXA
CG image
GPM core observatory launch
1. Introduction

## Slide 8: NASA-JAXA Joint First Images from the GPM Core Observatory
JAXA/NASA
NASA/JAXA
NASA/JAXA
↑ GMI 36-GHz H TB is overlaying to the Geostationary IR provided by JMA and NOAA.
↑ Three dimensional structure of precipitation captured by DPR.
→Surface precipitation captured by GMI.
Extratropical Cyclone over the northwest Pacific Ocean (around 40N, 167E) around 1330Z on 10 Mar. 2014.
1. Introduction

## Slide 9
L0 product
HK / Science Telemetry
Observation data
Satellite altitude
Sensor Temperature
Sensor Status etc
＜APID sorted Data＞
L1 algorithm
Transformation and Calibration
Transmitted/Received Power
Scan Time
Geolocation etc
＜Swath Data＞
L1 product
L2 algorithm
L2 product
L3 algorithm
L3 product
Calculate Physical value
Rain Rate
Rain Type
DSD (Drop Size Distribution)
Radar Reflectivity factor etc
＜Swath Data＞
Calculate Statistic value
Daily Mean
Monthly Mean
Grided data
＜Global Grid Data＞
power
geolocation
Rain Rate
Grided Precip Rate
DPR data processing flow
2. DPR Algorithm status
New version products will be released in March 2016.
Please access ‘ G-portal ’ to get the data.
https://www.gportal.jaxa.jp/gp/top.html

## Slide 10
The calibration of DPR is composed of ‘Internal calibration’ and ‘External calibration’
Internal Calibration
External Calibration
★
【Purpose】
To calibrate the FCIF-LUT which converts digital count to power.
【Frequency】
Per a week on board.
【Frequency】
It is planed 10 times in a year at the JAXA tsukuba space center in Japan.
Radio Frequency is not tramsmited to out of DPR
【Purpose】
To calibrate the absolute value of the DPR transmitted / received powers.
FCIF: Frequency Converter & IF
Concept of DPR calibration(1/2)
3. Calibration status
Notes: .

## Slide 11
FCIF-LUT by
Internal calibration
Transfer function
with offset by external calibration
Calibration
coefficients
Relationship between internal calibration
and external calibration
3. Calibration status
Concept of DPR calibration(2/2)

## Slide 12
Result of the internal calibration
The results of the internal calibration have been stable.
3. Calibration status

## Slide 13
Active Radar Calibrator (ARC)
The situation of external calibration
KuARC
KaARC
Concept of the external calibration(1/2)
W:717mm x D:700mm x H:2167mm
Weight: 130kg
Transmit power level : 1.2W
Transmit wave type : CW or Pulse
Two people treat two ARCs for KuPR and KaPR in once calibration.
The people need to carry out the calibration night and day, since the DPR has sun-asynchronous orbit.
3. Calibration status

## Slide 14
DPR receiver system
Received power
measured by DPR
Received power
estimated by calculation
DPR
JAXA aims that accuracy of the calibration becomes within ±1dB.
KaARC
Compare
DPR transmitter system
Transmitted power
estimated by calculation
DPR
Compare
KuARC
KaARC
KuARC
Transmitted power
measured by ARC
3. Calibration status
Concept of the external calibration(2/2)

## Slide 15
Trend of TRMM/PR calibration accuracies
【TRMM/PR calibration】
PR Transmitter System
PR Receiver System
The PR’s calibration is almost same as the DPR calibration method.
Calibration accuracies were satisfied within ±1dB in both transmitter and receiver system.
It means that both PR transmit system and PR receive system had worked well.
3. Calibration status

## Slide 16
DPR
DPR/
ARC2
PR
PR/
ARC
Absolute
Calibration
DPR σ0
PR σ0
Continuity
We need to conduct absolute calibration for DPR and PR while maintaining the continuity of σ0 of both.
The new version product which will be released in March 2016 satisfies the continuity of the σ0.
A slight offset bias seemed to exist in the results of the DPR external calibration.
The bias correction will not be applied in the new version product, since the DPR external calibration may have some error.
After a re-examination for the error, the bias correction may be applied in future algorithm.
Current status of the DPR calibration
3. Calibration status
Absolute
Calibration
It is very difficult to calibrate while keeping continuity of different sensors.
* σ0 is the good index for an inter-comparison between different sensors.

## Slide 17: 4. Summary
GPM Core Observatory was successfully launched on 28 Feb. 2014 (JST).
DPR has observed stably after the launch.
The new version product which will be released in March 2016 satisfies the continuity of σ0 between PR and DPR.
Some slight bias were found in DPR external calibration.
To increase the accuracy of calibration, JAXA is evaluating all calibration data in more detail.

## Slide 18: Information for DPR product
http://www.eorc.jaxa.jp/GPM/index_e.htm
https://www.gportal.jaxa.jp/gp/top.html
To get dataformat, news and so on.
To get DPR product.
Please access !!

## Slide 19: backup

## Slide 20: GPM / DPR calibration status and plan
GPM/DPR calibration is going well.
The internal calibration
  The DPR’s internal system is calibrated by this calibration.
  It has been conducted once per a week from the launch.
  It will be conducted same frequency in future.
The external calibration
  The absolute value of the DPR’s received and transmitted powers are calibrated by this calibration.
  It has been conducted 10 time in a year.
  It will be conducted same frequency in future.
To increase the accuracy of calibration, JAXA is evaluating these calibration data in more detail.

## Slide 21
＜External Calibration on Jun 14, 2015＞
Received power of KuPR
These figures show that received power of the DPR during external calibration on Jun 14th 2015.
The footprint where the received powers are high level shows that the DPR received the transmit power of ARC.
During the external calibration, the DPR observes 4 times density for cross track and 3 times density for along track corresponding to nominal observation.
3. DPR calibration status
Example of external calibration
nominal observation swath
Received power of KaPR
external calibration swath
★：ARC setting point
*The power is not calibrated in this figure.

## Slide 22
KaMS
KuNS
KaHS
PR
DPR：V04
PR：V7
sigma Zero (σ0) Measured
Monthly mean
sigma Zero (σ0) Measured
Deviation from PR
A slight offset bias seemed to exist in the results of the DPR external calibration (not shown) because of remaining issues for the DPR external calibration’s error.
After the re-examination of the error, the bias correction will be applied in future algorithm (it is not applied to new version products released in March 2016).
As for the new version products released in March 2016, the σ0 which is one of the calibration index satisfies continuity well between DPR and PR.
KaMS
KuNS
KaHS
Difference of the σ0 at incidence angle where SD is minimum.
KuPR – PR (dB)：
11.2 – 11.1 = +0.1
KuPR – KaMS (dB) ：
11.2 – 9.7 = +1.5
Over
ocean
Results of calibration for the DPR
15
10
5
0
-5
(dB)
0
(dB)
2
4
-2
-4
3. Calibration status

## Slide 23
Received power of KuPR
Received power of KaPR
1
49
13
25
37
26
49
1
Horizontal range
(AngleBin number)
Vertical range
(RangeBin number)
Horizontal range
(AngleBin number)
KuPR
KaMS (Matched-beam with KuPR)
KaHS (High-sensitivity beam)
Nov 9th 2014
Flight
direction
dBm
Example of DPR L1 product
KaMS
KaHS
KuPR
Ground echo
Ground echo
Scan pattern
New version products will be released in March 2016.
2. Algorithm status
*The power is not calibrated in this figure.